## Slide 1: Divertor-localized fluctuations in NSTX-U L-mode discharges
F. Scotti1, S. Zweben2, V. Soukhanovskii1
1LLNL, 2PPPL
59th Annual Meeting of the APS Division of Plasma Physics
Milwaukee, WI, US
October 24, 2017

## Slide 2: Characterization of divertor-localized turbulence in NSTX-U via imaging of divertor fluctuations
Divertor fluctuations due to:
  Upstream turbulence (‘blobs’)
  Divertor-localized instabilities:
    First observed in MAST [Harrison PoP 2015], Alcator C-Mod [Terry, NME 2017]
Divertor-localized fluctuations observed in region where upstream turbulence is disconnected from divertor plate
  Imaging fluctuations via emission from different species to isolate fluctuations in different regions
Possible implications for divertor heat/particle fluxes, interpretation of divertor measurements
Characterization of divertor localized fluctuations in NSTX-U
  Statistical properties, correlation lengths, radial localization, dynamics

## Slide 3: New fast camera and high X-point L-mode discharges enabled near-separatrix filaments imaging in NSTX-U
NBI-heated NSTX-U L-mode discharges
  Lower divertor biased double null
  Ip = 650 kA, fG ~ 0. 3, BT=0.65T
  X-point height ~ 0.5 m (κ~1.8, δ~0.45)
Simultaneous imaging with 3 fast cameras
Passive D-α imaging at midplane for upstream turbulence (GPI view)
  100 kHz, 9μs exposure
Passive C III imaging in divertor
  Emission along divertor leg
  100 kHz, 9μs exposure
Passive D-α imaging in divertor
  Surface localized emission
  280 kHz, 3μs exposure

## Slide 4: Field-aligned filaments observed in inner and outer divertor legs
Spatial calibration enables projection of 3D structures and spatial localization of emission
High pass filtering and cross correlation employed for analysis
Intermittent filamentary structures on both inner and outer divertor leg
  Observed in lower divertor biased or double null shape with attached plasma conditions
1ms average
Raw image
High pass

## Slide 5: Divertor leg fluctuations are proportional to ~ ñe, no correlation with upstream fluctuations
Broadband fluctuations at 10-50 kHz, δI/I ~10-20%, lifetime ~50-100 μs
Intensity fluctuations ~ ñe
  C III and D-α fluctuations are correlated (up to 0.7, peaked at zero delay)
Comparable near-Gaussian PDF for inner and outer legs filaments
No correlation with upstream turbulence
  Cf. correlation observed for SOL blobs
Flute-like filament shape suggests generation in divertor region

## Slide 6: Field-aligned fluctuations, no correlation between inner and outer leg filaments
Zero-delay cross corr. of pixel with rest of images over 5 ms
No correlation inner to outer
Poloidal correlation lengths 1-3 cm ~ 10-50 ρi
Parallel correlation lengths ~ 3m
Toroidal mode number for outer leg filaments ~10-20
Field-aligned, radially localized around leg
  Inner leg filaments localized to private flux region

## Slide 7: Outer leg filaments are connected to target plate, radially localized to strike point
Top-down view via D-α emission provides imaging of filaments footprint
Zero delay cross corr. at different radii:
  In SOL cross correlation regions are spirals with uniform toroidal cross correlations
    Footprint of upstream blobs
  Approaching LCFS cross correlation regions have finite toroidal correlation length, radial corr. lentgth ~1-2 cm
    Footprint of divertor filaments
  No correlation regions observed in private flux region

## Slide 8: Inner and outer leg filaments rotate in opposite toroidal direction, poloidal velocity ~1 km/s
Time-delayed cross corr. for average filament propagation
Poloidal motion (1-2km/s) for inner/outer leg filaments towards X-point
  Propagation reversal for inner leg filaments at low upstream density
Outer leg filaments propagate in counter current direction
  Small but finite radial propagation observed
  Opposite rotation to footprint of SOL blobs (downward poloidal motion)
Multi-fluid UEDGE simulations with full cross field drifts model
  Filament velocity in outer leg qualitatively consistent with UEDGE estimates for ExB velocity
Divertor leg
filament

## Slide 9: Summary
Observation and characterization of near-separatrix divertor-localized fluctuations in NSTX-U
  Intermittent filaments in C III, D-α emission on divertor legs with no correlation with upstream blobs
  Localized in private flux region on inner leg, separatrix on outer leg
  Comparable poloidal and radial correlation lengths (1-3 cm)
  Apparent filament motion is towards X-point on both legs
  Shape, dynamics and absence of upstream correlation suggest fluctuations are generated and localized on divertor legs
  Consistent observations with MAST, Alcator C-Mod