## Slide 1
Fast Time Response Electromagnetic Particle Injection System for Disruption Mitigation (EPI)
1R. Raman, W-S. Lay1,
1T.R. Jarboe, 2J.E. Menard, 2M. Ono
1University of Washington / 2PPPL
25 October 2017
APS DPP 2017 – PO4.00003
Milwaukee, WI
NSTX-U
Supported by
College W&M
Colorado Sch Mines
Columbia U
Comp-X
General Atomics
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec
This work is supported by US DOE contract numbers
DE-SC0006757 and DE-AC02-09CH11466

## Slide 2: Limitations of Present DM Systems
Most of the DM databases is from MGI experiments, but MGI has been dropped by ITER due to its slow response time.
    But, the MGI valve propels the SPI pellet
The speed of the un-fragmented high-mass / high-Z SPI pellets is about 200-300 m/s due to the use of gas propellant
    Shattering process further reduces fragment velocity
Because of the slow speed and size of the fragmented particles, the penetration depth will be severely restricted in high power ITER discharges
Will the SPI fragments penetrate sufficiently deep into the much more energetic ITER H-mode pedestal?

## Slide 3: There is Dramatic Difference in SPI Penetration in Low and High-Power DIII-D Plasmas

## Slide 4: DIII-D SPI Injection Movies (R. Moyer – UCSD / DIII-D)

## Slide 5: How does the EPI concept address present limitations?
The EPI concept injects grains of material (of the required size) and at the required velocity – & it does this on a fast time scale (2-3ms)
Because of this - one can precisely calculate the needed size / velocity combination of a spherical particle for penetrating to the center of any given plasma, including the ITER plasma

## Slide 6: How Does the EPI System Achieve These Essential Parameters for a Reactor DMS?
The EPI system accelerates a sabot
The sabot is a metallic capsule that can be accelerated to high-velocity using an electromagnetic impeller
At the end of the acceleration, within 2-3ms, the sabot will release granules of known velocity and distribution – or a Shell Pellet
The primary advantage of the EPI concept over SPI and other gas propelled systems is its potential to meet short warning time scales, while accurately delivering the required particle size and materials at the velocities needed for achieving the required core penetration in high power ITER discharges.
  Delivers radiative payload to the the core where the RE channel is generated

## Slide 7: The Ambient B-Field of a High-Field Tokamak such as ITER Can be Used to Improve Device Efficiency
Injector can be positioned very close to the vessel, which further improves the system response time
Use high-field SC boost coils (>8T) if located outside port plug

## Slide 8: ITER Scale Injector Should Attain 1 km/s in ~1 ms
@ 8T cap bank only 2x
DIII-D-scale system

## Slide 9: Small Scale System Built To Test Critical Parameters (Sabot motion tracked using magnetic Probes)

## Slide 10: Sabot Motion also Tracked Using Fast Video Camera

## Slide 11: Measured EPI system parameters with 0.3T B-field augmentation in agreement with simulation predictions
University of Washington

## Slide 12: Next Step is to Conduct an EPI Test on a Tokamak Vacuum Chamber Dimensions (1.5m x 0.6m x 0.5m)

## Slide 13: EPI can Deliver Radiative Payload Deep into the Tokamak Plasma on a Fast 2-3 ms Time-scale
EPI concept accelerates a metallic sabot to high velocity, which releases grains of particles of the required size and velocity
The EPI system has features needed for a reactor DMS
  Can deposit payload in the RE channel – triggering an inside out thermal quench
  It uses a single reliable actuator, and payload that is solid at room temperature – so it should be very reliable
  It can be located close to vacuum vessel further improving response time
Off-line setup at U-Washington has demonstrated key aspects of concept, including 150-200 m/s velocities with 1.5ms response time consistent with calculations
Tokamak tests are the next logical next step for concept development
  Develop experimental data base on solid particle injection for theory simulations