## Slide 1: Power exhaust scenarios & control for projected high-power NSTX-U operation
J.E. Menard, S.P. Gerhardt, C.E. Myers, A. Brooks, M. Mardenfeld (PPPL)
M.L. Reinke (ORNL)
NSTX-U Research and Engineering teams
59th Annual Meeting of the APS Division of Plasma Physics
Milwaukee, WI
October 23 – 27, 2017

## Slide 2: Abstract / Motivation
An important goal of the NSTX Upgrade (NSTX-U) research program is to characterize energy confinement in the low-aspect-ratio spherical tokamak configuration over a significantly expanded range of plasma current, toroidal field, and heating power, while increasing flattop durations to ~5 seconds.
However, the narrowing of the scrape-off layer at higher current combined with an improved understanding of expected halo-current loads has motivated a significant re-design of NSTX-U plasma facing components in the high-heat-flux regions of the divertor.
In order to reduce the expected divertor heat flux to acceptable levels, a combination of mitigation techniques will be used: increased divertor poloidal flux expansion and divertor radiation, and controlled strike-point sweeping.
The machine requirements for these various mitigation techniques are studied here using a newly implemented reduced heat-flux model.
Systematic equilibrium scans are used to quantify the required divertor coil currents and to verify vertical stability for a range of plasma shapes.
Free-boundary control schemes to constrain the strike-point location and field-line angle-of-incidence are also described.

## Slide 3: NSTX facility upgraded to access new physics using 2 major new tools:
Higher T, low n* from low to high 
 Unique regime, study new transport and stability physics
Full non-inductive current drive
 Not demonstrated in ST at high-T
Essential for any future steady-state ST
2. Tangential 2nd Neutral Beam
1. New Central Magnet

## Slide 4: NSTX-U integrated performance goals
2× toroidal field (0.5  1T)
2× plasma current (1  2MA)
5× longer pulse (1  5s)
2× heating power (5  10MW)
4× divertor heat flux ( ITER levels)
Up to 10× higher nTE (~MJ plasmas) and energy injected into vessel
2. Tangential 2nd Neutral Beam
1. New Central Magnet

## Slide 5: NSTX confinement increased at higher Te
Normalized electron collisionality ne*  ne / Te2
ITER-like scaling
ST-FNSF
?
constant q, b, r*
NSTX Upgrade
NSTX
Will confinement trend continue, or look like conventional A?

## Slide 6: Rationale for 1T, 2MA, 10MW requirement
2× increase in plasma current IP and toroidal field BT sufficient to differentiate between conventional (ITER 98y,2) and low-A (ST) H-mode confinement time t at higher plasma temperature and/or density:
2× heating power P needed to access high enough stored energy to access wide range of b at 2× higher field and current: bN ≤ ~4.5-5.5, bT ≤ ~15-20%

## Slide 7: NSTX-U magnet pulse duration requirement arises from goal of achieving current profile equilibration
Current redistribution time tCR  Te3/2  longest for highest confinement, lowest density
Physics ranges of interest:
  Normalized confinement: H98y2 = 1-1.5, HST ≤ 1
  Normalized density fGW = 0.5-1 – lower range for low n*
Longest tCR ~1.8s - for H98y2 = 1.4-1.5, fGW = 0.5-0.6
  This H98y2 and fGW combo accessed only transiently on NSTX
  Significant physics R&D needed to access such plasmas
Access then measure stationary profiles  Dtflat ~3tCR
3tCR ~ 5-5.5s  motivates goal of 5s IP flat-top

## Slide 8: Achievable pulse-lengths and Dtflat / tCR Constraint: maximum IP flat-top duration = 5s (set by TF)
Flat-top durations range from ~2.7 to ~6.3 tCR
Nearly all cases (97%) meet or exceed ~3 tCR
H98y2 ≥ 1.2: Dtflat = 5s for all fGW
Dtflat < 5s at lower H (high fGW)
Note: NSTX-U accessed H98y2 ~ 1.1-1.15 during initial ops

## Slide 9: Boundary shaping flexibility drives PF coil and structural requirements for plasma operation
2MA, 1T: 32 shapes × 3 OH states = 96 equilibria

## Slide 10: 96 scenarios primarily higher-k, lower-li high-performance H-modes (bN ~ 5)
Higher li ~1-1.5 L-modes not included in design requirements  L-mode IP < 2MA, Dtflat < 5s
2MA, 1T: 32 shapes / 96 scenarios

## Slide 11: Operating k depends on range of stable internal inductance (& impacts power-exhaust solution)
k = 2.8
k = 2.5
Internal inductance depends on bootstrap and NBI current profiles which depend on thermal transport
Risk: No NSTX-U transport data yet at high BT, IP, k
  This confinement physics data is a key motivation for the Upgrade in the first place!

## Slide 12: Reduced heat flux model

## Slide 13: Parametric fits to divertor heat flux
T. Eich, et al., Nucl. Fusion 53 (2013) 093031, Eqn 1

## Slide 14: Model for SOL heat flux width lq
T. Eich, et al., Phys. Rev. Lett. 107 (2011) 215001
  Equations 5, 7-10  Goldston heuristic drift model for lq
Use

## Slide 15: Data for private flux region width wpvt=S
M. Makowski et al., Phys. Plasma 19, 056122 (2012)
T. Eich, et al., Nucl. Fusion 53 (2013) 093031

## Slide 16: Generalized divertor heat-flux model consistent with Eich parametric fitting

## Slide 17: Choice of S for NSTX-U calculations
Options:
  SMak = S from Makowski scaling
  Srel = MIN(S / lq) × lq = 0.15 × lq
    MIN(S / lq) = 0.15, 0.17 for NSTX, MAST
  Sfix = fixed / constant value of S
NSTX-U model uses combination of all these options as follows:
  First set S = MIN( [SMak, Srel] )
  Then enforce Smin  S  Smax
    Smin = 0.1mm, Smax = 0.5mm
  S typically set by S = Srel  0.2-0.3mm
  S = 0.15 × lq  Smak(fG = 0.4, 2MA, 1T)
     Consistent w/ physics/ops goal fG ≥ 0.5

## Slide 18: Model for power conducted to divertor target
Pheat = total heating power (ohmic + auxiliary + alpha)
frad = fraction of heating power radiated from core
  For NSTX-U projections assume frad = 0.3
Prad = frad × Pheat = power radiated from core
Psol = Pheat × (1-frad) = power into SOL
Ndiv = Number of in/out divertor legs connected to target
  Ndiv = 1 for single null (SN), Ndiv = 2 for double null (DN)
fobl = fraction of power to outboard divertor leg(s)
  For NSTX-U projections assume fobl = 0.8 for DN, 0.65 for SN
fibl = (1-fobl) = fraction of power to inboard divertor leg
fleg = fobl or fibl = fraction of power to chosen divertor leg
Pdiv = Psol fleg / Ndiv = power conducted to divertor target

## Slide 19: NSTX example: low d, IP = 0.8MA
EFIT02
IP = 0.8 MA
Pheat = 6 MW
frad = 0.3
fobl = 0.8
fG = 0.624
S = SMak
D. Gates et al. Phys. Plasmas 13 (2006) 056122
EFIT02
IP = 0.8 MA
Pheat = 6 MW
frad = 0.2
fobl = 0.65
fG = 0.605
S = SMak

## Slide 20: NSTX example: high d, IP= 1.2MA
V.A. Soukhanovskii et al Nucl. Fusion 49 (2009) 095025
LRDFIT06
IP = 1.2 MA
Pheat = 6 MW
frad = 0.3
fobl = 0.65
fG = 0.6
S = SMak

## Slide 21: Strategies for Mitigating Heat Fluxes
Increase poloidal flux expansion
  changes the amount of wetted area on divertor, but also makes for shallow angles
Strikepoint sweeping in time
  use PF coils to move the strike point back and forth across the surface
Increase radiation fraction (30% assumed in models)
  contingency due to uncertainty of compatibility w/ physics goals
  adding new divertor fueling locations to help us exploit radiative exhaust
Div. Temperature, Heat Flux
Energy Conf. Time
how we move on this plot is a research focus of the fusion program worldwide

## Slide 22: Comments on comparison to NSTX and extrapolation to NSTX-U
Have looked at very limited number of NSTX cases
  frad = 0.2-0.3 and S = SMak might be reasonable scaling assumption for NSTX / NSTX-U
    Peak heat fluxes can match, but exact profile shapes differ
    There is substantial uncertainty in both frad and SMak
  Need DIVSOL TSG to identify more cases for comparison
  More detailed analysis of NSTX S-scaling would be valuable
For scaling to NSTX-U, use more conservative (i.e. smaller) S = Srel = 0.15 × lq
Detachment is option for reducing NSTX-U heat-flux
  Showed reduction of q by ~50-70% in NSTX
  Prefer not to rely on detachment for NSTX-U scenarios
    Beneficial to have more operating margin if PFCs will allow

## Slide 23: NSTX-U projection example: high d, IP = 2MA with high flux expansion divertor
A = 1.75, k = 2.74, balanced DN
IP = 2MA, BT = 1T, Pheat = 10MW
lq-mid =1.97mm, S/lq = 0.15
Poloidal flux expansion = 36
  Also assume B-field angle of incidence qB must be ≥ 1 (tile alignment / leading edge tolerance)
Radiation fraction = 30%
80% of power to outboard
50-50 split between upper/lower
Pdiv ~ 2.8MW to divertor target
qdiv-peak = 7.8 MW/m2
PF1A, C used
PF1B not used
qB = 1.1

## Slide 24: Example case from 96 with high IPF1A
A=1.84, k=2.5, dU, L = 0.193, 0.375, IOH=0, IPF1AU,L = 15, 7kA
qpeak ~20-25MW/m2
Dtflat < 1s without sweeping or other mitigation

## Slide 25: Example: Scan 1: No PF1B, use PF1C for high flux expansion IBDH tile heat flux projections
HD model lq
S / lq = 0.15
frad = 0.3

## Slide 26: Elongation Impacts Use of Poloidal Flux Expansion
Low-k shapes have x-point far from PFCs have useful scientific value
  Ip = 1 MA, PNBI = 3 MW L-mode
  flux expansion < 3, field line angles > 10 deg
  high stationary heat flux (> 6 MW/m2)
Increasing kappa and moving x-point closer to targets can mean higher Ip, PNBI are ‘easier’
  IP=1.00 MA, BT=0.75 T, 7.5 MW: qpeak ~ 12 MW/m2
  IP=1.25 MA, BT=0.75 T, 8.0 MW: qpeak ~ 7 MW/m2
Shape/heat flux coupling stronger in STs
qpeak ~ 12 MW/m2
qpeak ~ 7 MW/m2

## Slide 27: Initial Modeling of Sweeping Shows Benefits (Implemented in reduced model by M. Reinke, ORNL)
A
B
C
A
B
C
C
Single Equilibrium
Peak Across Scan
Time Averaged
assemble individual equilibria and interpolate
2 MA
1 T
10 MW
qperp

## Slide 28: HHF Tile Designs Converged to ‘Small Cubes’
larger tiles ‘bow’, enhancing stress, small cubes relieve this by ‘mushrooming’
design criteria using Tlimit ~ 1600 oC, and allowable stresses of 50% material limit
scoping simulation show Tmax = 2100 oC, max compressive stress of 55.8 MPa (86% of allowable) and max tensile stress of15.4 MPa (51% of allowable)
  example of design that is ‘temperature limited’ and not ‘stress limited’
compressive stress
tensile stress
temperature
ANSYS simulation of 10 MW/m2 for 5 sec onto isotropic graphite at normal incidence
30 mm
40 mm

## Slide 29: Developing Designs Using Castellated Tiles
Designs working to avoid front-surface holes in HHF regions
Side-access through removing low-heat flux tiles w/ front surface holes
Ex: cam-like action secures tiles against mounting plate/vessel
Beginning designs for inter/intra-tile diagnostics
example vertical divertor
cover HHF surfaces using 100 mm x 100 mm tiles made of 4 x 4 castellated ‘small cubes’

## Slide 30: Empirically Motivated Divertor Power Sharing (Implemented in reduced model by M. Reinke, ORNL)
NSTX only measured the outer, lower divertor heat flux
  model uses inner/outer split of 70/30 LSN and 55/45 USN, smooth transition in-between
MAST L-mode; Wenninger, IAEA 2016
LOWER NULL
UPPER NULL
C-Mod H-mode; Brunner APS 2016

## Slide 31: Tile Shaping Used to Avoid Leading Edges
exaggerated example
Small ramp toroidally,
  driven by max field line expected,
  impacted by alignment uncertainty,
This reduces wetted area (increases : ‘enhancement factor (EF)’
Large poloidal expansion leads to shallow attack angles,

## Slide 32: Method for simultaneously controlling strike-point position and angle of incidence
R
Z
Divertor target
n

t

BP
ap
Implemented in PPPL IDL-ISOLVER: Works well with all 3 divertor PF1 coils

## Slide 33: Summary
NSTX-U redesign of high-heat-flux PFCs motivated by projected narrowing of SOL at high IP and improved understanding of expected halo-current loads
Systematic equilibrium scans used to quantify the required divertor coil currents and to verify vertical stability for a range of plasma shapes
Tile designs developed to handle high heat fluxes
Free-boundary control schemes developed to constrain the strike-point location and field-line angle-of-incidence  supports use of fish-scaled tiles
Can support core confinement studies at the highest current, power, duration projected for NSTX-U