## Slide 1: Effects of the H species in the HHFW performance in NSTX/NSTX-U
Nicola Bertelli E.F. Jaeger (XCEL), R. W. Harvey (CompX), J.C. Hosea, E.-H. Kim, R.J. Perkins, G. Taylor, and E.J. Valeo, (PPPL)
APS-DPP 2017

## Slide 2: Abstract
One of the goal of NSTX-U is to operate at full eld (B = 1 T). For this magnetic field, the first and second harmonics of hydrogen (H) are located at the high-field side and in the core plasma, respectively. In principle, part of the high-harmonic fast-wave (HHFW) injected power can be absorbed by the H population reducing the electron and/or the fast-ion heating. For this reason, full wave simulations results of NSTX-U scenarios with different H concentrations for wave frequencies of 30 and 60 MHz will be presented and discussed. Plasma scenarios with and without neutral beam injection (NBI) will be considered. Furthermore, the balance between the beam ion and electron power absorption will be analyzed comparing both NSTX and NSTX-U plasmas.

## Slide 3: Outline
NSTX-U “Scenarios” considered
Antenna frequency = 30 MHz
  H Concentration scan
    w/ & w/o NBI
Antenna frequency = 60 MHz
  H concentration scan
    w/ and w/o NBI

## Slide 4: NSTX-U “Scenarios” considered (1)
NSTX-U plasma
  B = 1T
  Ion species: D, H, C, DBEAM
R [m]
Z [m]
rpol
ne
nD
n [x 1019 m-3]
rpol
Te
TD
T [keV]

## Slide 5: NSTX-U “Scenarios” considered (2)
NSTX-U plasma
  B = 1T
H concentration scan:
  nH/ ne = 1%
  nH/ ne = 2%
  nH/ ne = 5%
  nH/ ne = 10%
w/ and w/o NBI
Two antenna frequencies
  30 MHz and 60 MHz
Three nphi values: -5, -12, -21
Employed full wave code AORSA

## Slide 6: NSTX-U “Scenarios” considered (3)
NSTX-U plasma: B = 1 T and f = 30 MHz
D resonances
H resonances
R [m]
R [m]
Z [m]
Z [m]

## Slide 7: NSTX-U “Scenarios” considered (4)
NSTX-U plasma: B = 1 T and f = 60 MHz
D resonances
H resonances
R [m]
R [m]
Z [m]
Z [m]

## Slide 8
f = 30 MHz, H 1%, 2%, 5% and 10%
with NBI

## Slide 9: Power absorption vs. toroidal wave number
Electron absorption increases with larger nphi
(Fast) Ion abs. decreases with larger nphi
Not significant H power absorption for H 1% & 2%
H 1%
H 2%
nphi
nphi
Power abs [%]
Power abs [%]

## Slide 10: Power absorption vs. toroidal wave number
H 5%
H 10%
nphi
nphi
Not significant H power absorption for 5%
  except for nphi = |5| & H 10% and nphi = -5)
The “heating phase” (nphi = |21|) is quite good for electron absorption
Power abs [%]
Power abs [%]

## Slide 11: 2D Power deposition profiles (1)
10% H concentration case & nphi = -12
Electron power deposition
D thermal power deposition
W/cm3/MW
W/cm3/MW

## Slide 12: 2D Power deposition profiles (2)
10% H concentration case & nphi = -12
H power deposition
D-NBI power deposition
W/cm3/MW
W/cm3/MW

## Slide 13: Flux surface avg deposition profiles
10% H concentration case & nphi = -12
Electron & D-NBI power depositions peaked on axis
H power deposition localizedon 2nd H resonance
Thermal D & C are basically negligible
rpol
electron
D-NBI
H
D
Power density [W/m3]

## Slide 14: Flux surface avg. deposition profiles
2% H concentration
rpol
electron
D-NBI
H
D
Power density [W/m3]
nphi = -12
rpol
electron
D-NBI
H
D
Power density [W/m3]
nphi = -21

## Slide 15: Power absorption vs. H concentration
H power absorption increases with larger H concentration and decreases for larger nphi
In general, no significant impact by H concentration
  nphi = -21 case is basically independent from H concentration
H concentration [%]
nphi = -12
nphi = -21
H concentration [%]
H concentration [%]
nphi = -5

## Slide 16
f = 60 MHz, H 1%, 2%, 5% and 10%
with NBI

## Slide 17: Power absorption vs. nphi
Similar conclusions as f=30 MHz case
  Electron absorption increases with larger nphi
  (Fast) Ion absorption decreases with larger nphi
H 1%
H 2%
nphi
nphi
Power abs [%]
Power abs [%]

## Slide 18: Power absorption vs. nphi
H abs. increases with larger H concentration
nphi = -21 (“heating phase”) is quite good for electron abs.
No D & C contributions
H 5%
H 10%
nphi
nphi
Power abs [%]
Power abs [%]

## Slide 19: 2D Power deposition profiles (1)
10% H concentration case & nphi = -12
D-NBI
W/cm3/MW
H
electron

## Slide 20: Flux surface avg. deposition profiles
2% H concentration
Power density [W/m3]
Power density [W/m3]
electron
D-NBI
H
nphi = -12
rpol
rpol
electron
D-NBI
H
nphi = -21

## Slide 21: Power abs. vs. H concentration
H abs increases with larger H concentration and decreases for larger nphi
Power abs. is almost independent from H concentration

## Slide 22
Comparison between f = 30 and 60 MHz
H 1%, 2%, 5% and 10%
with NBI

## Slide 23: Power absorption vs. nphi (f = 30MHz solid, f = 60MHz dashed curves)
60 MHz case has higher fast ion abs. than 30 MHz case for nphi = -5 and -12
For nphi = -21, power abs. very similar between two cases
H 1%
H 2%
nphi
nphi
Power abs [%]
Power abs [%]

## Slide 24: Power abs. vs. nphi (f = 30MHz solid, f = 60MHz dashed curves)
Small H power absorption except for 10% concentration and lower nphi
H 5%
H 10%
nphi
Power abs [%]
Power abs [%]

## Slide 25: Conclusions for f = 30 and 60 MHz with NBI
Current drive phase (i.e, nphi = - 5) it seems to be bad
Large electron damping for nphi = -21 (i.e. heating phase)
  however, ~30% of power to fast ions
  NO significant differences between f = 30 and 60 MHz
For nphi = -5 and -12, higher fast ions abs. for 60 MHz case than 30MHz case
H absorption is significant (~10-30%) at low nphi and high H concentration (> 5%)
In principle, HHFW might modify either the electron or the ion temperature (through H species)
  Could be interesting for transport studies
  See cases without NBI below

## Slide 26
f = 30 MHz, H 1%, 2%, 5% and 10%
NO NBI

## Slide 27: Power absorption vs. nphi
For nphi = -12 and -21: dominant electron abs.
  Except for H 10%
Larger H absorption for higher H concentration
Possible H ions accelaration due to HHFW

## Slide 28
f = 60 MHz, H 1%, 2%, 5% and 10%
NO NBI

## Slide 29: Power absorption vs. nphi
Dominant electron abs. for all cases

## Slide 30
Comparison between f = 30 and 60 MHz
H 1%, 2%, 5% and 10%
NO NBI

## Slide 31: Power abs. vs. nphi (f = 30MHz solid, f = 60MHz dashed curves)
Dominant electron abs. for all nphi for 60 MHZ case
Significant H abs. for for nphi = -5 and -12 for 30MHz case

## Slide 32: Conclusions for f = 30 and 60 MHz without NBI
Large electron damping for all nphi for 60 MHz
No significant differences between f = 30 and 60 MHz cases for nphi = -21
Dominant H absorption for nphi = -5 and for 30 MHz case
Dominant electron absorption for nphi = -12 and for 30 MHz case & H concentration < 5%

## Slide 33: Future steps
Additional AORSA simulations for NSTX-U scenarios concentration scan
  B scan
  H concentration scan
  Temperature and density “scan”
  H plasma
  w/ & w/o NBI
  frequency = 15, 30, and 60 MHz
AORSA runs for NSTX cases (one or two cases)
  Temperature and density “scan”
  H concentration scan
  w/ & w/o NBI
Repeat simulations above with AORSA+CQL3D
  In case of H & NBI, consider both non-Maxwellian species