## Slide 1: Comparison of neutral density profiles measured using Da and C5+ in NSTXU
R.E. Bell, F. Scotti, A. Diallo, B.P. LeBlanc, M. Podestà, S. A. Sabbagh
59th Annual Meeting of the APS Division of Plasma Physics
Milwaukee, Wisconsin
October 23-27, 2017

## Slide 2: Abstract
Edge neutral density profiles determined from two different measurements are compared on NSTXU plasmas. Neutral density measurements were not typical on NSTX plasmas. An array of fibers dedicated to the measurement of passive emission of C5+, used to subtract background emission for charge exchange recombination spectroscopy (CHERS), can be used to infer deuterium neutral density near the plasma edge. The line emission from C5+ is dominated by charge exchange with neutral deuterium near the plasma edge. An edge neutral density diagnostic (ENDD) consisting of a camera with a Da filter was installed on NSTXU. The line-integrated measurements from both diagnostics are inverted to obtain local emissivity profiles. Neutral density is then inferred using atomics rates from ADAS and profile measurements from Thomson scattering and CHERS. Comparing neutral density profiles from the two diagnostic measurements helps determine the utility of using the more routinely available C5+ measurements for neutral density profiles. Initial comparisons show good agreement between the two measurements inside the separatrix.

## Slide 3: NSTXU Viewing Geometry
CHERS
Active
Sightlines
CHERS Background
Sightlines
ENDD
Sightlines
NB1
NB2
NB armor
SFLIP
CHERS Active views
  Charge exchange recombination spectroscopy measuring Ti, NC, Vf
  Optimized views across NB1
  Views CX emission and background emission for C5+
CHERS Background views
  View parallel to NB1
  View only C5+background emission
  Background measurement simultaneous with active measurement
ENDD
  Edge Neutral Density Diagnostic sightlines below midplane viewing upward
Second neutral beam (NB2) compromises CHERS Background views
  Bright CX emission contaminates background views

## Slide 4: NSTXU Viewing Geometry
CHERS Background
Sightlines
ENDD
Sightlines
CHERS Background views
  On midplane
  CHERS exposure 10 ms
  37 fibers in background view
ENDD
  Edge Neutral Density Diagnostic sightlines below midplane viewing upward
  ENDD exposure 3.7 ms
  Camera with Da filter
  Subset of 127 x 128 pixels used

## Slide 5: NSTX-U L-mode plasma
L-mode plasma
Brief H-mode 690-700 ms
Ip= 700 kA
neL
Te0
Ip
PNB
Da
H-mode

## Slide 6: Measured profiles of temperature and density are interpolated or extrapolated onto common fine grid

## Slide 7: Three Processes Contribute to C5+ passive emission
UNKNOWN:
  nC5+ Density of C5+
  n0 Density of thermal deuterium neutrals
MEASURED:
  E Emissivity of passive emission from C5+ n = 87
  ne Electron density
  nC6+ Density of C6+
COMPUTED:
  Qex Photoemission rate for electron impact excitation, [Te, ne]
  Qrec Photoemission rate for recombination from C6+ to C5+, [Te, ne]
  Qcx Photoemission rate for thermalthermal charge exchange [Te, ne, Zeff]
Excitation
Recombination
Thermal Charge Exchange

## Slide 8: Cannot independently determine both C5+ density and thermal neutral density
Determination of density of C5+ requires thermal neutral deuterium (n0) profile
Conversely, the thermal neutral density depends on the C5+ density or on the ratio of densities of C5+ to C6+

## Slide 9: Effective thermal-thermal charge-exchange rate is dominated by n=2 excited population fraction
Thermalthermal charge exchange rates for C6+ and D computed using ADAS 308 data.
Population fraction derived from ADAS photoemission coefficients, _________________________________________________________________________________or a from CollisionalRadiative model from DEGAS 2*
n=2 neutral fraction varies with electron density
n=2 population is less than a percent of the thermal neutral density
Contribution from n=1 ground state neutrals are only important at lower densities or low temperature
Effective CX rate:
*http://w3.pppl.gov/degas2/ehr3.dat

## Slide 10: At lower temperature (plasma edge), electron impact excitation can be neglected for carbon
For Te < 50 eV, the contributions to C5+ emission from electron impact excitation are negligible
Neglecting electron impact excitation:
Most of the emission is from thermal charge exchange (second term above is small)
This sets upper limit on thermal neutral density
Without electron impact excitation, knowledge of C5+ density is not needed to determine neutral density

## Slide 11: Neutral density is determined from Da emission
UNKNOWN:
  n0 Density of thermal deuterium neutrals
MEASURED:
  E Emissivity of passive emission from Da (n = 3-2)
  ne Electron density
COMPUTED:
  Qex Photoemission rate for electron impact excitation, [Te, ne]
Excitation rate

## Slide 12: Local carbon values are extracted from line-integrated measurements with a matrix inversion approach
Line integrated measurements
Spectral Brightness, Bl
Total Brightness,
Fitted Parameters
Amplitude, A
Line width, w
Line shift, (dl)
A
w
l0
l
Emissivity from Brightness
Subscript i refers to a particular sightline (line-integrated measurement)
Subscript j refers to a particular zone in the plasma (local value)
Lij is a matrix of path lengths
Line-integrated brightness (ph/s/cm2/st) can be related
to local emissivity (ph/s/cm3) by length matrix
Local emissivity is obtained using inverted length matrix
(Form for a Gaussian line shape)

## Slide 13: Local Da emissivity from line-integrated measurements with a matrix inversion approach
Line-integrated measurements
  Camera with 127 x 128 pixels
  Da filter
  Absolutely calibrated
Local tangency of sightline each pixel computed using EFIT equilibrium code
Tangency mapped to R at Z=0
Pixels binned to improve S/N
Emissivity from Brightness using matrix inversion with length matrix calculated for 3D geometry

## Slide 14: Neutral density profiles from C5+ and Da are comparable inside plasma edge
L mode plasma edge
Similar neutral density profiles over 45 cm inside LCFS
Neutral densities strongly diverge outside LCFS
n0 from C5+ exceeds n0 from Da by an order of magnitude just a few cm away from edge
n0 C5+
n0 Da
Various curves reflect range of assumed C5+/C6+ density ratio
Electron impact excitation small outside this radius

## Slide 15: Some variation is observed in neutral density profiles inferred from C5+ and Da
L mode
L mode
H mode

## Slide 16: Better agreement between n0 measurements at higher Te
Ratio of neutral densities plotted for multiple time
Ratio trends toward 1 as Te increases
At higher Te, agreement within a factor of 2
At lower Te, ratio of neutral densities ~10
Plotting data vs. R shows strong deviation outside LCFS

## Slide 17: C5+ emission observed beyond the LCFS
R=145.8 cm
R=148.8 cm
R=150.3 cm
R=151.8 cm
R=153.2 cm
R=154.7 cm
R=156.1 cm
C5+
C2+
C5+
C5+
C2+
C5+
C2+
C5+
C2+
C5+
C5+
C5+ emission in SOL is inconsistent with local Te, Ne
C5+ emission is observed outside of C2+ emission shell

## Slide 18: Convective transport from “blobs” could explain “extra” C6+ beyond LCFS
C6+ lifetime ~ 10-9 sec
Distance into SOL ~ 5 cm
Blob velocity ~ 105 cm/s
Edge Te ~ 50 eV
Edge ne ~ 1013 cm-3
Edge n0 ~ 1011 cm-3
Total recombination rate for Carbon Z=6
Qrec(50 eV, 1013 cm-3) = 2.7 x 10-13 cm2/s
Total charge exchange rate for Carbon Z=6
Qcx(50 eV, 1013 cm-3) = 6.9 x 10-8 cm2/s
Characteristic Times:

## Slide 19: Neutral density from C5+ is overestimated outside LCFS due to “extra” C5+ emission
Emeas
Ecalc
Emeas-Ecalc
nC6+
n0Dalpha
The required photoemission rate, QCX*=QCX(Te*, ne*) corresponds to different values of electron temperature and density
Subtracting the expected emission from the measured emission shows an excess signal, (Emeas-Ecalc)
Measured C5+ emissivity exceeds that expected with local Te, ne measurements and Da neutral density measurement

## Slide 20: Measured emissivity is a time average of steady emission and intermittent “blob” emission
E0=0
E0
Dt1
Dt2
A. Inner radii
C. SOL
B. Intermediate
radii
Emeas, E0
Emeas
] E1
time
Emissivity
Eb
Emeas
Introduce a simple model to describe the measurements
Steady emission (E0) is consistent with local measured Te, ne
Intermittent “blob” (E1) emission would correspond to different values (Te*, ne*)
The “duty cycle” of the blobs is given as f
If the neutral density remains relatively constant, then in the SOL,

## Slide 21: Intermittent signal from fast Gas Puff Imaging (GPI) system
Signal from GPI across L-H transition
Estimated “duty cycle” of blobs ~ 8% during L-mode
ENDD and CHERS signals will be time-averaged over many milliseconds
L-mode
H-mode
Increasing R

## Slide 22: Other Comments
n=2
n=3
n=4
Reflections (ruled on for NSTX-U views) might cause unexplained emission in edge
n0 from Da is an upper limit due to contributions to emission from molecular D2
The effective thermal-thermal charge exchange rate for carbon does not take into account contributions from n=3 and n=4 levels

## Slide 23: Summary
Neutral density measurements made with C5+ emission and Da emission
Neutral density profiles agree within a factor of 2 inside the LCFS for L-mode plasmas
Neutral density profiles outside the LCFS deviate up to an order of magnitude
C5+ emission is observed in SOL
Estimate of necessary photoemission rate outside LCFS suggests higher Te, Ne values than local measurements
Convective transport (blobs) of C6+ could explain 'extra' C5+ emission in SOL