## Slide 1: Integrated Tokamak Modeling: when physics informs engineering and research planning
Francesca M. Poli
Princeton Plasma Physics Laboratory
Notes: Transition between topics – summary of previous
Need to explain the figures: axes, plots.
Choice of words: non-axisymmetric instead of 3D
Write down more words to help me remember what I need to talk about
Self-consistent vs more comprehensive / complete
EP transport OR EP induced instabilities

## Slide 2: For sending material for this tutorial, many thanks go to:
USA: N. Bertelli, M. Boyer, N. Ferraro, W. Guttenfelder, D. Pfefferle, M. Podesta (PPPL), I. Krebs (PPPL/IPP), V. Soukhanovskii (LLNL), D. Green, J-M Park (ORNL), S. Kruger, T. Jenkins (TechX), P. Bonoli, N. Howard, S. Shiraiwa, J. Wright (PSFC), T. Rafiq (Univ. Lehigh)
EU: J. Citrin (DiFFer), E. Militello Asp, F. Koechl (CCFE)
JAPAN: N. Hayashi (QST), A. Fukuyama (Univ. Kyoto)
ITER Organization: X. Bonnin, Y. Gribov, S-H Kim, R. Pitts

## Slide 3: Fusion plasma physics encompasses a wide range of spatial and temporal scales
10-10
10-8
10-6
10-4
10-2
100
102
104
10-6
10-4
10-2
100
102
Wave propagation
wEC-1
wIC-1
wLH-1
tA
Plasma turbulence
Macroscopic stability
Transport current diffusion
tE
tR
tD
Full wave solvers
<1M CPU Hours
Gyrokinetic codes
<10M CPU hours
MHD codes
time (s)
space (m)
ITER
Equilibrium and
transport solvers
<102 CPU hours

## Slide 4: In a tokamak all temporal and spatial scales are coupled
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
Microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 5: In a tokamak particles and energy are ‘confined’ by magnetic fields
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
Microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 6: and they can also ‘flow’ along open magnetic field lines
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
Microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 7: Plasmas in a tokamak are in contact with the ‘wall’
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
Microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 8: Plasmas in a tokamak need to be ‘heated’
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
Microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 9: Plasmas need frequent pit stops for ‘re-fueling’
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 10: A different perspective on integrated modeling: looking at a tokamak with the eye of an engineer
Goal: simulate an entire plasma discharge from startup to termination optimizing ACCURATE PHYSICS and FAST TURNAROUND
  High fidelity physics at the core of time-slice integrated modeling
  Verified and validated reduced models at the core of (time-dependent) integrated modeling
Notes: Restricted range of applicability => this is where the verification enters and where the validation enters.

## Slide 11: We model tokamaks to understand experiments and to design stable and reliable reactors
[Fig. 1 - G. Jackson et al, Phys. Plasmas 17 056116 (2010)]
Experiment on DIII-D that simulates an ITER-like plasma
Heating and current drive (10-11-10-6s)
MHD equilibrium (10-6-10-2s)
MHD instabilities/turbulence (10-6-10-2s)
Density evolution (10-6-10-2s)
Neutral Beams (10-6-10-1s)

## Slide 12: A Whole Device Model (WDM) is a comprehensive picture of the complexity involved in modeling a tokamak
Extreme scale
First principle (Vlasov eq.)
Gyrokinetic codes
Full wave solvers
Advanced reduced
Fluid codes
Reduced full wave solvers
Reduced
Ray tracing codes
Neural networks
Validation
Experiments
uncertainty quantification
models and experiments
verification
[FES Integrated Modeling Workshop Report, 2015]

## Slide 13: A Whole Device Model (WDM) is a comprehensive picture of the complexity involved in modeling a tokamak
Extreme scale
First principle (Vlasov eq.)
Gyrokinetic codes
Full wave solvers
Advanced reduced
Fluid codes
Reduced full wave solvers
Reduced
Ray tracing codes
Neural networks
Computational time decreases:
millions CPU hours to minutes/seconds
Physics fidelity decreases
Verification/validation needed at each step
Time-slice
applications
Time-dependent
applications
Notes: NN: mention that you can use them for real-time control

## Slide 14
From high fidelity physics to reduced models
Combining two or more models for an integrated, converged solution on a time slice
Notes: Every time we use different sets of equations, but we need boundary conditions and input assumptions.
Here expand the bullet =>

## Slide 15
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 16: A plasma in equilibrium can be described by ideal MHD
[Credit, DIFFER website, The Netherlands]
Equilibrium condition:
j, B lie on nested surfaces
j, B, p are described by a flux function y
equilibrium entirely defined by:
Notes: Credit: Differ (replace comma)

## Slide 17
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 18: Ignited (burning) plasmas are dominated by alpha heating … but they need a boost from external sources before they can burn
minimum temperature for ignition => 15 keV
alpha heating dominates at temperature >5-7 keV
ohmic heating can heat plasmas only up to 3-5 keV
3.5MeV
nD + nT
50-50

## Slide 19: External sources do more than providing heating and current: they can provide momentum and control of MHD instabilities
RF antennas (IC, LH),
Gyrotrons (EC)
Neutral beams (NB)
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 6 | 3.2 | 1.4 | 1.2
NB
EC
IC
collisions
LH

## Slide 20: Perturbation of equilibrium enables description of waves propagation by representing the plasma with a dielectric tensor
Heating, current
profiles
density, temperature
Magnetic equilibrium
Dielectric tensor
full wave solver
(TORLH)
<106 CPU Hours
[courtesy of S. Shiraiwa (PSFC), VI2.00003]
CMod plasma

## Slide 21: Ray-tracing equations are accurate (and fast) approximations of high frequency wave propagation
ray-tracing
(GENRAY)
<10 minutes
Ray-tracing equations
dispersion relation
(another) CMod plasma
Heating, current
profiles
density, temperature
Dielectric tensor
Magnetic equilibrium

## Slide 22
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 23: Plasmas develop instabilities that can degrade performance
at specific locations (resonant surfaces)
they look like magnetic islands
they can be stabilized by
highly focalized beams of
high frequency (~100 GHz) waves
Courtesy of N. Ferraro (PPPL)
M3DC-1

## Slide 24: Self-consistent simulations of stabilization of magnetic islands can be done only in the framework of 3D nonlinear MHD
quasilinear corrections
to MHD equilibrium
to account for effect of waves
Ray tracing equations for
wave propagation
NIMROD/GENRAY
T. Jenkins (Tech-X)
Notes: Need to mention why this is a problem and why this is important.
Add bullet with goals?
Suppress instabilities by means of injected waves.
The waves are supposed to drive localized current.

## Slide 25: Reduced models are based on a Modified Rutherford Equation
Magnetic island evolution described by:
analytic expressions for instability threshold and driving
In a cylindrical approximation
Analytic expressions and fitting parameters for the stabilizing effect of RF waves
Notes: Need to mention why this is a problem and why this is important.
Add bullet with goals?
Suppress instabilities by means of injected waves.
The waves are supposed to drive localized current.

## Slide 26
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 27: Separation of scales enables representing (almost) any transport problem as a diffusion/convection-like problem
The goal is to obtain a set of diffusion-like equations of the form:
for a physical variable Q
identify the flux G
and the source and sink terms contained in S

## Slide 28: Understanding and modeling tokamak turbulent transport requires theory-based prediction of flux-gradient relationships
Gyrokinetic prediction
Reduced gyrofluid model
G. Staebler, Phys. Plasmas (2016)
State-of-the-art multi-scale (rire)
~50M CPU-hrs for 3-point scan
[N. Howard, Nucl. Fusion (2016)]
fluid eq. with right closure =>
Fit over limited set of GK
(< 1 sec with NN)
[Citrin NF 55 (2015), Meneghini, NF 57 (2017)]
6D Vlasov equations =>
5D nonlinear“gyrokinetic”
GYRO
TGLF
Notes: Add scales involved
Describe figure

## Slide 29
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 30: Steep gradient at the plasma edge drives MHD instabilities
Plasmas spontaneously develop a region (pedestal)
that encloses good confinement [P. Snyder FR1.00001]
MAST
The width and height of the pedestal can be determined
univocally by MHD calculations for a given value of density
Pressure (kPa)
Current (A/cm2)
Notes: add reference.
Steep gradientS [...] drive ...

## Slide 31: Efficient workflows allow combined solution of core transport and pedestal MHD stability
O. Meneghini, Phys. Plasmas 23 (2016)
Not yet a self-consistent solution:
model for pedestal density still missing
model for transition region that includes
microturbulence still missing
Electron temperature (keV)
Electron density (1019 m-3)
equilibrium
Core
transport
pedestal
Transition
region
700 cores
~minutes
Notes: I’d say “enable” instead of “allow”

## Slide 32: Replacing MHD stability pedestal calculations with a lookup table advantageous in time-dependent simulations
~6500 points cover the expected
ITER operational space
Plasma current
Pedestal density
Pedestal width (normalized poloidal flux)
Pedestal pressure (kPa)
[task under international collaboration]
A neural network has also been developed
[O. Meneghini, NF 57 (2017)]

## Slide 33
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 34: Where the plasma meets the wall: the Scrape-Off-Layer (SOL)
Courtesy of V. Soukhanovskii (LLNL)
SOL width determined by competition between parallel and perpendicular transport
Heat losses from the plasma can damage plasma facing components
R. Goldston, NF 52 (2012), PI3.00004

## Slide 35: Gyrokinetics simulations that extend the computation domain to the wall needed to develop reduced models for the edge plasma
We need a better model for the plasma edge,
Including the region inside the pedestal,
Microturbulence
coherent structures (blobs)
Separation of ion and electron scales
Wall sources
XGC
S-H Ku, DI2.00004
Notes: Mention time scales here.
Start text in bullets with capital letters

## Slide 36
External heating
Radiofrequency waves
Neutral beams
Fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
microturbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 37: Edge transport and fuelling are critical ingredients to model the plasma evolution in burning plasma conditions
PSOL
Courtesy of R. Pitts (ITER Organization)
Recombination zone
(Te<1eV)
Neutral friction zone
H0/D0/T0 ionization zone
(Te>5eV)
Impurity radiation zone
Heat conduction zone
Notes: Fueling
put in backup
Correct text color to be consistent with figure (cartoon on the right)

## Slide 38
External heating
Radiofrequency waves
Neutral beams
fueling
Gas injection
Pellets
The plasma is surrounded
by solid structures:
Plasma-material interactions
Confined plasma
(closed magnetic field lines)
Scrape-Off Layer plasma (SOL)
(open field lines)
turbulence,
ionization, recombination
radiation
MHD equilibrium/instabilities,
microturbulence,
energetic particles

## Slide 39: Modular coupling of 1.5D core and 2D edge transport implemented and validated on DIII-D steady-state plasma
  700 cores
  300 CPU-hr/iteration
  3-4 iterations
J-M. Park, D. Green (ORNL)
SOL
pedestal
Core transport
Neutrals transport
AToM SciDAC
equilibrium
pedestal
Wall sources
and sinks
Core
transport

## Slide 40: Integrated modeling on single time-slice has led to great insight
On small scales dynamics and multi-scale couplings
On how to plug-in models to describe the plasma from axis to wall
... but plasmas in tokamaks are dynamical, nonlinear systems …

## Slide 41: The other side of integrated tokamak modeling: an entire plasma discharge from startup to termination

## Slide 42: The basics …
A tokamak is like a transformer, where the plasma is the secondary winding

## Slide 43: In a transformer the circuits are magnetically connected
In the primary: IP(t) => BP(t)
In the secondary: IS(t) => BS(t)
Total magnetic flux density: B(t)=BP(t)+BS(t)
Limitation: it is pulsed, cannot operate continuously in steady-state
IP
IS
VP
VS
+
-
+
-

## Slide 44: In a tokamak the secondary circuit is a conducting fluid … … things get complicated
Transformer: source
of poloidal flux
Actuators (external)
Plasma (internal)
Central solenoid
Primary circuit
Plasma current
Secondary circuit
Toroidal field
Helical field
Poloidal field
Magnetic flux diffusion
transport

## Slide 45: A tokamak simulator needs to connect fast (transport) and slow (current diffusion) time scales
Transformer: source
of poloidal flux
Auxiliary
H&CD
External
momentum
a-heating
kinetic profiles
Heat, particle &
Momentum fluxes
Transport coefficients
Turbulent & neoclassical
Magnetic flux
diffusion
Conductivity
profiles
Self-generated
current
Actuators (external)
CD
H
Fuelling
& pumping
Wall sources
and sinks
Plasma (internal)
adapted from Politzer NF 45 (2005)
Notes: Fueling with 1 L
Change plasma (internal) color

## Slide 46: All the steps we take when we model an ITER plasma discharge
www.iter.org
Produce 500 MW of fusion power
Demonstrate integrated operation of technologies for a fusion power plant
Achieve a self-heated deuterium-tritium plasma
Test tritium breeding
Demonstrate safety of fusion devices
The goals of ITER: International Thermonuclear Experimental Reactor

## Slide 47: The first step is to get all coil currents and plasma shape right
Transformer source
of poloidal flux
Auxiliary
H&CD
External
momentum
a-particle
heating
P, T, n, v
profiles
Heat, particle &
Momentum fluxes
Transport coefficients
Turbulent & neoclassical
Magnetic flux
diffusion
Conductivity
profiles
Bootstrap
current
Actuators (external)
Plasma (internal)
CD
H
Fuelling
& pumping
Wall sources
and sinks
A GOOD EQUILIBRIUM SOLVER
to evolve the plasma boundary in response to the plasma-coil coupling IS CRITICAL (= free boundary solver)
Heating & Current sources: analytic
Transport: semi-empirical, analytic
HIGH FIDELITY PHYSICS NOT NEEDED
Notes: Before running the movie describe what this is = let it go 5 seconds and then start talking

## Slide 48: These simulations have been valuable to define and revise the ITER coil operational space and the plasma control capabilities
[C. Kessel et al, NF 49 (2009)]
New poloidal field coils layout expands operational space:
Flattop burn duration
Operation with broader current profile

## Slide 49
Simulations with simplified transport are designed to test engineering parameters, not to discuss physics
With assumptions on
transport, confinement to
satisfy target fusion power
Assessment of coil limits
[T. Casper et al, NF 54 (2014)]
Plasma termination is a critical area of ongoing research
CORSICA

## Slide 50
Simulations with simplified transport do not inform on plasma dynamic response to external actuators and internal MHD stability
Can this plasma really achieve the target?
How additional physics constraints affect the results?

## Slide 51: Physics-based models for thermal transport and current evolution can move the operational point away from target
current (MA)
Electron density (1019 m-3)
Alpha power (MW)
NB, IC, EC power (MW)
radiation (MW)
electron, ion temperature (keV)
alpha power Pa responds nonlinearly to
core transport and pedestal width and height
external power under feedback control
global MHD stability included in evolution of temperature and current
TRANSP
Plasma does not achieve the target of Pa=100MW
Notes: “away from initial target”

## Slide 52: Simulations with fully integrated 2D edge transport plasma have indicated the importance of fueling during ITER plasma termination
Pellet fueling at exit from H-mode needed to avoid accumulation of tungsten in the core
Model has been validated on JET, in dedicated ITER-like experiments.
JINTRAC
A. Loarte IAEA-FEC (2016)
F. Koechl, NF 57 (2017)
Time after start of ramp-down (s)
w/o pellets
pellets
Notes: Perhaps replace tags, e.g. Paux -> auxiliary power, Wplasma -> Plasma stored energy, nWax/nwped -> central accumulation of impurities, ...
Put labels “w/o and w pellets”
Big red arrow that points to Tungsten.
Be consistent in the references

## Slide 53: The path forward to an all-inclusive tokamak simulator
Reduced models:
  from nonlinear 3D MHD stability
  for edge plasma turbulence induced transport
  for wave propagation in the Scrape-off-Layer
  for energetic particle induced transport
  Plasma startup (SNU, Univ. Kyoto)
Notes: Simplify – “reduced models” only one

## Slide 54: The path forward to an all-inclusive tokamak simulator
Reduced models from nonlinear 3D MHD stability
  Plasma response to external perturbations
  Disruptions (trigger)
  MHD instabilities (onset, control)
  global instabilities, like sawtooth cycle [CP11.00113]
Reduced models for edge plasma turbulence induced transport
Reduced models for wave propagation in the Scrape-off-layer
Reduced models for energetic particle induced transport
Notes: List here what needs to be improved

## Slide 55: Better models for prediction of plasma rotation needed for modeling plasma response to applied magnetic perturbations
Time dep.
1D transport
2D MHD equ.
3D
torque from non-axisymmetric applied magnetic field
Non-axysimmetric
MHD equilibrium
NB calculations
torque by high energy beam
M. Honda, NF 57 (2017)
Courtesy of N. Hayashi (QST)
Notes: Torque from non-axisymmetric applied magnetic field

## Slide 56: The path forward to an all-inclusive tokamak simulator
Reduced models from nonlinear 3D MHD stability
Reduced models for edge plasma turbulence induced transport
Reduced models for wave propagation in the Scrape-Off-Layer
Reduced models for energetic particle induced transport
Notes: List here what needs to be improved

## Slide 57: Hybrid approach to modeling of RF wave propagation is a promising avenue towards implementation in tokamak simulator
Core: Axisymmetric flux surface grid
  Hot plasma conductivity
  Dense Matrix Solver
Edge: Unstructured mesh with complicated geometry (either 2D or 3D)
  Cold plasma with collision.
Boundary: matching technique to build integrated solution
Would benefit from realistic model of SOL
S. Shiraiwa (PSFC) VI2.00003

## Slide 58: The path forward to an all-inclusive tokamak simulator
Reduced models from nonlinear 3D MHD stability
Reduced models for edge plasma turbulence induced transport
Reduced models for wave propagation in the Scrape-off-layer
Reduced models for energetic particle induced transport
Notes: List here what needs to be improved

## Slide 59: Fast particles can drive instabilities, like Alfvenic modes
Instabilities eject fast particles (e.g. alphas)
  Decrease performance
  Cause localized losses and damage to wall
Challenges:
  Understand physics to develop scenarios not prone to instabilities
  Develop control tools to mitigate/suppress instabilities
[SciDAC project ISEP]
C. Collins NF 57 (2017)

## Slide 60: Experimental validation is critical

## Slide 61
Time-dependent validation is critical for modeling of wave propagation in plasmas
D=0.00 m2/s
D=0.04 m2
D=0.08 m2/s
J// [MA/m2]
r/a
[F. Poli, PPCF (2016)]
GENRAY/CQL3D
D=0.00 m2/s
D=0.04 m2/s
D=0.08 m2/s
J// [MA/m2]
r/a
[R. Mumgaard, APS 2014)]
Standalone ray-tracing +Fokker-Planck solver
large off-axis current, not seen in experiments
Time-dependent simulation
=> self-consistent evolution of wave field and magnetic equilibrium
Notes: Change title
Add labels: single time slice, time-dependent.
Add title to figure: “Parallel current density”
“... are critical to reproduce experimental measurements”
Perhaps split two long sentences into bullets?
Specify: standalone -> single time slice

## Slide 62: Concluding remarks
Increasing computing capabilities allow to solve bigger problems
Efficient workflows allow to solve complex problems
The path forward for an all-inclusive tokamak simulator should focus on reduced models
Validation against experiments and verification against extreme scale calculations are critical to retain fidelity while reducing computational time