## Slide 1: Multi-Mode Plasma Response and Experimental Validation
by Z.R. Wang1, with N.C. Logan1, Y.Q. Liu2,
S. Munaretto2, Y.W. Sun3, J.-K. Park1, S. Gu3, J.M. Hanson4,
Q.M. Hu1, T. Strait2, and J.E. Menard1
1 Princeton Plasma Physics Laboratory
2 General Atomics
3 ASIPP, China
4 Columbia University
Presented at the 60th Annual APS Meeting Division of Plasma Physics Portland, Oregon
November 5–9, 2018

## Slide 2: Understanding and Identifying Each Individual Eigenmode (Stability + Mode Structure) in Multi-Mode Plasma Response is Important for Tokamak Operation
Tokamak plasmas sensitively respond to non-axisymmetric (3D) magnetic fields
  Plasma response magnetic perturbation, plasma displacement, perturbed plasma current etc.
  Linear theory: plasma response generally contributed by multiple stable MHD eigenmodes multi-mode plasma response
Behavior of stable modes in multi-mode plasma response can significantly affect performance of tokamak operations e.g.
  Amplification of edge peeling response strongly couple to edge localized modes (ELMs) control [Y.Q. Liu NF 2011, C. Paz-Soldan et al, PRL 2015, J.-K. Park et al, Nature Physics 2018]
  Selective amplification of core/edge dominant modes control of plasma rotation through neoclassical toroidal viscosity (NTV) [W. Zhu et al, PRL 2006]
  Detect marginally stable modes predict and control MHD instabilities (much of previous work based on single mode approach) [Reimerdes et al, PRL 2004]

## Slide 3: Understanding and Identifying Each Individual Eigenmode (Stability + Mode Structure) in Multi-Mode Plasma Response is Important for Tokamak Operation
Sensor
arrays
LFS
HFS
Multi-mode plasma response has been qualitatively identified in DIII-D and EAST experiments.
C. Paz-Soldan et al, PRL 2015
N. Logan et al, Nucl. Fusion 2018
DIII-D n=1 plasma response
How many dominant modes contribute to multi-mode plasma response?
How about stability and behavior of dominant modes in multi-mode plasma response?
Multi-pole transfer function model is developed to reveal characters of stable dominant modes.
LFS
HFS
o Exp.
Multi-mode response

## Slide 4: Multi-Pole Response Transfer Function is Developed to Extract Stable MHD Eigenmodes from Plasma Response
Sensor
arrays
LFS
HFS
LFS
HFS
o Exp.
DIII-D n=1 plasma response
Multi-mode response
Multi-pole transfer function on 3D magnetic sensor measurement is systematically developed from generalized linear-MHD equation:
Represent dominant eigenmodes
Eigenvalue of mode
Same at any sensor
Re( stability index
Im( mode frequency
Coupling between coil and mode at sensor
Residual of vacuum response when
: coil frequency
Measured response at 3D sensor
Combined 3D MHD spectroscopy uses 3D coils to perform active detection (scan and ) to extract transfer function and stable eigenmodes
  Conventional passive spectroscopy detects unstable mode

## Slide 5: Multi-Pole Response Transfer Function Extracted from Experimental Data Reveals Three Dominant n=1 Modes in DIII-D Experiments
n=1 Transfer function extracted in DIII-D experiment
Multi-pole transfer function at 3D sensor is extracted in DIII-D experiments (Shot No. 170195-170220):
Sensor
arrays
LFS
HFS
= – 85.32 – 23.12i rad/s
2nd mode
1st mode
3rd mode
LFS
HFS
o Exp.
Vacuum
P()
= rad/s
= rad/s
Plasma MHD stability can be quantified by eigenvalue of least stable mode, Re()
For any (, ), multi-pole transfer function reveals contribution of each dominant mode at different poloidal locations of 3D sensors

## Slide 6: Multi-Mode Response Analysis for EAST Experiments Identifies Two Dominant n=1 Contributions
Experimental transfer function indicates two dominant eigenmodes in EAST experiment (shot No. 70617-70633):
= – 66.65 +0.06i rad/s
= rad/s
n=1 Transfer function extracted in EAST experiment
2nd mode
1st mode
P()
Amp )
Amp )
LFS
LFS
Upper coil
Lower coil
o Exp.
Advantage of to extract stable MHD modes:
Inclusion of phase dependence
  Reduce requirement of noisy high frequency scan in conventional Nyquist method [Reimerdes et al, PRL 2004]
  Better chance to observe significant eigenmode response
Extract transfer functions from multiple locations of 3D sensors simultaneously
  Strong constrains on eigenvalue and compensate for potential measurement errors
  Observe more aspects of eigenmode
Vacuum

## Slide 7: Outline
Theory of multi-mode plasma response model
Detection of n=1 modes in stable DIII-D plasma
Multi-mode plasma response model helps to understand n=2 mode locking in L-mode DIII-D plasma

## Slide 8: Outline
Theory of multi-mode plasma response model
Detection of n=1 modes in stable DIII-D plasma
Multi-mode plasma response model helps to understand n=2 mode locking in L-mode DIII-D plasma

## Slide 9: Multi-Mode Plasma Response Model is Systematically Derived From Generic Linear MHD Formulation
Discretization of computation domain
Only in plasma domain
Discretize direction
Fourier transformation
of (poloidal direction)
)
Linearized MHD equations including non-ideal effects
Kinetic pressure and
eigenvalue
Resistive term
Y.Q. Liu et al, PoP 2008
Resistive wall
Vacuum
Any perturbations have form
, ~ wall jump

## Slide 10: Multi-Mode Plasma Response Model is Systematically Derived From Generic Linear MHD Formulation
Matrix form of equations
full rank matrix
wall
plasma
vacuum
vacuum
Vacuum transformation
between two surfaces
3D Coil equations and inhomogeneous plasma response equations
coil frequency
Upper and lower coils
,
Eigenvalue matrix
Reduce
vacuum equations
=

## Slide 11: Multi-Mode Plasma Response Model is Systematically Derived From Generic Linear MHD Formulation
: sensor surface
Sensor transfer function including coil frequency and phasing :
: inverse Fourier transformation
: sensor measurement
Example of
Wall equation:
Plasma mode - Coil coupling
Vacuum-Coil coupling
Mode-Coil coupling
mode eigenvalue
(same for each sensor)
Residual of vacuum response when

## Slide 12: Proof of Principle Based on Simulated Response Data: Constructed Transfer Function Using Low-Frequency Data Recovers High-Frequency Data
Sensor
arrays
LFS Bp
MARS-F solves linearized ideal MHD for plasma response and eigenvalue problem
MARS-F simulates n=1 DIII-D plasma response by scanning
  [0deg, 60deg, 120deg, 180deg, 240deg, 300deg ]
  = [-110Hz, -60Hz, -30Hz, -10Hz, 10Hz, 30Hz, 60Hz, 110Hz]
Transfer function fits MARS-F simulated data points well
P agrees with Nyquist plot which is simulated by MARS-F by scanning frequency up to Hz
() (a.u.)
() (a.u.)
O MARS-F simulation
X Fitting points
Transfer function
P()
() (a.u.)
P()
() (a.u.)
MARS-F simulation of n=1 DIII-D plasma response
, ,
HFS Br

## Slide 13: Multi-Pole Transfer Functions can be obtained from both Experimental and Numerical Data
Multi-pole transfer function on 3D sensors is developed from generalized linear-MHD theory:
Detailed comparison between experiment and numerical modelling.
Experimental measurements
Eigenmode behavior at 3D sensors
Eigenvalue problem solver
Full solution of dominant eigenmode
Eigenvalues ()
stability index
Selective amplification of eigenmode
Difficult
Easy
Plasma response simulation
Simulation
(e.g. MARS code)

## Slide 14: Outline
Theory of multi-mode plasma response model
Detection of n=1 modes in stable DIII-D plasma
Multi-mode plasma response model helps to understand n=2 mode locking in L-mode DIII-D plasma

## Slide 15: Combined 3D MHD Spectroscopy: Scanning both Coil Phasing and Frequency to Extract Multi-Pole Transfer Function from DIII-D Experiments
Coil (kA)
MID-LFS
(G)
Keep equilibrium parameters stable with little change.
Repeat same discharge and scan coil phasing and frequency to measure n=1 plasma response.
  Change coil phasing in each discharge [170200 (0 deg), 170202 (60 deg), 170203 (120 deg), 170204 (180 deg), 170205 (240 deg),170220 (300 deg)]
  Randomly scan coil frequency Hz, Hz, Hz and Hz in each shot
Frequency scan: one time interval – one frequency with several periods
Extracted response at 3D sensor (Mid-LFS: , ; Mid-HFS: , ):
DIII-D Shot No. 170220,

## Slide 16: Combined 3D MHD Spectroscopy: Response Extracted by Simultaneous Fitting of DIII-D Data from Multiple Sensors
Multi-pole response transfer functions fit to multiple sensor measurements at Mid-HFS ( and ) and Mid-LFS ( and )
Nonlinear least square fitting is used to find , and by minimizing target function:
Three stable dominant modes are extracted:
= – 85.32 – 23.12i rad/s
= rad/s
= rad/s
Convergence test of transfer function:
Randomly perturbing initial guess
Increase pole number during fitting
Contribution of 4th and 5th modes is negligible
Experiment
real (o)
imag(◊)
Re()
Im()
HFS10Hz
HFS110Hz
LFS10Hz
LFS110Hz
Qualitative index of MHD modes’ stabilities
=16.5

## Slide 17: Construction of Transfer Functions from Both Measured and Simulated Response Data Allows Direct Comparison of Each Individual Mode
Transfer function can be extracted from MARS-F simulation by performing same phasing and frequency scan as experiments
Each dominant eigenmode can be compared separately between experiments and simulations
  General behavior of each mode is similar between experiment and simulation
HFS Br
Experiment | MARS-F
= –85.32 – 23.12i rad/s | –45.18 – 2.95i rad/s
= rad/s | –101.22 – 0.75i rad/s
= rad/s | –365.99+ 3.39i rad/s
Experiment | MARS-F
 | –45.18 – 2.95i rad/s
 | –101.22 – 0.75i rad/s
 | –365.99+ 3.39i rad/s
Experiment
MARS-F
Total
Response
2nd mode
1st mode
MARS-F
Exp.
3rd mode
MARS-F
Exp.
Exp.
MARS-F

## Slide 18: Reconstructed Stable Poles Are Used to Guide Eigenvalue Solver to Directly Compute Eigenmode Structure for 3 Dominant Modes
Eigenvalues from simulated transfer function, as initial guess of eigenvalue problem solved by MARS-F , help to find converged solutions.
Different eigenmode structure has potential for different application purpose.
  1st mode: core rotation control through NTV torque
  3rd mode: help edge island open for ELM suppression
Core dominant
Edge dominant
1st mode
R (m)
Z (m)
(a.u.)
2nd mode
(a.u.)
R (m)
3rd mode
R (m)
(a.u.)
Divertor dominant

## Slide 19: Transfer Function Reconstructed From Experimental Data Helps to Perform Selective Amplification of Mode in 2D Space of Coil Phasing and Frequency
G/kA
Phasing and frequency dependence of each dominant eigenmode can be evaluated by transfer function
2D scan of coil frequency and phasing could help to amplify preferred eigenmode.
Higher coil frequency makes stronger amplification of 2nd and 3rd modes in concerned DIII-D experiment
G/kA
1st mode
3rd mode
dependence of mode amplitude at HFS
X
G/kA
2nd mode
Frequency (Hz)
= – 85.32 – 23.12i rad/s
= rad/s
= rad/s

## Slide 20: Transfer Function Reconstructed From Experimental Data Helps to Perform Selective Amplification of Mode in 2D Space of Coil Phasing and Frequency
G/kA
Phasing and frequency dependence of each dominant eigenmode can be evaluated by transfer function
2D scan of coil frequency and phasing could help to amplify preferred eigenmode.
Higher coil frequency makes stronger amplification of 2nd and 3rd modes in concerned DIII-D experiment
G/kA
1st mode
3rd mode
dependence of mode amplitude at HFS
X
G/kA
2nd mode
Frequency (Hz)
= – 85.32 – 23.12i rad/s
= rad/s
= rad/s
Amplify 3rd mode

## Slide 21: Outline
Theory of multi-mode plasma response model
Detection of n=1 modes in stable DIII-D plasma
Multi-mode plasma response model helps to understand n=2 mode locking in L-mode DIII-D plasma

## Slide 22: More Efficient MHD Spectroscopy with Multi-Frequency Wave Package Applied in DIII-D L-Mode for n=2 Mode Identification
Efficiency of coil phasing and frequency scan is improved by applying multiple frequencies simultaneously .
~0.32
~3.1
~1.4 MA
0 deg
deg
18deg
270 deg
Mode locking
Upper Coil
Current
Current ramp up
LFS Bp 10Hz
Experiment
real (o)
imag(◊)
Re()
Im()
HFS Bp 110Hz
Two dominant modes are extracted from experiments
173359
Wave packet for given phasing (0, 90, 180, 270) is carefully designed by combining multiple waves (, , , ).
Time (s)
0.4s
= rad/s
= rad/s

## Slide 23: n=2 Combined MHD Spectroscopy Identifies Least Stable Mode as Stable Tearing Mode and Confirmed by MARS-F Eigenvalue Computation
: Lundquist number
Growth rates (rad/s)
Unstable
Mode comparison between Expt. and Simulation
1st mode computed by MARS-F similar to that extracted from experiment
MARS-F eigenvalue runs scanning plasma resistivity  1st mode corresponds to an unstable TM at high resistivity
Expt.
MARS-F
1st mode
f=0 Hz
LFS Br
Liu et al, PoP 2012
0
Mode frequency (rad/s)
2
MARS-F
Expt.
Experiment | MARS-F
= rad/s | rad/s
= rad/s | rad/s
Experiment | MARS-F

## Slide 24: Amplification of Stable Tearing Component at =0o  Strong Resonant Perturbations  Lower Mode Locking Threshold
-2
0
2
1st mode
2nd mode
1st mode
2nd mode
MARS-F solves eigenvalue problem to find eigenmode structure of two dominant modes
  Least stable mode is resistive eigenmode
  Secondary mode has global kink structure
n=2 Least Stable Mode is Amplified at =0 Degree Coil Phasing (Even Parity) with Clear Tearing Structure
HFS Bp
Tearing
Odd parity

## Slide 25: Thesis: Multi-Mode Plasma Response Model and Combined 3D MHD Spectroscopy Provide Pertinent Tools to Study Stable MHD Modes
  Multi-mode plasma response model/plasma transfer function developed from linear MHD and control theory can identify:
    Spatial structure of each dominant stable mode in multi-mode plasma response
    Damping rates of dominant modes as quantitative index of plasma stability
  Extraction of stable eigenmodes, using multi-mode plasma response model, is validated in tokamak experiments
  Comparison between experimentally extracted multi-mode response and MARS-F simulations:
    Identify n=2 resistive eigenmode as least stable and amplified at =0 deg, lead to lower mode locking threshold
  Multi-mode plasma response model is a powerful tool for
    Optimizing RMP spectrum to amplify preferred eigenmode for ELM suppression
    Real-time quantitative monitoring plasma stability
3rd mode
2nd mode
1st mode
H-mode
n=1
L-mode
n=2

## Slide 26: Backup slides

## Slide 27: Experimental Extracted Plasma Response Model is Verified with Independent Experiment
Experiment (shot No. 170196) only uses upper I-coil to scan frequency
Transfer function, extracted from phasing and frequency scan of I-coils, shows good agreement with sensor measurements in independent experiment
Experiment confirms linear approach of plasma response in theory
1st mode
2nd mode
3rd mode
HFS Br
LFS Br

## Slide 28: Multi-Mode Response Transfer Function Reveals Contribution of Each Eigenmode While Applying Different Coil Frequency and Phasing
This slides maybe not shown in talk
Eigenvalue of three dominant modes:
  = Hz
  = Hz
  = Hz
Contribution of each dominant
mode can be separated at any
frequency and phasing
=100 deg has least stable mode dominant. =240deg makes 2nd and 3rd modes more important
HFS Bp
f=0Hz
LFS Bp
HFS Bp
LFS Bp

## Slide 29: Resistive Wall Effect is Important to Determine Plasma Response While Rotating 3D Fields are Applied.
2D wall with uniform resistivity is not sufficient to resolve spatial details of wall eddy current patterns to simulate local magnetic measurements.
Exp. Transfer function
Wall time ~ 9ms
~ 6.75ms
~ 5.63ms
J.M. Hanson et al, Nucl. Fusion 2016
No wall
LFS
LFS
HFS Br
LFS Br
In coil frequency scan, simulated LFS with different wall time decays faster than experimental transfer function.
An sophisticated wall modelling is important to AC plasma response simulation.

## Slide 30: Well Restore Magnetic Response in Time Domain
Raw data
Band pass filter
Transfer function
Time(s)
Time(s)
HFS Br,

## Slide 31: Single Mode Response Also Leads to Different of Minimum Amplitude at LFS and HFS （Toy model）
Consider two driving terms , response measured by sensor at :
dependence of even for single mode

## Slide 32: Single Mode Response Also Leads to Different of Minimum Amplitude at LFS and HFS （Toy model）
Consider a complex linear system:
Eigen functions (span solution space): , , …,
Response to a driving term:
Eigen values: , , …,
Multi-mode solution:
If only one mode, single-mode solution:
Response measured by sensor S :
Consider two driving terms , response measured by sensor and at mid-plane of LFS and HFS respectively
Here, , ,…, are complex coupling coefficients of coil current to each mode.
Here, single mode is amplified by upper and lower coils respectively. It can have and .
At LFS and HFS, the coupling between mode and coil can be different, and . Therefore, .
The minimum point is determined by and
It is possible to have .
Physical understanding: single mode is amplified twice by upper and lower coils respectively. The coupling of single mode to upper and lower coils can be different at LFS and HFS. While changing , the combination of two amplifications can be different at LFS () and HFS().