## Slide 1
Overview of Physics Results from the National Spherical Torus Experiment
S. A. Sabbagh
Columbia University
for the NSTX Research Team
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC
24th IAEA Energy Fusion Conference
October 9th, 2012
San Diego, California
V2.0

## Slide 2: NSTX research targets predictive physics understanding needed for fusion energy development facilities
Fusion Nuclear Science Facility (FNSF)
ST Pilot Plant
Outline
New center-stack
NSTX-U
2nd neutral beam
Develop key physics understanding to be tested in unexplored, hotter ST plasmas
  Study high beta plasma transport and stability at reduced collisionality, for extended pulse
  Prototype methods to mitigate very high heat/particle flux
  Move toward fully non-inductive operation
BT
Ip
PNBI
pulse
1 T
2 MA
12 MW
5 s
ITER
3D effects are pervasive in this research
Enable devices: ST-FNSF, ST-Pilot/DEMO, ITER
  Leveraging unique ST plasmas provides new understanding for tokamaks, challenges theory

## Slide 3: First successful nonlinear microtearing simulations for NSTX predict reduced electron heat transport at lower collisionality
dBr (Gauss)
W. Guttenfelder, et al., PRL 106, 155004 (2011)
Predicted ce and scaling ~ ne1.1 consistent with experiment (WtE ~ BttE ~ n*e-0.8)
Transport dominated by magnetic “flutter”
  Significant dBr/B ~ 0.1%
120968
cesim ~ ne1.1
Increase in tE as n*e decreases
Trend continues when lithium is used
Experiment
Theory
experiment
NSTX-U computed to extend studies down to < 1/4 of present n*
BttE (T-s)
n*e (at r/a = 0.5)
Kaye EX/7-1
Guttenfelder TH/6-1

## Slide 4: Plasma characteristics change nearly continuously with increasing lithium evaporation; reach kink/peeling limit
Energy Confinement Time (ms)
Pre-discharge lithium evaporation (mg)
Global parameters generally improve
ELM frequency declines - to zero
  ELMs stabilize
Edge transport declines
  As lithium evaporation increases, transport barrier widens, pedestal-top χe reduced
Maingi EX/11-2
Canik EX/P7-16
Chang TH/P4-12
R. Maingi, et al., PRL 107 (2011) 145004
New bootstrap current calculation (XGC0 code) improves agreement with profile reaching kink/peeling limit
Norm. surface avg. current
0.5
0.6
0.7
0.8
0.9
1.0
1.0
0.8
0.6
0.4
0.2
0.0
yN
XGC0 model
Sauter model
Bootstrap current profile

## Slide 5: Simulations and lab results show importance of oxygen in lithium-graphite PMI for pumping deuterium
Accordingly, lab results support that Li on graphite can pump D effectively due to O
  XPS measurements show 2 µm of Li increases surface oxygen content of lithiated graphite to ~10%
  deuterium ion irradiation of lithiated graphite greatly enhances oxygen content to 20%-40%
    In stark contrast, D irradiation of graphite without Li decreases amount of surface O
  Li acts as an O getter, and the O retains D
%
O
Li
C
D
Quantum-classical atomistic simulations show surface oxygen plays key role in the retention of deuterium in graphite
1 2 3 4 5
atomic composition
D+ bombarded Li-graphite
D+ bombarded graphite
J.P. Allain, Taylor (Purdue U.)
P. Krstic, sub. to Nature Comm.
Jaworski EX/P5-31

## Slide 6: Experiments measuring global stability vs. n further support kinetic RWM stability theory, provide guidance for NSTX-U
RWM growth rate (γτw)
unstable
Marginal
stability
J. Berkery et al., PRL 106 (2011) 075004
Two competing effects at lower n
  Collisional dissipation reduced
  Stabilizing resonant kinetic effects enhanced (contrasts early theory)
Expectations at lower n
  More stabilization near ωφ resonances; almost no effect off-resonance
Collisionality
Plasma Rotation
Theory: RWM growth rate vs. n and wf
MISK code
Berkery EX/P8-07
RFA =
Bapplied
Bplasma
Exp: Resonant Field Amplification (RFA) vs n
Mode stability directly measured in experiment using MHD spectroscopy
  Decreases with n at lower RFA (“on resonance”)
  Independent of n at higher RFA (“off resonance”)
on resonance
off resonance
(trajectories of 20 experimental plasmas)
off-resonance
on resonance

## Slide 7: BES measured low-k turbulence in ELM-free H-mode pedestal steep gradient region is most consistent with TEMs
Beam emission spectroscopy (BES) array
R
Z
Measurements during MHD quiet periods, in steep gradient region
Large poloidal correlation lengths
  kq ≈ 0.2-0.4 cm-1 and kqri ≈ 0.2
Poloidal Correlation Length vs. Parameters
Smith EX/P7-18
Multivariate linear scaling coefficients ak
Turbulence measurements in the steep gradient of the pedestal
  Most consistent with Trapped Electron Modes
  Partially consistent with KBM and m-Tearing Modes
  Least consistent with ITG Modes

## Slide 8: Pedestal width scaling differs from tokamaks; turbulence correlation measurements consistent with theory
3 cm | 2 – 4 cm (reflecto-metery)
11 cm | 10 – 14 cm (BES)
8
8
Pedestal width scaling bqa applies to multiple machines
In NSTX, observed ped. width is larger
  e.g., 2.4 x DIII-D
  Data indicates stronger scaling: bq vs. bq0.5
Measured correlation lengths at pedestal top are consistent with theory
  BES and reflectometry
    spatial structure exhibits ion-scale microturbulence (k⊥ri ~ 0.2 - 0.7)
    Compatible with ITG modes and/or KBM
A. Diallo, C.S. Chang, S. Ku (PPPL), D. Smith (UW), S. Kubota (UCLA)
Pedestal width scaling
Turbulence correlation lengths
Theory
(non-linear XGC1 code)
R = 1.38m
Diallo EX/P4-04
Experiment
80% - 99% ELM cycle
radial
poloidal
139047
  (During inter-ELM period, at pedestal top)
C-Mod
DIII-D
NSTX
0.1
0.9
0.04
0.08
0.12
0.16
0.00
Pedestal width (yN)
0.3
0.5
0.7
~ 0.08 (bqped)
0.5
0.4 (bqped)
1.05
Notes: 8
8

## Slide 9: Stability control improvements significantly reduce unstable RWMs at low li and high bN; improved stability at high bN/li
Disruption probability reduced by a factor of 3 on controlled experiments
  Reached 2 times computed n = 1 no-wall limit of bN/li = 6.7
Lower probability of unstable RWMs at high bN/li
Mode stability directly measured in experiments using MHD spectroscopy
  Stability decreases up to bN/li = 10
  Stability increases at higher bN/li
  Presently analysis indicates consistency with kinetic resonance stabilization
Resonant Field Amplification (RFA) vs. bN/li
unstable
mode
Berkery EX/P8-07
Unstable RWM
Stable / controlled RWM
S.A. Sabbagh

## Slide 10: Disruptivity Studies and Warning Analysis of NSTX database are Being Conducted for Disruption Avoidance in NSTX-U
Disruption warning algorithm shows high probability of success
  Based on combinations of single threshold based tests
Results
  ~ 98% disruptions flagged with at least 10ms warning, ~ 6% false positives
  False positive count dominated by near-disruptive events
Disruptivity
Physics results
  Low disruptivity at relatively high bN ~ 6; bN / bNno-wall(n=1) ~ 1.3-1.5
    Consistent with specific disruption control experiments, RFA analysis
  Strong disruptivity increase for q* < 2.5
  Strong disruptivity increase for very low rotation
Warning Algorithms
Gerhardt EX/9-3
All discharges since 2006
bN
li
q*

## Slide 11: Improved stability control includes dual field component feedback and state space feedback, improved by 3D effects
Brn = 1 (G)
Br FB phase = 0o
Br FB phase = 90o
Br FB phase = 180o
t (s)
6
4
2
0
0.0
0.2
0.4
0.6
0.8
1.0
1.2
1.4
bN
140124
140125
140126
140127
6
4
2
0
Active n = 1 Bp + BR feedback (FB) control
Dt (s) (model)
Radial field n = 1 (G)
180 deg FB phase
90 deg FB phase
0 deg FB phase
Vacuum error field
Vacuum error field
Calculation of Br + Bp control (VALEN)
+ RFA
2.3
2.4
2.5
2.6
2.7
2.8
0.0
0.04
0.08
0.12
Br FB phase = 225o
S.A. Sabbagh, O. Katsuro-Hopkins, J.M. Bialek, S.P. Gerhardt
Feedback on
Inclusion of 3D mode and wall detail improves control
RWM State Space Controller
No NBI port
3D wall,
ports,
mode currents
Sensor Differences (G)
Measurement
Controller
Measurement
Controller
With 3D NBI port
1
2

## Slide 12: Fast ion redistribution associated with low frequency MHD measured by fast ion Da (FIDA) diagnostic
Caused by n = 1 global kink instabilities
Redistribution can affect stability of *AE, RWMs, other MHD
Full-orbit code (SPIRAL) shows redistribution in real and velocity space
  Radial redistribution from core plasma
  Particles shift towards V||/V = 1
Applied 3D fields alter GAE stability
  By altered fast ion distribution (SPIRAL)
Fast ion energy redistribution accounts for neutron rate decrease in H-mode TAE avalanches
Core localized CAE/GAEs measured in H-mode plasmas (reflectometer)
A. Bortolon
0.9
1.0
1.1
1.2
1.3
1.4
1.5
R(m)
Fast ion density reduction
Change in distribution due to kink mode
Z [m]
R [m]
Energy [keV]
V||\V
CAE resonances
SPIRAL code
Crocker EX/P6-02
Fredrickson EX/P6-05

## Slide 13: Snowflake divertor experiments provide basis for required divertor heat flux mitigation in NSTX-U
Needed, as divertor heat flux width strongly decreases as Ip increases
Snowflake divertor experiments (PNBI = 4 MW, PSOL = 3 MW)
  Good H-mode tE, bN, sustained during snowflake operation
  Divertor heat flux significantly reduced both during and between ELMs
    during ELMs: 19 to ~ 1.5 MW/m2
    steady-state: 5-7 to ~ 1 MW/m2
  Achieved by a synergistic combination of detachment + radiative snowflake divertor
Divertor heat flux (MW/m2)
Snowflake divertor in NSTX
Soukhanovskii EX/P5-21
CHI gap
R (m)
Z (m)
R (m)
Heat flux at peak ELM time

## Slide 14: Toroidal asymmetry of heat deposition measured during standard ELMs, but decreases for 3D field-triggered ELMs
132438
Type-I ELMs
qpeak,2D (MW/m2)
DoA(qpeak)
,2D
2D fast IR camera measurement (1.6kHz), heat flux from TACO code
Toroidal asymmetry
  Becomes largest at the peak heat flux for usual Type-I ELMs
  Reduced by up to 50% in ELMs triggered by n = 3 applied fields
Mean Peak 2D Heat Flux
During ELMs vs. t
Ahn EX/P5-33
Toroidal Degree of Asymmetry vs. qpeak
at ELM peak times
Standard ELMs
n=3 triggered
No 3D fields
Reduction with 3D fields

## Slide 15: L-mode discharge ramping to 1MA requires 35% less inductive flux when coaxial helicity injection (CHI) is used
Raman EX/P2-10
CHI generates plasmas with high elongation, low li and ne
TSC now used for full discharge modeling to 1MA
  CHI start-up + NBI current ramp-up
Results imply a doubling of closed flux current > 400kA in NSTX-U
TSC simulation of CHI startup
High elongation
Low inductance
Low density
CHI assisted startup in NSTX

## Slide 16: Significant fraction of the HHFW power lost in the SOL in front of antenna, flows to the divertor region
Visible camera image of edge RF power flow to divertor
SPIRAL modeling of field lines from antenna to divertor
HHFW
Antenna
Divertor
Top View
HHFW
Antenna
Divertor
Perkins EX/P5-40
R. Perkins, et al., PRL 109 (2012) 045001
RF power couples to field lines across entire SOL width, not just to field lines connected to antenna components
Shows importance of quantitatively understanding RF power coupling to the SOL for prediction to future devices
-1.0
0.0
1.0
R(m)

## Slide 17: Non-inductive current fractions of up to 65% sustained in NSTX, >70% transiently; Upgrade projected to achieve 100%
Ip (MA)
70- 100% non-inductive reached transiently using HHFW CD
G. Taylor (Phys. Plasmas 19 (2012) 042501)
BT=0.75 T
BT=0.75 T
BT=1 T
BT=1 T
NSTX Results
Maximum sustained non-inductive fractions of 65% w/NBI at IP = 0.7 MA
Total Non-inductive Fraction
NSTX Results
NSTX-U projections
NSTX-U
(100% NI)
100% non-inductive scenarios found over wide operation range
  Scenarios at 74% Greenwald density
via high harmonic FW
(ranges created by profile peakedness, tE scalings, etc.)
Menard FTP/3-4
S. Gerhardt, et al., Nucl. Fusion 51 (2011) 073031

## Slide 18: Rapid Progress is Being Made on NSTX Upgrade
2nd neutral beam moved into place
TF OD = 40cm
TF OD = 20cm
TF conductors being made
Old center stack
NEW Center Stack
(first plasma anticipated June 2014)
Menard FTP/3-4

## Slide 19: Continuing analysis of NSTX data targets a predictive physics understanding required for future fusion devices
Transport and stability at reduced collisionality
  tE scalings unified by collisionality; non-linear microtearing simulations match experimental ce, predict lower ce at lower ne* shown in experiment
  Nearly continuous increase of favorable confinement with increased lithium
  Stabilizing kinetic RWM effects enhanced at lower n when near resonances
Pedestal
  Width scaling stronger than usual (bpped)0.5; measured dne correlation lengths consistent w/non-linear gyrokinetics at pedestal top
Pulse sustainment / disruption avoidance
  Global stability increased + low disruptivity at high bN/li, advanced mode control
  Disruption detection algorithm shows high (98%) success rate
Power/particle handling and first wall
  Large heat flux reduction from synergistic combination of radiative snowflake divertor + detachment, both during, and between ELMs
Significant upgrade underway (NSTX-U)
  Doubled BT, Ip, NBI power; 5x pulse length, projected 100% non-inductive sustainment over broad operating range

## Slide 20: NSTX Presentations at the 2012 IAEA FEC
Thursday |  | 
Progress in Simulating Turbulent Electron Thermal Transport in NSTX | Guttenfelder | TH/6-1
The Dependence of H-mode Energy Confinement and Transport on Collisionality in NSTX | Kaye | EX/7-1
Friday |  | 
Disruptions in the High Beta Spherical Torus NSTX | Gerhardt | EX/9-3
Progress on Developing the Spherical Tokamak for Fusion Applications | Menard | FTP/3-4
The Nearly Continuous Improvement of Discharge Characteristics and Edge Stability with Increasing Lithium Coatings in NSTX | Maingi | EX/11-2
Tuesday |  | 
Lithium program | Ono | FTP/P1-14
Co-axial helicity injection | Raman | EX/P2-10
Wednesday |  | 
Bootstrap current XGC | Chang | TH/P4-12
Pedestal transport | Diallo | EX/P4-04
Power scrape-off width | Goldston | TH/P4-19
Vertical stability at low A | Kolemen | EX/P4-28
Blob dynamics / edge V shear | Myra | TH/P4-23
EHOs | Park | EX/P4-33
Core lithium levels | Podesta | EX/P3-02
C, Li impurity transport | Scotti | EX/P3-34
Snowflake divertor theory | Ryutov | TH/P4-18
Thursday |  | 
Divertor heat asymmetry | Ahn | EX/P5-33
L-H power threshold vs. X pt. | Battaglia | EX/P5-28
NBI-driven GAE simulations | Belova | TH/P6-16
CAE/GAE structure | Crocker | EX/P6-02
TAE avalanches in H-mode | Fredrickson | EX/P6-05
Li deposition / power exhaust | Gray | EX/P5-27
Liquid lithium divertor results | Jaworski | EX/P5-31
RF power flow in SOL | Perkins | EX/P5-40
Snowflake divertor | Soukhanovksii | EX/P5-21
Friday |  | 
Global mode control / physics | Berkery | EX/P8-07
Edge transport with Li PFCs | Canik | EX/P7-16
Particle code NTV simulation | Kim | TH/P2-27
Turbulence near OH L-H trans. | Kubota | EX/P7-21
ELM triggering by Li in EAST | Mansfield | PD
Electron-scale turbulence | Ren | EX/P7-02
Low-k turbulence vs. params. | Smith | EX/P7-18
Talks
Posters

## Slide 21: Tasks to Complete for this Presentation
Additions
  Add bullet on L-H power threshold – REF Battaglia talk EX/P5-28
Tasks
  Shorten talk to 18 slides
  Poster up to 24 slides

## Slide 22: Extra slides for poster follow

## Slide 23: Supporting slides follow

## Slide 24: Plasma characteristics change nearly continuously with increasing lithium evaporation inside vessel
Measured reduction in high-k turbulence consistent with reduced ce
Impact of collisionality and Ñn on turbulence is under investigation
  BttE ~ ne*-0.8 observed
Without Li
141314
141328
With Li
Outer plasma
R = 1.4 - 1.46 m
(r/a = 0.74 – 0.95)
Measured density fluctuation vs. k^rs
(dn/n)2 (arb)
k^rs
Energy Confinement Time (ms)
Pre-discharge lithium evaporation (mg)
Global parameters generally improve
ELM frequency declines - to zero
  ELMs stabilize
Edge transport declines
  As lithium evaporation increases, transport barrier widens, pedestal-top χe reduced
Maingi EX/11-2
Canik EX/11-2
Ren EX/P7-02

## Slide 25: Kinetic RWM stability theory further tested against NSTX experiments, provides guidance for NSTX-U
Marginal
Stability
unstable
J. Berkery et al., PRL 106, 075004 (2011)
Two competing effects at lower n
  Collisional dissipation reduced
  Stabilizing resonant kinetic effects enhanced (contrasts early theory)
Expectations at lower n
  More stabilization near ωφ resonances; almost no effect off-resonance
    Active RWM control important
Collisionality
Plasma Rotation
NSTX
NSTX-U
RWM growth rate contours (gtw)
MISK code
Improvements to physics model
  Anisotropy effects
  Testing terms thought small
    Already good agreement between theory and experiment of marginal stability point improved
RWM stability vs. wf
Berkery EX/P8-07

## Slide 26: Experiments using MHD spectroscopy show that highest bN/li plasmas are not the least stable
Low frequency (40Hz) rotating n = 1 applied field used as seed field
n = 1 resonant field amplification (RFA) of seed field used to measure global mode growth rate in stable plasmas
  Higher amplitude = less stability
n = 1 RFA (G/G)
bN/li
5
10
15
1.5
1.0
0.5
0.0
unstable RWMs
Discharges with bN/li > 10 have greater stability
  Presently thought to be due to differing plasma rotation profile
J.W. Berkery, S.A. Sabbagh
RFA =
Bapplied
Bplasma
NSTX
Berkery EX/P8-07

## Slide 27: Higher aspect ratio of NSTX-U tested in NSTX, vertical stability growth rate data obtained, compared to simulation
Improvements to vertical control capability and understanding
  Begun to compare measured growth rates to theoretical predictions (Corsica, GSPERT)
  Improved plasma position observer
  Modeled use of RWM coils for n=0 control
Vertical Stability Growth Rates vs. A
1.5 1.55 1.6 1.65
Aspect Ratio
5
4
3
2
1
g/g0
GSPERT
Corsica
Experiment
NSTX-U
PFC Boundary
NSTX Discharges have matched aspect ratio and elongation of NSTX-U without performance degradation
Kolemen EX/P4-28

## Slide 28: Single summary slides follows
NOTE: The single summary slide is not an adequate summary

## Slide 29: OV/3-1: NSTX research targets needed predictive physics understanding crucial for fusion energy development
Fusion Nuclear Science Facility (FNSF)
ITER
Enable devices: ST-FNSF, ST-Pilot/DEMO, ITER
  Leveraging unique ST plasmas provides new understanding for tokamaks, challenges theory
Transport, stability at reduced collisionality
  tE scalings unified by collisionality; microtearing code matches XP ce, predicts lower ce at lower ne*
  Stabilizing kinetic RWM effects enhanced
Pedestal
  Width scaling stronger than usual (bpped)0.5; measured dne correl. lengths agree w/non-linear gyrokinetics
Pulse sustainment / disruption avoidance
  Global stability increased + low disruptivity at high bN
Power/particle handling and first wall
  Radiative snowflake divertor mitigates high heat flux both between & during ELMs, Li wall cond. effects
Significant upgrade underway (NSTX-U)
  Doubled BT, Ip, NBI power, non-inductive sustainment
Highlights
disruption
warning analysis
te vs. collisionality
kink-induced fast ion redistribution
non-inductive
scenarios