## Slide 1
Isolation of Neoclassical Toroidal Viscosity Profile Under Varied Plasma and 3D Field Conditions in Low and Medium Aspect Ratio Tokamaks*
S.A. Sabbagh1, Y.S. Park1, R.E. Bell2, J. Kim3, J. Ko3, W.H. Ko3, K.C. Shaing4, Y. Sun5, B. LeBlanc2, S.G. Lee3, J. Lee3, J.W. Berkery1, S.P. Gerhardt2, S.H. Hahn3, Y. In3, Y.M. Jeon3, Y.K. Oh3, J.W. Yoo3
1Department of Applied Physics, Columbia University, New York, NY, USA
2Princeton Plasma Physics Laboratory, Princeton University, Princeton, NJ, USA
3National Fusion Research Institute, Daejeon, Republic of Korea
4National Cheng Kung University, Tainan, Taiwan
5ASIPP, Hefei Anhui, China
Supported by
*This work supported by the US DOE contract DE-AC02-09CH11466, DE-FC02-04ER54698, and DE-FG02-99ER54524
26th IAEA Fusion Energy Conference
19 October 2016
Kyoto, Japan
V1.2

## Slide 2: Key physical characteristics of NTV are investigated in low and medium aspect ratio tokamaks
Motivation
  Low magnitude (dB/B0 ~ O(10-3)) 3D magnetic fields are used favorably used in tokamaks (e.g. ELM suppression, MHD mode control)
  3D fields of this magnitude can produce neoclassical toroidal viscosity (NTV), which can:
    Alter plasma rotation non-resonantly (without mode locking)
    Potentially create stabilizing plasma rotation, Vf, Vf shear (e.g. in ITER)
  Therefore, it is important to understand NTV in tokamaks, backed by accurate (~O(1)) quantitative modeling
Outline
  NTV profile isolation experiments in NSTX and KSTAR
  NTV comparison of theory to experiment in NSTX
  Recent NTV offset rotation experiments in KSTAR (Sept 2016)

## Slide 3: Neoclassical Toroidal Viscosity (NTV) can be studied through the application of 3D fields in tokamaks
Theory: NTV strength varies with plasma collisionality n, dB2, rotation
NSTX 3D coils
plasma rotation
Ti5/2
K.C. Shaing, et al.,
PPCF 51 (2009) 035004
KSTAR 3D coils (IVCC)
NTV force in “1/n” collisionality regime
NTV “offset” rotation
(K.C. Shaing, K. Ida, S.A. Sabbagh, Nucl. Fusion 55 (2015) 125001)

## Slide 4: 3D field perturbation experiments conducted to isolate and measure the TNTV profile in NSTX and KSTAR
High normalized beta plasma targets typically chosen
  Typically near or above n = 1 no-wall limit (for higher Ti)
Apply or otherwise change 3D field on a timescale significantly faster than the momentum diffusion time, tm
  Analysis before/after 3D field application isolates TNTV in the momentum diffusion equation; ‑dL/dt = TNTV
dL/dt measured experimentally and compared to theoretically computed TNTV on this timescale
  dL/dt profile can change significantly on timescales > tm, (diffuses radially, broadens, leads to significant error compared to TNTV)
Emphasize non-resonant applied 3D field configurations
  Use n = 2 and 3 field configurations to avoid driving MHD modes
  n = 1 field configurations with different pitch investigated in KSTAR

## Slide 5: Theoretical NTV torque density profiles, TNTV are computed for NSTX using theory applicable to all collisionality regimes
Non-axisymmetric coils fully modelled in 3D
NTV analysis of NSTX – data interfaced to NTVTOK
  Use Shaing’s “connected NTV model”, covers all n, superbanana plateau regimes
  Full 3D coil specification and dB spectrum, ion and electron components computed, no aspect ratio assumptions
(K.C. Shaing, Sabbagh, Chu, NF 50 (2010) 025022)
(Y. Sun, Liang, Shaing, et al., NF 51 (2011) 053015)
x(m)
y(m)
z(m)
3D field definition
plasma displacement
General considerations
  In tokamaks, x not typically measured, can lead to large error
  “Fully-penetrated field constraint” used to define x
    Singularities avoided by standard finite island width assumption
  For NSTX, |x | ~ 0.3 cm << e0.5ri, therefore, ion banana width-averaging is used for ion channel
    Can explain why strong resonant peaks in NTV profile are not observed in experiment

## Slide 6: Measured NTV torque density profiles quantitatively compare well to computed TNTV using fully-penetrated 3D field
TNTV (theory) scaled to match peak value of measured -dL/dt
  Scale factor ((dL/dt)/TNTV) = 0.6 and 1.7 for cases shown above – O(1) agreement
Banana orbit-averaging reduces computed resonant perturbation effects
n = 2 coil configuration
Experimental
-dL/dt
yN
NSTX
NTVTOK
x1.7
K.C. Shaing, and S.A. Sabbagh, et al., Phys. Plasmas 23 (2016) 072511
Experimental
-dL/dt
NTVTOK
code
yN
NSTX
n = 3 coil configuration
x0.6

## Slide 7: KSTAR experiment using different 3D field spectra established isolated NTV profile using fast power supply
Results show non-resonant NTV characteristics; broad NTV torque profile
  Dwf does not change sign across profile (non-resonant); Dwf ~ 0 near plasma edge
  3D field spectrum varied: similar Dwf profiles, n = 1 pitch non-aligned has largest NTV
KSTAR n = 2 NTV experiments do not exhibit hysteresis (linear behavior)
See recent NTV review paper: K.C. Shaing, K. Ida, S.A. Sabbagh, et al., Nucl. Fusion 55 (2015) 125001
IVCC n = 2 configuration
n = 1 pitch non-aligned
n = 1 pitch aligned
Plasma rotation
Change in plasma rotation

## Slide 8: The NTV Offset Rotation Profile, V0NTV, was recently directly measured in KSTAR
Motivation
  Plasma rotation highly important for tokamak stability and confinement
  Future fusion devices are envisioned to have far less momentum input
   If sufficiently strong, this rotation could provide stabilization and improved performance in ITER and future devices
Experiment overview
  Used ECH for plasma heating, avoided issues of strong NBI torque
  Measured intrinsic rotation using NBI as a diagnostic beam for CES
Issues related to experiments with NBI torque
  TNBI term is
    Computed, not directly measured
    Typically much larger than the TNTV component due to offset rotation analysis is prone to error
    The TNBI profile matters – not just zero net input torque from NBI

## Slide 9: Intrinsic Torque due to Neoclassical Toroidal Viscosity (NTV) – a controllable momentum source via 3D field
Full Theory
  The non-ambipolar difference of ion and electron flux due to the application 3D fields yields a so-called “offset rotation profile”, V0NTV
  Generally, the local rotation speed can be either in the co- or counter-Ip direction if dominated by electron/ion flux, respectively
Highly Simplified Theory
  Consider a highly simplified theory to help understand characteristics
  Simplified NTV torque profile: TNTV = C1 dB2 (Vf – V0-NTV)
  Simplified V0NTV profile: V0NTV = C2 dTi/dr – C3 dTe/dr (for future analysis)
    Electron effects can dominate at low collisionality – important for ITER
  Unlike “intrinsic rotation”, the TNTV can be controlled by the applied 3D field spectrum and strength
(K.C. Shaing, K. Ida, S.A. Sabbagh, Nucl. Fusion 55 (2015) 125001)
(Y. Sun, K. Liang, K.C. Shaing, et al. Nucl. Fusion 51 (2011) 053015)

## Slide 10: Consider simple torque balance equation to further understand expected dynamics when measuring V0NTV profile
Simple torque balance
Consider equations with/without 3D field (in steady-state)
Use simple NTV model to express offset rotation
(e.g. W. Solomon, et al., Phys. Plasmas 17 (2010) 056108, Equation 8)
(without 3D field  L(0)  IVI/R)
(with 3D field  L  IV/R)

## Slide 11: As 3D field strength increases, Vf evolves from Vintrinsic toward a saturated profile V0NTV
Combine equations
  Assume (TRF + Tintrinsic) not function of 3D field; use simple TNTV model
Expected dynamics (4 different “conditions”)
    dB = 0: Vf = VI
    low dB: measured Vf profile close to VI
    increased dB and (|Vf| >> |V0NTV|): Vf  V0NTV
    sufficiently high dB: Vf saturates to V0NTV
dB
VI
Vf
V0NTV
a)
b)
c)
d)
(on each y surface)
- (VI is the toroidal velocity measured without 3D field applied)
- I  moment of inertia

## Slide 12: Target plasma with CES and XCIS measurement of plasma toroidal velocity (apply n = 2 field to this)
X-ray crystal (XCIS) and charge exchange spectroscopy (CES) data agreement shows that plasma velocity is well described by the early CES time point
NBI spins plasma in co-NBI direction – NOT ALWAYS true with 3D field!

## Slide 13: Comparison of measured intrinsic rotation profile (dB = 0) and low level of applied n = 2 field clearly alters Vf
Intrinsic rotation is defined as measured rotation profile with no applied 3D field
  Note: ECH applied in this case, but ohmic cases were run as well
Vf (km/s)
R (m)
16317 (0.0)
16315 (1.0)
t = 6.305s
Intrinsic rotation profile (dB = 0)
Shot (In=2 current) (kA/turn)
 Condition (a)
Low n = 2 field strength
 Condition (b)

## Slide 14: Increasing the applied n = 2 field strength leads to the saturation of the Vf profile expected for NTV offset profile
Vf (km/s)
16317 (0.0)
16314 (1.6)
16313 (2.4)
t = 6.305s
More than 2.2x increase in dB2 in this step, with almost no change to Vf profile
NTV drag with Vf profile >> V0NTV would produce change (more than 2.2x torque)
Shot (In=2 current) (kA/turn)
Increasing = 2 field strength
 Conditions (c), (d)
Intrinsic rotation profile (dB = 0)
R (m)

## Slide 15: Final saturated NTV offset Vf profile has much stronger Vf shear at large R compared to the intrinsic rotation profile
Shot (In=2 current) (kA/turn)
    V-1(dV/dr) (ECH) = 1.1 m-1
    V-1(dV/dr) (V0-NTV) = 15.4m-1
Vf (km/s)
16317 (0.0)
16313 (2.4)
16312 (3.2)
t = 6.305s
Intrinsic rotation profile (dB = 0)
Average shear (R > 2.14m)
15 times greater shear !
NTV offset Vf profile
NTV offset Vf profile has 15 times greater shear at large R
Saturated profile at highest applied n = 2 current confirms increased Vf at large R
R (m)

## Slide 16: The present results are potentially significant for ITER to provide strong plasma rotation and shear in outer plasma
Why unique?
  First time that V0NTV profile has been directly measured w/ TNBI = 0
  First time V0NTV has been measured dominated by electron effects
    V0NTV profile measured in the co-Ip direction
Why important?
  Co-Ip directed V0NTV can be higher than ECH-induced co-Ip rotation in edge region and is controllable
  Rotation shear in the outer plasma region is 15 times stronger than rotation shear due to ECH
ITER relevant: |V0NTV| strong compared to simulations
  ITER 15 MA ASTRA simulation: Wf ~ 2 krad/s in edge region
  Recent KSTAR experiment: Wf > 12 krad/s in edge region (scaling?)
  Potential to greatly increase rotation shear in outer plasma region

## Slide 17: The NTV offset effect is produced in ohmic plasmas, and is observed to be accentuated by ECH heating
Ohmic plasma Vf ~ 0 in core, weak further out
Applied n = 2 field increases Vf ~ in outer region
  Effect appears saturated at 4kA/turn (but no CES data outside R = 2.213m)
Stronger n = 2 field + ECH heating clearly yields counter-Ip rotation in core, co-Ip rotation in outer region
  Ctr-Ip only possible by V0NTV
  Large outer Vf shear
Vf (km/s)
R (m)
Co-Ip direction
Ohmic, In=2 = 0
Ohmic, In=2 = 2.4 kA/turn
ECH, In=2 = 4.9 kA/turn
Ohmic, In=2 = 4.0 kA/turn
Measured V0NTV profiles (when In=2 > 4)

## Slide 18: Varying plasma temperature shows V0NTV more strongly in co-Ip direction when Te is higher
Applied current for n = 2 field constant (4 kA/turn)
Plasma temperature varied by altering density
Results qualitatively follow NTV theory
  V0NTV is more strongly in co-Ip direction when Te is higher
Ti (eV)
R (m)
R (m)
Vf (km/s)
16308 (6.3s) core Te = 3.4 keV
16311 (6.3s) core Te = 2.2 keV
17014 (2.8s) core Te = 1.8 keV
Co-Ip direction
Core Te = 1.8 keV
Core Te = 2.2 keV
Core Te = 3.4 keV
In=2 = 4.0 kA/turn

## Slide 19: co-NB injection produces less co-rotation away from V0NTV as Ti increases in strong 3D field
Core plasma spins down with 3D field constant if dB, Ti are sufficiently high
Outer plasma velocity remains at V0NTV profile value
Non-intuitive result is consistent with NTV: Higher Ti increases NTV drag and/or makes NTV offset rotation migrate toward counter-NBI direction
Ti (eV)
R (m)
16308
R (m)
6.465s
6.385s
6.345s
6.305s
6.465s
6.385s
6.345s
6.305s
16308
Measured V0NTV profile
Start of NBI
In=2 = 4.0 kA/turn
Co-Ip
Vf (km/s)

## Slide 20: Experiments on NSTX and KSTAR isolated the NTV profile, and KSTAR XPs directly measured the offset rotation profile
Measured, isolated NTV torque density profiles created in KSTAR / NSTX, quantitatively compare well to theoretical TNTV using fully-penetrated 3D field (NSTX)
The NTV offset rotation profile was recently directly measured in KSTAR
  Incl. plasmas dominated by electron effects – measured in co-Ip direction
  shown to reverse sign in the core region to counter-Ip outside of error bars - can only happen if the NTV offset rotation profile is non-zero (not drag)
Relatively strong rotation and rotation shear were generated in outer region of the plasma by V0NTV - potentially highly important to ITER
  Suggests use of ITER ELM coils to generate rotation/shear
The |V0NTV| is strongest and in co-Ip direction in outer part of plasma and remains steady in higher temperature plasmas
  |V0NTV| shown to decrease as temperature (temperature gradient?) decreases
ANALYSIS CONTINUES on both NTV isolation analysis (e.g. plasma parameter and 3D spectrum dependence), NTV offset rotation profile comparison to theory

## Slide 21
Supporting Slides Follow

## Slide 22: Measured NTV torque density profiles quantitatively compare well to computed TNTV using fully-penetrated 3D field
TNTV (theory) scaled to match peak value of measured -dL/dt
  Scale factor ((dL/dt)/TNTV) = 0.6 and 1.7 for cases shown above – O(1) agreement
Banana orbit-averaging reduces computed resonant perturbation effects
n = 2 coil configuration
Experimental
-dL/dt
yN
NSTX
NTVTOK
x1.7
n = 3 coil configuration
Experimental
-dL/dt
NTVTOK
yN
NSTX
x0.6
K.C. Shaing, and S.A. Sabbagh, et al., Phys. Plasmas 23 (2016) 072511

## Slide 23: Measured NTV torque density profiles quantitatively compare well to computed TNTV using fully-penetrated 3D field
TNTV (theory) scaled to match peak value of measured -dL/dt
  Scale factor ((dL/dt)/TNTV) = 1.7 and 0.6 for cases shown above – O(1) agreement
Banana orbit-averaging reduces computed resonant perturbation effects
Experimental
-dL/dt
NTVTOK
code
yN
Experimental
-dL/dt
yN
NSTX
NSTX
NTVTOK code
n = 3 coil configuration
n = 2 coil configuration
x0.6
x1.7
K.C. Shaing, and S.A. Sabbagh, et al., Phys. Plasmas 23 (2016) 072511