## Slide 1: Outline
Introduction to Kinetic RWM Stability Theory (column 1)
  Rotational resonances and collisionality effects included
Modification of Ideal Stability by Kinetic Effects (2)
  MISK code calculation can explain experimental instability
Disruption Event Characterization and Forecasting (3)
  New DECAF code developed and used to analyze NSTX disruptions
Reduced Kinetic Model (4)
  Implemented in DECAF, successfully used on database
  Will enable real-time prediction of RWM growth rate
*This work supported by the US DOE contracts DE-AC02-09CH11466 and DE-FG02-99ER54524

## Slide 2: An unstable RWM is an exponential growth of magnetic field line kinking that can cause disruptions
The resistive wall mode (RWM) is a kinking of magnetic field lines slowed by penetration through vessel structures
where
Bp
RWMs can cause a collapse in β, disruption, and termination of the plasma
NSTX 130235
[S. Sabbagh et al., Nucl. Fusion 46, 635 (2006)]
βNno-wall
βNwith-wall
unstable
stable
0
Ideal Kink
Mode
Resistive Wall Mode
~τw-1

Copper plate

## Slide 3: A scalar critical plasma rotation model can not explain RWM stability; it depends on the ωφ profile
Early stability theories:
  Collisional dissipation of mode energy
  Rotational damping
    But models with scalar “critical rotation” for stability could not explain experiments
Plasma rotation
unstable
slowed by n=3 braking
[B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)]
Ideal Stability
Kinetic Effects
Unexplained experiments
New theory: consider kinetic effects
unstable RWM
NSTX
137722
140102

## Slide 4: “Kinetic effects” means taking into account complicated particle motion rather than treating the plasma as a fluid
Precession Drift
~ Plasma Rotation
Rotational resonance effect
[J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)]
MISK code
Solves for RWM growth rate
is solved by using from the drift kinetic equation
[R. Pitts et al., Physics World, March 2006
D. Pace et al., Physics Today 68, 34 (2015)]

## Slide 5: Kinetic theory consistent with RWM destabilization at intermediate plasma rotation and collisionality affects the strength of resonances
Collisionality
Rotation and Collisionality effects
Destabilization appears between:
  precession resonance at low ωφ
  bounce resonance at high ωφ
Stabilizing resonant kinetic effects enhanced at low ν
[J. Berkery et al., Phys. Rev. Lett. 106, 075004 (2011)]
(marginal stability)
ν/νexp (marginal stability)
instability
(NSTX
experiment)
ωφ/ωφexp (marginal stability)
MISK calculations of γτw contours vs. ν and ωφ
unstable
Precession drift resonance stabilization
Precession Drift
~ Plasma Rotation
[J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)]

## Slide 6: MISK calculations validated against unstable experimental plasmas; reproduce approach towards marginal stability
MISK calculations including kinetic effects have been tested against many marginally stable NSTX experimental cases
[J. Berkery et al., Nucl. Fusion 55, 123007 (2015)]
unstable
stable
NSTX
NSTX

## Slide 7: Kinetic RWM stability physics unites results from DIII-D and NSTX plasmas
[S. Sabbagh, J. Berkery, J. Hanson, et al., APS invited 2014]
Kinetic RWM stability analysis for experiments (MISK)
major disruption
minor disruption
DIII-D
NSTX
stable
Normalized growth rate (γτw)
Plasma rotation [krad/s] (ΨN = 0.5)
unstable
“weak stability” region
Addition of kinetic effects yields agreement with marginal point in NSTX
Further testing against DIII-D experiments shows good agreement
Strong bursting MHD modes can lead to non-linear destabilization before linear stability limits are reached

## Slide 8: Active MHD spectroscopy experiments show the importance of kinetic effects in stable plasmas as well
[H. Reimerdes et al., Phys. Rev. Lett. 106, 215002 (2011)]
DIII-D
[J. Berkery et al., Phys. Plasmas 21, 056112 (2014)]
Favorable rotation range
Resonant field amplification indicates weakening stability
  Plasma response is enhanced where kinetic effects and RWM stability are weak
Discharge trajectories for 20 NSTX plasmas shows favorable ω range
  Matches theoretical expectation for precession drift resonance
NSTX
MISK calculations match experiments

## Slide 9
Key analysis codes MARS-K and MISK were brought into agreement in γτw vs ωE for analysis of ITER
fluid growth rates
fluid plus kinetic growth rates
unstable
stable
low rotation
precession
resonance
high rotation
bounce/transit
resonance
expected ωφ
expected βα
unstable
stable
MISK calculation for ITER
Code benchmarking (growth rate vs. rotation)
[J. Berkery et al., Phys. Plasmas 21, 052505 (2014)]
The codes support the present understanding that RWM stability can be increased by kinetic effects
Case: βN = 2.9 (20% > no-wall limit)
Alpha particles are required for RWM stabilization at all ωφ
Near RWM marginal stability at βα/βtotal = 0.1 at expected rotation

## Slide 10: Physics understanding from previous research used to construct a reduced kinetic model
References
Goal is to forecast γ in real-time using parameterized reduced models for δW terms
Need δWK as a function of the most important, real-time measurable quantities
[J.W. Berkery et al., Nucl. Fusion 55, 123007 (2015)]
Kinetic effects1:
Fluid terms10
Rotation3
Collisionality5
Reduced Kinetic Model
[1] B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)
[2] B. Hu et al., Phys. Plasmas 12, 057301 (2005)
[3] J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)
[4] J. Berkery et al., Phys. Plasmas 17, 082504 (2010)
[5] J. Berkery et al., Phys. Rev. Lett. 106, 075004 (2011)
[6] H. Reimerdes et al., Phys. Rev. Lett. 106, 215002 (2011)
[7] J. Berkery et al., Phys. Plasmas 21, 056112 (2014)
[8] J. Berkery et al., Phys. Plasmas 21, 052505 (2014)
[9] S. Sabbagh APS invited (2014)
[10] J. Berkery et al., Nucl. Fusion 55, 123007 (2015)
… more
+ Energetic
Particles4
MISK2 Calculations
  Benchmarked8
  Compared to Experiments3,4,6,7,9

## Slide 11: Disruption event chain characterization capability started for NSTX-U as next step in disruption avoidance plan
Approach to disruption prevention
  Identify disruption event chains and elements
  Predict events in disruption chains
  Cues disruption avoidance systems to break event chains
    Attack events at several places with active control
  Builds upon both physics and control successes of NSTX
t
Disruption prediction/avoidance framework
[DOE report on Transient events (2015)]

## Slide 12: Disruption Event Characterization And Forecasting (DECAF) code is structured to ease parallel development
Main data structure
Code control workbooks
Density Limits
Confinement
Technical issues
Tokamak dynamics
Power/current handling
Mode stability
Physical event modules
Output processing
Kinetic RWM analysis used as a reduced stability model in DECAF
Physical event modules
  Present grouping expands work of deVries [P.C. de Vries et al., Nucl. Fusion 51, 053018 (2011)]
  – BUT, easily appended or altered
Warning algorithm
  Present approach expands [S.P. Gerhardt et al., Nucl. Fusion 53, 063021 (2013)]
  More flexible: arbitrary number of tests, thresholds, and user-defined levels and warning points

## Slide 13: The DECAF code is being used to characterize disruption event chains on NSTX, including RWMs
Several threshold tests are currently included in DECAF
Disruption event chain
  Resistive wall mode (RWM)
  Vertical stability control (VSC)
  Wall proximity control (WPC)
  Low density (LON)
  Plasma current not meeting request (IPR)
  Low q (LOQ)
  Excessive pressure peaking (PRP)
  Disruption (DIS)

## Slide 14: Initial DECAF analysis already finding common disruption event chains, giving new insight
Identifying common chains of events can provide insight into how to cue avoidance systems
  6 (out of theoretically 42) two-event combinations following RWM accounted for 70% of the cases in the database
VSC
WPC
IPR
WPC
PRP
VSC
Other
RWM
PRP
PRP
WPC
VSC
IPR
WPC
15.9%
13.6%
11.4%
11.4%
9.1%
9.1%
29.5%
Earlier RWM events not false positives
  cause large decreases in βN and stored energy with subsequent recovery (minor disruptions)

## Slide 15: Initial DECAF results detects disruption chain events when applied to dedicated 44 shot NSTX RWM disruption database
Several events detected for all shots
  DIS: Disruption occurred
  RWM: RWM event warning
  WPC: Wall proximity control
  IPR: Plasma current request not met
  LOQ: Low edge q warning
  Others:
    PRP: Pressure peaking warning (34/44)
    VSC: Vertical stability control (31/44)
    LON: low density warning (11/44)
RWM threshold near disruption limit
  RWM BPn=1 lower threshold 30G (δB/B0 ~ 0.67%)
  61% within 20 τw of disruption time (τw = 5 ms)

## Slide 16: Goal is to forecast γ in real-time using parameterized reduced models for δW terms
[B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)]
no-wall limit
no-wall limit
with-wall limit
with-wall limit
fluid RWM growth
rate
stabilized by kinetic effects
Growth rate
Kinetic effects
Fluid terms
RWM dispersion relation
Modeled estimates for NSTX no-wall limit
NSTX 138556
Internal inductance
Pressure peaking
Aspect ratio
Composite no-wall limit model
[J.W. Berkery et al., Nucl. Fusion 55, 123007 (2015)]
β limits
δW
growth
rate
(γτw)

## Slide 17: The unstable region of the stability diagram is determined by the fluid δW terms; Kinetic effects can stabilize the RWM
Stability diagram in kinetic stability space
The unstable region, inside the circle, moves when β changes
The size and position of the circle is determined by the fluid δW terms
Moderate levels of kinetic effects stabilize the RWM at certain beta values
Large kinetic effects – robustly stable

## Slide 18: DECAF contains modeled kinetic quantities for generation of stability maps
Kinetic effects
Bounce resonances
Precession resonance
<ν> = 1 kHz
Gaussian functions are used to model broad resonances
  Positions in <ωE> determined by ωD and ωb
  Height, width, and position dependent on ν
  Coefficients selected to reflect NSTX experience
Stability diagrams show trajectory of a discharge towards unstable regions

## Slide 19
84% of shots are predicted unstable
44% predicted unstable < 320 ms (approx. 60tw) before current quench
33% predicted unstable within 100 ms of a minor disruption
Predicted instability statistics (45 shots)
Normalized growth rate vs. time
Chart: 
Stable
(16%)
Instability within 100 ms of minor
disruption
(33%)
Instability < 320 ms
before disruption
(44%)
unstable
stable
(7%) False
positives
DECAF reduced kinetic model results initially tested on a database of NSTX discharges with unstable RWMs

## Slide 20: Reduced kinetic model distinguishes between stable and unstable NSTX discharges
Reduced kinetic model tested on a database of stable and unstable NSTX discharges
Model fails to capture an experimentally unstable RWM in 7/45 cases, 15.6%
Sometimes the model warning is associated with minor disruptions that subsequently recover
If <ωE> ~ 0 warnings are ignored, 10/13, or 77%, of stable cases are stable in the model
Model is successful in first incarnation - development continues to improve forecasting performance
Unstable cases
Stable cases

## Slide 21: Summary
Disruption prevention in tokamak fusion plasmas requires accurate identification and prediction of global MHD instabilities
  Resistive wall modes are crucial components of disruption event chains
DECAF code developed for disruption characterization and forecasting
Kinetic theory modifies ideal stability, includes rotation, collisionality
  MISK code calculations can explain experimental stability
Full MISK code calculations of δWK can not be performed in real time, but physics insight used to create a reduced model
Reduced kinetic model for disruption avoidance is implemented
  Success rate is surprisingly high given its initial state and relative simplicity
  This approach will enable, for the first time, for an unstable growing kinetic RWM to be anticipated, rather than responding to an already unstable growing mode

## Slide 22: MISK

## Slide 23: DECAF

## Slide 24: Reduced Kinetic Model

## Slide 25: Abstract of paper EX/P4-34
The new Disruption Event Characterization and Forecasting (DECAF) code has been written to analyze disruptions in tokamaks. A quantitative statistical characterization of the chains of events which most often lead to disruption in a database of discharges from NSTX which disrupted due to an unstable resistive wall mode (RWM) is presented. The recently implemented reduced kinetic model for RWM stability is described and shown to have the potential to track RWM stability in real-time for disruption avoidance. The reduced model was tested on a database of discharges from NSTX and experimentally stable and unstable discharges were separated noticeably on a stability map in ExB frequency, collisionality space. Initial results show the reduced model only failed to predict an unstable RWM in 15.6% of cases with an experimentally unstable RWM and performed well on predicting stability for experimentally stable discharges as well.

## Slide 26: Characterization and Forecasting of Unstable Resistive Wall Modes in NSTX and NSTX-U
Jack Berkery
Columbia University
S.A. Sabbagh1, Y.S. Park1, R.E. Bell2, S.P. Gerhardt2, C.E. Meyers2
1Columbia University, 2Princeton Plasma Physics Laboratory
26th IAEA Fusion Energy Conference
Kyoto, Japan, October 17-22, 2016
*This work supported by the US DOE contracts DE-AC02-09CH11466 and DE-FG02-99ER54524