## Slide 1: NSTX/NSTX-U Theory, Modeling and Analysis Results & Overview of New MAST Physics in Anticipation of First Results from MAST Upgrade
J.E. Menard for S.M. Kaye (PPPL), J. Harrison (CCFE) and the NSTX-U and MAST-U Teams
IAEA FEC, Oct. 23, 2018
MAST-U

## Slide 2: Missions of NSTX(-U) and MAST(-U)
Exploit unique Spherical Tokamak (ST) parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for plasma- material interface (PMI)
Explore ST physics towards reactor relevant regimes (e.g., Fusion Nuclear Science Facility and Pilot Plant)
Snowflake/X
ST-FNSF /
Pilot-Plant
ITER
Super-X

## Slide 3: NSTX(-U) and MAST address urgent issues for fusion science, ITER and next-step devices
Spherical Tokamaks (STs) can investigate turbulence over an extended range in β (tens %)
  Electrostatic and electromagnetic effects
STs Energetic Particle (EP) physics spans phase space expected in Burning Plasmas
  vfast/vAlfvén vs βfast/βtot
  Develop predictive and control methods
Reduced aspect ratio expands range of field line connection length to study and mitigate divertor heat flux

## Slide 4: MAST-U will emphasize boundary physics
MAST
MAST-U
Flexible divertor with Super-X capability for exhaust research
Off-midplane 3D magnetic coils for edge instability control
Super-X divertor configuration
On and off-midplane NBI
Ip | ≤ | 1.3 | 2 MA
RBT | ≤ | 0.44 | 0.64 m-T
PNBI | ≤ | 3.5 | 10 MW
τpulse | ≤ | 0.7 | 5 s
Maximum Parameters

## Slide 5: NSTX-U will emphasize core physics
NSTX
New tangential NBI for j(r) control
High BT (1 T at R0)  projected largest range in β and (lower) ν* in an ST
Greater stability (βn/li ≤ 14) + flexible NBI  high non-inductive current
Ip | ≤ | 1.4 | 2 MA
RBT | ≤ | 0.47 | 0.94 m-T
PNBI | ≤ | 6 | 15 MW
PRF | ≤ | 6 | 6 MW
τpulse | ≤ | 1 | 5 s
NSTX-U
Conducting plates can suppress global kink instabilities
Maximum Parameters

## Slide 6: This talk will cover recent complementary results from NSTX(-U) and MAST
Core transport and stability physics
Energetic particle physics/mode stability
Boundary and divertor physics
Future plans

## Slide 7: This talk will cover recent complementary results from NSTX(-U) and MAST
Core transport and stability physics
  ST confinement trends differ from those at higher aspect ratio
    NSTX/MAST: τE ~ Ip0.5BT1 ~ ν*-0.8
    (ITER-Basis: τE ~ Ip1BT0 ~ ν*0)
  Stability control methods necessary for high-β operation
Electron beta
Normalized collisionality (~n/T2)
e-s turbulence
e-m turbulence
NSTX-U
MAST-U
NSTX/MAST

## Slide 8: Core: Measurements and theory help in understanding the turbulence that underlies confinement trends in STs
ETG sims initially produce streamer-like structures before forming ‘vortex streets’
  Collisionality dependence due to damping of zonal flows
[G. Colyer et al., PPCF 59 055002 (2017)]
[M. F. J. Fox et al., PPCF 59 034002 (2017)]
[F. van Wyk et al., PPCF 59 114003 (2017)]
ITG turbulence often suppressed by flow shear
  MAST BES measurements of ITG ñ show flow shear breaks symmetry of turbulence in space (tilt) and amplitude (skewed PDF)
  Collisionality dependence controlled by electron transport due to
  electrostatic dissipative TEM/electromagnetic microtearing modes on NSTX
  electrostatic ETG on MAST
MAST
Low ν*
High ν*

## Slide 9: Core: Multi-scale and non-local effects potentially important for understanding underlying turbulence
Ion-scale (ITG/TEM) non-linear simulations (GTS) for NSTX L-mode illustrate importance of global effects
  Transport from global (GTS) lower than from local (GYRO) simulations  profile shearing effects at large ρ* important
    1/ρ* ~ 75 (NSTX), 200 (DIII-D), 350 (JET)
Electron-scale (ETG) non-linear simulations predict significant Qe; close to expt’l
  Similarity in Qe, high-k and Qi, low-k indicates cross-scale coupling may be important
Local GYRO
Global GTS
Neoclassical
Ion heat flux (MW)
Electron heat flux (MW)
Qi
Qe

## Slide 10
DECAF analysis of disruption event
  Shots analyzed at 10 ms intervals during Ip flat-top
  MAST: 8,902 plasmas analyzed; NSTX: 10,432 plasmas
Supports published result that disruptivity doesn’t increase with βN
Disruptivity plots provide important information, but can be misleading when used incorrectly
  Plasma conditions can change significantly between first problem detected and when disruption happens
  Circles mark the key region to study with DECAF: where events that lead to disruptions (X’s) start
MAST
NSTX
Core: Disruption Event Characterization and Forecasting (DECAF) code used to provide a cross-machine comparison of disruptivity
[Sabbagh et al., EX/P6-26 (DECAF)]

## Slide 11: This talk will cover recent complementary results from NSTX(-U) and MAST
Energetic particle physics/mode stability
  Energetic particle-driven instabilities may reflect those in ITER, next-step devices
  Will show examples of fast ion distribution effects by sawteeth, high-frequency AE to develop understanding, predictive capabilities, and control methods
  Instabilities in both frequency ranges may be important for ITER

## Slide 12: Energetic Particles: Sawteeth on MAST and NSTX-U have a significant effect on the fast particle population
Passing (Edge)
Trapped (Core)
MAST neutron camera measurements show drop in neutron rate (fast ion distribution) across profile
  Modeling indicates that sawteeth have comparable effect on both trapped and passing particles
FIDA & solid-state NPA measurements on NSTX-U indicate that passing particles strongly expelled from core by sawteeth [Liu, Nuc. Fusion (2018)]
  Little effect on trapped particles
NSTX-U ssNPA
MAST – Neutron Camera
After s-t crash
Before s-t crash
[M Cecconello et al., PPCF 60 055008 2018]
Radius (m)
Radius (m)

## Slide 13: Energetic Particles: Different sawtooth models on MAST and NSTX-U show agreement with experiment
Before S-T
After S-T
Full reconnection model (Kadomtsev) consistent with measurements in MAST
  Inversion of real and synthetic FIDA data show expulsion of trapped and passing particles from core
Simple sawtooth models cannot reproduce spatial redistribution of fast particles in NSTX-U [Kim, EX/P6-33]
  “Kick” model [Podesta, PPCF (2014)], based on orbit-following calculations of fast ions, lead to better agreement
[B. Madsen et al., RSI 89 10D125 (2018)]
TRANSP/FIDASIM (Kadomtsev model)
Experiment

## Slide 14: Energetic Particles: Different sawtooth models on MAST and NSTX-U show agreement with experiment
Are differences due to differences in injection energy, phase space distribution of EP?
Full reconnection model (Kadomtsev) consistent with measurements in MAST
  Inversion of real and synthetic FIDA data show expulsion of trapped and passing particles from core
Simple sawtooth models cannot reproduce spatial redistribution of fast particles in NSTX-U [Kim, EX/P6-33]
  “Kick” model [Podesta, PPCF (2014)], based on orbit-following calculations of fast ions, lead to better agreement
Kadomtsev model
Porcelli model

## Slide 15: Energetic Particles: Progress in developing tool for phase-space engineering of EP-driven instabilities in NSTX-U
High frequency global Alfvén Eigenmodes (GAEs) suppressed by off-axis beam injection [Fredrickson PRL (2017), Nuc. Fus. (2018)]
Non-linear HYM simulations show unstable counter-rotating GAEs
  Maximum growth rates for toroidal mode numbers -7 to -11
  Predicted frequencies match measurements
  Peak saturation amplitudes δB/B ~ 5e-3
  Effect on electron transport under investigation

## Slide 16: Energetic Particles: Progress in developing tool for phase-space engineering of EP-driven instabilities in NSTX-U
High frequency global Alfvén Eigenmodes (GAEs) suppressed by off-axis beam injection [Fredrickson PRL (2017), Nuc. Fus. (2018)]
Non-linear HYM simulations show unstable counter-rotating GAEs
  Maximum growth rates for toroidal mode numbers -7 to -11
  Predicted frequencies match measurements
  Peak saturation amplitudes δB/B ~ 5e-3
  Effect on electron transport under investigation
EP phase space engineering will be explored in MAST-U using on/off-midplane NB and off-midplane RMP coils

## Slide 17: This talk will cover recent complementary results from NSTX(-U) and MAST
Boundary and divertor physics
  Turbulence studies at midplane and in divertor SOL for aid in understanding processes controlling heat flux amplitude and profile

## Slide 18: Boundary: Gas puff imaging & theory being used to study edge turbulence near the midplane in NSTX
GPI measurements of edge turbulence show dipole-like 2-D spatial correlations with large negative regions (blue)
Semi-analytic model assuming blob-hole pairs shows similar 2D correlation patterns, dipole flip across separatrix [Myra, PPCF (2018)]
Edge turbulence is being better understood through a combination of semi-analytic models and numerical simulation (e.g. XGC1)
origin inside
separatrix
origin near
separatrix
origin outside
separatrix
radially out

## Slide 19: Divertor: Fast camera imaging of the divertor provides new insights into SOL turbulence
Non-linear 3D drift-fluid simulations (STORM/BOUT++) of SOL turbulence performed in realistic MAST geometry [Militello TH/7-1]
  Reproduces filaments seen in fast camera videos of main chamber and divertor
    SOL Dα profiles well described by superposition of independently moving filaments
  Quiescent region in SOL near X-point has been identified [Walkden et al., Nuc. Fus. 57 126028 (2017)]
  Synthetic diagnostics developed to enable direct comparison with experiments
BOUT++ simulation
Background subtracted fast camera data

## Slide 20: Divertor: Fast camera imaging of the divertor provides new insights into SOL turbulence
Rendering
Images in CIII emission
[Scotti, Nuc. Fusion (2018)]
Divertor leg fluctuations observed by fast imaging in NSTX-U
  Intermittent; localized to bad curvature side
Evidence for X-point disconnection
  Inner and outer filament legs not correlated
  Divertor filaments/midplane blobs not correlated
Simulations with ArbiTER code find unstable resistive ballooning modes [Baver, CCP (2016)]

## Slide 21: This talk will cover recent complementary results from NSTX(-U) and MAST
Future plans

## Slide 22: Expected benefits of Super-X divertor will be tested during first experimental campaign of MAST-U
Parallel heat flux gradients along Super-X leg should improve detachment control
  Scales with Bx-pt/Btarget; can be higher is STs (~3) than at conventional aspect ratio (~1-2)
Parallel particle flux (m-2s-1)
Density (m-3)
[D. Moulton et al., Proc 44th EPS Conf. 2017]
[B. Lipschultz, et al., NF 56 056007 2016]
Super-X expected to improve exhaust mitigation and control of detachment front position
Detachment in Super-X expected at lower density than in conventional

## Slide 23: MAST-U preparing for operation
MAST-U presently baking out; modifying TF linkages
Expected physics operation Autumn 2019
Detailed characterization of intrinsic error field carried out to optimize correction and broaden operating space
New diagnostics
  Divertor: 850 Langmuir probes, divertor TS, IR & visible cameras, bolometers
  Energetic particles: ssNPA, FILD

## Slide 24: NSTX-U Recovery underway
NSTX-U operated for 10 weeks in 2016, achieving good H-mode performance, surpassing magnetic field and pulse duration of NSTX
Run ended prematurely due to divertor PF fault
Full repair will consist of installing improved PF coils, graphite PFCs to handle heat fluxes of high-power, long-pulse scenarios, minimized error fields to increase reliability [Gerhardt, FIP/P3-63]
Projected to commence operations in early 2021
  Study transport and stability physics at high-β/low ν* (Bτ ~ ν*-0.8)
  Demonstrate full non-inductive operation (j(r) control with NBI)

## Slide 25: Close collaboration between NSTX-U and MAST-U on developing startup scenarios
Vacuum field calculations support magnetic calibrations and inductive startup scenario development
Procedure for producing MAST-U first plasma being developed using the PPPL-LRDFIT code
  Results from NSTX(-U) provide basis for first-plasma scenarios on MAST-U
  Extended on-site (CCFE) visits facilitate collaboration

## Slide 26: Summary: NSTX(-U) and MAST address urgent issues for fusion science, ITER and next-step devices
Core transport & turbulence studied over an extended range of β and ν*
  Electrostatic and electromagnetic effects drive strong favorable ν* scaling
  Multi-scale effects (low- & high-k) must be considered
Energetic particle effects and instabilities studied in portions of parameter space expected for α-burning plasmas
  Low and high frequency modes can have profound effect on EP distribution
  Predictive models and phase-space engineering techniques being developed
Boundary and divertor studies address processes controlling heat flux width
  Filamentary structures/turbulence
  Heat flux mitigation through innovative divertor designs
When operation commences, NSTX-U and MAST-U will be the most capable devices in the world-wide ST program
Relevant IAEA contributions follow

## Slide 27: NSTX(-U)/MAST(-U) related IAEA presentations
J. Menard: Fusion energy development utilizing the Spherical Tokamak OV/P-6 (Mon AM)
R. Lunsford: Electromagnetic particle injector FIP/P1-51 (Tues AM)
M. Podesta: Reduced EP transport models EX/1-2
E. Belova: Numerical simulations of GAE suppression TH/P2-16 (Tues PM)
S. Pamela: ELM and ELM-control simulations OV/4-4
S. Gerhardt: NSTX-U Recovery physics and engineering FIP/P3-63 (Wed AM)
V. Menon: Performance of large and small R/a fusion tokamaks FIP/P3-60
N. Bertelli: Impact of H+ on HHFW in NSTX-U TH/P4-13 (Wed PM)
G.Z. Hao: Centrifugal force driven low-f modes in STs TH/P5-13 (Thurs AM)
T. Rafiq: Effects of microtearing modes on Te evolution in NSTX TH/P5-10
S. Sabbagh: Disruption characterization and forecasting EX/P6-26 (Thurs PM)
N. Ferraro: EF impact on mode locking and divertor heat flux in NSTX-U EX/P6-40
E. Fredrickson/M. Podesta: GAE stability dependences on fast ion distribution EX/P6-32
D. Kim: Fast ion redistribution by sawteeth on NSTX-U EX/P6-33
L. D-Aparacio: Rotation-induced electrostatic potentials and density asymmetries in NSTX EX/P6-33
R. Goldston: Development of Li vapor box divertor for controlled plasma detachment FIP/3-6
T. Brown: A toroidal confinement facility to study liquid lithium divertor (Fri AM)
A. Hakim: Continuum g-k simulations of NSTX SOL turbulence with sheath-limited geometries TH/P7-33
I. Krebs: Nonlinear 3D simulations of VDEs in tokamaks TH/P8-10 (Fri PM)
F. Militello: Predicting Scrape-Off Layer profiles and filamentary transport for reactor relevant devices TH/7-1

## Slide 28: Backup

## Slide 29: NSTX(-U) and MAST research address urgent issues for fusion science, ITER and next-step devices
STs can investigate turbulence over an extended range in β (tens %)
  Electrostatic and electromagnetic effects at large ρ*
STs EP physics spans phase space expected in Burning Plasmas
  Develop predictive and control methods
Reduced connection length and surface area can lead to increased qtarget in conventional divertors in STs
  Developing strategies to mitigate heat fluxes in STs critical
Electron beta
Normalized collisionality (~n/T2)
e-s turbulence
e-m turbulence
NSTX-U
MAST-U
KBM
MTM
ITG/TEM/ETG
NSTX/MAST
MOVE TO BACKUP?

## Slide 30: NSTX(-U) and MAST research address urgent issues for fusion science, ITER and next-step devices
STs can investigate turbulence over an extended range in β (tens %)
  Electrostatic and electromagnetic effects at large ρ*
STs EP physics spans phase space expected in Burning Plasmas
  Develop predictive and control methods
Reduced connection length and surface area can lead to increased qtarget in conventional divertors in STs
  Developing strategies to mitigate heat fluxes in STs critical
MOVE TO BACKUP?

## Slide 31: Core: Disruption Event Characterization and Forecasting (DECAF) algorithm being developed for stable operation
DECAF utilizes physics-based models as much as possible to identify event chain leading to disruptions in a time-evolving fashion [Sabbagh et al., EX/P6-26]
  Couple to real-time control system for stable operation, disruption mitigation
DECAF MHD warning level
DECAF automated MHD events
n =
1
2
3
MHD-n1
PRP
DIS
IPR
WPC
VDE
(0.490s)
LTM-n1
(+.068s)
(+.073s)
(+.073s)
(+.077s)
(+.080s)
(+.045s)
DECAF event chain
n=1 appears
n=1 locks
large dIp/dt
p(r) peaks
hits wall
Multi-institutional effort [NSTX, MAST, KSTAR, DIII-D, TCV (so far)]
disruption
VDE
NSTX

## Slide 32: Energetic Particles: Microturbulence is a mediator of EP instabilities on NSTX-U
High βfast, vfast/vAlfvén>1 provide significant drive for enhanced wave-particle and nonlinear mode-mode interactions (chirping, avalanches)
  Seen predominantly at lower than at higher aspect ratio
Microturbulence can increase scattering of resonant fast ions to reduce chirping and avalanching [Duarte Nuc. Fusion (2018)]
  Global GTS non-linear simulations support theoretical prediction

## Slide 33
Counter-TAEs can be destabilized by off-axis co-NB injection from 2nd NB line
Single NB source from 2nd NBI
Low power, PNB~1MW
Off-axis NBI results in broad/hollow NB ion density profile
A transition is observed from co-TAEs only to cntr-TAEs

## Slide 34: Details of fast ion distribution explain destabilization of counter-TAEs by co-NBI
co-TAEs
cntr-TAEs
Single NB source from 2nd NBI
Low power, PNB~1MW
Stability analysis with TRANSP + kick model recovers observations
Drive results from competition between gradients in energy and canonical momentum
[Podestà, NF 2018]

## Slide 35: Boundary: Particle confinement control and turbulence being studied in MAST
First estimates of radial wave number of Geodesic Acoustic Mode in an ST in an ohmic L-Mode in good agreement with global 2-fluid simulations [Hnat, PPCF (2018)]
  Oscillation localized to boundary that can influence L-H transition dynamics
  10 kHz, krρp ~ -0.15, vr ~ 1 km/s, located 2 cm inside the separatrix
Application of Resonant Magnetic Perturbations (RMPs) reduces particle confinement
  τion reduced by ~20% in L-mode (with n=3 RMP) and 30% in H-mode (with n=4 RMP)
RMP ON
RMP OFF
τion (ms)
Time (s)
τion (ms)
Time (s)
RMP ON
RMP OFF
RMP OFF (29092)
RMP ON (29178)
L-mode
H-mode

## Slide 36: Divertor Physics: SOL turbulence can contribute of cross-field transport: being studied in both MAST and NSTX-U
MAST SOL density profiles are well described by the superposition of independently moving filaments
  Quiescent region in the SOL near X-point
Divertor leg fluctuations observed by fast imaging in NSTX-U
  Intermittent; localized to bad curvature side
  Connected to divertor target plate
Evidence for X-point disconnection
  Inner and outer filament legs not correlated
  Divertor filaments/midplane blobs not correlated
[F. Militello et al., PoP 25 056112 2018]
[N. Walkden et al., NF 57 126028 2017]
(“blobs”)

## Slide 37: Divertor Physics: Fast camera imaging of the divertor provides new insights into SOL turbulence
SOL turbulence being studied in both MAST and NSTX
  MAST SOL density profiles are well described by the superposition of independently moving filaments
Quiescent region in the SOL near the X-point has been identified
Divertor leg fluctuations observed by fast imaging in NSTX-U
  Intermittent; localized to bad curvature side
Evidence for X-point disconnection
  Inner and outer filament legs not correlated
  Divertor filaments/midplane blobs not correlated
[F. Militello et al., PoP 25 056112 2018]
[N. Walkden et al., NF 57 126028 2017]
Moving average subtracted unfiltered frame

## Slide 38: Divertor: Linear and non-linear simulations of SOL turbulence being performed in NSTX-U and MAST
Linear simulations with ArbiTER code for NSTX-U find unstable resistive ballooning modes [Baver, CCP (2016)]
  Higher mode numbers on outer than on inner legs
Non-linear 3D drift-fluid simulations (STORM/BOUT++) of SOL turbulence performed in realistic MAST geometry
  Reproduces filamentary structures seen in fast camera videos in main chamber and divertor
MAST

## Slide 39: Divertor Physics: Intermittent field-aligned filaments localized to bad curvature side of divertor legs in NSTX-U
Divertor leg fluctuations observed by fast imaging [Scotti, Nuc. Fusion (2018)]
  10-30 kHz, kpolρi~0.01-0.1, vpol~1-2 km/s
Connected to divertor target plate
Evidence for X-point disconnection
  Inner and outer filament legs not correlated
  Divertor filaments/midplane blobs not correlated
Simulations with ArbiTER code find unstable resistive ballooning modes [Baver, CCP (2016)]
  Higher mode numbers on outer than on inner legs
Rendering
Images in CIII emission

## Slide 40: Edge: NSTX is exploring L-H transition physics
Production term, P, related to Reynold’s stress
Find P<0 just prior to L-H in NSTX
  Energy transfer from ZF to turbulence
Inconsistent with Predator-Prey model [Diallo, Nuc. Fusion (2017)]
Zonal ExB energy
Thermal free
energy
Non-zonal
ExB energy
Turbulence fluctuation energies
P<0
P>0
NSTX