## Slide 1: 27th IAEA FUSION ENERGY CONFERENCE Gandhinagar (Ahmedabad) INDIA, October 2018
Numerical simulations of Global Alfven Eigenmode (GAE) stabilization in NSTX-U
E. V. Belova1, E. D. Fredrickson1, N. A. Crocker2, and the NSTX-U team
1) Princeton Plasma Physics Laboratory, Princeton NJ, USA
2) University of California, Los Angeles, California 90095, USA
TH/P2-16

## Slide 2
NSTX-U off-axis neutral beam suppresses Global Alfven Eigenmodes (GAEs) [E. Fredrickson, PRL 2017]
1a
1b
1c
2a
2b
2c
Counter-propagating GAEs are frequently observed in the sub-cyclotron frequency range of 0.1fci up to 0.5fci, in NSTX and NSTX-U.
Driven by cyclotron resonance with beam ions
New neutral beam sources ― ability to control the fast ion distribution.
Off-axis neutral beams inject fast ions onto trajectories largely parallel to the magnetic field, with pitch 0.8<V||/V<1.
Reliable suppression of the counter-propagating GAE when an additional 1.3MW is injected using the outboard beam.
Sketch of neutral beam geometry. Original beams in green, labeled 1a, 1b, 1c; new beams for NSTX-U shown in red labeled 2a, 2b and 2c.

## Slide 3
GAE stabilization has been well documented for many NSTX-U shots
The measured GAE suppression time ~ few ms is much smaller than slowing-down time (~50ms), suggesting that it takes relatively few high-pitch fast ions to suppress the GAE.
Three examples of GAE being suppressed by the injection of one of the three off-axis beam sources.
Figure 1(c) also shows that the GAE can reappear when the 2c power is turned off.

## Slide 4
HYM – HYbrid and MHD code
Code description
3-D nonlinear.
Physical models:
- Resistive MHD & Hall-MHD
- Hybrid (fluid electrons, particle ions)
- MHD/particle (one-fluid thermal plasma, + energetic particle ions)
- Drift-kinetic particle electrons
Full-orbit kinetic ions.
For particles: delta-f / full-f numerical scheme.
Parallel (3D domain decomposition, MPI)
Applications
NSTX
- Sub-cyclotron frequency Alfven eigenmodes (GAE and CAE)
ICC Theory and Modeling
- Hybrid simulations of spheromak merging
- FRC: Effects of beam ions on stability
- Rotation control
- n=2 rotational and n=1 wobble modes

## Slide 5
Self-consistent MHD + fast ions coupling scheme
ρ, V and p are thermal plasma density, velocity and pressure, nb and jb are beam ion density and current, and nb << ne – is assumed.
Background plasma - fluid:
Fast ions – delta-F scheme:
- particle weight

## Slide 6
Self-consistent anisotropic equilibrium including the NBI ions
Beam
Modifications of equilibrium due to beam ions:
more peaked current profile,
anisotropic pressure,
increase in Shafranov shift
might have indirect effect on stability.
Grad-Shafranov equation for two-component plasma:
MHD plasma (thermal) and fast ions [Belova et al, Phys. Plasmas 2003].
, G – poloidal stream
function
Beam effects

## Slide 7
Fast ions – delta-f scheme: F0=F0(ε,μ,pφ)
Equilibrium distribution function F0 = F1(v) F2(λ) F3(pφ,v)
where v0 = 2-5vA, v*= v0 /2, λ= μB0/ε – pitch angle parameter, λ0= 0.5-0.7 (typical of on-axis
beam), and μ= μ0 + μ1 includes first-order corrections [Littlejohn’81]:
Parameters are chosen to match TRANSP beam profiles.

## Slide 8
Simulations have been performed to study the excitation and stabilization of GAEs in the NSTX-U
ψ
q(ψ)
nb/n0(R)
0.3 0.5 1.0 1.5 R(m)
Plasma shape, q- and nb profiles for NSTX-U shot 204707 t=0.44 from TRANSP and HYM GS solver + FREE_FIX.
Simulations using the HYM code have been performed for NSTX-U shot #204707 right before (t=0.44s) and shortly after (t=0.47s) the additional off-axis beam injection.
Plasma and beam profiles have been chosen to match TRANSP profiles for t=0.44s and t=0.47s.
The beam ion distribution function matches TRANSP data, with pitch distribution in the form
Fb~ exp[-(λ-λ0(ε))2/Δλ(ε)2] –
improved fit includes energy dependence of pitch distribution.
 HYM
- - - - TRANSP
(a) Spectrogram on magnetic fluctuations (n=8-11 counter-GAEs).
(b) Rms magnetic fluctuations;
(c) Injected beam power.
t=0.44
t=0.47

## Slide 9
NSTX-U linear simulations: n=-10 counter-GAE (t=0.44s)
Radial profile of ωA/ωci for n=-10, m=0-2; location of GAE.
Radial profile of δB and δn for n=-10 counter-GAE.
dB||
dB┴
Unstable modes are counter-rotating and have shear Alfven polarization
Located near min of ωA
R(m)
R(m)

## Slide 10
HYM reproduces experimentally observed unstable GAEs
Simulations reproduce most unstable toroidal mode numbers and GAEs frequencies.
HYM overestimates growth rates compared experimental analysis by 2-3 times.
Experimental estimates [Fredrickson, NF 2018]:
n=-10 γ/ωci=0.84%
n=-11 γ/ωci=0.6%
Growth rates are sensitive to distribution function parameters – resonance particles are in ‘tail’ of distribution.
γ/ωci
ω/ωci
-n
HYM #204707 t=0.44
(a) Growth rates and (b) frequencies of unstable counter-GAEs from HYM simulations for t=0.44s. Blue line is Doppler-shift corrected frequencies, points – experimental values.

## Slide 11
Improved Fbeam fit allows more accurate description
V||/VA
δF/F
Location of resonant particles in phase space: λ=μB0/ε vs pφ.
Particle weight w ~ δF/F vs orbit-averaged parallel velocity. Particle color corresponds to different energies: from E=0 (purple) to E=90keV (red).
V||/V
TRANSP fast-ion distribution before the outboard beam injection t=0.44.
HYM fast-ion distribution from n=-11 GAE simulations; dots show resonant particles.
cyclotron
resonance
b)

## Slide 12
Resonant region is wider in nonlinear phase
Location of resonant particles in phase space; from linearized and nonlinear simulations of n=-11 GAE. Particle color corresponds to different energies: from E=0 (purple) to E=90keV (red); ‹V||› - orbit averaged velocity.
LIN
NL
pφ
λ
λ
LIN
NL
‹V||›/V
Energy (keV)
0 50 100
Energy (keV)
0 50 100

## Slide 13
Nonlinear simulations: n=-11 counter-GAE (t=0.44s)
Time evolution of perturbed magnetic field components from nonlinear simulations for n=-11 GAE.
Nonlinear simulations show peak saturation amplitudes of δB/B0~5×10-3 at R~1.2m close to the minimum of the Alfvén continuum, and δB/B0~10-3 near the edge at the midplane.
Unstable modes have shear Alfven polarization in the core, and mixed polarization at the edge.

## Slide 14
Approximate peak amplitudes averaged over the time window. A correction factor (the ratio between peak and average amplitude) varied between 1.2 and 2.7.
Experimental estimates of the peak mode amplitudes are δB/B0≈2.7•10-3 for the n=-10 and δB/B0≈(1-2)•10-3 for the n=-11 modes at t~0.44s.
Large uncertainty is in the reflectometer reconstructions which depend on accurate density profile gradient data.
Experimental amplitudes estimates are comparable to nonlinear simulation results
Time evolution of peak amplitude of n=-11 GAE in NSTX-U shot 204707, based on reflectometer reconstructions [E. Fredrickson].

## Slide 15
HYM simulations reproduce experimental finding: off-axis neutral beam injection reliably and strongly suppresses unstable GAEs
n= -11
tci
|dB|2
Time evolution of magnetic energy of n=-11 GAE from HYM simulations for t=0.44s (red), and t=0.47s (blue).
HYM #204707, t=0.44, t=0.47
t=0.44s
t=0.47s
tci
Growth rates of n=-11 (blue), -10 (red), -9 (green) GAEs vs fraction of outboard beam ion population.
Nadd/Ntot
γ/ωci
Off-axis beam injection has been modelled by adding beam ions with distribution Fadd ~ exp[-λ2/Δλ (ε)2], and varying density.
For NSTX-U beam parameters, HYM shows complete linear stabilization of all unstable GAEs.
In additional simulations, fraction of off-axis beam population of the total fast ion inventory has been varied from 4% to 17%.
Unstable n=-11 GAE is stabilized when the fraction of the off-axis beam ions is larger than 7%
Stabilization threshold is lower for lower |n| modes.
Fraction of outboard beam power vs total beam power in NSTX-U was ~24-30%, but the GAEs become suppressed at the point where the fast ion population has increased by 6% (based on the neutron rate increase by 6%) – excellent agreement with simulations.

## Slide 16
TRANSP fast-ion distribution before and after the outboard beam injection. Fast ions with pitch v||/v~1 are responsible for GAE suppression [Fredrickson,2017].
GAE stabilization is consistent with analytic predictions
Analytical instability condition: 2 < k⊥ρb< 4 [Gorelenkov,2003] – large pitch particles are stabilizing.
Fast-ion distribution from HYM simulations before the outboard beam injection and for case with Nadd/Ntot=5% (n=9,10 are stable). Cyclotron resonance lines are shown for n=9,10,11 GAEs.
t=0.44s
Nadd/Ntot=5%
Nadd/Ntot=0
n=9
n=10
n=11

## Slide 17
Summary
Simulations confirm robust stabilizing mechanism for beam-driven global Alfvén eigenmodes (GAEs) discovered experimentally in NSTX-U, where new beam sources injecting nearly parallel to magnetic field reliably and strongly suppressed unstable GAEs [E. Fredrickson, PRL 2017].
GAEs have been linked to flattening of electron temperature profiles and anomalously low central temperature at high beam power in the NSTX.
Good agreement of simulations with experimental observations:
  - range of toroidal mode numbers, frequencies, and saturation amplitudes of unstable GAEs match the experimentally observed.
A very effective mechanism for stabilizing GAEs - threshold for stabilization of all modes for extra beam is less than 7% of total beam power – demonstrated both experimentally and numerically.
Relevant to ITER, and other fusion devices where super-Alfvénic fast ions might be present.