## Slide 1
The snowflake divertor: a game-changer for magnetic fusion devices ?
V. A. Soukhanovskii
Lawrence Livermore National Laboratory
Workshop on Innovation in Fusion Science and US-Japan Workshop on Compact Torus Plasma August 16-19, 2011 Seattle, Washington
NSTX
Supported by
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
NFRI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep

## Slide 2: Acknowledgements
D. D. Ryutov, T. D. Rognlien, M. V. Umansky (LLNL),
R. E. Bell, D. A. Gates, A. Diallo, S. P. Gerhardt, R. Kaita,
S. M. Kaye, E. Kolemen, B. P. LeBlanc, J. E. Menard, D. Mueller, S. F. Paul, M. Podesta, A. L. Roquemore, F. Scotti (PPPL),
J.-W. Ahn, R. Maingi, A. McLean (ORNL),
D. Battaglia, T. K. Gray (ORISE),
R. Raman (U Washington),
S. A. Sabbagh (Columbia U)
Supported by the U.S. DOE under Contracts
DE-AC52-07NA27344, DE AC02-09CH11466,
DE-AC05-00OR22725, DE-FG02-08ER54989.

## Slide 3: Outline: Experimental results from snowflake divertor experiments in NSTX are very encouraging
Tokamak divertor challenge
Snowflake divertor configuration
Snowflake divertor in NSTX
  Magnetic properties realized in steady-state
  Core H-mode confinement unchanged
  Core impurities reduced
  Divertor heat flux significantly reduced
  Consistent w/ 2D edge transport model
Conclusions and outlook

## Slide 4: Poloidal divertor concept enabled progress in tokamak physics studies in the last 30 years
Divertor challenge
  Steady-state heat flux
      present limit qpeak ≤ 10 MW/m2
      projected to qpeak ≤ 80 MW/m2 for future devices
  Density and impurity control
  Impulsive heat and particle loads
  Compatibility with good core plasma performance
Spherical tokamak: additional challenge - compact divertor
NSTX (Aspect ratio A=1.4-1.5)
  Ip ≤ 1.4 MA, Pin ≤ 7.4 MW (NBI), P / R ~ 10
  qpeak ≤ 15 MW/m2, q|| ≤ 200 MW/m2
  Graphite PFCs with lithium coatings
National Spherical
Torus Experiment

## Slide 5: Various techniques developed for reduction of heat fluxes q|| (divertor SOL) and qpeak (divertor target)
Promising divertor peak heat flux mitigation solutions:
  Divertor geometry
    poloidal flux expansion
    divertor plate tilt
    magnetic balance
  Radiative divertor
Recent ideas to improve standard divertor geometry
  X-divertor (M. Kotschenreuther et. al, IC/P6-43, IAEA FEC 2004)
  Snowflake divertor (D. D. Ryutov, PoP 14, 064502 2007)
  Super-X divertor (M. Kotschenreuther et. al, IC/P4-7, IAEA FEC 2008)

## Slide 6: Snowflake divertor geometry attractive for heat flux mitigation
Snowflake divertor
  Second-order null
      Bp ~ 0 and grad Bp ~ 0 (Cf. first-order null: Bp ~ 0)
  Obtained with existing divertor coils (min. 2)
  Exact snowflake topologically unstable
Predicted geometry properties (cf. standard divertor)
  Larger region with low Bp around X-point: ped. stability
  Larger plasma wetted-area Awet : reduce qdiv
  Larger X-point connection length Lx : reduce qII
  Larger effective divertor volume Vdiv : incr. Prad , PCX
Experiments
  TCV (F. Piras et. al, PRL 105, 155003 (2010))
  NSTX
snowflake-minus
snowflake-plus
Exact
snowflake
divertor
D. D. Ryutov, PoP 14, 064502 2007

## Slide 7: Outline: Experimental studies of snowflake divertor in NSTX
Tokamak divertor challenge
Snowflake divertor configuration
Snowflake divertor in NSTX
  Magnetic properties realized in steady-state
  Core H-mode confinement unchanged
  Core impurities reduced
  Divertor heat flux significantly reduced
  Consistent w/ 2D edge transport model
Conclusions and outlook

## Slide 8: Possible snowflake divertor configurations were modeled with ISOLVER code
ISOLVER - predictive free-boundary axisymmetric Grad-Shafranov equilibrium solver
  Input: normalized profiles (P, Ip), boundary shape
  Match a specified Ip and b
  Output: magnetic coil currents
Standard divertor discharge below:
Bt=0.4 T, Ip=0.8 MA, dbot~0.6, k~2.1
Quantity | Standard divertor | Simulated snowflake
X-point to target parallel length Lx (m) | 5-10 | 10
Poloidal magnetic flux expansion fexp at outer SP | 10-24 | 30-60
Magnetic field angle at outer SP (deg.) | 1.5-5 | ~1-2
Plasma-wetted area Awet (m2) | ≤ 0.4 | 0.95

## Slide 9: Snowflake divertor configurations obtained in NSTX with three existing divertor coils
Standard
Snowflake
Bp
fexp

## Slide 10: Plasma-wetted area and connection length are increased by 50-90 % in NSTX snowflake divertor
These properties observed in first 30-50 % of SOL width
Btot angles in the strike point region: 1-2o, sometimes < 1o
  Concern for hot-spot formation and sputtering from divertor tile edges

## Slide 11: Good H-mode confinement properties and core impurity reduction obtained with snowflake divertor
0.8 MA, 4 MW H-mode
k=2.1, d=0.8
Core Te ~ 0.8-1 keV, Ti ~ 1 keV
bN ~ 4-5
Plasma stored energy ~ 250 kJ
H98(y,2) ~ 1 (from TRANSP)
Core carbon reduction due to
  Type I ELMs
  Edge source reduction
    Divertor sputtering rates reduced due to partial detachment

## Slide 12: Significant reduction of steady-state divertor heat flux observed in snowflake divertor (at PSOL~ 3 MW)
Partial detachment at or after snowflake formation time
  Heat and ion fluxes in the outer strike point region decreased
  Divertor recombination rate and radiated power are increased

## Slide 13: Divertor profiles show low heat flux, broadened C III and C IV radiation zones in the snowflake divertor phase
Heat flux profiles reduced to nearly flat low levels, characteristic of radiative heating
Divertor C III and C IV brightness profiles broaden
High-n Balmer line spectroscopy and CRETIN code modeling confirm outer SP detachment with Te ≤ 1.5 eV,
ne ≤ 5 x 1020 m-3
  Also suggests a reduction of carbon physical and chemical sputtering rates

## Slide 14: Snowflake divertor heat flux consistent with NSTX divertor heat flux scalings
Snowflake divertor (*): PSOL~3-4 MW, fexp~40-60, qpeak~0.5-1.5 MW/m2
  Low detachment threshold
T. K. Gray et. al, EX/D P3-13, IAEA FEC 2010
V. A. Soukhanovskii et. al, PoP 16, 022501 (2009)
0.8 MA
flux expansion
*
*
50
*

## Slide 15: 2D modeling shows a trend toward reduced temperature, heat and particle fluxes in the snowflake divertor
2D multi-fluid code UEDGE
  Fluid (Braginskii) model for ions and electrons
  Fluid for neutrals
  Classical parallel transport, anomalous radial transport
    D = 0.25 m2/s
    ce,i = 0.5 m2/s
  Core interface:
    Te,i = 120 eV
    ne = 4.5 x 1019
  Rrecy = 0.95
  Carbon 3 %

## Slide 16: Outline: Experimental studies of snowflake divertor in NSTX
Tokamak divertor challenge
Snowflake divertor configuration
Snowflake divertor in NSTX
  Magnetic properties realized in steady-state
  Core H-mode confinement unchanged
  Core impurities reduced
  Divertor heat flux significantly reduced
  Consistent w/ 2D edge transport model
Conclusions and outlook

## Slide 17: Divertor heat flux mitigation is key for present and future fusion plasma devices
ST-based Plasma Material Interface (PMI) Science Facility
ST-based Fusion Nuclear Science (FNS) Facility
NSTX
NSTX-U
ST / NSTX goals:
  Study high beta plasmas at reduced collisionality
  Access full non-inductive start-up, ramp-up, sustainment
  Prototype solutions for mitigating high heat & particle flux
NSTX-Upgrade
  Development of divertor solutions to address
    2-3x higher input power
    Projected peak divertor heat fluxes up to 24 MW/m2
    Up to 30 % reduction in Greenwald fraction
    3-5 x longer pulse duration
  Additional divertor coil PF1C
    Flux expansion variation with fixed X-point height

## Slide 18: NSTX studies suggest the snowflake divertor configuration may be a viable divertor solution for present and future tokamaks
Steady-state snowflake (up to 600 ms, many tE’s)
Good H-mode confinement (tE, Te,i(0), bN, H98(y,2) )
Reduced core carbon concentration
Significant reduction in divertor steady-state heat flux
Potential to combine with radiative divertor for increased divertor radiation

## Slide 19: Backup slides

## Slide 20: Open divertor geometry, three existing divertor coils and a good set of diagnostics enable divertor geometry studies in NSTX
Ip = 0.7-1.4 MA
Pin ≤ 7.4 MW (NBI)
ATJ and CFC graphite PFCs
Lithium coatings from lithium evaporators
Three lower divertor coils with currents 1-5, 1-25 kA-turns
Divertor gas injectors (D2, CD4)
Extensive diagnostic set

## Slide 21: Heat flux mitigation is more challenging in compact divertor of spherical torus
NSTX
  Ip = 0.7-1.4 MA, tpulse < 1.5 s, Pin ≤ 7.4 MW (NBI)
  ATJ and CFC graphite PFCs
  P / R ~ 10
  qpk ≤ 15 MW/m2
  q|| ≤ 200 MW/m2
Quantity | NSTX | DIII-D
Aspect ratio | 1.4-1.5 | 2.7
In-out plasma boundary area ratio | 1:3 | 2:3
X-point to target parallel length Lx (m) | 5-10 | 10-20
Poloidal magnetic flux expansion fexp at outer SP | 5-30 | 3-15
Magnetic field angle at outer SP (deg.) | 1-10 | 1-2

## Slide 22: Steady-state asymmetric snowflake-minus configuration has been obtained in FY2010 experiments in NSTX
Snowflake-minus with three coils (w/ reversed PF1B) transformed from a standard medium-d LSN at ~ 500 ms
Snowflake with three coils (w/ reversed PF1B) transformed from a standard high-d LSN at ~ 500 ms

## Slide 23: Preliminary indications that ELM heat flux is effectively dissipated in snowflake divertor
Type I ELMs is a concern for divertor lifetime
  Erosion
  Evaporation, melting
Radiative buffering of ELMs ineffective
In NSTX snowflake divertor
  Type I ELMs 5-12 % DW/W
  Significant dissipation of ELM energy in strike point region
  Reduction in low flux expansion region (at larger Rdiv)
  Need more data to analyze mechanisms and trends
    Heat diffusion over longer conn. length
    Field line mixing in null-point region
    Radiative / collisional dissipation
    Plasma-wetted area effect

## Slide 24: High-n Balmer line emission measurements suggest high divertor recombination rate, low Te and high ne
Te=0.8-1.2 eV, ne=2-7 x 1020 m-3 inferred from modeling
Balmer series spectra modeled with CRETIN; Spectra sensitive to
  Line intensity <-> Recombination rate
  Te <-> Boltzman population distribution
  ne <-> Line broadening due to linear Stark effect from ion and electron microfield

## Slide 25: 1D estimates indicate power and momentum losses are increased in snowflake divertor
1D divertor detachment model by Post
  Electron conduction with non-coronal carbon radiation
  Max q|| that can be radiated as function of connection length for range of fz and ne
  -> Greater fraction of q|| is radiated with increased Lx
Three-body electron-ion recombination rate depends on divertor ion residence time
  Ion recombination time: ion~ 1−10 ms at Te =1.3 eV
  Ion residence time:ion  3-6 ms in standard divertor, x 2 in snowflake
  -> Greater parallel momentum sink

## Slide 26: 2D multi-fluid edge transport code UEDGE is used to study snowflake divertor properties
Fluid (Braginskii) model for ions and electrons
Fluid for neutrals
Classical parallel transport, anomalous radial transport
Core interface:
  Te = 120 eV
  Ti = 120 eV
  ne = 4.5 x 1019
D = 0.25 m2/s
ce,i = 0.5 m2/s
Rrecy = 0.95
Carbon 3 %
Standard Snowflake

## Slide 27: Radiated power is broadly distributed in the outer leg of snowflake divertor
UEDGE model