## Slide 1
ST-FNSF Mission and Performance Dependence on Device Size
J. Menard1
T. Brown1, J. Canik2, L. El-Guebaly3, S. Gerhardt1, A. Jaber3, S. Kaye1,
E. Meier4, L. Mynsberge3, C. Neumeyer1, M. Ono1, R. Raman5, S. Sabbagh6,
V. Soukhanovskii4, P. Titus1, G. Voss7, R. Woolley1, A. Zolfaghari1
17th International Spherical Torus Workshop
University of York
16-19 September 2013
This work supported by the US DOE Contract No. DE-AC02-09CH11466
1Princeton Plasma Physics Laboratory, Princeton, NJ 08543
2Oak Ridge National Laboratory, Oak Ridge, TN, USA
3University of Wisconsin, Madison, WI, USA
4Lawrence Livermore National Laboratory, Livermore, CA, USA
5University of Washington, Seattle, WA, USA
6Columbia University, New York, NY, USA
7Culham Centre for Fusion Energy, Abingdon, Oxfordshire, UK

## Slide 2: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 3: Successful operation of upgraded STs (NSTX-U/MAST-U) could provide basis for design, operation of ST-based FNSF
Fusion Nuclear Science Facility (FNSF) mission:
  Provide continuous fusion neutron source to develop knowledge-base for materials and components, tritium fuel cycle, power extraction
FNSF  CTF would complement ITER path to DEMO
Studying wide range of ST-FNSF configurations to identify advantageous features, incorporate into improved ST design
M. Peng et al., IEEE/NPSS Paper S04A-2 - 24th SOFE Conf. (2011)
M. Abdou et al. Fus. Technol. 29 (1996) 1
Investigating performance vs. device size
  Require: Wneutron ≥ 1 MW/m2, test area ≥ 10 m2, volume ≥ 5 m3

## Slide 4: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 5: ST-FNSF equilibrium inductance, elongation based on values achieved/anticipated in NSTX/NSTX-U
Most probable NSTX thermal pressure peaking ~ 1.7 – 2.2
  If similar in NSTX-U/FNSF  full non-inductive li ~ 0.45 – 0.7 (BS + NBI)
NSTX A=1.7, li = 0.45 – 0.7 plasmas can operate stably at k ~ 2.7 – 2.9
  Expect to improve n=0 control in NSTX-U
  Anticipate k  3 possible in NSTX-U/FNSF

## Slide 6: ST-FNSF free-boundary elongation is reduced with increasing li to match NSTX/NSTX-U trends
ST-FNSF equilibrium k versus li
ST-FNSF plasma boundaries

## Slide 7: ST-FNSF operating point of fGreenwald = 0.8, H98y,2=1.2 chosen to be at/near values anticipated for NSTX-U
H98y,2  1.2 accessed for a range of Greenwald fractions in NSTX
  However, much more research needs to be carried out in NSTX-U to determine if H = 1.2 can be achieved reliably
  Note: H98y,2 ~ 1 would require much higher Paux (~1.8×)
Need to assess feasibility of access to H98y,2 ~ 1.2 at k ~ 2.7-2.9 in NSTX-U

## Slide 8: NSTX disruptivity data informs FNSF operating point with respect to global stability
Increased disruptivity for q* < 2.7
  Significantly increased for q* < 2.5
Lower disruptivity for bN = 4-6 compared to lower bN
  Higher bN increases fBS, broadens J profile, elevates qmin
  Operation above no-wall limit aided by:
    NBI co-rotation
    Close-fitting conducting wall
    Active error-field and RWM control
Strong shaping also important
  S  q95 IP/aBT
  S > 30 provides strongest stabilization
  S > 22-25 good stability
  S < 22 unfavorable

## Slide 9: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 10: Increased device size provides modest increase in stability, but significantly increases T consumption
Scan R = 1m  2.2m (smallest FNSF  pilot plant with Qeng ~ 1)
Fixed average neutron wall loading = 1MW/m2
BT = 3T, A=1.7, k=3, H98 = 1.2, fGreenwald = 0.8
100% non-inductive: fBS = 75-85% + NNBI-CD (ENBI=0.5MeV JT60-SA design)
Larger R lowers bT & bN, increases q*
Comparable/higher bT and bN values already sustained in NSTX
Q = 1  3, Pfusion = 60MW  300MW  5× increase in T consumption

## Slide 11: Beyond neutron wall loading and T breeding, FNSF study is also tracking electrical efficiency Qeng
Note: blanket and auxiliary heating and current-drive efficiency + fusion gain largely determine Qeng
Electricity produced
Electricity consumed
th = thermal conversion efficiency
aux = injected power wall plug efficiency
Q = fusion power / auxiliary power
Mn = neutron energy multiplier
Pn = neutron power from fusion
P = alpha power from fusion
Paux = injected power (heat + CD + control)
Ppump = coolant pumping power
Psub = subsystems power
Pcoils = power lost in coils (Cu)
Pcontrol = power used in plasma or plant control that is not included in Pinj
Pextra = Ppump + Psub + Pcoils + Pcontrol
    FNSF assumptions (from Pilot study):
    Mn = 1.1
    Ppump = 0.03×Pth
    Psub + Pcontrol = 0.04×Pth
    haux = 0.4 (presently unrealistically high)
    hCD = ICDR0ne/PCD = 0.3 × 1020A/Wm2
For more details see J. Menard, et al., Nucl. Fusion 51 (2011) 103014

## Slide 12: High performance scenarios can access increased neutron wall loading and Qeng > 1 at large R
Decrease BT = 3T  2.6T, increase H98 = 1.2  1.5
Fix bN = 6, bT = 35%, q* = 2.5, fGreenwald varies: 0.66 to 0.47
Size scan: Q increases from 3 (R=1m) to 14 (R=2.2m)
Average neutron wall loading increases from 1.8 to 3 MW/m2 (not shown)
Smallest ST for Qeng ~ 1 is R=1.6m  requires very efficient blankets
Note: Outboard PF coils are superconducting
Qeng 
Pelectric produced
Pelectric consumed

## Slide 13: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 14: Cost of T and need to demonstrate self-sufficiency motivate analysis of tritium breeding ratio (TBR)
Example costs of T w/o breeding at $0.1B/kg for R=1  1.6m
  FNS mission: 1MWy/m2 $0.33B  $0.9B
  Component testing: 6MWy/m2 $2B  $5.4B
Implications:
  TBR << 1 likely affordable for FNS mission with R ~ 1m
  Component testing arguably requires TBR approaching 1 for all R
Performed initial analysis of R=1.6m FNSF using conformal and straight blankets, ARIES-ST neutron source profiles:
Neutron Source
63%
32%
5%

## Slide 15: R=1.6m TBR calculations highlight importance of shells, penetrations, and top/bottom blankets
Extended
conformal blanket
TBR = 1.1
Conformal blanket
TBR = 1.046
TBR = 1.02
10 NBI penetrations
NBI penetration at midplane
TBR = 1.07
Stabilizing
shell
+ 3cm thick stabilizing shell
Straight blanket
TBR = 0.8
Extended
straight blanket
TBR = 1.0
TBR = 1.047
Straight blanket
with flat top
Extended conformal + 3cm shell + NBI

## Slide 16: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 17: FNSF center-stack can build upon NSTX-U design, incorporate NSTX stability results
Like NSTX-U, use TF wedge segments (but brazed/pressed-fit together)
  Coolant paths: gun-drilled holes or NSTX-U-like grooves in wedge + welded tube
Bitter-plate divertor PF magnets in ends of TF enable high triangularity
  NSTX data: High d > 0.55 and shaping S  q95IP/aBT > 25 minimizes disruptivity
  Neutronics: MgO insulation can withstand lifetime (6 FPY) radiation dose

## Slide 18: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 19: Divertor PF coil configurations identified to achieve high d, maintain peak divertor heat flux ≤ 10MW/m2
qpeak ~ 10MW/m2
Flux expansion = 15-25
1/sin(qplate) = 2-3
Rstrike = 1.15m, dx ~ 0.55
Snowflake
Field-line angle of incidence at strike-point = 1˚
Conventional
Super-X
qpeak ~ 3MW/m2
Flux expansion = 2
1/sin(qplate) = 15
Rstrike = 2.6m, dx ~ 0.56
qpeak ~ 10MW/m2
Flux expansion = 40-60
1/sin(qplate) = 1-1.5
Rstrike = 1.05m, dx ~ 0.62

## Slide 20: Combined super-X + snowflake divertor configuration has many attractive features
li = 0.40 k = 3.0
li = 0.82 k = 2.55
2nd X-point/snowflake lowers BP, increases line-length
Outboard PF coils shielded by blankets  can be SC
Possible location for T breeding to increase TBR
PF coil design supports wide range of li values (0.4 – 0.8) with fixed strike-point location/region and controllable B-field angle of incidence (0.5-5˚)
Divertor coils in TF coil ends for equilibrium, high d
In-vessel coils not-required for shaping – will be used for vertical control (to be studied in future)
Increased strike-point radius to reduce B and q||, further increase line-length
Strike-point PFCs shielded by blankets
Normally conducting PF coil features:

## Slide 21: Super-X  ~3× reduction in qpeak: 10  3MW/m2 for fixed radiation fraction and angle of incidence

## Slide 22
R=1.6 device configuration with Super-X
S/C PF coils housed in VV upper lid
VV outer shell expanded to add shield material
S/C PF coils housed in VV lower shell structure
S/C PF coils pairs located in common cryostat
Angled DCLL concentric lines to external header
Reshaped TF leads
Vertical maintenance approach
Design features

## Slide 23: Summary
Present STs (NSTX, MAST) providing preliminary physics basis for ST-FNSF performance studies
  Upgraded devices will provide more extensive and definitive basis
Neutron wall loading of 1MW/m2 feasible for range of major radii for b and H98 values at/near values already achieved
  High wall loading and/or pilot-level performance require bN ~ 6 and H98 ~ 1.5 which are at/near maximum values attained in present STs
TBR near 1 possible if top/bottom neutron losses minimized
  TBR ≥ 1 may only be possible for R ≥ 1.6m – under active investigation
Divertor PF coils in ends of TF bundle enable high d, shaping
Conventional, snowflake, super-X divertors investigated, PF coils incorporated to reduce peak heat flux << 10MW/m2
Vertical maintenance strategies for either full and/or toroidally segmented blankets being investigated

## Slide 24: Future work
Physics basis for operating points
  Perform sensitivity study of achievable performance vs. baseline configuration assumptions: A, k, H98y,2, ST vs. tokamak tE scaling
  TRANSP calculations of NBI heating, current drive, neutron production
Performance vs. device size
  Could/should overall machine configuration change at smaller R?
    Example questions: could/should vessel take more load?
  Is there sufficient shielding for divertor PF coils at smaller R?
Tritium breeding ratio calculations
  Extend calculations to smaller R
  Include 3D effects and final machine layout
Maintenance strategies
  Assess space/lift requirements above machine for vertical maintenance

## Slide 25: Backup

## Slide 26: Boundary shape parameters vs. internal inductance
A = 1.81.7 at higher li
High d = 0.5-0.6 maintained
k reduced at higher li
Negative squareness at low li

## Slide 27
Glidcop plates
Insulator
Bitter coil insert for divertor coils in ends of TF

## Slide 28: Neutronics analysis indicates organic insulator for divertor PF coils unacceptable

## Slide 29: MgO insulation appears to have good radiation resistance for divertor PF coils
UW analysis of divertor PFs
  1.8x1012 rad = 1.8x1010 Gy at 6FPY for Pfus = 160MW
Pilot mission for R=1.6m:
  Pfus = 420MW vs. 160MW  2.6x higher  4.7x1010 Gy
  Even for Pilot mission, dose is < limit of 1011 Gy
Limiting factor may be Cu
Need to analyze CS lifetime
Revisit option for multi-turn TF and small OH solenoid