## Slide 1: Field-Aligned SOL Losses of HHFW Power and RF Rectification in the Divertor of NSTX
R. J. Perkins1, J. C. Hosea1, M. A. Jaworski1, J.-W. Ahn2, A Diallo1, R. E. Bell1, N. Bertelli1,
S. Gerhardt1, T. K. Gray2, G. J. Kramer1, B. P. LeBlanc1, A. McLean3, C. K. Phillips1,
M. Podestà1, L. Roquemore1, S. Sabbagh4, G. Taylor1 and J. R. Wilson1
1 Princeton Plasma Physics Laboratory
2 Oak Ridge National Laboratory
3 Lawrence Livermore National Laboratory
4 Columbia University
November 5, 2015

## Slide 2
Significant loss of HHFW power to the divertor
along SOL field lines; possibly due to RF rectification
Up to 60% of coupled power is not reaching the core
Hot spirals form on upper & lower divertor during RF
  Heat flux up to 2 MW/m2 (for 1.8 MW coupled PRF)
RF rectification could be converting HHFW power to heat flux
  Requires RF fields in divertor region
  Could be general to ICRF systems
Divertor diagnostics respond strongly to RF when under spiral

## Slide 3: HHFW strongly affects floating potential when probe is under spiral
Probe P4 floating potential (red plot) responds strongly to RF
Probe P2 has much weaker response (black plot)
RF-induced effects are localized to spiral
Similarly, tile currents increase under spiral

## Slide 4: RF rectification is an phenomena due to non-linear IV characteristic of probe/surface
IV characteristic of probe (or divertor tile) is nonlinear
  Exponential for Maxwellian distribution

## Slide 5: RF rectification is an phenomena due to non-linear IV characteristic of probe/surface
IV characteristic of probe (or divertor tile) is nonlinear
  Exponential for Maxwellian distribution
Adding an oscillating potential produces non-zero average of collected current
VRF

## Slide 6: RF increases electron current New floating potential depressed
Equation for current collected at bias V

## Slide 7: RF increases electron current New floating potential depressed
Equation for current collected at bias V
Add RF potential and average over an RF cycle

## Slide 8: RF increases electron current New floating potential depressed
Equation for current collected at bias V
Add RF potential and average over an RF cycle
New floating potential VflRF
A. Boschi and F. Magistrelli, Nuovo Cimento 29 487 (1963 )

## Slide 9: Langmuir probe IV characteristics altered by RF spiral
Probe 4 (under spiral, red curve) characteristic altered by HHFW
Could be a ~ 30 V shift in floating potential due to RF rectification
  However, could be ~ 16 eV of plasma heating
Divertor turbulence prevents accurate determination

## Slide 10: Averaging sweeps smooths turbulence, allows better fitting
Assume RF rectification
  Fit both characteristics with exponentials with same Te and ne
Departure from exponential at higher bias expected for oblique magnetic fields
Change in floating potential: 24 V
Estimated VRF: 44 V

## Slide 11: Midplane Te measurements support RF rectification hypothesis
Thomson Scattering provides Te profile at midplane
Assuming RF rectification: Te = 13.5 eV,
  Decent agreement with TS
Assuming plasma heating: Te = 31 eV
  Much larger than TS measurements
R. J. Perkins et al., Phys. Plasma 22, 042506 (2015)

## Slide 12: Heat flux to surface consists of ion and electron contributions
Ion energy flux from sheath voltage drop
Ion thermal flux
Electron
thermal flux
P. Stangeby “The plasma boundary of magnetic fusion devices,” Ch. 2

## Slide 13: Adding RF increases heat flux (at same bias) due to increased electron current
Ion energy flux from sheath voltage drop
Ion thermal flux
Electron
thermal flux
Add RF potential and average over an RF cycle

## Slide 14: Adding RF increases heat flux (at same bias) due to increased electron current
Electron current without RF
Electron current with RF

## Slide 15: Adding RF increases heat flux (at same bias) due to increased electron current
Add RF potential and average over an RF cycle
VRF ~ 44 V  ΔQRF = 0.1 MW/m2

## Slide 16
Comparison of QRF prediction by RF rectification to heat flux measured by IR camera is currently difficult
Heat flux profiles obtained at Bay I
Langmuir probes located at Bay B
  150o of toroidal separation
Strong toroidal variations in spiral intensity

## Slide 17: Rough extrapolations suggest RF-rectification prediction is plausible, but better data is needed
δQ = QRF – QnoRF reveals different spiral passes across Bay I
Probe radius closest to second spiral pass
Subtract off estimate of plasma exhaust from second peak
  Estimate 0.3 MW/m2 from heat flux profile
  Larger than prediction from VRF but does not account for spiral variation
Heat Flux Profile at Bay I
Probe Radius
R. J. Perkins et al., Phys. Plasma 22, 042506 (2015)

## Slide 18: Improved diagnostics on NSTX-U will allow for definitive comparisons
New radial array of divertor Langmuir probes
  Located at Bay I where most intense part of spiral is anticipated to fall
  Probe electronics will detect RF (30 MHz) component of signal
    Direct measurement of VRF
ORNL is providing a wide-angle IR view of divertor
  Obtain heat flux measurement at probe location
Will perform a dedicated power scan
  Determine scaling of measured heat flux and VRF
  Determine if RF-rectification predictions of heat flux are accurate

## Slide 19: Conclusions
SOL losses of HHFW power are significant for NSTX
  Possibly a fast-wave propagation effect that is more apparent in ST geometry
RF rectification is a likely explanation for changes to floating potential and currents
RF rectification can potentially explain the spiral heat flux
  Potentially the long sought mechanism converting HHFW power to heat flux to outer divertor
  Current predictions are in the right range, but better data is needed
Experiments and diagnostics upgrades on NSTX-U will allow for more a definitive comparison