## Slide 1: Studies of NSTX L and H-mode Plasmas with Global Gyrokinetic Simulation
Y. Ren1
W. Wang1, W. Guttenfelder1, S.M. Kaye1, S. Ethier1, J. Ruiz-Ruiz2, R.E. Bell1, B.P. LeBlanc1, E. Mazzucato1, D.R. Smith3, C.W. Domier4, H. Yuh5 and the NSTX-U Team
1. PPPL 2. MIT 3. UW-Madison 4. UC-Davis 5. Nova Photonics
18th International Spherical Torus Workshop
and 2015 US-Japan Workshop on ST Plasmas
Princeton, NJ, USA
November 3rd - 6th, 2015

## Slide 2: Why are Global Effects Important?
Global effects are considered to be important for STs
  Local assumption of flux tube simulations based on ρ*->0
  Large ρ* of STs due to weaker toroidal field compared to conventional tokamaks (ρ* ~ 0.01 for NSTX)
  Global effects, e.g. profile variation, requiring global GK codes
Study of global effects are important for achieving predictive capability for future STs
  Need to validate first principle model for developing reduced transport model with global effects
Serious validation efforts, applying global GK codes to ST plasmas, are still lacking

## Slide 3: Outline
GYROKINETIC TOKAMAK SIMULATION (GTS) code
Global GTS simulations of NSTX L and H-mode plasmas
  NSTX RF-heated L-mode plasmas
    Fast response of electron-scale turbulence to RF cessation
  NSTX H-mode plasmas
    Density gradient stabilization of electron-scale turbulence

## Slide 4: GTS - a Global Gyrokinetic Code with Robust Capability to Simulate Turbulence & Transport for Tokamak Experiments
PIC code solving modern GK equation in conservative form
New, improved weight scheme ensuring phase space incompressibility
Full geometry, global simulation (without local ballooning approximation)
  Real space field solvers with field-line-following mesh
  Retains all toroidal modes allowed by resolution and full channels of nonlinear energy couplings
  Enable to treat modes with low-n, with finite k||, (e.g., shear flow mode)
Fully kinetic electrons (both trapped and untrapped electron dynamics)
Linearized Fokker-Plank operator with particle, momentum and energy conservation for i-i and e-e collisions; Lorentz operator for e-i collisions
Include neoclassical physics self-consistently in turbulence simulations
  Significant impact on some important transport & confinement issues (bootstrap current, poloidal flow, GAMs and particle transport, etc.)
Applied to wide experiments for various physics studies:
NSTX/U, DIII-D, C-MOD, KSTAR and ASDEX-U

## Slide 5
NSTX RF-heated L-mode plasmas with fast response of electron-scale turbulence to RF cessation

## Slide 6
Drop in turbulence frequency spectral power at the time of RF cessation
  The drop happens in 0.5 to 1 ms
Electron heat flux decreases by about a factor of 2 after the RF cessation
Measured Turbulence Frequency Spectral Power Shows a Significant Drop Following the RF Cessation
A sudden drop in spectral power
Shot=140301
RF-heated L-mode plasma with
BT =5.5 kG and Ip=300 kA
Ren et al., accepted by PoP

## Slide 7: What Causes the Sudden Drop of Electron-scale Turbulence?
Time of the RF cessation
Equilibrium quantities not expected to change significantly on the time scale on which the turbulence changes (0.5-1 ms)
  Energy confinement time~ 10 ms
<15% variation in equilibrium quantities in the high-k measurement region
High-k measurement region

## Slide 8: Changes in Linear Growth Rate Cannot Explain the Observed Significant Drop in High-k Turbulence
Ion scale modes are ITG/TEM hybrid
  Growth rate similar before and after the RF cessation
Stability Analysis was performed with the GS2 code (Kotschenreuther et al., 1995)
ExB shearing rate
Ion direction
Electron direction
After the RF cessation
R=135 cm

## Slide 9: Changes in Linear Growth Rate Cannot Explain the Observed Significant Drop in High-k Turbulence
Ion scale modes are ITG/TEM hybrid
  Growth rate similar before and after the RF cessation
ETG mode maximum growth rates show small increase from t=465 to 482 ms
  Inconsistent with the drop in the measure high-k spectral power
Stability Analysis was performed with the GS2 code (Kotschenreuther et al., 1995)
ExB shearing rate
Ion direction
Electron direction
After the RF cessation

## Slide 10: Are Global Effects Able to Explain the Observation?
Global effects, e.g. profile variation, may be important
  Turbulence could spread from one region to another
GTS simulations are carried out with experimental equilibria
  Linear local GS2 simulations help determine the radial domain for GTS simulations
  Focus on ion-scale turbulence, since ExB shear is weak
High-k measurement region R=133~137 cm

## Slide 11: Robust Ion-scale Turbulence is Seen
Strong ion-scale turbulence generated
  ExB shear is weak without strong NBI
Turbulence propagates in the electron diamagnetic direction
t=465 ms

## Slide 12: Electron Energy Flux from GTS is Significantly Less than Experimental Value with RF Heating
Ion energy flux is over-predicted
Experimental values from TRANSP+TORIC analysis
Electron energy flux
Ion energy flux

## Slide 13: Similar Energy Fluxes from GTS are Seen before and after the RF cessation
Consistent with observed small change in equilibrium profiles
Electron energy flux matches experimental value after the RF cessation but not before
Ion energy flux is over-predicted for both cases
Electron energy flux
Ion energy flux

## Slide 14: Gradient-driven Gyrokinetic Models have Difficulty Explaining Experimental Observations
Turbulence decreases on 0.5 -1 ms time scale; About a factor of 2 decrease in Âe after the RF cessation
  Equilibrium profiles not expected to vary significantly on 0.5 – 1 ms time scale (much smaller than confinement time ~ 10 ms)
  <15% variation in equilibrium quantities in the high-k measurement region are found before and right after the RF cessation (over 17 ms)
Local and global gyrokinetic simulations using experimental profiles are unable to explain observed change in turbulence and electron thermal transport
Nonlocal flux-driven mechanism may be important (S.-I Itoh and K. Itoh, Sci. Rep. 2012)

## Slide 15
NSTX H-mode plasmas with
density gradient stabilization of electron-scale turbulence

## Slide 16
Current Ramp-down in NSTX H-mode Plasma Leads to Core Density Gradient Increase
Shot=141767
NBI-heated H-mode plasma with
BT =5.5 kG
Ruiz-Ruiz et al., submitted to PoP

## Slide 17
ETG turbulence suppressed by large density gradient
  See Ruiz-Ruiz’s poster P1-10
Is ion-scale turbulence driving thermal transport?
  Here, we focus on ion-scale GTS simulations and thermal transport
Current Ramp-down in NSTX H-mode Plasma Leads to Core Density Gradient Increase
Shot=141767
NBI-heated H-mode plasma with
BT =5.5 kG
Ruiz-Ruiz et al., submitted to PoP

## Slide 18
GTS Simulation Domains are Chosen to Have Significant Gradients
t= 332 ms
t= 565 ms
Both electron temperature and density gradients are significantly larger at t=565 ms than at t=332 ms

## Slide 19: Robust Ion-scale Turbulence is Seen at t=332 ms
Strong ion-scale turbulence generated
  ExB shear is turned on from the beginning of the simulation
Turbulence propagates in the ion diamagnetic direction, due to toroidal rotation
t=332 ms

## Slide 20: Ion Energy Flux from GTS is in Agreement with Experiment at t=332 ms
Ion energy flux from ion-scale turbulence contributes significantly at R>135 cm
Neoclassical ion thermal transport is important further in the core of the plasma
  Neoclassical ion thermal transport from NCLASS
t=332 ms

## Slide 21: Electron Thermal Transport is Significantly Under-predicted by GTS at t=332 ms
Electron energy flux from GTS is only significant at R>135 cm
  Much smaller than experimental electron thermal transport
Contribution from ETG and electromagnetic effects may be important
t=332 ms

## Slide 22: Ion-scale Turbulence is Robustly Suppressed in GTS Simulation for t=565 ms
Turbulence is suppressed after ExB shear is turned on at t~600
No turbulence growth if ExB shear is turned on at the beginning of the simulation
t=565 ms, R=134.5 cm

## Slide 23: Ion Energy Flux from GTS is Still in Agreement with Experiment at t=565 ms
Neoclassical ion thermal transport is comparable to experimental ion thermal transport level
  Neoclassical ion thermal transport from NCLASS
ETG is significantly suppressed by density gradient (see poster P1-10)
  Electromagnetic effects may be important
t=565 ms

## Slide 24: Summary
We have started to make serious efforts to validate global gyrokinetic simulations with NSTX experiments
Global gyrokinetic simulations with GTS have helped identify the possible importance of nonlocal flux-driven mechanics in electron thermal transport in NSTX RF-heated L-mode plasmas
Global ion-scale gyrokinetic simulations with GTS for a NSTX NBI-heated H-mode plasma showed nice agreement with experiment in ion thermal transport but not in electron thermal transport

## Slide 25
Backup slides

## Slide 26: Fast Response of Electron-scale Turbulence to RF Cessation was Observed in a Set of NSTX L-mode Plasmas
Shot=140301
RF-heated L-mode plasma with
BT =5.5 kG
Time range of interest:
around the RF cessation at t=479.6 ms

## Slide 27: High-k Microwave Scattering System is Used to Measure High-k Turbulence
Probe beam
280 GHz microwave is launched as the probe beam.
Coherent scattering by plasma density fluctuations occurs when the three-wave coupling condition is satisfied:
Bragg condition determines kp:
kp=2kisin(θs/2)
The scattered light has a frequency of:
ωs=ωp+ωi
with ωs and ωi >> ωp
The scattering system characteristics are:
  Frequency bandwidth: 5 MHz
  Heterodyne receiver: Wave propagation direction resolved
  Measurement: kr spectrum
  Wavenumber resolution: 0.7 cm-1 (2/a with a ≈ 3 cm)
  Wavenumber range (kr): 5-30 cm-1 (~5-30 )
  Radial resolution: ±2 cm
  Tangential resolution: 5-15 cm
  Radial range: R=106 – 144 cm
  Minimal detectable density fluctuation:
Scattered light
Spherical mirror
kp
ks
2a
Probe beam
ki
ks
kp
=
+
θs
ki
D.R. Smith, PhD thesis, 2009

## Slide 28: Turbulence Wavenumber Spectra Show Significant Reduction in Smaller Wavenumbers, k┴ρs <9-10
Up to a factor of 7 drop in wavenumber spectral power right after the RF cessation
At the RF cessation
Right after the RF cessation
Time of the RF cessation, t=479.6 ms

## Slide 29: Turbulence Wavenumber Spectral Power is Correlated with Electron Thermal Diffusivity
About a factor of 2 decrease in electron thermal diffusivity after the RF cessation
  Correlated with the decrease in turbulence wavenumber spectral power
High-k measurement region
After the RF cessation
After the RF cessation
From TRANSP analysis with TORIC

## Slide 30: Te and Ti Profile Changes are Small across the RF Cessation
One Thomson measurement point is at t=482 ms, right after the drop of high-k turbulence
Ti profile is measured by CHERS
High-k measurement region r/a~ 0.57-0.63
Time of the RF cessation

## Slide 31
A Time Delay between the Drop in Spectral Power and RF Cessation Indicates a Causal Relationship
Time of the RF cessation, t=479.6 ms
Spectral power decreases within 0.5 - 1 ms and the delay time is about 1-2 ms
Turbulence propagates in electron diamagnetic direction

## Slide 32: ITG/TEM and ETG Modes are Robustly Unstable
Te and Ti gradients are scanned with ¯’ fixed
The ion-scale modes are driven by both electron and ion temperature gradients
  a/LTe,exp=3.6
  a/LTi,exp= 2.83
ETG modes critical a/LTe is determined to be 2.1 (a/LTe,exp=3.6) from Te gradient scan
t=465 ms, r/a=0.6
max

## Slide 33: Are Global Effects Able to Explain the Observation?
Global effects, e.g. profile variation, may be important
  Global simulations with experimental profiles before and after the RF cessation
GTS simulations are carried out with experimental equilibria
  Linear local GS2 simulations help determine the radial domain for GTS simulations
  Focus on ion-scale turbulence, since ExB shear is weak

## Slide 34: Are Global Effects Able to Explain the Observation?
Global effects, e.g. profile variation, may be important
  Turbulence can spread from one region to another
Reasonable linear growth phase seen in the GTS simulation
  ExB shear is turned on from the beginning
Linear phase

## Slide 35: Similar Turbulence Intensity is Found before and after the RF Cessation
  Before RF cessation (t=465 ms)
After the RF cessation (t=482 ms)
R=134 cm

## Slide 36: Energy Fluxes from Local Nonlinear Ion-scale GYRO Simulations are Significantly Higher
Local nonlinear ion-scale GYRO simulations were carried out for R=135 cm
  Te and Ti gradients varied by 25% to assess profile stiffness
    Weak stiffness is seen
Electron energy flux
Ion energy flux

## Slide 37: Electron Energy Fluxes from Local Nonlinear ETG GYRO Simulations are Small before and after the RF Cessation
Electron energy fluxes from ETG turbulence have large variation vs radial location
Electron energy flux

## Slide 38: Electron Energy Fluxes from Local Nonlinear ETG GYRO Simulations are Smaller than Experiment
Electron energy fluxes from ETG turbulence have large variation vs radial location
  Energy flux from 0.02 MW to 0.04 MW with a 25% increase in Te gradient
Electron energy flux

## Slide 39: Simulation Quantities are Averaged Over a Quasi-steady Period
Energy flux drops after significant interaction with boundary in the simulation
t=332 ms