## Slide 1: Profile measurements of ion temperature and toroidal rotation velocity from optical emission spectroscopy in VEST
Yoosung Kim, Yue-Jiang Shi, Jae-young Jang, Kyoung-Jae Chung, and Y.S. Hwang
2017.09.19
19th International Spherical Torus Workshop

## Slide 2
Introduction
Experiment setup
Calibration
Spectral inversion and Phantom test
Preliminary result in Ohmic plasma
Summary
Contents

## Slide 3
Introduction
Characteristics
  Without neutral beam
  Wide measurement range for VEST  intermediate to edge region cf. 10 eV < Te < 200 eV in VEST
Difficulties
  Line integrated spectra  inversion process to obtain local properties
Te 30 eV
H. P. Summers, Monthly Notices of the Royal Astronomical Society 158.3 (1972)
Passive emission spectroscopy in visible range
  CIII – 464.74 nm
  OII – 464.90 nm
Spectral shape  rotation and temperature
  Line shift : rotation
  Line broadening : ion temperature
Z*
Te 20 eV
Fractional abundance of carbon and oxygen at ne=1018m-3
Carbon
Oxygen

## Slide 4
Experiment Setup
Collecting part
  Canon 50 mm f/1.8
  Fiber array : 35(radial) x 4(vertical)
Spectrometer
  Transmission grating (HDG : Kaiser Optical Systems, inc.)
  Spatial channel : 7 channel
  Dispersion : 0.013 nm/pixel
Detector : EMCCD (Andor iXonUltra888)
  Temporal resolution : 2 ms with binning (1.4 ms exposure + 0.6 ms readout)
Slit
35 (radial)
4개
Edge (R=0.65 m)
Core (R=0.38 m)
140 channel
7 channel
HDG
105 mm
f/14
CCD
85 mm
f/1.4

## Slide 5
Spatial & Intensity Calibration
Image size = 20-25 mm
Spatial calibration
  Check the specific measurement point
  Two spatial point measurement
Intensity calibration
  Intensity calibration with wavelength
  Spatial channel to channel sensitivity
Spatial calibration
Intensity calibration with integrating sphere
Position 1
Position 2
R=377-653 mm
At 465 nm

## Slide 6
Wavelength calibration
Cubic spline
Calibration with Xe discharge lamp
  Wavelength calibration
  Instrument broadening
Wavelength calibration
  Cubic polynomial fitting
= A0+A1+ A2+A3
: pixel number
Ai : fitting coefficient (i=0, 1, 2, 3)
Ch1
Ch2
Ch3
Ch4
Ch5
Ch6
Ch7
Image curvature
 Short f and large f/#
Horizontal pixel  wavelength
Wavelength(nm) | Transition
462.4276 | 
467.1226 | 
469.0972 | 
469.7021 | 
473.4152 | 
Wavelength(nm) | Transition
462.4276 | 
467.1226 | 
469.0972 | 
469.7021 | 
473.4152 | 
462.43 nm
467.12 nm
469.10 nm
469.70 nm
473.42 nm
Kramida, A., Ralchenko, Yu., Reader, J., and NIST ASD Team (2015). NIST Atomic Spectra Database (ver. 5.3), [Online].
Xe lamp image
After calibration

## Slide 7
Necessity of Spectral Inversion
To obtain the local properties
Need to inversion process
Spectral inversion
Intensity (emissivity)
Profile shape (broadening & shift)
Plasma
boundary
Each spatial point,
Different rotation velocity and ion temperature  different wavelength shift and broadening
Line integrated spectrum!!
Line of sight
Position 1
Position 2
Position 3
Measurement

## Slide 8
Inversion Method
Intensity inversion
Rotation inversion
Temperature inversion
: Length of an intersection b/w sightline i and emitting zone j
L55
Instrument broadening
R.E. Bell, Rev.Sci.Instrum 68 1273 (1997)
I. Condrea et al., Phys. Plasmas 7 3641 (2000)
Y.J. Shi et al., Rev.Sci.Instrum 83 10D717 (2012)
Where
: Line integrated emissivity
: Local emissivity
Where
: Line integrated velocity
: Local velocity
Where
: Temperature from line integrated spectrum
: Local temperature
Line integrated parameter
, ,
Local property
, ,

## Slide 9
Phantom Test
Phantom test is conducted to confirm the uncertainties of spectral inversion
Phantom profile (emissivity, )
Hollow, Center-peaked, flat emission profile
Parabolic profile as function of R
Estimate the line-integrated spectra
Assume toroidal symmetry
7 line of sight (Experiment setup)
Conduct spectral inversion
Obtain local properties from line-integrated phantom spectra
Noise sensitivity test (10% error)
Comparison
Compare inverted profile with phantom profile
ch2
ch1
ch3
ch4
ch5
ch6
ch7
Line integrated spectra
Collecting optics
7 channel measurement
 Smooth cubic spline interpolation and extrapolation

## Slide 10
Phantom Test Result
Case1. Hollow emission profile
Case2. Flat emission profile
Case3. Center-peaked profile

## Slide 11
Line-integrated spectra in Ohmic discharge
ch7
ch1
#17474 305 ms
R=0.38 m
R=0.45 m
R=0.50 m
R=0.54 m
R=0.58 m
R=0.62 m
R=0.65 m
Strong passive emission is located in near 465 nm
  CIII triplet (3s3S-3p3P) : 464.742, 465.025, 465.15 nm
  OII (3s4P-3p4D) – 464.91 nm
Comparison of two passive emission CIII and OII
Interference line
For the boundary condition
  Emissivity=0 at R=0.76 m (Limiter position)

## Slide 12
Emissivity profile of CIII and OII
Smoothed cubic spline interpolation is used in line-integrated emissivity
Emission peak location
  CIII & OII emission peak is in near 0.6 m
  CIII peak is more shifted to the core than OII peak
Measurement range for vT, Ti
  R > ~ 0.55 m
Profile shape
  Line integrated emissivity : Flat
  Local emissivity : Hollow

## Slide 13
vT, Ti profile in VEST Ohmic discharge
Instrument temperature For C, Tinst~38 eV For O, Tinst~51 eV
Co current
Counter current
Toroidal rotation and ion temperature of CIII and OII is measured by passive emission
Toroidal rotation in counter current direction is observed in the edge region (R>0.6 m  r/a >0.65)
Ion temperature is about 25-40 eV in the intermediate range in VEST Ohmic discharge

## Slide 14
Summary
Toroidal rotation and ion temperature profile is measured from the passive emission with OII, CIII lines.
7 channel spectroscopy system is installed and calibrated to measure the toroidal rotation and ion temperature profile.
Spectral inversion is conducted to extract the toroidal rotation and ion temperature as well as local emissivity.
Toroidal rotation is in counter current direction observed in the edge region in the VEST Ohmic plasma.
Ion temperature in the intermediate region is about 25-40 eV.

## Slide 15
Future work
Hardware improvement
  Image curvature correction  curved entrance slit (R.E.Bell RSI 2004)
  Increase the number of line of sight (especially edge region)
  Preparation of active beam diagnostic  CES/BES combined system
Data analysis
  Uncertainty analysis for emissivity, rotation, and temperature
Experiment
  Passive emission spectroscopy with high charge state emission (candidates : OV-650.0 nm, BV 494.4 nm, CVI-529.1 nm)
  Rotation and ion temperature profile change in heating NB injection
CVI Te>~30 eV
OV : Te <~150 eV

## Slide 16
Thank you

## Slide 17
Back up – Photo emission coefficient
Ne=1018m-3
Local emissivity
Photo emission coefficient (from CR model)
H. P. Summers, Monthly Notices of the Royal Astronomical Society 158.3 (1972)
OPEN-ADAS http://open.adas.ac.uk
Electron impact excitation

## Slide 18
Back up – Error propagation