## Slide 1
Y.S. Hwang, and VEST team
September 19, 2017
CARFRE and CATS
Dept. of Nuclear Engineering
Seoul National University
Overview of Versatile Experiment Spherical Torus (VEST)
ISTW 2017, Sept. 18-22 2017, Seoul National Univ., Seoul, Korea

## Slide 2: Outline
Versatile Experiment Spherical Torus (VEST)
  Device and discharge status
Start-up experiments
  Low loop voltage start-up using trapped particle configuration
  EC/EBW heating for pre-ionization
  Solenoid-free start-up from outboard with outside PF coils
Studies for Advanced Tokamak
  Research directions for high-beta and high-bootstrap STs
  Preparation of long-pulse ohmic discharges
  Preparation for heating and current drive systems
  Preparation of profile diagnostics
Long-term Research Plans
Summary

## Slide 3: VEST device and Machine status
VEST device and
Machine status

## Slide 4: VEST (Versatile Experiment Spherical Torus)
 | Present | Future
Toroidal B Field [T] | 0.1 | 0.3
Major Radius [m] | 0.45 | 0.4
Minor Radius [m] | 0.33 | 0.3
Aspect Ratio | >1.36 | >1.33
Plasma Current [kA] | ~100 kA | 300
Elongation | ~1.6 | ~2
Safety factor, qa | ~6 | ~5
Specifications
Objectives
Basic research on a compact, high- ST (Spherical Torus)
with elongated chamber in partial solenoid configuration
Study on innovative start-up, non-inductive H&CD, high  and innovative divertor concept, etc

## Slide 5: History of VEST Discharges
#2946: First plasma (Jan. 2013)
#10508: Hydrogen glow discharge cleaning (Nov. 2014) Ip of ~70 kA with duration of ~10 ms
#14945: Boronization with He GDC (Mar. 2016) Maximum Ip of ~100 kA
#16942: Long pulse with coil power supply upgrade (May. 2017)

## Slide 6: VEST Discharge Status : 100kA with Boronization (#14945)
EC-assisted OH discharge
  Plasma current 100 kA
  Hydrogen plasma with Boroination
  Tungsten & Graphite (inboard) limiter
Equilibrium parameters
  R=0.45m/a=0.33m (A=1.36)
  Elongation: 1.6 – 2.5
  Edge safety factor: ~ 7
Limited discharge length
  Fast ramp-up
   Require large Bv in the beginning
  Wall eddy current
   Limited time response of Bv

## Slide 7: VEST Discharge Status : 100kA with Boronization (#14945)
Kinetic plasma parameters from magnetics
  Spitzer temperature*: < 300 eV (average)
  Diamagnetic flux  Stored energy (perpendicular) < 1.2 kJ
  Estimated plasma density: < 3×1019 m-3 (average)
*Zσ = 3 / trapped particle fraction 90%
  # Greenwald density limit: ~3×1019 m-3
Diamagnetic flux measurement
  TF current filtering method
  Error bar 1 mWb
Parameters
  Poloidal beta ~ 0.6 (paramagnetic)
  Stored energy < 1.2 kJ
  Ohmic heating < 400 kW

## Slide 8: Start-up Experiments
Start-up Experiments

## Slide 9: Start-up experiments Trapped Particle Configuration (TPC)
Efficient and robust tokamak start-up demonstrated at VEST and KSTAR
Mirror like magnetic field configuration
  Enhanced particle confinement
  Inherently stable decay index structure
Y. An et al., Nucl. Fusion 57 016001 (2017)
Jeongwon Lee et al 2017 Nucl. Fusion in press https://doi.org/10.1088/1741-4326/aa8511
Notes: These devices are not typical tokamaks. Field null formation is used almost all tokamaks, not only above mentioned tokamaks.

## Slide 10: Start-up Experiment in VEST Closed Flux Surface Formation for Successful Start-up in TPC
Successful ohmic start-up at low loop voltage in TPC depends on vertical field strength
Smaller resistivity initiate higher initial current to form sufficient size of closed flux surface
Threshold vertical field strength for successful inductive start-up
H.Y. Lee

## Slide 11: Start-up Experiment in VEST Solenoid-free Start-up from Outboard with Outer Poloidal Field Coils
No closed flux surfaces with up to 16 kW due to their high resistivity of > 1.0 E-5.
In the case of the resistivity of less than 1.0 E-5, the closed flux surface may be formed.
Once current column is formed, inward moving current can grow with decreasing external inductance
To reach target resistivity, higher ECH power of ~30kW may be needed to have sufficient density and temperature in the pre-ionization phase.
H.Y. Lee

## Slide 12: Preparation for Advanced Tokamak Studies
Studies for Advanced Tokamak

## Slide 13: Preparation for Advanced Tokamak Studies Scopes of Advanced Tokamak Studies in VEST
Fusion reactor requires
high beta (or Q) and high bootstrap current
Simultaneously
Alpha heating dominant (high Q)
 Centrally peaked pressure profile
Confinement and Stability?
High power neutral beam heating
High Bootstrap current fraction (high fb)
 Hollow current density profile (low li)
Current density profile control
Bootstrap/EBW/LHFW
Profile diagnostics

## Slide 14: Preparation for Advanced Tokamak Studies Simulations for the VEST Advanced Tokamak Scenario
C.Y. Lee
The integrated modeling system constructed.
ASTRA+TGLF and NEO for heat & particle transport: Valid even in low aspect ratio tokamak
The steady state solution of beam discharges showing that , can be achieved with considering beam heating & fueling simultaneously.
, ,

## Slide 15: Preparation for Advanced Tokamak Studies Diagnostics, Heating and Current Drive Systems in VEST
Neutral Beam Injection System
with ~500kW at 15keV
from KAERI
Thomson Scattering
with Nd:YAG laser
from SNU/NFRI/JNU/SogangU
Low Hybrid Fast Wave H/CD
with ~10kW at 500MHz
from KAERI/KAPRA/KWU
ECH
Electron Cyclotron/Bernstein Wave H/CD
with ~30kW at 2.45GHz
from SNU/KAPRA
Interferometry
with 94GHz, multi-channel
from SNU/UNIST
Magnetics and Spectroscopy
Interferometer
Heating and Current Drive Systems
Profile Diagnostic Systems

## Slide 16: High power central heating High Power NBI System : Dual Beam to Single Beam
NBI beam loss calculation with NUBEAM code
Too large orbit loss for counter-injection
 Dual beam to single beam
Large shine through loss even for co-injection
 Require high plasma density
Beam at 20keV

## Slide 17: High power central heating High Power NBI System : System Design
3.1 m
Max Power
: 32.72 MW/m2
2.6 m
Max Power
: 35.16 MW/m2
1.8 m
Max Power
: 36.16 MW/m2
1.4 m
Max Power
: 32.77 MW/m2
0.7m
Max Power
: 28.12 MW/m2
Defl. angle, # of slits
- 2 degree 29
- 1 degree 3
0 degree 13
1 degree 3
2 degree 29
Focusing beam profile calculation
Beam power density at beamline
Calculated by BTR code
Slit beam focusing
3D beam line design
Chart: Distance from Beam Exit [ m ]
| 0.2 | 0.4 | 0.7 | 1 | 1.4 | 1.8 | 2.2000000000000002 | 2.6 | 3
2016-10-22 | 22.82 | 22.77 | 23.11 | 24.93 | 27.68 | 31.14 | 33.56 | 34.47 | 32.74
2016-09-23 | 22.84 | 22.73 | 23.28 | 25.6 | 28.2 | 31.92 | 34.26 | 34.75 | 32.76
2016-08-24 | 22.83 | 22.71 | 23.81 | 26.24 | 28.72 | 32.68 | 34.74 | 34.73 | 32.68
2016-07-25 | 22.84 | 22.7 | 24.7 | 26.89 | 29.46 | 33.5 | 35.1 | 35.14 | 32.62
2016-06-26 | 22.87 | 22.71 | 25.74 | 27.67 | 30.16 | 34.25 | 35.96 | 35.34 | 32.75
2016-05-27 | 22.84 | 23.13 | 26.72 | 28.5 | 30.86 | 34.98 | 35.72 | 35.31 | 32.61
2016-04-28 | 22.82 | 24.62 | 27.43 | 28.77 | 31.9 | 35.31 | 36.47 | 35.48 | 32.62
2016-03-29 | 22.84 | 26.23 | 28.12 | 28.82 | 32.77 | 36.16 | 36.34 | 35.16 | 32.72

## Slide 18: High power central heating High Power NBI System : Ion Source Test, installation
Neutral beam injector
  Co-directional
  Design power: 500 kW
Ion source test completed
  750 kW at 15 keV
  300 kW at 10 keV
Two-step beam energy PS
B.K. Jung

## Slide 19: High power central heating Reduced Beam Loss with Magnetic Well Formation
(NUBEAM, Optimized injection condition for VEST)
 | well shape 1 | well shape 1 | well shape 2 | well shape 2
Beam energy () | 20 keV | 25 keV | 20 keV | 25 keV
() |  |  |  | 
( |  |  |  | 
Injection angle () |  |  |  | 
Shine through () |  |  |  | 
Orbit loss |  |  |  | 
Total beam loss |  |  |  | 
 | well shape 1 | well shape 1 | well shape 2 | well shape 2
 | 20 keV | 25 keV | 20 keV | 25 keV
Orbit loss |  |  |  | 
Total beam loss |  |  |  | 
Well shape 1
Well shape 2
S.K. Kim et al., Nucl. Fusion 56 106006 (2016)

## Slide 20: Current density profile control Core Heating and Current Drive with LHFW
For high density plasma in fusion reactor
  Slow wave branch of LHW
  → Absorbed at the edge region
  Fast wave branch of LHW
  → Possible absorption at the core region
Proof of principle for current drive scheme
by fast wave branch of LHW in VEST
S.H. Kim (KAERI)

## Slide 21
Ey
In collaboration with KAERI and Kwangwoon Univ.
Current density profile control LHFW H/CD Coupling simulation and experiment
LH Fast Wave
  Good core accessibility
  Efficient plasma coupling of combline antenna
Hardware
  UHF Klystron, Combline antenna
  N|| = 3-5 / 470~510 MHz
S.H. Kim/J.G. Jo
Notes: These devices are not typical tokamaks. Field null formation is used almost all tokamaks, not only above mentioned tokamaks.

## Slide 22: Current density profile control EBW Heating and Current Drive with XB Mode Conversion
GENRAY, CQL3D, mode conversion codes are used
Perpendicular, LFS, X-mode injection
  Short distance between R(X) cut-off and UHR
  High XB mode conversion efficiency with low n||
  Good central heating and current drive expected
► Core heating and current drive with XB mode conversion
Absorption near EC fundamental resonance
EBW
propagation
ECR
S.H. Kim

## Slide 23
EBW heating (6kW cw+10kW pulse at 402ms) on Ohmic plasmas
Current density profile control EBW Heating with XB Mode Conversion
H.Y. Lee
Boronization (impurity removal) and higher plasma current (higher electron temperature)
No change along the electron density profile with additional MW – no collisional damping
Electron temperature rises two times near 3rd harmonics ECR resonance : the first resonance position after EBW mode conversion

## Slide 24: Preparation for Advanced Tokamak Studies VEST Diagnostic Systems
Diagnostic Method |  | Purpose | Remarks
Magnetic Diagnostics | Rogowski Coil | Plasma current & eddy current | 3 out-vessel & in-vessel coils
 | Pick-up Coil & Flux Loop | Bz, Br & Loop voltage, flux | 56 pick-up coils 9 loops
 | Magnetic Probe Array | Bz, Br measurement inside plasma | Movable single array
Probes | Electrostatic Probe | Radial profile of Te, ne | 2 Triple Probes Mach probe
Optical Diagnostics | Fast CCD camera | Visible Image | 20kHz
 | Hα monitoring | Hα | Hα filter+ Photodiode
 | Impurity monitoring | O & C lines | Spectrometer
 | Interferometry | Line averaged ne | 94GHz, multi-channel
 | Reflectometry | Radial profile of ne | Edge density profile
 | EBE radiometer | Core, edge Te | BX mode conversion
 | Charge Exchange Spectroscopy | Rotation and Ti | DNB
 | Thomson Scattering | Te, ne profile | Nd:YAG laser

## Slide 25: Profile diagnostics Movable Magnetic Probe Array System
Equilibrium reconstruction with internal probe data
Direct derivation of JT(R)
  w/o vertical displacement
  Plasma degradation ~ 10%
J.H. Yang et al., Rev. Sci. Instrum. 83 10D721 (2012)
J.H. Yang et al., Rev. Sci. Instrum. 85 11D809 (2014)

## Slide 26: Profile diagnostics 94 GHz Multi-channel Interferometer
Microwave system with heterodyne interferometer
3.2 GHz IF (avoid EC noise)
  EC 2.45 GHz
Single chord  multi-chord
In collaboration with UNIST and KNU
J.I. Wang

## Slide 27: Profile diagnostics Thomson Scattering System
Measurement target
  ne: > 5×1018 m-3
  Te: 10-500 eV
  core plasma
Laser: 0.65 J/pulse, 1064 nm
Collection solid angle: ~50 msr
Scattering length: ~5 mm
Filter polychromator: 4 channels
Spectral Response
of the polychromator
Expected signal level [V]
(calibration: Rayleigh scattering)
In collaboration with
Schematic of the TS system
Y.G. Kim/D.Y. Kim

## Slide 28: Profile diagnostics Visible optical spectroscopy
Slit
35 (radial)
4개
Edge (R=0.65 m)
Core (R=0.38 m)
140 channel
7 channel
HDG
105 mm
f/14
CCD
85 mm
f/1.4
Measurement quantities : , ,
Passive emission spectroscopy
  CIII line (3s3S-3p3P) – 464.74 nm
  Line-integrated spectra  spectral inversion
Specification
  Detection range : 0.38 m< R <0.65 m
  Spatial resolution : 20-22 mm
  Temporal resolution : 2 ms/frame
CES/BES combined system is in preparation
Y.S. Kim

## Slide 29: Summary
VEST has achieved successful ohmic operation with plasma currents of up to ~100 kA, elongation of ~ 2 and safety factor of ~6 with efficient ECH pre-ionization.
Efficient start-up method is developed with TPC(Trapped particle configuration) and EBW heating.
  Enhanced pre-ionization and stable equilibrium field with TPC improves start-up with low loop voltage, low ECH power, and wider pressure window.
  Solenoid-free start-up may be developed by utilizing efficient pre-ionization at outboard with EBW heating.
  EBW heating with direct XB mode conversion from LFS launching by generating over-dense plasma.
Preparation for the study of Advanced Tokamak is progressing
  VEST Advanced Tokamak scenario is simulated with transport codes.
  High power (>500 kW) NBI system has been developed and installed.
  EBW/LHFW heating and current drive experiments are under preparation.
  Profile diagnostics are under preparation
Reactor-relevant fusion research by developing both AT scenario and innovative divertor concept will be continued.

## Slide 30: Thank you for your attention !

## Slide 31: Start-up experiments in VEST Pre-ionization with Low-Field-Side Launch EC/EBW Heating
LFS perpendicular injection of ECW 10 kW
  Over-dense plasma (X-wave tunneling)
  Parametric decay with mode conversion
  High density with collisional heating near UHR
J.G. Jo et al., Phys. Plasmas 24 012103 (2017)
TPC configuration for Pre-ionization
  Higher density plasma with broad density profile
  Different density profile with Bt strength
Low TF (Bo ~ 0.5 kG)
High TF (Bo ~ 1 kG)
Notes: These devices are not typical tokamaks. Field null formation is used almost all tokamaks, not only above mentioned tokamaks.

## Slide 32: Preparation for Advanced Tokamak Studies Discharge Improvement with Boronization
Boronization during Helium Glow discharge cleaning
  Carborane (C2B10H12) is used for non-toxic boronization
  Water concentration recovery slowed down (RGA)
Oxygen atom line emission (777.0 nm) reduced by 3 fold
  High density expected: More prefill gas (Hα line emission)
Diaphragm valve
Top flange (CF 6 inch)
Caborane oven (baked 50°C)
Helium flow (MFC 2.0 sccm)
With great help from Dr. S.H. Hong (NFRI)

## Slide 33
Start-up Experiment in VEST
Robust and Reliable TPC Start-up Applied to KSTAR Successfully
Feasibility study of TPC in KSTAR
  Even though low mirror ratio than ST, achieving efficient start-up with TPC
  2nd harmonic delay of 20 ms and ECH plasma density of 4x1018 m-2
  Ip formation with low Et less than 0.2 V/m
Earlier plasma colomn formation than field null
Jeongwon Lee et al 2017 Nucl. Fusion in press https://doi.org/10.1088/1741-4326/aa8511

## Slide 34: DC Helicity Injection DC Helicity Injection Start-up
Lower Gun Location
R = 0.25 m
Z = - 0.804 m
Magnetic Field Structure
Stacking ratio, G = 7 ~ 8
Multiplication, M = ~ 16
The Electron Gun for DC Helicity Injection
High current electron beam based on arc discharge w/ washer stacks
Low impurity
A toroidal current of up to ~20 kA has been generated by the electron gun
Increased multiplication factor confirmed as current streams reconnect
Very dynamic states of current sheet observed
401 ms
402 ms
403 ms
400.4 ms
The electron gun
J.Y. Park

## Slide 35: Future Research Plans
Long-term Research Plans
Reactor-relevant Advance Tokamak research
  AT scenario for high beta and steady-state operation
  Innovative divertor to handle long-pulse high-performance operation
  Energetic particle transport …

## Slide 36: Preparation for Advanced Tokamak Studies Simulations for the VEST Advanced Tokamak Scenario
0-D system code analysis
Low toroidal field 0.1 T
High beta N 7
Plasma current 80 kA
Non-inductive 100%
Bootstrap fraction 80%
Required NB power 500 kW
1-D transport simulation
NBI heating with NUBEAM code
  (Density and equilibriums are given.)
1D integrated modelling with ASTRA code with TGLF module
  (Density profile is given.)
L-mode (edge at r=0.9) and H-mode cases are compared
C.Y. Lee

## Slide 37: Preparation for Advanced Tokamak Studies Simulations for the VEST Advanced Tokamak Scenario
Total power loss is calculated using NUBEAM simulations in various conditions ()
Based on the result, R = 35 cm equilibrium is chosen for better NBI power absorption.
15 degree of the injection angle is chosen considering both power loss and engineering issue in VEST and its heating power profiles are calculated.
 | R = 35 cm | R = 40 cm
 | 27% | 33%
 | 43% | 70%
 | R = 35 cm | R = 40 cm
 | 27% | 33%
 | 43% | 70%
Total loss (
at 15 injection
Heating power (
C.Y. Lee