## Slide 1: Next-Step Low-Aspect-Ratio Tokamaks Using High-Temperature Superconductors and Liquid Metal Plasma Facing Components*
J. Menard, T. Brown, M. Jaworski,
R. Maingi, R. Majeski, Y. Zhai
International Spherical Torus Workshop - 2017
Seoul National University, Seoul, South Korea
September 19-22, 2017
*Work Supported by U.S.D.O.E. Contract No. DE-AC02-09CH11466

## Slide 2: Possible missions for next-steps
Integrate high-performance, steady-state, exhaust
  Divertor test-tokamak - DTT
Fusion-relevant neutron wall loading
  Gn ~ 1-2MW/m2, fluence: ≥ 6MW-yr/m2
Tritium self-sufficiency
  Tritium breeding ratio TBR ≥ 1
Electrical self-sufficiency
  Qeng = Pelectric / Pconsumed ~ 1
Large net electricity generation
  Qeng >> 1, Pelectric = 0.5-1 GWe
This talk will discuss PPPL-led studies of how low-A “spherical” tokamaks could fulfill these missions

## Slide 3: Recent design studies show ST potentially attractive as Fusion Nuclear Science Facility (FNSF) and Pilot Plant
FNSF with copper TF coils
A=1.7, R0 = 1.7m, x = 2.7, BT=3T
Fluence = 6MWy/m2, TBR ~ 1
FNSF / Pilot Plant with HTS TF coils
A=2, R0 = 3m, x = 2.5, BT = 4T
6MWy/m2, TBR ~ 1, Qeng ~ 1
FNSF: Provide neutron fluence for material/component R&D (+ T self-sufficiency?)
Pilot Plant: Electrical self-sufficiency: Qeng = Pelec / Pconsumed ≥ 1 (+ FNSF mission?)
Designs integrate ST higher k , bN and advanced divertors (+ HTS TF for Pilot Plant)
J.E. Menard, et al., Nucl. Fusion 56 (2016) 106023

## Slide 4: Possible missions for next-steps
Integrate high-performance, steady-state, exhaust
  Divertor test-tokamak - DTT
Fusion-relevant neutron wall loading
  Gn ~ 1-2MW/m2, fluence: ≥ 6MW-yr/m2
Tritium self-sufficiency
  Tritium breeding ratio TBR ≥ 1
Electrical self-sufficiency
  Qeng = Pelectric / Pconsumed ~ 1
Large net electricity generation
  Qeng >> 1, Pelectric = 0.5-1 GWe
2015-2016:
HTS TF
R = 3m
A=1.6-4
“Pilot Plant”

## Slide 5
A=2, R0 = 3m HTS-TF FNSF / Pilot Plant
BT = 4T, IP = 12.5MA
k = 2.5, d = 0.55
bN = 4.2, bT = 9%
H98 = 1.8, HPetty-08 = 1.3
fgw = 0.80, fBS = 0.76
Startup IP (OH) ~ 2MA
JWP = 70MA/m2
BT-max = 17.5T
No joints in TF
Vertical maintenance
Pfusion = 520 MW
PNBI = 50 MW, ENBI = 0.5MeV
QDT = 10.4
Qeng = 1.35
Pnet = 73 MW
Wn = 1.3 MW/m2
Peak n-flux = 2.4 MW/m2
Peak n-fluence = 7 MWy/m2
Cryostat volume ~ 1/3 of ITER

## Slide 6
Base-design Pilot uses long-leg / deep-V slot divertor
PF coils outside TF
Increase strike-point radius ~2× to reduce q|| and peak heat flux
Divertor PFCs in region of reduced neutron flux
Narrow divertor aperture for increased TBR
More space for breeding at top/bottom of device

## Slide 7: Long-leg / Super-X aids heat flux reduction
A=2 HTS TF FNSF/Pilot
lq ~ 1mm, assume S ≈ lq (closed divertor)
(T. Eich NF 2013)
(Partial) detachment likely reduces peak q by further factor of 2-7

## Slide 8: Another option: Liquid metal (LM) divertor w/ shorter outer leg Pdiv = 9  21MW/m2 for Rstrike = 4.2m  2.5m
Long-leg / Super-X
Shorter leg LM divertor
Geometry also compatible with
“vapor box” concepts (Ono / Goldston)

## Slide 9: Why (flowing) liquid metals in divertor?
Replenish divertor material lost to steady-state, transient erosion (ELMs, control excursions)
  Potentially more resilient to disruptions (?)
First-wall erosion materials will very likely end up in divertor  need active dust removal
Dissipate higher heat fluxes than is possible with solids  widens divertor design space
Lithium H/D/T pumping may increase energy confinement  important for compact Pilots
  ELMs suppressed by Li in NSTX, EAST

## Slide 10: HTS ST-FNSF design with Li flow on divertor and inboard surfaces
Double null liquid metal divertor system
Li flows from upper divertor down the inboard wall, exiting just after the lower inboard divertor.
Separate Li cooling of lower divertor
Thickness = 5-10 mm, flow speed ~5-10 m/s (see Dick Majeski for more details)

## Slide 11: Basic liquid metal divertor concept
Plates (in blue) provide
J x B pump electrodes
Li flow direction
J x B pumping to high-field side nozzle
Heat exchanger in reservoir
Li supply

## Slide 12: Concepts with LM flow only in divertors
Space for inboard blanket piping

## Slide 13: Benefits of shorter-leg LM high-heat-flux divertor:
Significantly reduce outboard PF coil current
  Reduced PF size, force, structure
Eliminate separate upper cryo-stat (for PF5U)
1
2
3
4
5
6
7
8
Li wall pumping could help increase H-factor

## Slide 14: Comparison of long vs. shorter-leg divertor Pilots:
3m HTS ST-FNSF with
long-leg/Super-X divertor
3m HTS ST-FNSF with Liquid Metal divertor
Simplify vertical maintenance
Reduce outboard PF currents  can use LTS PF coils

## Slide 15: Possible missions for next-steps
Integrate high-performance, steady-state, exhaust
  Divertor test-tokamak (DTT) emphasizing liquid metals
Fusion-relevant neutron wall loading
  Gn ~ 1-2MW/m2, fluence: ≥ 6MW-yr/m2
Tritium self-sufficiency
  Tritium breeding ratio TBR ≥ 1
Electrical self-sufficiency
  Qeng = Pelectric / Pconsumed ~ 1
Large net electricity generation
  Qeng >> 1, Pelectric = 0.5-1 GWe

## Slide 16: Beginning to assess smaller dedicated low-A HTS tokamak for liquid metal divertor development
TF: REBCO, likely CORC
CS coil insert possibilities:
    YBCO pancakes (needs insulation scheme for flux-swing)
    Bi-2212 solenoids
Physics bifurcation
Concept for vessel + TF coil cases
R = 1.2m, A = 2.3, k = 2.1
BT = 4-5T, PNBI = 35MW
H98 = 0.8-1.6, bN = 2-4, full non-inductive
IP = 1.5-3.4MA, BP = 0.35-0.8T
Vary Twall = 20-500ºC, P/S ~ 1MW/m2
lq 1-2mm, access q  20MW/m2

## Slide 17: Summary
Developed self-consistent low-A FNSFs / Pilot Plants
  Long-leg and/or liquid metal (LM) divertors, T self-sufficient, only ex-vessel TF and PF coils, vertical maintenance
Compact Pilot Plants achievable by combining improved stability of low-A + advanced magnets
  Optimal aspect ratio will be informed by upcoming NSTX-U and MAST-U results and REBCO TF magnet R&D
Liquid metal divertors for high heat flux could simplify cryostat, reduce coil currents/forces
  Higher confinement from liquid Li would also be beneficial
Exploring lower-A toroidal configurations to test liquid-metal divertors under DEMO-relevant conditions

## Slide 18
Backup slides

## Slide 19: HTS cables using REBCO tapes achieving high winding pack current density at high field
10 mm
10 mm
6 mm
7 kA CORC (4.2K, 19 T) cable
Base cable: 50 tapes YBCO Tapes with 38 mm substrate (Van Der Laan, HTS4Fusion, 2015)
Higher Jcable HTS cable concepts under development:
Base Conductor
He Gas Cooled
8kA,
JWP ~ 160MA/m2
7 mm
SS conductor jacket for strength
7 mm
Copper
Conductor on Round Core Cables (CORC)
JWP ~ 70MA/m2 19T

## Slide 20: What is optimal A for HTS FNSF / Pilot Plant?
Pfus / V ~ e(bN k BT )4 at fixed bootstrap fraction
bN and k increase at lower aspect ratio
BT decreases at lower A – depends strongly on:
  Inboard shielding, HTS allowable field and current density
Approach:
Fix plasma major radius and heating power (50MW)
  R0 = 3m – smallest size for Qeng > 1 and high fluence
Apply magnet & plasma constraints (see backup)
  HTS strain: 0.3%, bN: n=1 no-wall, k: 0.95×limit, fGW = 0.8
Vary aspect ratio from A = 1.6 to 4
Vary HTS current density, peak field
  Also scan inboard shielding thickness (not shown)
Compute QDT, Qeng, and required H98 (unconstrained)

## Slide 21: High TF winding-pack current density required to access highest BT at lower A
12T: ITER-like TF coil limit
(Nb3Sn, 11.8T)
19T: Present CORC HTS limit
JWP [MA/m2]
Chart: Max BT at TF coil [T]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
160 | 18.3214 | 18.7622 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19
80 | 16.433 | 17.1602 | 17.7576 | 18.1294 | 18.4409 | 18.7044 | 18.9935 | 18.9996 | 18.9999 | 19 | 19 | 19
40 | 11.266 | 13.8912 | 16.0357 | 16.4935 | 16.8683 | 17.1797 | 17.6277 | 18.277 | 18.8214 | 19 | 19 | 19
30 | 8.4495 | 10.4184 | 12.1777 | 13.3057 | 14.277 | 15.1135 | 16.3799 | 17.2829 | 17.8659 | 18.3192 | 18.9755 | 19
20 | 5.633 | 6.9456 | 8.1185 | 8.8704 | 9.518 | 10.0757 | 10.9199 | 12.2231 | 13.3857 | 14.3299 | 15.7496 | 16.7393
20 (12T) | 5.633 | 6.9456 | 8.1185 | 8.8704 | 9.518 | 10.0757 | 10.9199 | 12 | 12 | 12 | 12 | 12
Chart: BT at geometric center [T]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
160 | 2.1314 | 2.8724 | 3.5298 | 3.927 | 4.2687 | 4.5627 | 5.0076 | 5.6937 | 6.3054 | 6.802 | 7.5484 | 8.0687
70 | 1.9117 | 2.6272 | 3.299 | 3.7471 | 4.1431 | 4.4917 | 5.0059 | 5.6935 | 6.3054 | 6.802 | 7.5484 | 8.0687
40 | 1.3106 | 2.1267 | 2.9791 | 3.4089 | 3.7897 | 4.1256 | 4.6459 | 5.477 | 6.2462 | 6.802 | 7.5484 | 8.0687
30 | 0.98296 | 1.595 | 2.2623 | 2.7501 | 3.2076 | 3.6294 | 4.317 | 5.1791 | 5.929 | 6.5583 | 7.5387 | 8.0687
20 | 0.6553 | 1.0634 | 1.5082 | 1.8334 | 2.1384 | 2.4196 | 2.878 | 3.6629 | 4.4422 | 5.1301 | 6.2571 | 7.1086
20 | 0.6553 | 1.0634 | 1.5082 | 1.8334 | 2.1384 | 2.4196 | 2.878 | 3.596 | 3.9824 | 4.296 | 4.7674 | 5.096
Coil structure sized to maintain ≤ 0.3% strain on winding pack for all cases shown here

## Slide 22: High current density HTS cable motivates consideration of low-A tokamak pilot plants
ITER-like TF constraints:
  JWP=20MA/m2, Bmax ≤ 12T
  Pfusion ≤ 130MW
  Pnet < -90MW
JWP ~ 30MA/m2, Bmax ≤ 19T
  Pfusion ~ 400MW
  Small Pnet at A=2.2-3.5
JWP ≥ 70MA/m2,Bmax ≤ 19T
  Pfusion ~500-600MW
  Pnet = 80-100MW at A=1.9-2.3
Chart: Pfusion [MW]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
0.3 | 246.0028 | 432.7379 | 583.3162 | 607.5533 | 606.7621 | 589.7419 | 571.4392 | 537.6294 | 500.4852 | 453.345 | 358.4489 | 278.381
0.4 | 174.8919 | 332.4576 | 482.5278 | 533.6621 | 558.8914 | 564.7819 | 570.7858 | 537.5829 | 500.4765 | 453.3423 | 358.4484 | 278.3808
0.5 | 51.1869 | 172.9943 | 358.5903 | 407.2527 | 434.1847 | 444.1135 | 462.48 | 481.3769 | 487.0152 | 453.345 | 358.4489 | 278.381
0.6 | 19.8048 | 68.1159 | 153.2279 | 212.6847 | 264.1296 | 304.1657 | 373.389 | 409.141 | 418.1467 | 406.719 | 357.0235 | 278.381
0.7 | 5.343 | 17.8599 | 40.6874 | 57.346 | 72.1979 | 83.986 | 104.837 | 139.6142 | 171.0165 | 189.3741 | 197.5059 | 184.0685
20 | 5.343 | 17.8599 | 40.6874 | 57.346 | 72.1979 | 83.986 | 104.837 | 131.5217 | 119.8912 | 105.974 | 79.8077 | 59.401
Chart: Pnet [MWe]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
0.3 | -42.5779 | 36.6802 | 100.5919 | 110.8791 | 110.5433 | 103.3192 | 95.5508 | 81.2005 | 65.435 | 45.4267 | 5.1489 | -28.8353
0.4 | -72.7603 | -5.8829 | 57.8131 | 79.5166 | 90.225 | 92.7252 | 95.2754 | 81.181 | 65.4314 | 45.4256 | 5.1487 | -28.8353
0.5 | -125.2658 | -73.5657 | 5.2089 | 25.8632 | 37.2943 | 41.5085 | 49.304 | 57.3246 | 59.7178 | 45.4267 | 5.1489 | -28.8353
0.6 | -138.5857 | -118.0805 | -81.9554 | -56.7195 | -34.8841 | -17.8912 | 11.4901 | 26.6647 | 30.4871 | 25.6367 | 4.5439 | -28.8353
0.7 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -87.7336 | -74.4052 | -66.6135 | -63.162 | -68.8654
20 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -91.1684 | -96.1049 | -102.0119 | -113.118 | -121.7794
JWP [MA/m2]
A ~ 2 attractive at high JWP
(12T)

## Slide 23: A ≥ 2 pilot plant scenarios have elevated H > 1, fBS ~ 80%, IP = 6-12MA
JWP [MA/m2]

## Slide 24: Breeding calculations for A=2, R=3 Pilot Plant
Outboard TBR ~ 0.92
Thin inboard blanket (10 cm) provides TBR = 1.04
Step 1- Infinite media of LiPb
Step 2- LiPb confined to OB FW/blanket
Step 3- Assembly gaps added
Step 4- Homogeneous mixture of blanket in upper and lower ends of OB blanket
Step 5- FW material added
Step 6- Side, back, and front walls added
Step 7- Cooling channels added
Step 8- SiC FCI added
Step 9- Stabilizing shells added
Step 10- MTM only inserted (TBR relative to Step #9)
Step 11- 4 TBMs only inserted (TBR relative to Step #9)
Step 12- 4 NBIs only inserted (TBR relative to Step #9)
Step 13- all MTM, 4 TBMs, and 4 NBIs inserted
Step 14 – include inboard breeding blanket
1.04

## Slide 25: Comparison of low-A FNSF / Pilot Plants

## Slide 26: Comparison of low-A FNSF / Pilot Plants

## Slide 27
Backup slides
HTS TF FNSF / Pilot

## Slide 28: Plasma constraints
Fix plasma major radius at R0 = 3m
  Chosen to be large enough to allow space for HTS neutron shield and access Qeng > 1 for range of A
Inboard plasma / FW gap = 4cm
Use e-dependent k(e), bN (e) (see next slide)
Greenwald fraction = 0.8
q* not constrained
  q* is better e-invariant than q95 for current limit
  Want to operate with q* > 3 to reduce disruptivity
0.5 MeV NNBI for heating/CD – fixed PNBI = 50MW
H98y2 adjusted to achieve full non-inductive CD

## Slide 29: Aspect ratio dependence of limits: k(e), bN(e)
NSTX data at low-A
  Also NSTX-U/ST-FNSF modelling
DIII-D, ARIES-AT for higher A
  k  1.9 for A  
Profile-optimized no-wall stability limit at fBS ≈ 50%
  Menard PoP 2004
bN  3.1 for A  
bT  A-1/2 (1+k2) bN2 / fBS
 Pfus  e [k(e) bN(e) BT(e)]4
e = A-1
Pilot study uses 0.95×k value shown here:

## Slide 30: Engineering constraints
Magnet constraints
  Maximum stress in TF magnet structure = 0.66 GPa
  HTS tape/cable strain limit 0.3% (equivalent to 0.4 GPa)
  Winding pack current density (CORC 2015) 70 MA/m2
  OH at small R  higher solenoid flux swing for higher A
Shielding / blankets
  HTS fluence limit: 3.5x1022 n/m2
  Shield:10x n-shielding factor per 15-16cm WC for HTS TF
  Include inboard & outboard breeder thickness for TBR ~ 1
    “Effective shield thickness” includes shield + DCLL blanket
Electrical system efficiency assumptions:
  30% wall plug efficiency for H&CD - typical of NNBI
  ≥ 45% thermal conversion efficiency - typical of DCLL
    Also include pumping, controls, other sub-systems
    See Pilot Plant NF 2011 paper for more details

## Slide 31: Simplified TF magnet design equations
From J. Schwartz, Journal of Fusion Energy, Vol. 11, No. 1, 1992

## Slide 32
A=2, R0 = 3m device TF inboard leg showing
allocated space for case and winding
0.167 m2 winding area
Current per coil: 6 MA
Winding Cd: 35.9 MA/m2

## Slide 33
CORC Conductor – Achieved now
10 mm
10 mm
6 mm
857 turns @ 7 kA
(848 turns shown; a few additional turns required)
Base Conductor – Helium Gas Cooled
7 mm
SS conductor jacket for strength
7 mm
Copper
750 turns @ 8 kA
(750 turns shown)

## Slide 34: HTS performance vs. field and fast neutron fluence

## Slide 35: Neutronics analysis for HTS TF shielding

## Slide 36: Breeding blanket thickness model

## Slide 37: HTS TF lifetime is very strong function of inboard shielding thickness
Inboard shield + blanket equivalent to 60cm WC 
3FPY  6-7MWy/m2  fulfill FNSF requirement

## Slide 38: 3-D Neutronics Model
Simple CAD Model outlining components (from T. Brown):
  10 cm IB modules
  20 cm OB modules
R-Z neutron source
IB shield and VV optimization and composition by UW.
OB blanket internals and composition by UW
Detailed CAD of blanket by UW
UW DAGMC code couples CAD to 3D MCNP neutronics code.

## Slide 39: CAD Geometry of OB Blanket with Ports
Detailed Blanket Internals
Stabilizing
Shells
MTM
TBM
4 NBIs

## Slide 40: Lower-A maximizes TF magnet utilization
0.3m
0.4m
0.5m
0.6m
0.7m
Eff. shield
thickness:

## Slide 41: A = 2.5-3 maximizes blanket utilization

## Slide 42: Need inboard breeding for TBR > 1 at A=2
10cm IB shield sufficient for TBR > 1.04
Outboard TBR ~ 0.92
TBR
Required TBR = 1.04
(4% margin)