## Slide 1: Secondary ELM filaments in MAST
S. Elmore, J Harrison, A Kirk, N Walkden and the MAST Team

## Slide 2: Introduction
Secondary ELMs occur following the first 50-200µs and have been seen on tokamaks such as NSTX[1]
Not routinely seen on MAST but were identified during high time resolution ELM ion temperature measurements
The hypothesis is that they occur when sufficient interaction with PFCs results in neutrals
Unlike in MAST, MAST-U will have more in-vessel structures for the closed divertor
  interaction with PFCs is almost guaranteed during ELMs
Close fitting structures around X-point location
[1] Maqueda R et al 2009 JNM

## Slide 3: Secondary Filaments on MAST
20kHz Ti measurements made with a retarding field energy analyser probe (RFEA)
  temperature evolution within ELM [2]
Ti measurements made at ΔRtgt ~ 15cm
Significant Ti 20eV seen in a region where no inter-ELM signal measured
Filaments occur beyond time for primary filaments stopped
  Blue: t-tELM = 300-600µs
  Green: t-tELM = 600-900µs
[2] Elmore S et al 2016 PPCF

## Slide 4: When do secondary filaments occur in MAST?
Comparisons between LSN and DND
  LSN operates closer to PFC
  Strong plasma interaction with the in-vessel poloidal coil
Propose that secondary filaments occurred due to the interaction with PFC
  May be what effects the edge transport causing secondary instability [1]
Investigate similar ELMs in these specific scenarios to give plasma-wall gap ‘scan’
[1] Maqueda R et al 2009 JNM

## Slide 5: Diagnostics for identifying secondary filaments
Analysis using target arrays of Langmuir probes
  Use LP measurements of Isat to identify presence of filaments
  Use database of similar ELMs to build up Isat target profiles using probe array
  Analyse time windows of 300µs after tELM

## Slide 6: Diagnostics for identifying secondary filaments
Visible camera with fast frame rate operated at 90-100kHz
  Midplane view of plasma allows identification of filaments beyond ψN = 1
  Fast frame rate ~10µs can resolve filaments
  Statistical analysis on 300µs time windows to match LP analysis

## Slide 7: LSN Type I ELM filaments
LSN type I ELMy H-mode
  Same scenario as RFEA measurements (IP = 600kA)
Isat measured along divertor target
Filaments clearly seen at target consistent with RFEA
  ΔRtgt > 15cm
Isat filaments signals high at large radius until t-tELM ~ 1ms
At t-tELM = 900-1200µs still large Isat fluctuations up to ΔRtgt = 10cm

## Slide 8: LSN Type I ELM filaments
Inter-ELM is equivalent to t-tELM > 1.5ms
LSN type I ELMy H-mode
  Same scenario as RFEA measurements (IP = 600kA)
Isat measured along divertor target
Filaments clearly seen at target consistent with RFEA
  ΔRtgt > 15cm
Isat filaments signals high at large radius until t-tELM ~ 1ms
At t-tELM = 900-1200µs still large Isat fluctuations up to ΔRtgt = 10cm

## Slide 9: DND Type I ELM filaments
Inter-ELM is equivalent to t-tELM > 1.5ms
DND type I ELMy H-mode
  Magnetic equilibrium means LCFS is further from PFCs
Secondary filaments do exist after DND type I ELMs
Isat due to filaments reduces across target profile
  t-tELM = 900 – 1200µs:
    Isat is close to level of inter-ELM SOL
Camera data will be used to show if any interaction with PFCs in this case

## Slide 10: DND Type I ELM filaments
Inter-ELM is equivalent to t-tELM > 1.5ms
DND type I ELMy H-mode
  Magnetic equilibrium means LCFS is further from PFCs
Secondary filaments do exist after DND type I ELMs
Isat due to filaments reduces across target profile
  t-tELM = 900 – 1200µs:
    Isat is close to level of inter-ELM SOL
Camera data will be used to show if any interaction with PFCs in this case

## Slide 11: DND Small Type I ELM filaments
Same DND plasma scenario
  ΔW smaller than previous set of type I ELMs
Same t-tELM windows as previous analysis
  Isat signal almost overlays inter-ELM measurements
During t-tELM = 300-600µs higher Isat indicative of small filamentary behaviour
  low compared to previously studied secondary filaments
Inter-ELM is equivalent to t-tELM > 1.5ms

## Slide 12: Fast camera data of ELMs
LSN Type I ELM
DND Small Type I ELM
DND Type I ELM
Notes: Interaction
Turbulent filaments
How long they continue

## Slide 13: LSN Type I ELMs
Average intensity of all frames in time window following set of ELMs occurring at tELM
Strong plasma interaction seen in all three time windows on the lower P3 coil
LCFS
Mean

## Slide 14: LSN Type I ELMs
Strong plasma interaction seen in all three time windows on the lower P3 coil can
Filamentary behaviour visible beyond ψN = 1 continuing for each time window analysed
Filaments extend out to beyond ψN = 1.4
ψN = 1.4
Standard deviation

## Slide 15: LSN Type I ELMs
ψN = 1.4
Standard deviation
Filamentary behaviour visible beyond ψN = 1 continuing for each time window analysed
Filaments extend out to beyond ψN = 1.4

## Slide 16: DND Type I ELMs
Average intensity of all frames in time window following set of ELMs occurring at tELM
Plasma interaction seen in first time window on the upper and lower P3 coil
Likely that the presence of secondary filaments in this magnetic configuration is due to plasma interaction with PFCs
LCFS
Mean

## Slide 17: DND Type I ELMs
Plasma interaction on the PFCs visible in first time window
Filamentary behaviour visible beyond ψN = 1
Filamentary indications reduce with increasing t-tELM
Filaments extend out to beyond ψN = 1.4
ψN = 1.4
Standard deviation

## Slide 18: DND Type I ELMs
Filamentary indications reduce with increasing t-tELM
Filaments extend out to beyond ψN = 1.4
Standard deviation

## Slide 19: Small Type I ELMs in DND
Plasma interaction on the PFCs not visible
Little or no filamentary behaviour can be seen
Small filamentary activity close to ψN = 1 only visible up to t-tELM = 600µs
LCFS
Standard deviation
Mean

## Slide 20: Implications for MAST-U
With MAST-U in-vessel structures for closed divertor expect all ELMs to interact with PFCs
Power from secondary filaments not significant issue compared to primary ELM filaments but some consequences
Increased turbulence for prolonged periods following an ELM
  effect H-mode pedestal recovery
In detached H-mode plasmas expect strike point to reattach due to primary ELM
  prolonged periods of secondary filaments may delay getting back into detachment
In MAST-U will investigate optimum scenario by altering X-point position and flux through divertor throat
  Monitor with LPs in nose and divertor tiles operated in Isat mode
  Several fast cameras available to study the turbulence and filamentary structures

## Slide 21: Conclusions
Secondary filaments have been identified on MAST and are seen to occur following plasma interaction with PFCs
Assumption is that neutrals from the plasma-surface interaction effect the edge transport and enhance the turbulence
  Further study required to understand the relationship between plasma-surface interaction and the secondary filament instability
Secondary filaments have been measured at the divertor target in MAST by LPs in LSN and DND with type I ELMs
  Measured up to ΔRtgt = 20cm persisting for > 1ms after ELM
Fast camera data from a midplane view of the plasma confirmed plasma interaction with in vessel coils occurred in cases with secondary filaments
  Turbulent filamentary behaviour seem for more than 1.2ms after an ELM event extending to ψN = 1.4