| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: Injection and Dispersion of Li Powder in NSTX Discharges |
| OP-XP-738 | Revision: 1 | Effective Date: 5/2/07 Expiration Date: 5/2/09 (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Responsible Author: D. K. Mansfield | Date 5/2/07 |
| ATI – ET Group Leader: V. A. Soukhanovskii (H. W. Kugel) | Date |
| RLM - Run Coordinator: D. Gates | Date |
| Responsible Division: Experimental Research Operations |
| Chit Review Board (designated by Run Coordinator) |
| MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

TITLE: Injection and Dispersion of Li Powder in NSTX Discharges No.  OP-XP-738

AUTHOR: D. K. Mansfield  	DATE: 5/2/07

# 1.	Overview of planned experiment

This work will allow an assessment to be made of the efficacy of Li powder for the purposes of improving plasma performance and reducing plasma density.

# 2.	Theoretical/ empirical justification

Recent experiments involving Li pellets (XP718) and the LITER system (XP 719) on NSTX 	have demonstrated the usefulness of Li coatings for improving plasma performance. Neither 	experiment, however, demonstrated a sustainable reduction in density. There is reasonable 	cause to speculate that the introduction of Li powder into the SOL of an NSTX H-Mode plasma 	might lead to improvements in plasma performance which were similar to those demonstrated 	during XPs 718 and 719 while simultaneously reducing the plasma density. If such 	improvement 	in performance can be demonstrated, it will allow NSTX to have a more flexible 	Li conditioning capability than is presently available.

The highest flux of lithium introduced into the plasma edge during an NSTX discharge 	(excluding pellet injection) was accomplished during XP719. That rate was approximately 1 	mg/sec. If successful, this experiment will introduce at least an order of magnitude more 	lithium into a 1 second long discharge.

# 3.	Experimental run plan

The run plan will be divided into two parts: (1) the assessment of Li powder in an 	unconditioned machine (i.e. one that has received no Li from LITER) and (2) the assessment of 	Li powder in a conditioned machine (i.e. one that has experienced the benefits of LITER 	conditioning). See Table page 4 for a summary of the run sequence.

* Modified experimental run plan

During XMP 52, it was observed that 5 Torr Liter of He gas was introduce into NSTX when a 	single empty sabot was fired by LPI. It was subsequently decided to attempt a limited number 	of shots with one sabot only. The modified run plan is presented on page 5.  At the beginning of 	the XP a blank sabot will be fired with He propellant in order to assess the effects of the 	“leakage” gas on the discharge. A decision about whether to switch to Deuterium propellant 	will be made after shot 3 of the modified run plan.

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

XMP-52: “Practice Injection of Li Powder into NSTX” Must be completed before this XP 	can be started. This XMP simply allows the LPI to be exercised with Li powder in a piggyback 	manner.

The No-Conditioning fiducial discharge for this XP will be 123474 - the same as was 	employed during XP 719. The LSN H-Mode template for 123474 was 121323 with only 2 	beam sources.

In the second part of this XP, as the PFC conditioning changes with the introduction of lithium 	from LITER, it is possible that the interaction of the plasma with the RF antenna might have 	to be reduced by using 123515 as a template discharge.

He GDC will be used as needed.

# 5.	Planned analysis

UEDGE, TRANSP, etc.

# 6.	Planned publication of results

PSI08, Nuclear Fusion or Physics of Plasmas, IAEA08

Experimental Sequence

| Shot No. | Nom. Mass Injected mg | Oven Btwn Shot mg* | # Barrels Employed | Arrival Time secs | ( Lithium Mass mg |
| --- | --- | --- | --- | --- | --- |
| 1 | 0 | 0 | 0 | - | 0 |
| 2 | 0 | 0 | 0 | - | 0 |
| 3 | 5 | 0 | 1 | 0.2 | 5 |
| 4 | 5 | 0 | 1 | 0.2 | 10 |

Start LITER heat-up 1 hour to reach  450 degrees -  No significant deposition

| 5 | 10 | 0 | 1 | 0.2 | 20 |
| --- | --- | --- | --- | --- | --- |
| 6 | 10 | 0 | 1 | 0.2 | 30 |
| 7 | 20 | 0 | 2 | 0.2, 0.4 | 50 |
| 8 | 20 | 0 | 2 | 0.2, 0.4 | 70 |
| 9 | 30 | 0 | 3 | 0.2, 0.4, 0.6 | 100 |
| 10 | 30 | 0 | 3 | 0.2, 0.4, 0.6 | 130 |

LITER to  15mg/min -  Requires  10 Min and  100 mg deposition

| 11 | 0 | 150 | - | - | 380 |
| --- | --- | --- | --- | --- | --- |
| 12 | 0 | 150 | - | - | 530 |
| 13 | 5 | 150 | 1 | 0.20 | 685 |
| 14 | 5 | 150 | 1 | 0.20 | 840 |
| 15 | 10 | 150 | 1 | 0.2, 0.4 | 1000 |
| 16 | 10 | 150 | 1 | 0.2, 0.4 | 1160 |
| 17 | 20 | 150 | 2 | 0.2, 0.4 | 1330 |
| 18 | 20 | 150 | 2 | 0.2, 0.4 | 1500 |
| 19 | 30 | 150 | 3 | 0.2, 0.4, 0.6 | 1680 |
| 20 | 30 | 150 | 3 | 0.2, 0.4, 0.6 | 1860 |

* For 10 min of evaporation between shots

Modified Experimental Sequence – One Barrel Only – No LITER Employed

| Shot No. | Nom. Mass Injected mg | Oven Btwn Shot mg* | # Barrels Employed | Arrival Time secs | ( Lithium Mass mg |
| --- | --- | --- | --- | --- | --- |
| 1 | 0 | 0 | 0 | - | 0 |
| 2 | 0 | 0 | 1 MT Sabot | 0.3 | 0 |
| 3 | 5 | 0 | 1 | 0.3 | 5 |
| 4 | 5 | 0 | 1 | 0.3 | 10 |
| 5 | 10 |  | 1 | 0.3 | 20 |
| 6 | 10 |  | 1 | 0.3 | 30 |
| 7 | 20 |  | 1 | 0.3 | 50 |
| 8 | 20 |  | 1 | 0.3 | 70 |
| 9 | 30 |  | 1 | 0.3 | 100 |
| 10 | 30 |  | 1 | 0.3 | 130 |

PHYSICS OPERATIONS REQUEST

Title: Injection and Dispersion of Li Powder in NSTX Discharges	OP-XP-738

Machine conditions (specify ranges as appropriate)

ITF (kA):-53	Flattop start/stop (s):-0.01/1.1

IP (MA):1.0	Flattop start/stop (s): 0.2/1.0

Configuration: LSN

Outer gap (m): 		Inner gap (m):

Elongation :		Triangularity :

Z position (m):

Gas Species: D	Injector(s): CS mid,OM#2

NBI - Species: D	Sources: A,C	Voltage (kV): 90	Duration (s): 1.0

ICRF – Power (MW): 	Phasing: 	Duration (s):

CHI:

Either:	List previous shot numbers for setup: Shot # 123471 or 123474

Or:	Sketch the desired time profiles, including inner and outer gaps, , , heating, fuelling, etc. as appropriate. Accurately label the sketch with times and values.

DIAGNOSTIC CHECKLIST

Title	OP-XP-738

| Diagnostic | Need | Desire | Instructions |
| --- | --- | --- | --- |
| Bolometer – tangential array |  | x |  |
| Bolometer – divertor |  |  |  |
| CHERS – toroidal | x |  |  |
| CHERS – poloidal | x |  |  |
| Divertor fast camera | x |  |  |
| Dust detector |  | x |  |
| EBW radiometers |  |  |  |
| Edge deposition monitors | x |  |  |
| Edge pressure gauges | x |  |  |
| Edge rotation diagnostic | x |  |  |
| Fast ion D_alpha - FIDA |  |  |  |
| Fast lost ion probes - IFLIP |  |  |  |
| Fast lost ion probes - SFLIP |  |  |  |
| Filterscopes | x |  |  |
| FIReTIP | x |  |  |
| Gas puff imaging |  |  |  |
| H camera - 1D | x |  |  |
| High-k scattering |  |  |  |
| Infrared cameras | x |  |  |
| Interferometer - 1 mm |  |  |  |
| Langmuir probes - divertor | x |  |  |
| Langmuir probes – RF antenna |  |  |  |
| Magnetics – Diamagnetism | x |  |  |
| Magnetics - Flux loops | x |  |  |
| Magnetics - Locked modes | x |  |  |
| Magnetics - Pickup coils | x |  |  |
| Magnetics - Rogowski coils | x |  |  |
| Magnetics - RWM sensors |  |  |  |
| Mirnov coils – high frequency | x |  |  |
| Mirnov coils – poloidal array |  |  |  |
| Mirnov coils – toroidal array |  |  |  |
| MSE |  |  |  |
| NPA – ExB scanning |  |  |  |
| NPA – solid state |  |  |  |
| Neutron measurements | x |  |  |
| Plasma TV | x |  |  |
| Reciprocating probe |  |  |  |
| Reflectometer – 65GHz | x |  |  |
| Reflectometer – correlation |  |  |  |
| Reflectometer – FM/CW |  |  |  |
| Reflectometer – fixed f |  |  |  |
| Reflectometer – SOL | x |  |  |
| RF edge probes | x |  |  |
| Spectrometer – SPRED | x |  |  |
| Spectrometer – VIPS | x |  |  |
| SWIFT – 2D flow |  |  |  |
| Thomson scattering | x |  |  |
| Ultrasoft X-ray arrays |  |  |  |
| Ultrasoft X-ray arrays – bicolor |  |  |  |
| Ultrasoft X-rays – TG spectr. |  |  |  |
| Visible bremsstrahlung det. | x |  |  |
| X-ray crystal spectrometer - H |  | x |  |
| X-ray crystal spectrometer - V |  | x |  |
| X-ray fast pinhole camera |  |  |  |