| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: Shear profile effects on core high-k fluctuations |
| OP-XP-620 | Revision: 2006 | Effective Date: (Ref. OP-AD-97) Expiration Date: (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Authors: D. Smith, H. Park, E. Mazzucato, M. Bell, L. Delgado-Aparicio, F. Levinton, J. Menard, D. Stutman, K. Tritz, and H. Yuh | Date |
| ATI – ET Group Leader: M. Bell and K. Tritz | Date |
| RLM - Run Coordinator: R. Raman | Date |
| Responsible Division: Experimental Research Operations |
| Chit Review Board (designated by Run Coordinator) |
| MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

Shear profile effects on core high-k fluctuations	OP-XP-620

# 1.	Overview of planned experiment

Utilize the high-k scattering system to measure ρe-scale fluctuations in reverse shear (RS) and conventional shear (CS) discharges.  Measure fluctuations both inside and outside the location of the “Te knee”.

# 2.	Theoretical/ empirical justification

Recent publications (Stutman, to be published in PoP; LeBlanc, NF 2004; and Bourdelle, PoP 2003) have explored the connection between ETG turbulence, electron thermal transport, and reverse shear profiles on NSTX.  Reverse shear discharges exhibit improved core electron confinement and more peaked Te profiles compared to conventional shear discharges.  The improved electron confinement may be related to reduced electron gyroscale fluctuations and ETG turbulence suppression.

The high-k scattering system can measure electron gyroscale fluctuations (k┴ρe≤1) with spatial and k-space resolution at several discrete values of k┴.  With steerable optics, the scattering volume can be positioned throughout the plasma minor radius.

A prerequisite of this XP is the development of reproducible RS and CS discharges at the same plasma current, similar density profiles, and quiescent MHD.  This is the objective of XP-610 (F. Levinton).

Scattering system alignment in real-space and k-space should take into account the results of XMP-44.

# 3.	Experimental run plan

The plan is to position the scattering region at three tangency radii (107, 115, and 122 cm) and take two shots each for three discharge scenarios (CS, mild RS, and RS) for
18 shots total.  Controlled accesses will be required to reposition the scattering system.

|  | CS | mild RS | RS |
| --- | --- | --- | --- |
| Rtan = 107 cm | ×2 | ×2 | ×2 |
| Rtan = 115 cm | ×2 | ×2 | ×2 |
| Rtan = 122 cm | ×2 | ×2 | ×2 |

The target plasmas are 121034 (CS), 121030 (mild RS), and 121040 (RS)

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

Thomson, CHERS, NBI, reflectometer, FIRETIP, all x-ray diagnostics, all magnetics, XP610, XMP44

# 5.	Planned analysis

TRANSP, LRDFIT, GS2

# 6.	Planned publication of results

PoP or maybe even PRL

PHYSICS OPERATIONS REQUEST

Error! Reference source not found.	OP-XP-620

Machine conditions (specify ranges as appropriate)

ITF (kA): ______	Flattop start/stop (s):  _____/_____

IP (MA): 900	Flattop start/stop (s):  _____/_____

Configuration:

Outer gap (m):	_____,	Inner gap (m):	_____

Elongation :	_____,	Triangularity :	_____

Z position (m):

Gas Species:  D,	Injector:

NBI - Species: D,	Sources: A,	Voltage (kV): 90,	Duration (s): _____

ICRF – Power (MW): ____,	Phasing:      ,	Duration (s): _____

CHI:  Off

Either:	List previous shot numbers for setup: 121040, 121034, 121030

Or:	Sketch the desired time profiles, including inner and outer gaps, , , heating, fuelling, etc. as appropriate. Accurately label the sketch with times and values.

DIAGNOSTIC CHECKLIST

Error! Reference source not found.	OP-XP-620

| Diagnostic | Need | Desire | Instructions |
| --- | --- | --- | --- |
| Bolometer - tangential array | ( |  |  |
| Bolometer array - divertor | ( |  |  |
| CHERS | ( |  |  |
| Divertor fast camera |  |  |  |
| Dust detector |  |  |  |
| EBW radiometers |  |  |  |
| Edge deposition monitor |  |  |  |
| Edge pressure gauges |  |  |  |
| Edge rotation spectroscopy |  |  |  |
| Fast lost ion probes – IFLIP |  |  |  |
| Fast lost ion probes – SFLIP |  |  |  |
| Filtered 1D cameras |  |  |  |
| Filterscopes | ( |  |  |
| FIReTIP | ( |  |  |
| Gas puff imaging |  |  |  |
| High-k scattering | ( |  |  |
| Infrared cameras |  |  |  |
| Interferometer – 1 mm |  | ( |  |
| Langmuir probes - PFC tiles |  |  |  |
| Langmuir probes - RF antenna |  |  |  |
| Magnetics – Diamagnetism | ( |  |  |
| Magnetics – Flux loops | ( |  |  |
| Magnetics – Locked modes | ( |  |  |
| Magnetics – Pickup coils | ( |  |  |
| Magnetics - Rogowski coils | ( |  |  |
| Magnetics - RWM sensors | ( |  |  |
| Mirnov coils – high frequency | ( |  |  |
| Mirnov coils – poloidal array | ( |  |  |
| Mirnov coils – toroidal array | ( |  |  |
| MSE | ( |  |  |
| Neutral particle analyzer | ( |  |  |
| Neutron Rate (2 fission, 4 scint) |  |  |  |
| Neutron collimator |  |  |  |
| Plasma TV |  |  |  |
| Reciprocating probe |  |  |  |
| Reflectometer - FM/CW |  | ( |  |
| Reflectometer - fixed frequency homodyne quadrature |  | ( |  |
| Reflectometer - homodyne correlation |  | ( |  |
| Reflectometer - HHFW/SOL |  | ( |  |
| RF antenna camera |  |  |  |
| RF antenna probe |  |  |  |
| Solid State NPA | ( |  |  |
| SPRED | ( |  |  |
| Thomson scattering - 20 channel | ( |  |  |
| Thomson scattering - 30 channel | ( |  |  |
| Ultrasoft X-ray arrays | ( |  |  |
| Ultrasoft X-ray arrays - 2 color | ( |  |  |
| Visible bremsstrahlung det. |  | ( |  |
| Visible spectrometers (VIPS) |  | ( |  |
| X-ray crystal spectrometer - H |  | ( |  |
| X-ray crystal spectrometer - V |  | ( |  |
| X-ray PIXCS (GEM) camera |  | ( |  |
| X-ray pinhole camera |  | ( |  |
| X-ray TG spectrometer |  | ( |  |