| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: Effect of Rotation on the L-H Threshold |
| OP-XP-841 | Revision: 0 | Effective Date: 6/19/08 Expiration Date: (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Responsible Author: Stanley Kaye | Date 6/22/08 |
| ATI – ET Group Leader: Stanley Kaye | Date |
| RLM - Run Coordinator: Michael Bell | Date |
| Responsible Division: Experimental Research Operations |
| Chit Review Board (designated by Run Coordinator) |
| MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

| TITLE: Effect of rotation on L-H threshold | No. OP-XP-841 |
| --- | --- |
| AUTHORS: S. Kaye | DATE: June 19, 2008 |

REVISED: Feb. 5, 2009

# 1.	Overview of planned experiment

# The goal of this experiment is to study the effect of rotation on the L-H threshold power. n=3 braking will be used to vary the rotation.

# 2.	Theoretical/ empirical justification

This XP studies the effect of rotation, and by extension rotational shear at the edge, on the L-H threshold. This has direct bearing on developing an understanding of the effect of this edge rotational shear and how it might impact thresholds in future devices at both low rotation (ITER) and at higher rotation (NHTX, ST-CTF). This study is an element of an ITPA JEX.

# 3.	Experimental run plan

- Establish L-H threshold power in high-LSNdischarge (127267 baseline) using one source (use B or B+C as needed, initially); vary voltage in source to achieve threshold. If necessary modulate source to lower power even farther

  - Use optimal n=3 error field correction (-300 A in SPA1) and n=1 mode control

  - Source C will allow lower power (voltage) if necessary

- Vary n=3 SPA coil current to 0 A, 400 A, 800 A

  - Establish threshold in same manner at each level.

- Use 10-15 mg/min Li evaporation, if available.

- No HeGDC between shots.

- Shorten shot to 500-600 ms to reduce shot cycle to 10 minutes.

TABULAR SHOT LIST

| Condition | Ip (MA) | BT (T) | SPA 1 Current (steady) |
| --- | --- | --- | --- |
| 1 | 0.8 | 0.45 | -300 A (optimum) |
| 2 | 0.8 | 0.45 | 0 A |
| 3 | 0.8 | 0.45 | 400 A |
| 4 | 0.8 | 0.45 | 800 A |

# Total: 18 shots

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

Discharge reproducibility, ability to achieve H-mode with one source.

Optional feature is to use NBI pre-heat (source A only) from 80-140 ms, then turn source back on after Ip flattop, at 220 ms. Will not use this if discharge well-behaved without (starting point).

# 5.	Planned analysis

EFIT, TRANSP, specialized codes

# 6.	Planned publication of results

Joule milestone, TTF, ITPA, IAEA

PHYSICS OPERATIONS REQUEST

| TITLE: Effect of rotation on L-H threshold | No. OP-XP-841 |
| --- | --- |
| AUTHORS: S. Kaye | DATE: June 19, 2008 |

Machine conditions (specify ranges as appropriate)

ITF (kA): 52 (4.5 kG)	Flattop start/stop (s):

IP (MA): 0.9	Flattop start/stop (s):

Configuration: LSN

Outer gap (m): 		Inner gap (m):

Elongation : ~1.8	Upper/lower triangularity : ~ 0.45

Z position (m):	0

Gas Species: D		Injector(s):

NBI Species: D	Sources: 	3	Voltage (kV): 	55-80 (B, C), 90 (A)	Duration (s): <0.6 s

ICRF Power (MW):	0	Phasing: 		Duration (s):

CHI:	Off	Bank capacitance (mF):

LITER:  Off (during initial attempt at XP)

Either:	List previous shot numbers for setup:	127267

Or:	Sketch the desired time profiles, including inner and outer gaps, , , heating, fuelling, etc.

DIAGNOSTIC CHECKLIST

| TITLE: Effect of rotation on L-H threshold | No. OP-XP-841 |
| --- | --- |
| AUTHORS: S. Kaye | DATE: June 19, 2008 |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| Bolometer – tangential array | √ |  |
| Bolometer – divertor |  |  |
| CHERS – toroidal | √ |  |
| CHERS – poloidal | √ |  |
| Divertor fast camera |  |  |
| Dust detector |  |  |
| EBW radiometers |  |  |
| Edge deposition monitors |  |  |
| Edge neutral density diag. |  | √ |
| Edge pressure gauges |  | √ |
| Edge rotation diagnostic | √ |  |
| Fast ion D_alpha - FIDA | √ |  |
| Fast lost ion probes - IFLIP |  |  |
| Fast lost ion probes - SFLIP |  | √ |
| Filterscopes | √ |  |
| FIReTIP |  | √ |
| Gas puff imaging |  | √ |
| H camera - 1D |  | √ |
| High-k scattering |  | √ |
| Infrared cameras |  |  |
| Interferometer - 1 mm |  |  |
| Langmuir probes – divertor |  | √ |
| Langmuir probes – BEaP |  |  |
| Langmuir probes – RF ant. | √ |  |
| Magnetics – Diamagnetism | √ |  |
| Magnetics – Flux loops | √ |  |
| Magnetics – Locked modes | √ |  |
| Magnetics – Pickup coils | √ |  |
| Magnetics – Rogowski coils | √ |  |
| Magnetics – Halo currents | √ |  |
| Magnetics – RWM sensors | √ |  |
| Mirnov coils – high f. | √ |  |
| Mirnov coils – poloidal array | √ |  |
| Mirnov coils – toroidal array | √ |  |
| Mirnov coils – 3-axis proto. |  |  |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| MSE |  | √ |
| NPA – ExB scanning |  |  |
| NPA – solid state |  | √ |
| Neutron measurements | √ |  |
| Plasma TV | √ |  |
| Reciprocating probe |  |  |
| Reflectometer – 65GHz |  |  |
| Reflectometer – correlation |  |  |
| Reflectometer – FM/CW |  |  |
| Reflectometer – fixed f |  | √ |
| Reflectometer – SOL |  |  |
| RF edge probes |  |  |
| Spectrometer – SPRED | √ |  |
| Spectrometer – VIPS | √ |  |
| SWIFT – 2D flow |  |  |
| Thomson scattering | √ |  |
| Ultrasoft X-ray arrays | √ |  |
| Ultrasoft X-rays – bicolor |  | √ |
| Ultrasoft X-rays – TG spectr. |  |  |
| Visible bremsstrahlung det. | √ |  |
| X-ray crystal spectrom. - H |  |  |
| X-ray crystal spectrom. - V |  |  |
| X-ray fast pinhole camera |  |  |
| X-ray spectrometer - XEUS |  | √ |

# Text boxes

A

B or C or C

Vary level of n=3 braking current

200 ms

Start without Source A preheat; use only if necessary.