| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: Strike Point Dynamics |
| OP-XP-904 | Revision: | Effective Date: Expiration Date: (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Responsible Author: Egemen Kolemen | Date |
| ATI – ET Group Leader: David Gates | Date |
| RLM - Run Coordinator: Mike Bell | Date |
| Responsible Division: Experimental Research Operations |
| Chit Review Board (designated by Run Coordinator) |
| MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

| TITLE: Strike Point Dynamics | No. OP-XP-904 |
| --- | --- |
| AUTHORS: Egemen Kolemen | DATE: 2/18/09 |

# 1.	Overview of planned experiment

A liquid lithium divertor (LLD) is being installed on NSTX to enable experiments with the first complete liquid metal divertor target in a high-power device. Because the lithium will continue reacting with hydrogen or deuterium until it is volumetrically converted to hydrides, the LLD is expected to provide better pumping than lithium coatings on carbon PFC’s.

The shape of the plasma dictates the pumping rate of the lithium with LLD by channeling the plasma to LLD. Among the shape parameters strike point is the most important one. Experimentally it was shown that the density reduction depends on proximity of outer strike point to LLD.

The aim of this experiment is to study the dynamics of the strike point, design a new controller to change the location of the strike point to desired location and design a controller to stabilize the strike point at the desired position.

# 2.	Theoretical/ empirical justification

Strike point is the most important parameter that dictates the pumping rate of the lithium with LLD. Experimentally it was shown that the density reduction depends on proximity of outer strike point to LLD. This experiment is designed to control the strike point location via new controller designs and study its dynamics.

# 3.	Experimental run plan

- Match the desired shape given to us in shot 115495 at 0.501 seconds with the conditions in the reference shot 120001. To this set the coil currents to:

Coil  Current (kA) (for Ip = 1 MA)

OH     -9.990697   ;       PF1AU      3.000062     ;   PF2U      3.152069       ;   PF3U     -8.529646

PF5   -9.412524  ; PF3L     -9.580102    ;   PF2L      4.527283 ;  PF1AL  3.055423  ;  PF1B    3.842131

- Stabilize the plasma for the 1st shape

- From previously defined strike point versus PF2L coil current curves, set the PF2L coil current in a step impulsive way to get the strike point between 0 and 25 cm. The coil current depends on li and ranges between 0.00 and 0.02 (Current/Ip). This will take 8-10 shots. We will set the strike point distance starting with 0 then 25 cm then interpolate as much points as possible in the experiment day. 1st 0 cm, 2nd  25 cm, 3rd 12 cm, 4th  6 cm,  5th 18 cm...

- Measure the response of the strike point.

- Obtain the time constant, rise time, delay and other parameters of the strike point motion response to the impulsive change in PF2L current.

- Repeat for the same procedure with PF1B coil current change (as opposed to PF2L). The range of PF1B coil current will be 0.00 to 0.01 (Current/Ip) with corresponding strike point distance of (0-4) cm to (10-13) cm. This will take 8-10 shots, in the same fashion as PF2L coil current steps.

- Test and tune the strike point controller.

- Study the compromise with respect to the loss in control for shape control and other control aims.

Physical operating conditions for the experiment will be similar to the previously tested 120001 shot.

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

See below.

# 5.	Planned analysis

We will require EFIT analysis and preferably correlations between magnetic strike point location and power deposition on the diverter. The time constants for the step responses will be analyzed. Based on control theory, a PID controller for the strike point position with lower PF1/2 inputs will be obtained.

# 6.	Planned publication of results

The results will be published in “Fusion Engineering and Design”.

PHYSICS OPERATIONS REQUEST

| TITLE: Strike Point Dynamics | No. OP-XP-904 |
| --- | --- |
| AUTHORS: Egemen Kolemen | DATE: 2/18/09 |

Machine conditions (specify ranges as appropriate)

ITF (kA):  	Flattop start/stop (s):

IP (MA): 1	Flattop start/stop (s):

Configuration: Limiter / DN / LSN / USN

Outer gap (m): 	0.09	Inner gap (m): 	0.03

Elongation :	1.8-2.1	Upper/lower triangularity :	~0.6

Z position (m):

Gas Species: 	D	Injector(s):  Source A

NBI Species: D	Sources: 		Voltage (kV): 	90	Duration (s): TBD

ICRF Power (MW):	N/A	Phasing: 		Duration (s):

CHI: Off	Bank capacitance (mF):

LITER:  Off

Either:	List previous shot numbers for setup:	120001.

Or:	Sketch the desired time profiles, including inner and outer gaps, , , heating, fuelling, etc. as appropriate. Accurately label the sketch with times and values.

DIAGNOSTIC CHECKLIST

| TITLE: Vertical Stability Physics and Performance Limits in Tokamaks with Highly Elongated Plasmas | No. OP-XP-811 |
| --- | --- |
| AUTHORS: Egemen Kolemen | DATE: 1/17/08 |

| Diagnostic | Need | Want | Conditions |
| --- | --- | --- | --- |
| Bolometer – tangential array |  |  |  |
| Bolometer – divertor |  |  |  |
| CHERS – toroidal |  |  |  |
| CHERS – poloidal |  |  |  |
| Divertor fast camera |  |  |  |
| Dust detector |  |  |  |
| EBW radiometers |  |  |  |
| Edge deposition monitors |  |  |  |
| Edge neutral density diag. |  |  |  |
| Edge pressure gauges |  |  |  |
| Edge rotation diagnostic |  |  |  |
| Fast ion D_alpha - FIDA |  |  |  |
| Fast lost ion probes - IFLIP |  |  |  |
| Fast lost ion probes - SFLIP |  |  |  |
| Filterscopes |  |  |  |
| FIReTIP |  |  |  |
| Gas puff imaging |  |  |  |
| H camera - 1D |  |  |  |
| High-k scattering |  |  |  |
| Infrared cameras |  |  |  |
| Interferometer - 1 mm |  |  |  |
| Langmuir probes - divertor |  |  |  |
| Langmuir probes - BEaP |  |  |  |
| Langmuir probes – RF ant. |  |  |  |
| Magnetics – Diamagnetism |  |  |  |
| Magnetics - Flux loops |  |  |  |
| Magnetics - Locked modes |  |  |  |
| Magnetics - Pickup coils |  |  |  |
| Magnetics - Rogowski coils |  |  |  |
| Magnetics – Halo currents |  |  |  |

| Diagnostic | Need | Want | Conditions |
| --- | --- | --- | --- |
| Magnetics - RWM sensors |  |  |  |
| Mirnov coils – high f. |  |  |  |
| Mirnov coils – poloidal array |  |  |  |
| Mirnov coils – toroidal array |  |  |  |
| Mirnov coils – 3-axis proto. |  |  |  |
| MSE |  |  |  |
| NPA – ExB scanning |  |  |  |
| NPA – solid state |  |  |  |
| Neutron measurements |  |  |  |
| Plasma TV |  |  |  |
| Reciprocating probe |  |  |  |
| Reflectometer – 65GHz |  |  |  |
| Reflectometer – correlation |  |  |  |
| Reflectometer – FM/CW |  |  |  |
| Reflectometer – fixed f |  |  |  |
| Reflectometer – SOL |  |  |  |
| RF edge probes |  |  |  |
| Spectrometer – SPRED |  |  |  |
| Spectrometer – VIPS |  |  |  |
| SWIFT – 2D flow |  |  |  |
| Thomson scattering |  |  |  |
| Ultrasoft X-ray arrays |  |  |  |
| Ultrasoft X-rays – bicolor |  |  |  |
| Ultrasoft X-rays – TG spectr. |  |  |  |
| Visible bremsstrahlung det. |  |  |  |
| X-ray crystal spectrom’r - H |  |  |  |
| X-ray crystal spectrom’r - V |  |  |  |
| X-ray fast pinhole camera |  |  |  |
| X-ray spectrometer - XEUS |  |  |  |