| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: Dependence of L-H power threshold on X-point radius |
| OP-XP-909 | Revision: | Effective Date: (Approval date unless otherwise stipulated) Expiration Date: (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Responsible Author: R. Maingi | Date |
| ATI – ET Group Leader: K. Tritz | Date |
| RLM - Run Coordinator: R. Raman | Date |
| Responsible Division: Experimental Research Operations |
| Chit Review Board (designated by Run Coordinator) |
| MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

| TITLE: Dependence PLH on X-point radius | No. OP-XP-909 |
| --- | --- |
| AUTHORS: R. Maingi, S. Gerhardt, C.S. Chang, G. Park | DATE: 5-Feb-09 |

# 1.	Overview of planned experiment

The goal of this experiment is to measure the L-H power threshold (PLH) as a function of lower X-point radius/triangularity and compare the measured Er profiles with predictions from the XGC code. Three different triangularities are being targeted: ~ 0.4, 0.5, and 0.7.

# 2.	Theoretical/ empirical justification

The XGC-0 has shown that the thermal ion loss at the X-point increases with the X-point radius, leading to the predicted formation of a larger radial electric field, Er ,and shear, Er’. Operating from a premise that a critical Er or Er’might be needed for H-mode access, it follows that discharges with large X-point radii (i.e. reduced lower triangularity dL) would have a lower L-H power threshold than discharges with a higher dL. Experimentally such a trend has been noted in control room lore but never documented.

Fig. 1 shows the 3 target shapes envisioned for this study: a lo, mid, and high dL shape. The elongation and X-point height will be maintained during this triangularity scan. The low dL discharge has a more recent rtEFIT version, but this one was chosen because of an existing XGC calculation of the Er.

Figure 2 shows a comparison of the computed Er from the XGC-O code for the low and high dL discharges, using the EFIT02 pressure profiles as a starting point. I can be seen that the Er and Er’ are substantially higher for the low dL discharge, as previously presented by C.S. Chang. We note that all three of the time slices in Fig. 1 and the analysis in Fig. 2 are from the H-mode phase; it is expected that the thermal ion loss leading to the difference in Er would also be present in the L-mode phase prior to the L-H transition.

This experiment could be run in either lower-single null (LSN) or double-null configuration, the latter having a lower PLH typically. Here we choose LSN because it will simplify analysis with XGC.

# 3.	Experimental run plan

The main scan in this XP is a power (NBI) scan at three different triangularities to localize PLH. The target parameters are Ip=0.8 MA, Bt=0.45 T, k ~ 2, drsep ~ -1.5cm, X-point height ~ 20cm. The intermediate and higher dL discharges were run in 2008, and an rtEFIT version of #107714 is #119837. S. Gerhardt has been doing ISOLVER calculations to better understand the PF coil current changes needed to insure a good shape scan.

Shot sequence:

The dL ~ 0.4 discharge will be run first. PLH will be localized by reducing the voltage on sources A/B/C as needed. Historically source C has the easiest time running at ~ 55kV ~ 800 kW. Sources A and B usually don’t run as reliably below 65 kV ~ 1 MW. We will request source C to be at the lowest voltage possible, source B at 65 kV, and source A at 90 kV to have the possibility of MSE if PLH > 2 MW. If PLH < 0.8 MW, we will use pulse-width modulation to localize PLH.

An important consideration is whether to use an NBI pre-heat from ~ 60-120ms, i.e. well before the Ip flat-top to save V-S. If sufficient flat-top is available at 800 kA, no pre-heat will be used. If the flat-top is limited because of the long ohmic phase, we will add in a short pre-heat phase during the Ip ramp.

A correlated decision is the choice of Ip level. In NSTX, PLH increases with Ip, thus making it easier to distinguish the effects of the shape scan. On the other hand, the Ip flat-top decreases quickly with Ip, particularly if a long ohmic phase is used. The actual value of Ip used will thus be somewhere between 0.7 and 0.9 MA, depending on the flat-top duration.

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

H-mode access at reasonable power is required.  HeGDC between shots will be adjusted according to need, probably ~ 6.5 min for a 12.5 minute rep rate.

# 5.	Planned analysis

EFIT/LRDFIT needed, TRANSP for absorbed power, XGC to compute Er and compare with CHERs and ERD.

# 6.	Planned publication of results

APS; possible H-mode workshop paper.

PHYSICS OPERATIONS REQUEST

| TITLE: Dependence PLH on X-point radius | No. OP-XP-909 |
| --- | --- |
| AUTHORS: R. Maingi, S. Gerhardt, C.S. Chang, G. Park | DATE: 5-Feb-09 |

Machine conditions (specify ranges as appropriate)

ITF (kA):   54 (0.45 T)	Flattop start/stop (s):

IP (MA):   0.8	Flattop start/stop (s):   ~ 0.16-0.2

Configuration: LSN (drsep ~ - 1.5 cm)

Outer gap (m):   ~ 0.1	Inner gap (m):   varies

Elongation :   ~2	Upper/lower triangularity : L~ 0.4/0.5/0.7

Z position (m):   ~ 0.0

Gas Species: D		Injector(s): HFS midplane

NBI Species: D	Sources: A/B/C	Voltage (kV): 	varied	Duration (s): <1 sec

ICRF Power (MW):	no	Phasing: 		Duration (s):

CHI:	Off	Bank capacitance (mF):

LITER:  Off

Either:	List previous shot numbers for setup:	use 127267, 127281, 119840

Or:	Sketch the desired time profiles, including inner and outer gaps, , , heating, fuelling, etc. as appropriate. Accurately label the sketch with times and values.

DIAGNOSTIC CHECKLIST

| TITLE: Dependence PLH on X-point radius | No. OP-XP-909 |
| --- | --- |
| AUTHORS: R. Maingi, S. Gerhardt, C.S. Chang, G. Park | DATE: 5-Feb-09 |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| Bolometer – tangential array | √ |  |
| Bolometer – divertor |  | √ |
| CHERS – toroidal | √ |  |
| CHERS – poloidal | √ |  |
| Divertor fast camera |  | √ |
| Dust detector |  |  |
| EBW radiometers |  |  |
| Edge deposition monitors |  |  |
| Edge neutral density diag. |  | √ |
| Edge pressure gauges |  | √ |
| Edge rotation diagnostic | √ |  |
| Fast ion D_alpha - FIDA |  |  |
| Fast lost ion probes - IFLIP |  |  |
| Fast lost ion probes - SFLIP |  |  |
| Filterscopes | √ |  |
| FIReTIP |  | √ |
| Gas puff imaging |  | √ |
| H camera - 1D |  | √ |
| High-k scattering |  |  |
| Infrared cameras |  | √ |
| Interferometer - 1 mm |  |  |
| Langmuir probes – divertor |  | √ |
| Langmuir probes – BEaP |  |  |
| Langmuir probes – RF ant. |  |  |
| Magnetics – Diamagnetism | √ |  |
| Magnetics – Flux loops | √ |  |
| Magnetics – Locked modes | √ |  |
| Magnetics – Pickup coils | √ |  |
| Magnetics – Rogowski coils | √ |  |
| Magnetics – Halo currents | √ |  |
| Magnetics – RWM sensors |  | √ |
| Mirnov coils – high f. | √ |  |
| Mirnov coils – poloidal array | √ |  |
| Mirnov coils – toroidal array | √ |  |
| Mirnov coils – 3-axis proto. |  |  |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| MSE |  | √ |
| NPA – ExB scanning |  |  |
| NPA – solid state |  |  |
| Neutron measurements |  |  |
| Plasma TV |  | √ |
| Reciprocating probe |  | √ |
| Reflectometer – 65GHz |  | √ |
| Reflectometer – correlation |  | √ |
| Reflectometer – FM/CW |  |  |
| Reflectometer – fixed f |  |  |
| Reflectometer – SOL |  | √ |
| RF edge probes |  |  |
| Spectrometer – SPRED |  |  |
| Spectrometer – VIPS |  |  |
| SWIFT – 2D flow |  |  |
| Thomson scattering | √ |  |
| Ultrasoft X-ray arrays | √ |  |
| Ultrasoft X-rays – bicolor |  | √ |
| Ultrasoft X-rays – TG spectr. |  | √ |
| Visible bremsstrahlung det. |  | √ |
| X-ray crystal spectrom. - H |  |  |
| X-ray crystal spectrom. - V |  |  |
| X-ray fast pinhole camera |  |  |
| X-ray spectrometer - XEUS |  |  |

# Text boxes

(l=0.38, (u=0.25

(l=0.52, (u=0.33

(l=0.7, (u=0.35

Fig. 1

Fig. 2

#127281@500ms

#127267@500ms

#107714@400ms

Fig. 2