## Slide 1
Is there any confinement degradation going to NSTX-Upgrade Elongation and Aspect Ratio?
(XP-1103)
Stefan Gerhardt,…
NSTX Team Review
NSTX
Supported by
College W&M
Colorado Sch Mines
Columbia U
CompX
General Atomics
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec

## Slide 2: Big Picture Description
Aspect (A) ratio and elongation (k) are the lowest order shape parameters in a tokamak…and their impact on the ST is the focus of R11-2.
NSTX has a large database of confinement with A<1.55 and k<2.4.
  NSTX upgrade will run at larger values of both these parameters.
It is hard to scan these parameters independently in NSTX.
  Will be even harder in NSTX-U…this may be the last chance.
Propose to do three scans:
  A scan at fixed k
  k scan at fixed A
  Push to very high A and k
Goals:
  1: Confirm (or not) confinement and current drive assumptions used in Upgrade modeling.
  H98=1 is accessible?
  Ion transport remains neoclassical?
  NUBEAM+Sauter BS+Vloop analysis can predict the current profile?
  2: Determine if there is a strong A or k dependence of the above.
  3: Develop the shapes to be used in further XPs targeting R11-2, JRT, Upgrade support.

## Slide 3: Limited Data Set Last Year Showed a Reduction in Confinement When A & k Were Increased
IP=900 kA, BT=0.45 T
Some drop in bN at higher A (for fixed Pinj).
Big hit in q95. (10->7.5)
Confinement is degraded by ~10%.
  H from 1.02 to 0.85.
Te is a bit lower, which hurts the NBCD.
Data collected at the end of the run, when machine performance was sub-optimal.

## Slide 4: NSTX-U Scenarios Need H~1.0 at Higher A to Meet Aggressive Scenario Goals
Comparisons of Upgrade Scenarios To Existing Data
Effect of degraded confinement on NSTX-Upgrade 100% non-inductive scenarios.

## Slide 5: Use of SFD in NSTX-Upgrade Will Mandate High Elongation
(D)SFD Works Best with Small Top/Bottom Gaps
DN, k=2.93
DSFD, k=2.88, A=1.83
DSFD, k=3.06, A=1.89

## Slide 6: In General, It is Hard to Scan A and k Independently
Space of aspect ratio and elongation for NSTX and some proposed next step devices.
Space of aspect ratio and elongation for NSTX and interesting upgrade scenarios.

## Slide 7: Scan of Kappa At Fixed A. With Constant IP or Constant q95
Low elongation limit is set by current limit on the PF-1A coil.
  Otherwise the inner gap shrinks
  700 kA plasma need 19.6 kA of PF-1A
Chart: 
| 2.69 | 2.55 | 2.3
"PF-1A Current (kA) vs. Elongation" | 6.3 | 11.55 | 19.6
A | k | IP | q95 | IPF-1A
1.56 | 2.66 | 825 | 12.1 | 10.7
1.55 | 2.69 | 700 | 17.9 | 6.3
1.55 | 2.55 | 700 | 13.9 | 11.6
1.52 | 2.3 | 700 | 12.03 | 19.6
Scan of k at fixed A and IP

## Slide 8: Scan of A at Fixed Kappa With Constant IP or Constant q95
High aspect ratio limit set by the PF-1A coil current limit.
Chart: 
| 1.54 | 1.65 | 1.74
PF-1A Current (kA) vs. Aspect Ratio | 7 | 13.3 | 19.6
A | k | IP | q95 | IPF-1A
1.53 | 2.64 | 1000 | 9 | 18.9
1.54 | 2.7 | 700 | 18 | 7
1.65 | 2.69 | 700 | 12 | 13.3
1.74 | 2.67 | 700 | 9.5 | 19.6
Scan of A at fixed k and IP
700 & 1000 kA

## Slide 9: Maximal Aspect Ratio and Kappa Can Be Studied.
Three cases here
  k=2.8, A=1.75,IP=750 kA shape typical of fni=1 in NSTX-upgrade. 15 cm outer gap. (Should get this in the other scans)
  k=2.95, A=1.81, IP=750 kA shape typical of high-bT in NSTX-upgrade. 20 cm outer gap helps elevate qmin at high IN.
  k=3.1, A=1.81, IP=850 kA shape with 20 cm outer gap…a shape approaching the needs of next-step STs. For k>3, should we minimize the inner or outer gap? Trade aspect ratio against proximity to plates? May get some indication in A scans.

## Slide 10: Shapes In Study Are Designed to Mimic Upgrade Scenarios Proposed Shape NSTX-Upgrade Scenarios
A=1.8
k=2.95
High-bT optimization
Maximize Off Axis NBCD
A=1.75
k=2.8
fNI=1 optimization