| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: Controlled lithium introduction with Mo tiles |
| OP-XP-1133 | Revision: | Effective Date: (Approval date unless otherwise stipulated) Expiration Date: (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Responsible Author: R. Maingi | Date |
| ATI – ET Group Leader: C. Skinner | Date |
| RLM - Run Coordinator: S. Sabbagh | Date |
| Responsible Division: Experimental Research Operations |
| RESTRICTIONS or MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

| TITLE: Controlled lithium introduction with Mo tiles | No. OP-XP-1133 |
| --- | --- |
| AUTHORS: R. Maingi, the LRTSG group members | DATE: June 9, 2011 |

# 1.	Overview of planned experiment

The goal of this experiment is to introduce lithium in a controlled manner for the 2011-2012 run, as done in the 2008 and 2009 runs.  The dependence of discharges on amount of lithium evaporation will be thoroughly documented. This experiment will mesh with the discharge development XMP as much as practical.

# 2.	Theoretical/ empirical justification

The controlled introduction of lithium in 2008 provided substantial insight into lithium effects, as well as a number of refereed journal articles.  To the extent possible, we will add lithium to discharges methodically to document the effects of the new Mo tiles. Comparison will be made with the 2009 data at high triangularity, and also to the 2008 data at lower triangularity.

# 3.	Experimental run plan

1. Start with a high triangularity 4 MW fiducial with no lithium, or 50 mg at most. If the pre-requisite XMP did not achieve pre-lithium discharges with 100-200 ms flat-top, try again at this point for the no-lithium reference points with 6.5 minutes of HeGDC between. Repeat ~ 4 times, making adjustments to LFS and HFS gas if needed. Do at least 2 identical discharges before moving to next step.  If the first set of discharges had 0 lithium, then repeat this step with 50mg between discharges for ~ 5 discharges.

2. Increase inter-discharge lithium evaporation to 100 mg, and repeat as above, for 4-5 discharges.

3. Increase inter-discharge lithium evaporation to 150-200 mg, and repeat as above, for 4-5 discharges. The amount to use will be a control room decision, based on discharge characteristics.

4. Increase inter-discharge lithium evaporation to 250-300 mg, and repeat as above, for 4-5 discharges. The amount to use will be a control room decision, based on discharge characteristics.

5. Time permitting, repeat with an even higher evaporation of ~ 500mg, and repeat ~ 5 discharges.

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

Up to 6 MW NBI, no rf, no CHI. Nominally plan for 4-5 MW NBI.

# 5.	Planned analysis

EFIT, TRANSP, and pedestal/stability analysis.

# 6.	Planned publication of results

Results allowing, this will be published at the next PSI meeting.

PHYSICS OPERATIONS REQUEST

| TITLE: Controlled lithium introduction with Mo tiles | No. OP-XP-1133 |
| --- | --- |
| AUTHORS: R. Maingi, the LRTSG group members | DATE: June 9, 2011 |

Brief description of the most important operational plasma conditions required: High delta fiducial with 4 MW NBI. Option to use 5 MW if better for pre-lithium discharge performance.

Previous shot(s) which can be repeated: Previous shot(s) which can be modified:

Machine conditions (specify ranges as appropriate, strike out inapplicable cases) ITF (kA): 4.5 kG Flattop start/stop (s): IP (MA): 0.9 MA Flattop start/stop (s): Configuration: Limiter / DN / LSN / USN: LSN drsep=-5mm Equilibrium Control: Outer gap / Isoflux (rtEFIT) / Strike-point control (rtEFIT) Outer gap (m): 8-10cm Inner gap (m): Z position (m): Elongation: 2.4 Triangularity (U/L): 0.8 OSP radius (m): Gas Species: D Injector(s): NBI Species: D Voltage (kV) A: 90 B: 90 C: 70-90 Duration (s): ICRF Power (MW): Phase between straps (°): Duration (s): CHI: Off / On Bank capacitance (mF): LITERs: Off / On Total deposition rate (mg/min): LLD: Temperature (°C): EFC coils: Off/On Configuration: Odd / Even / Other

DIAGNOSTIC CHECKLIST

| TITLE: Controlled lithium introduction with Mo tiles | No. OP-XP-1133 |
| --- | --- |
| AUTHORS: R. Maingi, the LRTSG group members | DATE: June 9, 2011 |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| Beam Emission Spectroscopy |  |  |
| Bolometer – divertor |  |  |
| Bolometer – midplane array |  | √ |
| CHERS – poloidal |  | √ |
| CHERS – toroidal | √ |  |
| Divertor L-alpha array |  | √ |
| Divertor visible camera |  | √ |
| Dust detector |  |  |
| Edge deposition monitors |  | √ |
| Edge neutral density diag. |  |  |
| Edge pressure gauges |  | √ |
| Edge rotation diagnostic |  |  |
| Fast cameras – divertor/LLD |  | √ |
| Fast ion D_alpha - poloidal |  |  |
| Fast ion D_alpha - toroidal |  |  |
| Fast lost ion probes - IFLIP |  |  |
| Fast lost ion probes - SFLIP |  |  |
| Filterscopes | √ |  |
| FIReTIP |  | √ |
| Gas puff imaging – divertor |  |  |
| Gas puff imaging – midplane |  | √ |
| H camera - 1D |  | √ |
| High-k scattering |  |  |
| Infrared camera – standard |  |  |
| Infrared camera – 2-color |  | √ |
| Infrared camera – wide-angle |  | √ |
| Interferometer - 1 mm |  |  |
| Langmuir probes – divertor |  | √ |
| Langmuir probes – LLD |  | √ |
| Langmuir probes – bias tile |  |  |
| Langmuir probes – RF ant. |  |  |
| Magnetics – B coils | √ |  |
| Magnetics – Diamagnetism | √ |  |
| Magnetics – Flux loops | √ |  |
| Magnetics – Locked modes |  | √ |
| Magnetics – Rogowski coils | √ |  |
| Magnetics – Halo currents |  |  |
| Magnetics – RWM sensors |  | √ |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| MAPP |  |  |
| Mirnov coils – high f. |  | √ |
| Mirnov coils – poloidal array |  | √ |
| Mirnov coils – toroidal array |  | √ |
| Mirnov coils – 3-axis proto. |  |  |
| MSE-CIF |  | √ |
| MSE-LIF |  |  |
| NPA – E¦¦B scanning |  |  |
| NPA – solid state |  |  |
| Neutron detectors |  |  |
| Plasma TV |  | √ |
| Reflectometer – 65GHz |  |  |
| Reflectometer – correlation |  |  |
| Reflectometer – FM/CW |  |  |
| Reflectometer – fixed f |  |  |
| Reflectometer – SOL |  |  |
| RF edge probes |  |  |
| Spectrometer – divertor |  |  |
| Spectrometer – SPRED |  | √ |
| Spectrometer – VIPS |  |  |
| Spectrometer – LOWEUS |  |  |
| Spectrometer – XEUS |  |  |
| SWIFT – 2D flow |  |  |
| TAE Antenna |  |  |
| Thomson scattering | √ |  |
| USXR – pol. arrays |  | √ |
| USXR – multi-energy |  |  |
| USXR – TG spectr. |  |  |
| Visible bremsstrahlung det. |  | √ |
| X-ray crystal spectrom. - H |  |  |
| X-ray crystal spectrom. - V |  |  |
| X-ray tang. pinhole camera |  |  |