| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: Low Plasma Current, Fully Non-Inductive, HHFW H-Mode Plasmas |
| OP-XP-1160 | Revision: 3 | Effective Date: (Approval date unless otherwise stipulated) Expiration Date: (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Responsible Author: G. Taylor | Date |
| ATI – ET Group Leader: G. Taylor/R. Raman | Date |
| RLM - Run Coordinator: S. Sabbagh | Date |
| Responsible Division: Experimental Research Operations |
| RESTRICTIONS or MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

| TITLE: Low Plasma Current, Fully Non-Inductive, HHFW H-Mode Plasmas | No. OP-XP-1160 |
| --- | --- |
| AUTHORS: G. Taylor, D. Mueller, S. Gerhardt, J.C. Hosea, C. Kessel, B.P. LeBlanc, C.K. Phillips, S. Zweben, R. Raman, R. Maingi, P.M. Ryan | DATE: May 25, 2011 |

# 1.	Overview of planned experiment

HHFW heating and current drive may enable fully non-inductive plasma current (Ip) ramp-up in NSTX. The initial approach to achieving this goal has been to heat low plasma current (Ip = 250-350 kA) inductive plasmas with HHFW power in order to generate an H-mode with significant bootstrap and RF-driven current. This experiment aims to achieve a non-inductive current fraction, fNI ≥ 1 by coupling 
3-4 MW of RF power into an Ip ~ 300 kA plasma. This experiment contributes to the NSTX research milestone R12-2.

# 2.	Theoretical/ empirical justification

TSC simulations predict that coupling 6 MW of HHFW power into the Ip ramp-up can result in bootstrap current overdrive. In 2005 (XP-521) 2.5 MW of kf = 14 + 18 m-1 HHFW power (heating antenna phasing) was coupled into an Ip = 250 kA deuterium plasma, but RF coupling could not be maintained when the plasma transitioned to H-mode due to poor plasma position control. In 2010 HHFW experiments with 
Ip = 300 kA plasmas (XP-1009) coupled 1.4 MW of kf = -8 m-1 HHFW power (current drive antenna phasing) producing a sustained H-mode with an internal transport barrier (ITB) and achieving an 
fNI ~ 0.65. This positive result was the consequence of better plasma control, improved RF coupling due to Li conditioning, and the positive feedback between the generation of the ITB, a high Te(0) ~ 3 keV, and a relatively high RF current drive efficiency ~ 0.1 MA/MW. However, the RF antenna was poorly conditioned so that the maximum arc-free HHFW power was only ~ 1.4 MW, insufficient to achieve an fNI ≥ 1 at Ip ~ 300 kA. Also, source A was not available to provide beam blips for documenting the evolution of q(R) and Ti.

# 3.	Experimental run plan

The plan is to start with the best HHFW-heated Ip = 300 kA plasma from XP-1009 (shot 138506) using 
kf = -8 m-1 HHFW power (-90o current drive antenna phasing). The HHFW heating pulse will be started as early as possible in order to maintain the HHFW heating for at least a current relaxation time (~ 200 ms). Once significant HHFW power is reliably being coupled into the plasma, the q(R) and Ti evolution will be documented with source A beam blips stepped through the discharge. If it proves difficult to control the 
Ip = 300 kA discharge at high HHFW powers, Ip will be increased to ~ 350 kA. If reproducible 
Ip ~ 300 kA discharges with significant (3-4 MW) HHFW power can be produced, Ip will be reduced to 
~ 250 kA. If time permits, experiments will be repeated with -60o antenna phasing (kf = -3 m-1 + 
kf = -8 m-1). This experiment is expected to take 1-1.5 run days to complete.

The run plan is as follows:

- Setup an ohmically-heated Ip = 300 kA deuterium discharge similar to shot 138506. 
Add kf = -8 m-1 HHFW power (-90o antenna phasing), coupled from 150 to 450 ms, with a 50 ms ramp-up in power at the start of the RF pulse. Increase PRF to 3-4 MW, while adjusting the lithium evaporation rate, the gas injection rate and the outer gap to optimize HHFW heating efficiency.  A 50 ms beam pulse for MSE q(R) and CHERS Ti(R) will be injected from 430 to 480 ms (Fig. 1). (5-10 shots)

Figure 1: Schematic of the HHFW and NBI pulse timing for step 1.

- Move the start of the HHFW pulse as early as possible while maintaining good coupling to the plasma. A 50 ms beam pulse for MSE and CHERS will be injected from 430 to 480 ms (Fig. 2). 
(5 shots)

Figure 2: Schematic of the HHFW and NBI pulse timing for step 2.

- When reproducible plasmas have been obtained a 20 ms beam blip will be stepped from 400 ms to 200 ms (Fig. 3) over a sequence of 5 shots to acquire the time evolution of q(R) and Ti(R). If it proves difficult to control the Ip = 300 kA plasma during HHFW heating Ip will be increased to 
~ 350 kA. (5 shots)

- If 1-3 are successful, reduce Ip to 250 kA and couple 3-4 MW of kf = -8 m-1 HHFW power. Measure q(r) and Ti(R) as in step 2 and 3. (15 shots)

Figure 3: Schematic of the HHFW and NBI pulse timing for step 3.

- If not already attempted, some shots with Ip increased to 350kA will be run, in preparation for 
XP-1159. (3-5 shots)

- Repeat steps 1-3 with -60o antenna phasing. (15 shots)

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

This experiment should follow the HHFW plasma conditioning XMP, and requires PRF = 3-4 MW at 
-90o and -60o antenna phasing, although it could still be scheduled if only 2.5 MW is available, since this is significantly more power than was used in XP-1009. This experiment requires rtEFIT isoflux control for the outer gap, and a LiTER deposition rate sufficient to maintain good RF coupling. 20-50 ms 90 keV NBI blips are required from source A for MSE q(r) and CHERS Ti(R) data. Thomson scattering Te(R) and ne(R) data are required for core and edge electron heating analysis. For analysis of edge power loss and coupling efficiency the experiment requires SOL reflectometry and edge ion heating data from the edge rotation diagnostic. Visible and IR camera imaging of the antenna and lower divertor are also required.

# 5.	Planned analysis

The RF deposition, bootstrap current and rf–driven current profile will be calculated by TRANSP-TORIC and GENRAY-ADJ.

# 6.	Planned publication of results

The results will be submitted for publication in Physical Review Letters, Nuclear Fusion or Physics of Plasmas, and may contribute to an HHFW IAEA paper.

PHYSICS OPERATIONS REQUEST

| TITLE: Low Plasma Current, Fully Non-Inductive, HHFW H-Mode Plasmas | No. OP-XP-1160 |
| --- | --- |
| AUTHORS: G. Taylor, D. Mueller, S. Gerhardt, J.C. Hosea, C. Kessel, B.P. LeBlanc, C.K. Phillips, S. Zweben, R. Raman, R. Maingi, P.M. Ryan | DATE: May 25, 2011 |

Brief description of the most important operational plasma conditions required: Stable plasma operation at Ip = 250-350 kA, with reproducible outer gap = 0.05 – 0.1 m. Request D. Mueller as operator.

Previous shot(s) which can be repeated: 138506 Previous shot(s) which can be modified:

Machine conditions (specify ranges as appropriate, strike out inapplicable cases) ITF (kA): 66 Flattop start/stop (s): 0/0.7 IP (MA): 0.25-0.35 Flattop start/stop (s): 0.08/0.6 Configuration: LSN Equilibrium Control: Outer gap / Isoflux (rtEFIT) / Strike-point control (rtEFIT) Outer gap (m): 0.05-0.08 Inner gap (m): Z position (m): 0.0 Elongation: Triangularity (U/L): OSP radius (m): Gas Species: D Injector(s): NBI Species: D Voltage (kV) A: 90 B: C: Duration (s): 480-550 ms, and 20 ms blip stepped between 200 to 400 ms from shot to shot ICRF Power (MW): 2.5-4 Phase between straps (°):-60, -90 Duration (s): 0.35 CHI: Off Bank capacitance (mF): LITERs: On Total deposition rate (mg/min): 20 mg/min to start, adjust as needed LLD: N/A Temperature (°C): EFC coils: Off Configuration: Odd / Even / Other

DIAGNOSTIC CHECKLIST

| TITLE: Low Plasma Current, Fully Non-Inductive, HHFW H-Mode Plasmas | No. OP-XP-1160 |
| --- | --- |
| AUTHORS: G. Taylor, D. Mueller, S. Gerhardt, J.C. Hosea, C. Kessel, B.P. LeBlanc, C.K. Phillips, S. Zweben, R. Raman, R. Maingi, P.M. Ryan | DATE: May 25, 2011 |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| Beam Emission Spectroscopy |  |  |
| Bolometer – divertor | √ |  |
| Bolometer – midplane array | √ |  |
| CHERS – poloidal | √ |  |
| CHERS – toroidal | √ |  |
| Dust detector |  |  |
| Edge deposition monitors |  |  |
| Edge neutral density diag. |  | √ |
| Edge pressure gauges |  | √ |
| Edge rotation diagnostic | √ |  |
| Fast cameras – divertor/LLD | √ |  |
| Fast ion D_alpha - FIDA |  |  |
| Fast lost ion probes - IFLIP |  |  |
| Fast lost ion probes - SFLIP |  |  |
| Filterscopes | √ |  |
| FIReTIP |  | √ |
| Gas puff imaging – divertor |  |  |
| Gas puff imaging – midplane |  | √ |
| H camera - 1D |  | √ |
| High-k scattering |  |  |
| Infrared cameras | √ |  |
| Interferometer - 1 mm |  | √ |
| Langmuir probes – divertor |  | √ |
| Langmuir probes – LLD |  |  |
| Langmuir probes – bias tile |  | √ |
| Langmuir probes – RF ant. |  | √ |
| Magnetics – B coils | √ |  |
| Magnetics – Diamagnetism | √ |  |
| Magnetics – Flux loops | √ |  |
| Magnetics – Locked modes | √ |  |
| Magnetics – Rogowski coils | √ |  |
| Magnetics – Halo currents | √ |  |
| Magnetics – RWM sensors | √ |  |
| Mirnov coils – high f. | √ |  |
| Mirnov coils – poloidal array | √ |  |
| Mirnov coils – toroidal array | √ |  |
| Mirnov coils – 3-axis proto. | √ |  |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| MSE | √ |  |
| NPA – E¦¦B scanning |  |  |
| NPA – solid state |  |  |
| Neutron detectors |  |  |
| Plasma TV | √ |  |
| Reflectometer – 65GHz |  |  |
| Reflectometer – correlation |  |  |
| Reflectometer – FM/CW |  |  |
| Reflectometer – fixed f |  |  |
| Reflectometer – SOL | √ |  |
| RF edge probes | √ |  |
| Spectrometer – divertor | √ |  |
| Spectrometer – SPRED | √ |  |
| Spectrometer – VIPS | √ |  |
| Spectrometer – LOWEUS |  |  |
| Spectrometer – XEUS |  | √ |
| SWIFT – 2D flow |  |  |
| Thomson scattering | √ |  |
| Ultrasoft X-ray – pol. arrays | √ |  |
| Ultrasoft X-rays – bicolor | √ |  |
| Ultrasoft X-rays – TG spectr. |  |  |
| Visible bremsstrahlung det. | √ |  |
| X-ray crystal spectrom. - H |  |  |
| X-ray crystal spectrom. - V |  |  |
| X-ray tang. pinhole camera |  |  |