Comparison of MAST and NSTX Engineering Parameters

| Parameter | MAST | NSTX |
| --- | --- | --- |
| Plasma parameters |  |  |
| Aspect ratio | >1.3 | >1.26 |
| Major radius R0 | 0.7m | 0.854m |
| Maximum plasma current | 2.0MA | 1.0MA |
| Flat top pulse length (inductive) | 0.5s | 0.5s |
| Flat top pulse length(non-inductive) | 5.0s | 5.0s |
| Elongation | <2.4 | 1.6-2.2 |
| Triangularity | 0.45 | 0.2-0.5 |
| Toroidal field at R0 | 0.62T | 0.3T (0.6T) |
| OH solenoid double flux swing | 1.0V-s | 0.9V-s |
| Initial plasma formation | Induction-compression ~500kA | Coaxial helicity injection ~ 500kA |
| Pre-ionisation | filaments | electron cyclotron |
| Neutral beam injection | <5.0MW | <5.0MW |
| RF heating | ECRH 1.0MW | HHFW 6.0MW |
| Bakeout temperature | <200C | <350C PFCs 150C vessel |
| TF coil system |  |  |
| Maximum TF coil current | 91.66kA | 35.6kA (71.2kA) |
| Maximum TF coil voltage | 450V | 1kV |
| No of turns in TF coil | 24 | 36 |
| TF Inner leg construction | Extruded wedges containing single cooling channel | Extruded & machined bars. Cooling pipe soldered into slot |
| TF outer leg construction | Demountable extruded straight bars containing single cooling channel arranged in pairs | Bow shaped demountable bars arranged in 3s with a single cooling pipe soldered to each |
| TF inner leg insulation | VPI of glass tape with epoxy resin | B-stage glass/epoxy |
| Inner leg insulation thickness | 1mm | 1.625mm |
| Outer ground insulation thickness | 1.5mm | 1.727mm |
| Max shear stress on insulation | <18MPa | <13MPa |
| Maximum conductor temperature | 55C | ~70C |
| Total cooling water flow rate | 150l/min | 432 l/min |
| TF coil inductance | 1.82mH | 4.18mH |
| TF coil resistance | 2.8m( | 6.5m( |
| Strain isolation between inner and outer legs | Sliding joints | Flexible connectors |
| OH Solenoid |  |  |
| Number of turns | 304 | 962 |
| Number of layers | 4 | 4 |
| Winding configuration | Extruded conductor containing single cooling channel , wound 2-in-hand | Extruded conductor containing single cooling channel , wound 2-in-hand |
| Tail/feeder configuration | Quadrupole | Dipole |
| Inter-turn insulation | VPI of glass tape with epoxy resin | B-stage glass/Kapton/epoxy |
| Inter-turn insulation thickness | 1.0mm | 1.33mm |
| Total outer ground insul. thickness | 1.5mm | 2.03mm |
| Total inner ground insul. thickness | 2.0mm | 1.57mm |
| Axial expansion mechanism | Removeable slip plane between TF inner legs and solenoid coil | Teflon layer on stainless steel tension tube slipped over TF inner legs |
| Outer electrostatic ground plane | None | Low resistance paint |
| Thermal insulation between solenoid and centre casing | 3-4.5mm air gap | Microtherm insulation blanket |
| Max. shear stress on insulation | <10 MPa | 6.6 MPa |
| Max. tensile stress on insulation | <14 MPa | 14.7 MPa |
| Maximum conductor hoop stress | 100 MPA | 136 MPa |
| Maximum conductor temperature | 60C | 80C |
| Total cooling water flow rate | 12 l/min | 22 l/min |
| Max. pressure drop across solenoid | 16 bar | 27 bar |
| Cool-down time | 780s | 600s |
| Maximum operating temperature | <300C | 600C |
| PFC material | EK98 graphite tiles | ATJ graphite and CFC tiles |
| Vacuum vessel |  |  |
| Vessel wall thickness | 20mm | 16mm |
| Vessel material | 316LN stainless steel | 304 stainless steel |
| Horizontal ports | 12 x 600mm dia. 24 x 400mm dia. | 7 x 24inch dia 2 x non circular 3 x 16.5 inch dia. 26 x 4 inch dia. |
| Vertical ports | 36 x 150mm dia. 12 x 64mm dia. | 20 x 16.5 inch dia. |
| Port seals | Conflat flanges | Conflat flanges |
| End flange seals | Double polymer O-rings with interspace pumping | Helica-flex seals |
| Outer thermal insulation | 50mm blanket | 2 inch blanket + 0.5 inch silicone foam |
| Centre column casing and PFC |  |  |
| Casing material | Inconel 625 | Inconel |
| Heating method during bakeout | 50Hz AC induction from solenoid | DC current heating |
| Maximum operating temperature | <300C | 600C |
| PFC material | EK98 graphite tiles | ATJ graphite and CFC tiles |