MAST Upgrade Plans

NSTX/MAST Engineering Workshop

Princeton Plasma Physics Laboratory

21-24 September 2001

Garry Voss

MAST Upgrades

Short term

( New Centre column is being manufactured.

Completion expected Christmas 2001

Solenoid is ~10% longer than first centre column.

Solenoid design incorporates revised end-turn

design.

( Move P2 coils apart to match increased solenoid

length.

( New divertor structure is being designed and

manufactured, for installation summer 2002,

which has a higher power handling capability.

( EBW antenna is being manufactured for installation summer 2002 (possibly before).

( New source/accelerator currently being installed

on NBI system.

Test deuterium operation at up 60 kV in Oct.

1.5MW from each NBI expected next spring

Long term

Long term upgrades are focussed on:

increased elongation

increased pulse duration

methods of start-up and current ramp up

New Divertor Structure