13-010514-CLN-01

# TO: DISTRIBUTION

FROM: C NEUMEYER

SUBJECT: TF FLAT TOP TIME LIMITATIONS

In order to reduce the risk of TF water leaks, it has been decided to limit the operation of the TF system in such a way that the peak current and flat top time are only has high as they need be to satisfy the minimum components of the near term mission. It is been judged that a peak field of 4.5kG and a maximum adiabatic temperature rise of 30oC are appropriate limits to impose at this time.

On this basis the maximum prospective ∫i2(t)dt needs to be limited to 2.64e9A2-sec. To ensure that this level is not exceeded even at the maximum permitted current, the I2T protective device must be set to trip with anticipation of the L/R decay from that current. Furthermore, to avoid a trip of the protective device during each pulse, the nominal waveform must be design such that, following the current shutdown driven by the power supply, the final ∫i2(t)dt value does not exceed the trip setting.

Relevant calculations are given in the following table. It is noted that the RIS I2T setting shall be 1.85e9 A2-sec, and that at 4.5kG the available flat top time is 442mS. This could be increased to approximately 500mS without exceeding the thermal limit but the protective device would then trip every pulse. Furthermore, it is noted that if we do not experience a trip from full current, then the ∆T will only be around 20oC.

| Iflat | 53400 | Amp |
| --- | --- | --- |
| Tau | 0.369 | sec |
| ∆Tallow | 30 | degC |
| T0 | 12 | degC |
| Tallow | 42 | degC |
| Gallow | 8.3488E+15 | (A/m^2)^2-sec |
| G0 | 2.53E+15 | (A/m^2)^2-sec |
| ∆Gallow | 5.82E+15 | (A/m^2)^2-sec |
| I2Tallow | 2.64E+09 | A^2-sec |
| Trise | 0.361 | sec |
| I2T Rise | 4.31E+08 | A^2-sec |
| I2T L/R | 7.98E+08 | A^2-sec |
| I2Tflatmax | 1.42E+09 | A^2-sec |
| Tflatideal | 4.96E-01 | sec |
| I2TEOFT (Trip) | 1.85E+09 | A^2-sec |
| Tfall | 0.246 | sec |
| I2T Fall | 1.55E+08 | A^2-sec |
| I2Tflat no-trip | 1.26E+09 | A^2-sec |
| Tflatmax no-trip | 0.442 | sec |
| Nominal I2T | 1.85E+09 | A^2-sec |
| TEOP nominal | 3.25E+01 | degC |
| ∆T nominal | 2.05E+01 | degC |

Available flat top times at other field levels are given in the following table and figure.

Tflat (sec) vs. Bt vs. ∆T (degC)

| ∆Tmax (degC) | 20 | 25 | 30 | 35 | 40 | 45 |
| --- | --- | --- | --- | --- | --- | --- |
| 4.5kG | 0.142 | 0.293 | 0.442 | 0.588 | 0.733 | 0.875 |
| 4.0kG | 0.855 | 1.046 | 1.234 | 1.419 | 1.602 | 1.782 |
| 3.5kG | 1.283 | 1.533 | 1.779 | 2.021 | 2.259 | 2.494 |
| 3.0kG | 1.924 | 2.264 | 2.598 | 2.928 | 3.252 | 3.572 |

cc:

E Baker	M Bell 	W Blanchard	R Camp	D Gates	R Hatcher

S Kaye		R Marsala	J Menard	D Mueller 	M Ono

S Ramakrishnan	E Synakowski		A Von Halle	M Williams	NSTX File