# 13-020227-CLN-01

# TO: R WOOLLEY

# FROM: C NEUMEYER

# SUBJECT: NSTX OH CURRENT INCREMENT DUE TO PLASMA DISRUPTION

Reference: NSTX-CALC-11-08 “Plasma Disruption Calculation”

Per our discussion I report herein the results of my simulation of the effect of a plasma disruption on the OH current, using LRSIM. The methodology is identical to that described in the reference, except that the OH coil is short circuited.

Assumptions:

- Ip decay from 1.5MA to 0 in 9ms

- Plasma represented by two cylindrical conductors r=0.8m, z=+/-0.6m, a=0.6m

- OH, PF3, PF5 short circuited

- PF1A, PF2 open circuited

- Vacuum vessel (VV), center stack  casing (CSC), inboard divertor horizontal (IBDH) and vertical (IBDV), outboard divertor (OBD), secondary passive plate (SPP), and primary passive plate (PPP) represented by a total of 66 filaments

Results:

The following graphs show the current waveforms. The increment in OH current is approximately 1.1kA.

## Passive Structure Currents (summed over half plane) and OH current

Coil Currents

OH Coil Current