13_031022_CLN_01.doc

TO: DISTRIBUTION

FROM: C NEUMEYER

SUBJECT: TF TURN-TURN VOLTAGES

Winding pattern at the top of the machine, viewed from above, is shown in the following figure.

The following matrix shows the voltages between the turns, in per unit of total applied voltage. Row at bottom is the maximum of voltage which turn (identified by column number) faces. Turn 23 sees the minimum turn-turn voltage.

The same result is plotted in the following figure.

Based on these results the following recommendations are made:

- Following the final ground insulation curing process, low voltage (250V) megger readings should be taken from each turn to the remaining turns jumpered and grounded, to determine the relative leakage currents through the turn insulation.

- Clocking of center stack, which determines how the turns appear in series sequence, should be optimized so that turns with high leakage readings are placed in positions with minimal turn-turn voltage. Per the results above, turn 23 sees the lowest voltage.

- Once the clocking plan is established, turn-turn test voltages can be customized based on the series sequence. Since the TF power supply applies E=1kV to the coil, the base test voltage is 2E+1=3kV. Then, based on the results above, the fraction of the 3kV, and the actual test voltage, to be applied to each turn, with the other turns jumpered and grounded, is given in the following table.

| Turn | Vfraction | Vtest |
| --- | --- | --- |
| 1 | 0.972 | 2917 |
| 2 | 0.944 | 2833 |
| 3 | 0.917 | 2750 |
| 4 | 0.861 | 2583 |
| 5 | 0.833 | 2500 |
| 6 | 0.778 | 2333 |
| 7 | 0.75 | 2250 |
| 8 | 0.694 | 2083 |
| 9 | 0.667 | 2000 |
| 10 | 0.611 | 1833 |
| 11 | 0.583 | 1750 |
| 12 | 0.528 | 1583 |
| 13 | 0.5 | 1500 |
| 14 | 0.444 | 1333 |
| 15 | 0.417 | 1250 |
| 16 | 0.361 | 1083 |
| 17 | 0.333 | 1000 |
| 18 | 0.278 | 833 |
| 19 | 0.25 | 750 |
| 20 | 0.194 | 583 |
| 21 | 0.167 | 500 |
| 22 | 0.111 | 333 |
| 23 | 0.083 | 250 |
| 24 | 0.639 | 1917 |
| 25 | 0.667 | 2000 |
| 26 | 0.167 | 500 |
| 27 | 0.25 | 750 |
| 28 | 0.333 | 1000 |
| 29 | 0.417 | 1250 |
| 30 | 0.5 | 1500 |
| 31 | 0.583 | 1750 |
| 32 | 0.667 | 2000 |
| 33 | 0.75 | 2250 |
| 34 | 0.833 | 2500 |
| 35 | 0.917 | 2750 |
| 36 | 0.972 | 2917 |

Cc: 	J Chrzanowski	     P Heitzenroeder	T Meighan	M Ono	    M Williams