13_031106_CLN_01.doc

TO: DISTRIBUTION

FROM: C NEUMEYER

SUBJECT: OPTIMIZATION OF CLOCKING OF TF BUNDLE

Reference: 13_031022_CLN_01.doc

In the reference memo, the pattern of voltages appearing turn-turn in the TF bundle was reported. In this memo, based on the leakage current measurements reported in run copy of D-NSTX-IP-2845, taken on various dates after semi-cure of the quadrants, along with the voltages reported in the reference, a clocking of the bundle is selected which minimizes the sum of the ratios of voltage to leakage resistance, i.e. the sum of the leakage currents. In this way the risk of insulation failure should be minimized.

Winding pattern at the top of the machine, viewed from above, is shown in the following figure. Numbers refer to the series electrical sequence of the turns.

The following table shows the optimum clocking and the basis for same. Nsn refers to the serial number of the turn. R is the measured leakage resistance per the test procedure run copy. V is the highest voltage between the turn and its neighbors when normal operating voltage of 1kV is applied to the coil terminals. I = V/R is the corresponding leakage current. The turns which fell below spec (1000Mohm) are highlighted.

| Nsn | R(Mohm) | Ns | V(kV) | I(microAmp) |
| --- | --- | --- | --- | --- |
| 19 | 30000 | 11 | 0.583 | 0.019 |
| 15 | 36000 | 12 | 0.528 | 0.015 |
| 34 | 36000 | 13 | 0.500 | 0.014 |
| 16 | 3000 | 14 | 0.444 | 0.148 |
| 27 | 48000 | 15 | 0.417 | 0.009 |
| 37 | 60000 | 16 | 0.361 | 0.006 |
| 13 | 36000 | 17 | 0.333 | 0.009 |
| 23 | 48000 | 18 | 0.278 | 0.006 |
| 33 | 48000 | 19 | 0.250 | 0.005 |
| 17 | 36000 | 20 | 0.194 | 0.005 |
| 35 | 42000 | 21 | 0.167 | 0.004 |
| 36 | 200 | 22 | 0.111 | 0.556 |
| 30 | 30000 | 23 | 0.083 | 0.003 |
| 22 | 1800 | 24 | 0.639 | 0.355 |
| 29 | 30000 | 1 | 0.972 | 0.032 |
| 18 | 42000 | 2 | 0.944 | 0.022 |
| 20 | 42000 | 3 | 0.917 | 0.022 |
| 21 | 30000 | 4 | 0.861 | 0.029 |
| 31 | 30000 | 5 | 0.833 | 0.028 |
| 25 | 35000 | 6 | 0.778 | 0.022 |
| 28 | 40000 | 7 | 0.750 | 0.019 |
| 24 | 45000 | 8 | 0.694 | 0.015 |
| 26 | 45000 | 9 | 0.667 | 0.015 |
| 14 | 40000 | 10 | 0.611 | 0.015 |
| 5 | 45000 | 32 | 0.667 | 0.015 |
| 6 | 45000 | 33 | 0.750 | 0.017 |
| 4 | 45000 | 34 | 0.833 | 0.019 |
| 2 | 42000 | 35 | 0.917 | 0.022 |
| 3 | 48000 | 36 | 0.972 | 0.02 |
| 1 | 600 | 25 | 0.667 | 1.111 |
| 7 | 100 | 26 | 0.167 | 1.667 |
| 12 | 54000 | 27 | 0.250 | 0.005 |
| 11 | 42000 | 28 | 0.333 | 0.008 |
| 10 | 36000 | 29 | 0.417 | 0.012 |
| 9 | 2400 | 30 | 0.500 | 0.208 |
| 8 | 36000 | 31 | 0.583 | 0.016 |
|  |  |  |  | 4.492 |

The sum of the leakages from all turns is given in the last row of the last column of the table. The clocking shown above was found to result in the lowest total leakage sum, which represents the best compromise of voltage and resistance, considering all turns. If only the turns which fell out of spec are considered, the same clocking again gives the best result. If only the worst turn sn#7 is considered then the best result would place that turn in series sequence 23, which has the lowest voltage. However, when the other turns are considered, the optimum shifts as indicated.

Based on the concept of selecting the turn-turn test voltage based on the fraction of operating voltage appearing on the turns, the following table shows the hipot voltage and leakage current for each turn, with the base hipot level set by 2E+1=2*1+1=3kV.

| Nsn | R(Mohm) | Ns | Vtest(kV) | I(microAmp) |
| --- | --- | --- | --- | --- |
| 19 | 30000 | 11 | 1.750 | 0.058 |
| 15 | 36000 | 12 | 1.583 | 0.044 |
| 34 | 36000 | 13 | 1.500 | 0.042 |
| 16 | 3000 | 14 | 1.333 | 0.444 |
| 27 | 48000 | 15 | 1.250 | 0.026 |
| 37 | 60000 | 16 | 1.083 | 0.018 |
| 13 | 36000 | 17 | 1.000 | 0.028 |
| 23 | 48000 | 18 | 0.833 | 0.017 |
| 33 | 48000 | 19 | 0.750 | 0.016 |
| 17 | 36000 | 20 | 0.583 | 0.016 |
| 35 | 42000 | 21 | 0.500 | 0.012 |
| 36 | 200 | 22 | 0.333 | 1.667 |
| 30 | 30000 | 23 | 0.250 | 0.008 |
| 22 | 1800 | 24 | 1.917 | 1.065 |
| 29 | 30000 | 1 | 2.917 | 0.097 |
| 18 | 42000 | 2 | 2.833 | 0.067 |
| 20 | 42000 | 3 | 2.750 | 0.065 |
| 21 | 30000 | 4 | 2.583 | 0.086 |
| 31 | 30000 | 5 | 2.500 | 0.083 |
| 25 | 35000 | 6 | 2.333 | 0.067 |
| 28 | 40000 | 7 | 2.250 | 0.056 |
| 24 | 45000 | 8 | 2.083 | 0.046 |
| 26 | 45000 | 9 | 2.000 | 0.044 |
| 14 | 40000 | 10 | 1.833 | 0.046 |
| 5 | 45000 | 32 | 2.000 | 0.044 |
| 6 | 45000 | 33 | 2.250 | 0.05 |
| 4 | 45000 | 34 | 2.500 | 0.056 |
| 2 | 42000 | 35 | 2.750 | 0.065 |
| 3 | 48000 | 36 | 2.917 | 0.061 |
| 1 | 600 | 25 | 2.000 | 3.333 |
| 7 | 100 | 26 | 0.500 | 5.000 |
| 12 | 54000 | 27 | 0.750 | 0.014 |
| 11 | 42000 | 28 | 1.000 | 0.024 |
| 10 | 36000 | 29 | 1.250 | 0.035 |
| 9 | 2400 | 30 | 1.500 | 0.625 |
| 8 | 36000 | 31 | 1.750 | 0.049 |

Finally, it is recommended that another set of leakage resistance readings be taken at a low voltage, e.g. 250V, prior to finalizing the clocking. The reason is to determine whether or not the pattern observed is still in effect after completing the cure of the bundle. If it is substantially different, then the exercise described herein should be repeated.

Cc: 	J Chrzanowski	     P Heitzenroeder	T Meighan	M Ono	    M Williams