13-040507-CLN-01

TO: DISTRIBUTION

FROM: C NEUMEYER
SUBJECT:  PF4 & 5 ALLOWABLE CURRENTS WITH EXISTING STRUCTURE

References:

[1] 13-040505-CLN-01, “Preliminary Analysis of PF4 Energization”, C. Neumeyer

Based on the analysis presented in [1] the magnitude of the axial force on PF4 (directed away from the midplane) can be calculated per the expression below and should be limited to ≤ 45400lbf in order to maintain a safety factor of 1.5 on the mechanical loading of the PF4 support pad studs, assuming that the existing support structure is retained and not improved.

Allowable PF4 and PF5 currents based on the above are listed in the following tabular array. The column headings are IPF5 in kA (positive values), and the row headings are IPF4 in kA (negative values). For those combinations which satisfy FzPF4 ≤ 45400lbf the array elements are filled in with the calculated value of the force. For those combinations which would produce excessive force, the elements are blank.

|  | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| -1 | 2994 | 4251 | 5508 | 6764 | 8021 | 9278 | 10535 | 11792 | 13048 | 14305 |
| -2 | 5884 | 8398 | 10911 | 13425 | 15939 | 18452 | 20966 | 23479 | 25993 | 28507 |
| -3 | 8671 | 12441 | 16211 | 19982 | 23752 | 27523 | 31293 | 35063 | 38834 | 42604 |
| -4 | 11353 | 16380 | 21408 | 26435 | 31462 | 36489 | 41516 |  |  |  |
| -5 | 13932 | 20216 | 26500 | 32784 | 39068 | 45352 |  |  |  |  |
| -6 | 16407 | 23948 | 31489 | 39029 |  |  |  |  |  |  |
| -7 | 18778 | 27576 | 36373 | 45171 |  |  |  |  |  |  |
| -8 | 21046 | 31100 | 41154 |  |  |  |  |  |  |  |
| -9 | 23209 | 34520 |  |  |  |  |  |  |  |  |
| -10 | 25269 | 37837 |  |  |  |  |  |  |  |  |
| -11 | 27225 | 41050 |  |  |  |  |  |  |  |  |
| -12 | 29077 | 44159 |  |  |  |  |  |  |  |  |
| -13 | 30826 |  |  |  |  |  |  |  |  |  |
| -14 | 32470 |  |  |  |  |  |  |  |  |  |
| -15 | 34011 |  |  |  |  |  |  |  |  |  |
| -16 | 35448 |  |  |  |  |  |  |  |  |  |
| -17 | 36781 |  |  |  |  |  |  |  |  |  |
| -18 | 38011 |  |  |  |  |  |  |  |  |  |
| -19 | 39136 |  |  |  |  |  |  |  |  |  |
| -20 | 40158 |  |  |  |  |  |  |  |  |  |

Please note that the current polarities correspond to the engineering convention (clockwise viewed from above),  and that the above is consistent with the present operating limits set on the other NSTX PF coils.

Under the above conditions, the safety factor on the other components of the structures of PF4 and PF5 will also be acceptable. Even if the attractive load between PF5U&L is assumed to flow 100% through the turnbuckle strut, with zero through the supports cantilevered off of the VV, the safety factor on the shear on the clevis bolt is still 1.3.

M Bell		J Chrzanowski		L Dudek	T Egebo	P Heitzenroeder

C Jun		J Menard		M Ono		S Ramakrishnan

A Von Halle	M Williams		R Woolley	I Zatz