13_041120_CLN_01.doc

TO: DISTRIBUTION

FROM: C NEUMEYER

SUBJECT: UPDATE OF NSTX INFLUENCE MATRICIES AND EM LOADS

Reference:

[1] NSTX-CALC-13-020, “PF Coil Axial and Radial Force Calculation”, R1, 5/3/4

This memo describes an analysis performed to generate influence matricies for calculation of in-plane loads on the OH and PF coils as well as the out-of-plane loads on the TF coil inner bundle elements. It supercedes the prior revision of the reference calculation, which only addressed the PF coils. In addition to the inclusion of the TF, it also includes the revised PF1a coil geometry.

As shown in figure 1, the finite element analysis program FEMLAB was used to model the PF coils using the 2-d axisymmetric magnetics mode. Subdomains were created to represent regions of the TF coil so that fields and forces could be calculated based on interaction with the OH and PF. However, the TF conductors do not effect the in-plane field calculations, which are generated only by the out-of-plane currents in OH and PF.

Figure 1 – FEMLAB Model (fields shown for the case with rated current in each coil, except PF4)

Characteristics of the PF and TF coils in each half plane are given in Table 1 below.

TABLE 1: PF Coil Summary

| Coil | R (center) | ∆R | Z (center) | ∆Z | Turns |
| --- | --- | --- | --- | --- | --- |
|  | (in) | (in) | (in) | (in) |  |
| OH | 5.2088 | 1.7335 | 41.7490 | 83.4980 | 482 |
| PF1a | 7.2403 | 1.6265 | 62.6215 | 9.1820 | 20 |
| PF1b | 11.9768 | 3.3055 | 71.8570 | 7.5030 | 32 |
| PF2a | 31.4634 | 6.4060 | 76.1225 | 2.6760 | 14 |
| PF2b | 31.4634 | 6.4060 | 72.9385 | 2.6760 | 14 |
| PF3a | 58.8370 | 7.3400 | 64.3114 | 2.6760 | 15 |
| PF3b | 58.8370 | 7.3400 | 61.1274 | 2.6760 | 15 |
| PF4b | 70.6540 | 3.6040 | 31.7800 | 2.6760 | 8 |
| PF4c | 71.1210 | 4.5380 | 34.9640 | 2.6760 | 9 |
| PF5a | 78.5280 | 5.3500 | 25.6840 | 2.6980 | 12 |
| PF5b | 78.5280 | 5.3500 | 22.7440 | 2.6980 | 12 |
| PFAB1 | 16.9530 | 0.8565 | 69.1550 | 2.6725 | 48 |
| PFAB2 | 24.8750 | 0.8565 | 75.8210 | 2.6725 | 48 |
| TF Inner | 1.1090 | 2.2180 | 55.7500 | 111.5000 | 12 |
| TF Inner Flag | 13.8590 | 20.2820 | 109.0000 | 5.0000 | 12 |
| TF Inner Flag Stub | 2.9680 | 1.5000 | 109.0000 | 5.0000 | 12 |
| TF Outer | 3.0750 | 1.5460 | 49.6875 | 99.3750 | 24 |
| TF Outer Flag | 13.9240 | 20.1520 | 96.8750 | 5.0000 | 24 |
| Coil | R (center) | ∆R | Z (center) | ∆Z | Turns |
|  | (cm) | (cm) | (cm) | (cm) |  |
| OH | 13.2302 | 4.4031 | 106.0425 | 212.0849 | 482 |
| PF1a | 18.3902 | 4.1313 | 159.0586 | 23.3223 | 20 |
| PF1b | 30.4209 | 8.3960 | 182.5168 | 19.0576 | 32 |
| PF2a | 79.9170 | 16.2712 | 193.3510 | 6.7970 | 14 |
| PF2b | 79.9170 | 16.2712 | 185.2637 | 6.7970 | 14 |
| PF3a | 149.4460 | 18.6436 | 163.3510 | 6.7970 | 15 |
| PF3b | 149.4460 | 18.6436 | 155.2637 | 6.7970 | 15 |
| PF4b | 179.4612 | 9.1542 | 80.7212 | 6.7970 | 8 |
| PF4c | 180.6473 | 11.5265 | 88.8086 | 6.7970 | 9 |
| PF5a | 199.4611 | 13.5890 | 65.2374 | 6.8529 | 12 |
| PF5b | 199.4611 | 13.5890 | 57.7698 | 6.8529 | 12 |
| PFAB1 | 43.0606 | 2.1755 | 175.6537 | 6.7882 | 48 |
| PFAB2 | 63.1825 | 2.1755 | 192.5853 | 6.7882 | 48 |
| TF Inner | 2.8169 | 5.6337 | 141.6050 | 283.2100 | 12 |
| TF Inner Flag | 35.2019 | 51.5163 | 276.8600 | 12.7000 | 12 |
| TF Inner Flag Stub | 7.5387 | 3.8100 | 276.8600 | 12.7000 | 12 |
| TF Outer | 7.8105 | 3.9268 | 126.2063 | 252.4125 | 24 |
| TF Outer Flag | 35.3670 | 51.1861 | 246.0625 | 12.7000 | 24 |

Since the PF1b coil is located in the lower half plane only, the calculations for TF were performed in the lower half plane only, since that represents the worst case. For the force coefficients on the PF and OH coils the procedure used was to inject an excitation current in each of the PF and OH coils, one coil at a time, and then calculate the total radial (JxBv) and vertical (JxBr) force on each of the other coils, per unit of current. This involves the calculation of the average field over the cross section of the coil, multiplied by the circumference of the coil…

where Cxy is the coefficient of force on coil x due to the current in coil y. The resultant influence matricies are given in Tables 2 and 3.

TABLE 2: Radial Force Coefficients (lbf/kA^2)

| Fr | OH | PF1aU | PF1aL | PF1b | PF2U | PF2L | PF3U | PF3L | PF4U | PF4L | PF5U | PF5L |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| OH | 24620 | 1069 | 1069 | 1681 | 972 | 972 | 1017 | 1017 | 660 | 660 | 896 | 896 |
| PF1aU | -19 | 129 | 0 | 1 | 95 | 1 | 67 | 5 | 24 | 6 | 28 | 11 |
| PF1aL | -19 | 1 | 129 | 179 | 2 | 95 | 5 | 67 | 6 | 24 | 11 | 28 |
| PF1b | -76 | 1 | 10 | 545 | 4 | 374 | 12 | 192 | 15 | 61 | 27 | 70 |
| PF2U | -19 | -6 | 1 | 2 | 444 | 6 | 443 | 19 | 112 | 25 | 129 | 47 |
| PF2L | -19 | 1 | -6 | -73 | 6 | 444 | 19 | 443 | 25 | 112 | 47 | 129 |
| PF3U | -17 | -3 | 1 | 3 | -113 | 9 | 575 | 33 | 222 | 43 | 266 | 85 |
| PF3L | -17 | 1 | -3 | -18 | 9 | -113 | 33 | 575 | 43 | 222 | 85 | 266 |
| PF4U | -11 | 0 | 1 | 2 | -4 | 7 | 14 | 28 | 189 | 38 | 612 | 80 |
| PF4L | -11 | 1 | 0 | -1 | 7 | -4 | 28 | 14 | 38 | 189 | 80 | 612 |
| PF5U | -17 | 0 | 1 | 2 | -3 | 8 | 7 | 36 | -300 | 46 | 392 | 105 |
| PF5L | -17 | 1 | 0 | -1 | 8 | -3 | 36 | 7 | 46 | -300 | 105 | 392 |

TABLE 3: Vertical Force Coefficients (lbf/kA^2)

| Fz | OH | PF1aU | PF1aL | PF1b | PF2U | PF2L | PF3U | PF3L | PF4U | PF4L | PF5U | PF5L |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| OH | 0 | 6 | -6 | -72 | 54 | -54 | 27 | -28 | 7 | -7 | 6 | -6 |
| PF1aU | -6 | 0 | 0 | 0 | 11 | 0 | 0 | 0 | -1 | 0 | -2 | -1 |
| PF1aL | 6 | 0 | 0 | -88 | 0 | -11 | 0 | 0 | 0 | 1 | 1 | 1 |
| PF1b | 72 | 0 | 90 | 0 | 1 | -20 | 2 | 10 | 2 | 7 | 3 | 8 |
| PF2U | -55 | -11 | 0 | -1 | 0 | -2 | -99 | -7 | -39 | -9 | -41 | -16 |
| PF2L | 55 | 0 | 11 | 21 | 2 | 0 | 7 | 99 | 9 | 39 | 16 | 41 |
| PF3U | -28 | -1 | -1 | -2 | 99 | -7 | 0 | -26 | -225 | -36 | -214 | -66 |
| PF3L | 28 | 1 | 1 | -9 | 7 | -99 | 26 | 0 | 36 | 225 | 66 | 214 |
| PF4U | -7 | 1 | -1 | -2 | 39 | -9 | 228 | -36 | 0 | -52 | -533 | -100 |
| PF4L | 7 | 1 | -1 | -6 | 9 | -39 | 36 | -228 | 52 | 0 | 100 | 533 |
| PF5U | -6 | 2 | 0 | -3 | 42 | -15 | 214 | -65 | 530 | -99 | 0 | 200 |
| PF5L | 6 | 0 | -2 | -8 | 15 | -42 | 65 | -214 | 99 | -530 | 200 | 0 |

Using these results the force on coil x due to its current and the forces in the other y coils is is calculated as follows…

where the currents are in kA and the resultant force in lbf.

For the TF coil, the forces and moments (taken w.r.t. machine axis) of interest are as follows:

Finner = total force generated on an inner flag due to JTF x Bv

Fouter = total force generated on an outer flag due to JTF x Bv

Minner = total moment generated on inner flag due to JTF x Bv

Mouter = total moment generated on outer flag due to JTF x Bv

Reff_inner = effective radius of Finner

Reff_outer = effective radius of Fouter

Minner bundle = moment on inner turn in bundle due to JTF x Br and reacted by hub

Mouter bundle = moment on outer turn in bundle due to JTF x Br and reacted by hub

Mbundle = total moment generated on 12 inner and 24 outer turns and reacted by hub

Mflag = total torsional moment generated on 12 inner and 24 outer flags JTF x Bv

Mnet = net moment of bundle and flags transmitted through vacuum vessel

Equations for the influence matrix coefficients are as follows…

Flags:

where w is the width of the flag (1”)

Bundle:

where zmax is the turn height in a half plane. The z/zmax term is used to approximate the amount of torsional load taken out at the hub end of the bundle as if it was a fixed boundary.  The remainder is taken by the bundle twist. Note also that the second term in the inner calculation accounts for the flag stub.

The resultant matrix is given in Table 4.

TABLE 4: TF Influence Coefficients

|  | OH | PF1aU | PF1aL | PF1b | PF2U | PF2L | PF3U | PF3L | PF4U | PF4L | PF5U | PF5L |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| F_Inner (lbf/kA^2) | 0.222 | 0.003 | 0.024 | 0.175 | 0.011 | 0.652 | 0.037 | 0.655 | 0.049 | 0.195 | 0.092 | 0.240 | lbf |
| F_Outer (lbf/kA^2) | 0.471 | 0.004 | 0.048 | 0.382 | 0.015 | 1.178 | 0.048 | 0.890 | 0.063 | 0.260 | 0.115 | 0.310 | lbf |
| M_Inner (lbf-in/kA^2) | 2.7 | 0.0 | 0.3 | 2.1 | 0.1 | 8.5 | 0.5 | 8.9 | 0.7 | 2.7 | 1.2 | 3.3 | in-klbf |
| M_Outer (lbf-in/kA^2) | 5.1 | 0.1 | 0.6 | 4.3 | 0.2 | 15.7 | 0.7 | 12.2 | 0.9 | 3.6 | 1.6 | 4.2 | in-klbf |
| Reff_Inner (in) | 12.2 | 13.3 | 12.7 | 12.3 | 13.5 | 13.1 | 13.6 | 13.5 | 13.6 | 13.7 | 13.5 | 13.6 | in |
| Reff_Outer (in) | 10.7 | 13.1 | 12.1 | 11.4 | 13.5 | 13.3 | 13.7 | 13.8 | 13.7 | 13.7 | 13.9 | 13.7 | in |
| ∑M_Bundle (lbf-in/kA^2) | -188 | -0.2 | -8 | -10 | -0.5 | 0.1 | -1 | -1 | -1 | -2 | -2 | -3 | ft-klbf |
| ∑M_Flag (lbf-in/kA^2) | 154 | 2 | 17 | 130 | 7 | 478 | 22 | 400 | 29 | 117 | 53 | 141 | ft-klbf |
| ∑M_Net (lbf-in/kA^2) | -34 | 2 | 10 | 120 | 6 | 478 | 21 | 399 | 27 | 115 | 51 | 138 | ft-klbf |

Maximum values for the TF forces and moments are given in Table 5. These values result from all coils being at maximum current in the same polarity, and are equivalent to prior published results, except for M_bundle. Prior

TABLE 5: TF Forces and Moments for Maximum Possible Conditions

| F_Inner_TF_Flag | 3077 | lbf |
| --- | --- | --- |
| F_Outer_TF_Flag | 5077 | lbf |
| M_Inner_TF_Flag | 40 | in-klbf |
| M_Outer_TF_Flag | 65 | in-klbf |
| Reff_Inner_TF_Flag | 13 | in |
| Reff_Outer_TF_Flag | 13 | in |
| ∑M_TF_Bundle | -30 | ft-klbf |
| ∑M_TF_Flag | 171 | ft-klbf |
| ∑M_TF_Net | 141 | ft-klbf |

Maximum values for the TF and PF forces under realistic maximum conditions are given in Table 6. These forces result from the coils being in worst case current combination within the range indicated in Table 7, which is constrained by the polarity considerations associated with normal plasma operation. Specific worst case current combinations were derived for each case and are given in Table 8. Note that PF4 energization is not included; this is a special case to be treated separately. Cases shown are limited to those relevant to the limiting structural support clamp designs, i.e. forces away from the midplane, except for PF5, whose struts must react the forces toward the midplane as well.

TABLE 6: TF and PF Forces and Moments for Realisitic Maximum Conditions

| F_Inner_TF_Flag | 1848 | lbf |
| --- | --- | --- |
| F_Outer_TF_Flag | 2765 | lbf |
| M_Inner_TF_Flag | 25 | in-klbf |
| M_Outer_TF_Flag | 36 | in-klbf |
| Reff_Inner_TF_Flag | 13 | in |
| Reff_Outer_TF_Flag | 13 | in |
| ∑M_TF_Bundle | -28 | ft-klbf |
| ∑M_TF_Flag | 96 | ft-klbf |
| ∑M_TF_Net | 78 | ft-klbf |
| Fz_OH | 35 | klbf |
| Fz_PF1a (max toward MP) | 11 | klbf |
| Fz_PF1b (max toward MP) | 82 | klbf |
| Fz_PF2 (max away from MP) | 92 | klbf |
| Fz_PF3 (max away from MP) | 156 | klbf |
| Fz_PF5 (max away from MP) | 144 | klbf |
| Fz_PF5 (max toward MP) | 157 | klbf |

TABLE 7: Realistic Maximum Current Range

|  | Min | Max |
| --- | --- | --- |
| Ioh | -24.0 | 24.0 |
| Ipf1a | -24.0 | 5.0 |
| Ipf1b | -20.0 | 0.0 |
| Ipf2 | -20.0 | 0.0 |
| Ipf3 | -20.0 | 20.0 |
| Ipf4 | 0.0 | 0.0 |
| Ipf5 | 0.0 | 20.0 |
| Itf | 0.0 | 71.2 |

TABLE 8: Worst Case Currents for Forces Toward and Away from Midplane

|  | OH Launch | PF1a Away | PF1b Away | PF2 Away | PF3 Away | PF5 Away | PF5 Toward | TF (all except M_Net) | TF (M_Net) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Ioh | 24 | 24 | -24 | 24 | 24 | -24 | 24 | 24 | -24 |
| Ipf1a | -24 | 5 | -24 | 5 | 5 | 5 | -24 | 5 | 5 |
| Ipf1b | -20 | -20 | -20 | 0 | -20 | -20 | -20 | 0 | 0 |
| Ipf2 | -20 | -20 | 0 | -20 | -20 | 0 | -20 | 0 | 0 |
| Ipf3 | -20 | 20 | -20 | 20 | -20 | 20 | -20 | 20 | 20 |
| Ipf4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Ipf5 | 0 | 20 | 0 | 20 | 20 | 20 | 20 | 20 | 20 |
| Itf | 71 | 71 | 71 | 71 | 71 | 71 | 71 | 71 | 71 |

cc:

M. Bell	J. Chrzanowski	F. Dahlgren 	M. Ono	J. Schmidt

R. Woolley	I. Zatz