22-020801-CLN-01

TO: DISTRIBUTION
FROM: C NEUMEYER
SUBJECT: CHI ABSORBER FIELD NULLING COIL DESCRIPTION

This memo provides basic information concerning the CHI Absorber Field Nulling Coils

# Coil Descriptions

As shown in figure 1, there are two coils, named PFAB1 and PFAB2 (“PF” stands for poloidal field, “AB” stands for absorber). Note also the flux loop “FL” locations above and below PFAB1.

FIGURE 1: PF ABSORBER FIELD NULLING COILS (Dwg. E-DC1277)

Coil construction details are shown in figures 2 and 3.

FIGURE 2: PFAB-1 (Dwg. E-DC1284)

FIGURE 3: PFAB-2 (Dwg. E-DC1286)

Coil dimensions are given in Table 1, and electrical impedances in Table 2. Coil electrical ratings are given in Table 3.

## Table 1: CHI Absorber Coil Dimensions

| Coil | Rcenter (m) | Zcenter (m) | ∆Z (m) | ∆R (m) | #turns | Packing Fraction |
| --- | --- | --- | --- | --- | --- | --- |
| PFAB1 | 0.4306 | 1.7565 | 0.06788 | 0.02176 | 48 | 0.561 |
| PFAB2 | 0.6318 | 1.9259 | 0.06788 | 0.02176 | 48 | 0.561 |

## Table 2: CHI Absorber Coil Impedances

| Coil | R (mΩ) | L (mH) |
| --- | --- | --- |
| PFAB1 | 129.7 | 3.93 |
| PFAB2 | 190.2 | 6.46 |

## Table 3: CHI Absorber Coil Electrical Ratings

| Peak Current | 1.0 kA |
| --- | --- |
| Equivalent Square Wave (∆T=80oC) | 4.0 sec |
| ∫I2(t)dt (∆T=80oC) | 4 x 106 A2-sec |
| Terminal to Terminal Voltage | 1kV |
| Maximum Voltage to Ground | 2kV |
| Hipot Voltage to Ground | 5kV |

Notes:

- The above is based on a conductor cross section of 0.1875” x 0.1875” with 0.1” diameter cooling hole and 0.025” corner radius. Adjustments may have to be made based on actual as-built measurements.

- PFAB1 is mounted on the inner VV, and can therefore see a total of 1kV from its power supply plus 1kV from CHI, total of 2kV

- PFAB2 is mounted on the outer VV, and can therefore see a total of 1kV from its power supply plus 1kV from CHI, total of 2kV

# Coil Support Structures

As shown in figure 1, PFAB1 is wound into a stainless steel ring, with cross section of ∆Z=7.3” and ∆R=2.0”.  The ring is welded to the flange of the center stack casing.

As shown in figure 1 and figure 4, PFAB2 is secured by 11 clamps which contain the coil between a stainless steel support ring located underneath the coil, and a set of 6 tabs located above the coil which the attach to the top side of the PF2 coil support clamps. The support ring cross section is ∆Z=0.5” and ∆R=2.5”. Bolting hardware is 3/8” diameter.

FIGURE 4: PFAB-2 Support Scheme (Dwg. E-DC1285)

### Mutual Inductances

Overall NSTX PF system mutual inductance matrix including the subject coils is given in Table 4.

Table 4: PF Coil Inductances (Henry)

|  | OH | PF1AU | PF1AL | PF1B | PF2U | PF2L | PF3U | PF3L | PF4 | PF5 | PFAB1 | PFAB2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| OH | 1.30E-02 | 7.31E-04 | 7.31E-04 | 3.74E-04 | 2.76E-04 | 2.76E-04 | 2.95E-04 | 2.95E-04 | 3.79E-04 | 5.28E-04 | 6.18E-04 | 4.86E-04 |
| PF1AU | 7.31E-04 | 3.76E-04 | 1.95E-07 | 2.25E-07 | 7.23E-05 | 1.35E-06 | 6.04E-05 | 5.29E-06 | 3.16E-05 | 4.16E-05 | 1.95E-04 | 1.22E-04 |
| PF1AL | 7.31E-04 | 1.95E-07 | 3.76E-04 | 9.01E-05 | 1.35E-06 | 7.23E-05 | 5.29E-06 | 6.04E-05 | 3.16E-05 | 4.16E-05 | 8.07E-07 | 1.45E-06 |
| PF1B | 3.74E-04 | 2.25E-07 | 9.01E-05 | 5.36E-04 | 1.66E-06 | 1.86E-04 | 6.61E-06 | 1.01E-04 | 4.15E-05 | 5.43E-05 | 9.69E-07 | 1.78E-06 |
| PF2U | 2.76E-04 | 7.23E-05 | 1.35E-06 | 1.66E-06 | 1.98E-03 | 1.03E-05 | 7.31E-04 | 4.11E-05 | 2.64E-04 | 3.45E-04 | 6.50E-04 | 1.84E-03 |
| PF2L | 2.76E-04 | 1.35E-06 | 7.23E-05 | 1.86E-04 | 1.03E-05 | 1.98E-03 | 4.11E-05 | 7.31E-04 | 2.64E-04 | 3.45E-04 | 5.92E-06 | 1.10E-05 |
| PF3U | 2.95E-04 | 6.04E-05 | 5.29E-06 | 6.61E-06 | 7.31E-04 | 4.11E-05 | 5.18E-03 | 1.66E-04 | 1.16E-03 | 1.49E-03 | 3.57E-04 | 7.42E-04 |
| PF3L | 2.95E-04 | 5.29E-06 | 6.04E-05 | 1.01E-04 | 4.11E-05 | 7.31E-04 | 1.66E-04 | 5.18E-03 | 1.16E-03 | 1.49E-03 | 2.35E-05 | 4.39E-05 |
| PF4 | 3.79E-04 | 3.16E-05 | 3.16E-05 | 4.15E-05 | 2.64E-04 | 2.64E-04 | 1.16E-03 | 1.16E-03 | 5.16E-03 | 4.81E-03 | 1.48E-04 | 2.79E-04 |
| PF5 | 5.28E-04 | 4.16E-05 | 4.16E-05 | 5.43E-05 | 3.45E-04 | 3.45E-04 | 1.49E-03 | 1.49E-03 | 4.81E-03 | 1.23E-02 | 1.93E-04 | 3.66E-04 |
| PFAB1 | 6.18E-04 | 1.95E-04 | 8.07E-07 | 9.69E-07 | 6.50E-04 | 5.92E-06 | 3.57E-04 | 2.35E-05 | 1.48E-04 | 1.93E-04 | 3.93E-03 | 1.33E-03 |
| PFAB2 | 4.86E-04 | 1.22E-04 | 1.45E-06 | 1.78E-06 | 1.84E-03 | 1.10E-05 | 7.42E-04 | 4.39E-05 | 2.79E-04 | 3.66E-04 | 1.33E-03 | 6.46E-03 |

Coupling with PF2 and Nearby Structure

To facilitate the evaluation of the coupling effects with PF2 and nearby structure the electrical characteristics of the simplified configuration shown in Figure 5 (to scale) was modeled. Parts can be recognized by comparison with Figure 1.  Dimensions are summarized in Table 5, resistances in Table 6, and mutual inductances in Table 7. Note that all of the structure is 304SS (=7.7e-7Ω-m) except for the CS casing flange and ceramic insulator sealing ring which are Inconel (=1.3e-6Ω-m).

FIGURE 5: Simplified Model of absorber coils, structure, and PF2

Table 5: Dimensions

| Inches.... | Rcenter | Zcenter | ∆Z | ∆R |
| --- | --- | --- | --- | --- |
| PFAB1 | 16.953 | 69.155 | 2.673 | 0.857 |
| PFAB2 | 24.857 | 75.821 | 2.673 | 0.857 |
| SS Ring | 16.400 | 71.773 | 2.064 | 2.000 |
| SS Ring | 15.847 | 69.155 | 3.047 | 0.894 |
| SS Ring | 16.400 | 66.843 | 1.438 | 2.000 |
| SS Ring | 24.857 | 73.985 | 0.500 | 2.500 |
| Inconel Ring | 18.297 | 69.905 | 7.688 | 1.000 |
| Inconel Ring | 16.828 | 65.624 | 0.938 | 10.250 |
| SS Ring | 22.078 | 68.530 | 0.875 | 2.563 |
| SS Ring | 22.984 | 71.061 | 4.063 | 0.750 |
| SS Ring | 24.734 | 72.593 | 0.938 | 2.688 |
| SS Ring | 24.859 | 71.593 | 0.938 | 2.438 |
| SS Ring | 24.109 | 69.343 | 3.438 | 0.938 |
| SS Ring | 16.703 | 76.405 | 2.000 | 1.750 |
| SS Ring | 20.484 | 76.905 | 1.000 | 5.750 |
| PF2Ua | 31.464 | 76.123 | 2.676 | 6.406 |
| PF2Ub | 31.464 | 72.939 | 2.676 | 6.406 |
| Meters.... | Rcenter | Zcenter | ∆Z | ∆R |
| PFAB1 | 0.4306 | 1.7565 | 0.0679 | 0.0218 |
| PFAB2 | 0.6314 | 1.9259 | 0.0679 | 0.0218 |
| SS Ring | 0.4166 | 1.8230 | 0.0524 | 0.0508 |
| SS Ring | 0.4025 | 1.7565 | 0.0774 | 0.0227 |
| SS Ring | 0.4166 | 1.6978 | 0.0365 | 0.0508 |
| SS Ring | 0.6314 | 1.8792 | 0.0127 | 0.0635 |
| Inconel Ring | 0.4647 | 1.7756 | 0.1953 | 0.0254 |
| Inconel Ring | 0.4274 | 1.6668 | 0.0238 | 0.2604 |
| SS Ring | 0.5608 | 1.7407 | 0.0222 | 0.0651 |
| SS Ring | 0.5838 | 1.8050 | 0.1032 | 0.0191 |
| SS Ring | 0.6282 | 1.8438 | 0.0238 | 0.0683 |
| SS Ring | 0.6314 | 1.8184 | 0.0238 | 0.0619 |
| SS Ring | 0.6124 | 1.7613 | 0.0873 | 0.0238 |
| SS Ring | 0.4243 | 1.9407 | 0.0508 | 0.0445 |
| SS Ring | 0.5203 | 1.9534 | 0.0254 | 0.1461 |
| PF2Ua | 0.7992 | 1.9335 | 0.0680 | 0.1627 |
| PF2Ub | 0.7992 | 1.8526 | 0.0680 | 0.1627 |

Table 6: Resistances

| Element | R(Ω) |
| --- | --- |
| PFAB1 | 1.30E-01 |
| PFAB2 | 1.90E-01 |
| SS Ring | 7.57E-04 |
| SS Ring | 1.11E-03 |
| SS Ring | 1.09E-03 |
| SS Ring | 3.79E-03 |
| Inconel Ring | 7.65E-04 |
| Inconel Ring | 5.63E-04 |
| SS Ring | 1.88E-03 |
| SS Ring | 1.43E-03 |
| SS Ring | 1.87E-03 |
| SS Ring | 2.07E-03 |
| SS Ring | 1.43E-03 |
| SS Ring | 9.08E-04 |
| SS Ring | 6.78E-04 |
| PF2U | 4.17E-03 |

Table 7: Inductance Matrix (Henry)

|  | PFAB1 | PFAB2 | SS Ring | SS Ring | SS Ring | SS Ring | Inc Ring | Inc Ring | SS Ring | SS Ring | SS Ring | SS Ring | SS Ring | SS Ring | SS Ring | PF2U |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PFAB1 | 3.93E-03 | 1.33E-03 | 5.02E-05 | 6.28E-05 | 5.30E-05 | 3.05E-05 | 5.66E-05 | 3.77E-05 | 4.26E-05 | 3.80E-05 | 3.27E-05 | 3.36E-05 | 3.62E-05 | 2.62E-05 | 2.71E-05 | 6.50E-04 |
| PFAB2 | 1.33E-03 | 6.46E-03 | 2.93E-05 | 2.39E-05 | 2.25E-05 | 1.02E-04 | 3.41E-05 | 2.21E-05 | 4.45E-05 | 6.14E-05 | 8.08E-05 | 7.13E-05 | 5.48E-05 | 3.34E-05 | 6.15E-05 | 1.83E-03 |
| SS Ring | 5.02E-05 | 2.93E-05 | 1.56E-06 | 1.00E-06 | 6.96E-07 | 6.50E-07 | 1.03E-06 | 5.58E-07 | 7.36E-07 | 7.47E-07 | 6.72E-07 | 6.69E-07 | 6.71E-07 | 7.39E-07 | 6.80E-07 | 1.32E-05 |
| SS Ring | 6.28E-05 | 2.39E-05 | 1.00E-06 | 1.51E-06 | 1.06E-06 | 5.45E-07 | 9.54E-07 | 7.33E-07 | 7.34E-07 | 6.64E-07 | 5.79E-07 | 5.92E-07 | 6.35E-07 | 5.11E-07 | 5.04E-07 | 1.17E-05 |
| SS Ring | 5.30E-05 | 2.25E-05 | 6.96E-07 | 1.06E-06 | 1.65E-06 | 5.22E-07 | 9.47E-07 | 1.01E-06 | 7.94E-07 | 6.62E-07 | 5.67E-07 | 5.93E-07 | 6.71E-07 | 4.06E-07 | 4.34E-07 | 1.18E-05 |
| SS Ring | 3.05E-05 | 1.02E-04 | 6.50E-07 | 5.45E-07 | 5.22E-07 | 2.93E-06 | 7.81E-07 | 5.22E-07 | 1.09E-06 | 1.56E-06 | 2.20E-06 | 1.87E-06 | 1.38E-06 | 6.76E-07 | 1.15E-06 | 3.88E-05 |
| Inc Ring | 5.66E-05 | 3.41E-05 | 1.03E-06 | 9.54E-07 | 9.47E-07 | 7.81E-07 | 1.37E-06 | 7.91E-07 | 1.04E-06 | 9.60E-07 | 8.31E-07 | 8.46E-07 | 8.96E-07 | 6.53E-07 | 7.05E-07 | 1.62E-05 |
| Inc Ring | 3.77E-05 | 2.21E-05 | 5.58E-07 | 7.33E-07 | 1.01E-06 | 5.22E-07 | 7.91E-07 | 1.08E-06 | 8.48E-07 | 6.70E-07 | 5.74E-07 | 6.11E-07 | 7.24E-07 | 3.53E-07 | 3.99E-07 | 1.24E-05 |
| SS Ring | 4.26E-05 | 4.45E-05 | 7.36E-07 | 7.34E-07 | 7.94E-07 | 1.09E-06 | 1.04E-06 | 8.48E-07 | 2.43E-06 | 1.63E-06 | 1.25E-06 | 1.37E-06 | 1.78E-06 | 5.46E-07 | 7.18E-07 | 2.42E-05 |
| SS Ring | 3.80E-05 | 6.14E-05 | 7.47E-07 | 6.64E-07 | 6.62E-07 | 1.56E-06 | 9.60E-07 | 6.70E-07 | 1.63E-06 | 2.33E-06 | 1.83E-06 | 1.90E-06 | 1.88E-06 | 6.45E-07 | 9.35E-07 | 2.91E-05 |
| SS Ring | 3.27E-05 | 8.08E-05 | 6.72E-07 | 5.79E-07 | 5.67E-07 | 2.20E-06 | 8.31E-07 | 5.74E-07 | 1.25E-06 | 1.83E-06 | 2.77E-06 | 2.39E-06 | 1.64E-06 | 6.48E-07 | 1.03E-06 | 3.74E-05 |
| SS Ring | 3.36E-05 | 7.13E-05 | 6.69E-07 | 5.92E-07 | 5.93E-07 | 1.87E-06 | 8.46E-07 | 6.11E-07 | 1.37E-06 | 1.90E-06 | 2.39E-06 | 2.84E-06 | 1.92E-06 | 6.16E-07 | 9.48E-07 | 3.68E-05 |
| SS Ring | 3.62E-05 | 5.48E-05 | 6.71E-07 | 6.35E-07 | 6.71E-07 | 1.38E-06 | 8.96E-07 | 7.24E-07 | 1.78E-06 | 1.88E-06 | 1.64E-06 | 1.92E-06 | 2.53E-06 | 5.57E-07 | 7.97E-07 | 3.08E-05 |
| SS Ring | 2.62E-05 | 3.34E-05 | 7.39E-07 | 5.11E-07 | 4.06E-07 | 6.76E-07 | 6.53E-07 | 3.53E-07 | 5.46E-07 | 6.45E-07 | 6.48E-07 | 6.16E-07 | 5.57E-07 | 1.64E-06 | 1.04E-06 | 1.39E-05 |
| SS Ring | 2.71E-05 | 6.15E-05 | 6.80E-07 | 5.04E-07 | 4.34E-07 | 1.15E-06 | 7.05E-07 | 3.99E-07 | 7.18E-07 | 9.35E-07 | 1.03E-06 | 9.48E-07 | 7.97E-07 | 1.04E-06 | 1.76E-06 | 2.27E-05 |
| PF2U | 6.50E-04 | 1.83E-03 | 1.32E-05 | 1.17E-05 | 1.18E-05 | 3.88E-05 | 1.62E-05 | 1.24E-05 | 2.42E-05 | 2.91E-05 | 3.74E-05 | 3.68E-05 | 3.08E-05 | 1.39E-05 | 2.27E-05 | 1.98E-03 |

cc:

M Bell 		J Chrzanowski		D Gates	R Hatcher	M Kalish

D Lotz			R Marsala		J Menard	B Nelson	M Ono

S Ramakrishnan	R Raman		A Von Halle	I Zatz