71-980921-CLN-01

TO: DISTRIBUTION

FROM:  C NEUMEYER

SUBJECT:  CENTER STACK CASING/OUTER VV ELECTRICAL CONNECTIONS

References:

[1] NSTX-CALC-33-01, “ CS Ohmic Heating”

## INTRODUCTION

Capability for electrical connections to/between the center stack casing and outer vacuum vessel is required as follows:

- Connection to CHI power supply circuit for CHI operations, along with ground reference

- Jumpering between CS casing and outer VV during non-CHI operations

- to establish common voltage (jumpers across upper or lower ceramic insulator), and provide ground reference

- to simulate continuous vacuum vessel (jumpers across upper and lower ceramic insulators), and provide ground reference

- Connection to external power supply for bakeout ohmic heating, along with ground reference.

The GRD requires the aforementioned connections to be provided at four toroidally symmetric locations.

# 1) Connection to CHI power supply circuit for CHI operations

CHI power supply system can provide voltage up to 2kV to drive 50kA peak

current into the plasma.

With 4 parallel connections, current per strap is 50/4 = 12.5kA. Sustainment mode calls for injection of 20kA-5 seconds once every 300 seconds (∫I2t =  2 x 109 amp2-sec). Corresponding rms current is 20*sqrt(5/300)= 2.6kA. With four parallel connections rms current per connection is 650 amps.

2.a) Jumpering between CS casing and outer to establish common voltage and ground reference

CS casing and outer VV jumpered and connected to ground. One of the ceramic insulators is jumpered, the other is open. Current through jumper and to ground is minimal. There is no complete path for poloidal currents.

- 2.b) Jumpering between CS casing and outer VV during non-CHI operations

- to simulate continuous vacuum vessel and provide ground reference

CS casing and outer VV jumpered together across both ceramic insulators and connected to ground. A complete path is available for poloidal currents. Two poloidal current sources are identified herein: mutual coupling with TF coils, and halo currents driven by the plasma.

According to [1] the poloidal resistance of the vacuum vessel, including the CS casing, is approximately 800µΩ. If the vacuum vessel was perfectly coupled to the TF then the peak poloidal loop voltage would be 1000volts/36 turns = 27.8 volts/turn. The maximum possible poloidal current flow would then be 27.8volts/800µΩ = 34.7kA. Assuming that there are four jumpers, the maximum current per jumper due to TF ramping would be 34.7/4 = 8.7kA.

Per the GRD the poloidal halo current can amount to 10% of Ip with toroidal peaking factor of 2. This amounts to 0.1*1e6/4*2 = 50kA per jumper.  It is clear that the halo current case will produce the largest current magnitude.

- Connection to external power supply for bakeout ohmic heating, along with ground reference

Per [1] a current of up to 2.6kA shall be driven by a DC power supply through the center stack casing and returned through jumpers across the opposite ceramic insulator.  Current per jumper in this condition is 2.6kA/4 = 650 amps, continuous.

During bakeout the flanges of the center stack casing to which the jumpers must connect are heated by Dowtherm fluid to 350C.

SUMMARY OF REQUIREMENTS

Electrical connections must provide for CHI and bakeout power supply connection, as well as jumpered modes.  Current carrying requirements, per each of four connections, are as follows:

Peak current					50kA

Max. ∫I2t 					2 x 109 amp2-sec

Min. rep period				300 sec

Max. Irms					650 amp

Prospective short circuit current		120kA (due to 2 parallel power supply

sections)

Physical configuration is such that connection must run approximately 14” vertical downward from flange, 20” radial, and then 17” vertical back to outer vacuum vessel to provide path for jumper. Corresponding forces due to the halo current (50kA) are derived in the following spreadsheet. Background poloidal field values are based on field plots with worst case currents in OH, PF1b, and PF2 coils.

|  | CSC-Jumper | Jumper | Jumper-VV |  |
| --- | --- | --- | --- | --- |
| Ip | 1.00E+06 | 1.00E+06 | 1.00E+06 | Amp |
| k | 0.10 | 0.10 | 0.10 |  |
| peaking | 2.00 | 2.00 | 2.00 |  |
| #segment | 4.00 | 4.00 | 4.00 |  |
| Ipoloidal | 50000.00 | 50000.00 | 50000.00 | Amp |
| R1 | 0.384 | 0.384 | 0.892 | m |
| Z1 | 1.654 | 2.010 | 2.010 | m |
| R2 | 0.384 | 0.892 | 0.892 | m |
| Z2 | 2.010 | 2.010 | 1.578 | m |
| Theta | 90.000 | 0.000 | -90.000 | degrees |
| Ravg | 0.384 | 0.638 | 0.892 | m |
| Forces Due to Bt… |  |  |  |  |
| R0 | 0.854 | 0.854 | 0.854 | m |
| Bt(R0) | 0.600 | 0.600 | 0.600 | T |
| Bt(Ravg) | 1.334 | 0.803 | 0.574 | T |
| L poloidal | 0.356 | 0.508 | 0.432 | m |
| Fnormal/segment | 23714.38 | 20394.03 | 12399.72 | N |
|  | 5330.99 | 4584.58 | 2787.46 | lbs |
| Fradial/segment | -5330.99 | 0.00 | 2787.46 | lbs |
| Fvertical/segment | 0.00 | 4584.58 | 0.00 | lbs |
| Forces Due to Bp… |  |  |  |  |
| Br | 0.56 | 0.44 | 0.33 | T |
| Bv | 0.78 | 0.78 | 0.78 | T |
| Ftoroidal/segment due to Br | 27800.00 | 0.00 | -16400.00 | N |
|  | 6249.44 | 0.00 | -3686.72 | lbs |
| Ftoroidal/segment due to Bv | 0.00 | 22100.00 | 0.00 | N |
|  | 0.00 | 4968.08 | 0.00 | lbs |

Orientation of forces due to interaction with toroidal field is indicated in the following figure. As indicated, it is prudent to assume that the currents, fields, and forces, could occur in either direction.

Isometric view of toroidal force due to interaction with the vertical and radial poloidal fields is shown in the following figure. Again, it is safe to assume that the  forces could be imposed in either direction.

In addition to the above requirements, it is noted that the connection scheme must accommodate power supply voltage up to 2kV and must attach to flange at 350C.

DESIGN OF CONNECTIONS

3D model of proposed scheme is shown in the following figures. One of the four connection points is depicted.

Connection to center stack casing flange is accomplished using four 1-1/4” diameter copper rods, approximately 16” in length,  which are screwed into flange.  Connection to rod is accomplished using bronze straight tee “tubing to flat bar tap” standard bus bar connector such as Square D part TTF-1230-1 (catalog sheet attached). This is designed to connect a 1-1/4” tube (or rod) to a 3” wide bus bar.

A similar part (TTF-1220-1) can be used to connect 1/4” thick stainless steel straps from rod to rod to provide structural rigidity.

Connection to the outer vacuum vessel is accomplished using copper straps which are attached to the domes in the region adjacent to the ribs. The attachment could consist of a stainless steel tabs, welded on to the vessel, then bolted on to the copper straps.

Connection between the center stack casing and the outer vacuum vessel is accomplished via bolting a 3” wide by 1/4” thick straight copper shorting jumper connecting from the tube-to-bar tap across to the copper angle pieces, where it is sandwiched in between.

Feeds from the CHI or bakeout power supply are accomplished by connecting vertical riser bus bars, 1” x 1” square, 1/4” water cooling hole, spaced 1” apart, with copper flags brazed on at each end. These bus bars are uninsulated. Jumper straps connect these flags to the center stack casing and outer vacuum vessel when the shorting jumper is removed.   These feeds are joined together electrically and connected to the incoming power source via copper bus bar rings mounted on insulators to the pedestal assembly. Although shown toroidally continuous in the figures given herein, there would be a toroidal break to avoid closed toroidal loops.

JUSTIFICATION OF THE DESIGN

Copper rods, rather than stainless steel rods, are used in order to keep the resistance down. If the rods were constructed of stainless steel, then the resistance of each rod would be of order 400 µΩ, and the equivalent of 4 in parallel, 2 in series ≈ 200 µΩ net in the poloidal loop. This is to be compared [1] to the effective poloidal resistance of the center stack casing  @ 720 µΩ and outer vacuum vessel @ 80 µΩ.

If the rods are constructed of copper then their resistance will be negligible compared to the center stack casing and outer vacuum vessel.

The stainless steel rods would easier to implement (stronger, lower thermal conductivity, and could be tack welded after insertion to prevent turning), but they would likely cause the halo current behavior to deviate considerably from that which would result from a continuous vacuum vessel, due to the extra impedance they present, especially to localized currents.

The 1/4” x 2” stainless steel straps which bridge between the four rods serve to provide structural rigidity. It is noted that, if it were not for the toroidal asymmetry of the halo current, the net force on the four rods would be zero. So, by tying the rods together, they need only react the asymmetric component of the force.

The 1/2” thick x 3” wide copper straps which connect to the outer vacuum vessel provide a lower impedance, symmetric connection to the vessel at eight locations above and below the midplane.

The shorting jumpers provide a direct, low impedance path across the ceramic insulator assemblies.

The vertical riser bus bars, 1” x 1” with 1/4” diameter cooling passage, can carry the required 650 amps continuous, even without water cooling. The purpose of the water cooling is, mainly, to remove the heat flowing down the 1-1/4” diameter copper rods attached to the center stack casing flange, which can be at 350C during bakeout. This scheme, which holds the temperature of the bars well below 100C,  permits the use of G-10 clamps to react the short circuit force due to the prospective 100kA fault current which could flow in the (+) and (-) conductors. If the water cooling is lost during bakeout, there is a concern that the heat from the center stack casing could raise the temperature of the vertical riser bars well above 100C. However, the fact that they are uninsulated means that there will be significant heat lost to the ambient air in case of loss of water flow, so as to minimize the temperature rise in case of such an occurrence.

Thermal electrical design of the vertical riser bus bars is given in the following spreadsheet.  This includes, in addition to the conductor I2R losses, 500 watt additional power input due to a gradient of 350-10 = 340 C across the 16” long, 1-1/4” diameter copper rod.

| Cond resistivity @ 20C | 1.73E-06 | Ω-cm |
| --- | --- | --- |
| Cond res temp coeff | 0.00393 | 1/degC |
| Cond heat capacity | 0.386 | J/gm-degC |
| Cond density | 8.89 | gm/cc |
| Ambient Temperature | 35 | deg C |
| Max Current | 5000.0 | amp |
| Max ∫i^2dt | 6.45E+02 | A^2-s |
| Min ESW | 5.000 | sec |
| Min Repetition Period | 300.0 | sec |
| Max RMS Current | 645.5 | amp |
| Bus length per pole | 6 | feet |
| Inlet temperature | 35 | deg C |
| Max temperature | 80 | deg C |
| Conductor width | 1 | in |
| Conductor height | 1 | in |
| Cooling hole dia | 0.25 | in |
| Corner radius | 0.0625 | in |
| # Conductors | 1 |  |
| Cond CSA | 0.9 | sq in |
|  | 6.1 | sq cm |
| Res @ 20C per pole | 5.17E-05 | Ω |
| Res @ 25C per inch | 7.32E-07 | Ω/inch |
| Water flow/conductor | 2 | GPM |
| Water flow velocity | 13.1 | feet/sec |
|  | 398.4 | cm/sec |
| #Series Water Paths | 2 |  |
| ∆P | 16.5 | psi |
| Heat Capacity | 7.67E+03 | J/degC |
| Heat Capacity per inch | 1.07E+02 | J/degC/in |
| Thermal Res of Coolant | 1.89E-03 | deg C/watt |
| Film Res Cond to Coolant | 6.22E-04 | deg C/watt |
| Total Res Cond to Coolant | 2.51E-03 | deg C/watt |
| Thermal tau | 19.3 | sec |
| Res @ Tmax per pole | 5.78E-05 | Ω |
| Voltage Drop @ Imax (both poles) | 0.6 | volt |
| Conductor I^2R Loss per pole | 24.1 | watt |
| Total Conductor Loss | 48.2 | watt |
| Additional Heat Input | 500.0 | watt |
| Total Heat Input | 548.2 | watt |
| Tmax @ Irms | 36.4 | deg C |
| Tmax @ Irms + ∆T @ Imax @ ESW min | 38.0 | deg C |

Electromechanical design aspects of the vertical riser bus bars is given in the following spreadsheet.  This indicates the need for a G-10 support clamp every 8” or so.

| Separation | 1 | in |
| --- | --- | --- |
| CL-CL Bus Spacing s | 2 | in |
| width a | 1 | in |
| height b | 1 | in |
| a/b ratio | 1 |  |
| (s-a)/(a+b) | 0.5 |  |
| k factor | 0.983333 |  |
| Operating Current | 5000.0 | amp |
| Operating Force | 6.6375 | #/foot |
| Short Circuit Current | 120000 | amp |
| Short Circuit Force | 3823.2 | #/foot |
|  | 318.6 | #/in |
| Support Spacing | 8 | in |
| Support Force | 2548.8 | # |
| #Bolts | 2 |  |
| Bolt Load | 1274.4 | # |
| Moment of Inertia | 0.083333 | in^4 |
| Section Modulus | 0.166667 | in^3 |
| Elasticity | 1.60E+07 |  |
| Force/length | 318.6 | #/in |
| Bending Moment | 2548.8 | in-lb |
| Stress | 15292.8 | psi |
| Deflection | 0.012744 | in |

### OPEN ISSUES

Detailed layout study needs to be performed to insure that there are no interferences, and that access is available to parts as needed. Specific items which need to be confirmed are:

- Will the vertical riser bars pass through the radial TF flex connection region without interference?

- Can the shorting jumper be accessed after all parts are assembled? If not, then the shorting needs to be accomplished in the area of the rings mounted to the pedestal.

Detailing is needed in terms of:

- Means of connection to outer vacuum vessel

- Method of support, particularly of straps which connect to outer vacuum vessel.

3) G-10 clamps associated with vertical riser bus bars

4) Actual dimensions of required parts and associated hardware

Further analysis is needed to:

- Confirm mechanical integrity of the scheme, given the loads.

- Temperature of parts in case of loss of cooling water during bakeout.

- Finally, Physics has indicted a desire to measure the currents flowing in the jumpers when the center stack casing is shorted to the outer vacuum vessel. If the rods connecting to the center stack casing flange were constructed of stainless steel, they might have served well as current viewing resistors. However, with copper rods the resistance is probably too low for this purpose (e.g. at 50kA there would be a 275 mV drop across 10” of the rod length). Therefore it is recommended that Rogowski coils be used for this purpose, at exact locations TBD.

Cc:

J Chrzanowski

P Heitzenroeder

S Kaye

H Kugel

M Ono

S Ramakrishnan

NSTX File