| Procedure Title: NSTX COIL ENERGIZATION TESTS |
| --- |
| Number ISTP-NSTX-001 | Revision: 2 | Effective Date: 01/11/01 Expiration Date: _____ (2 yr. unless otherwise stipulated) |
| Procedure Approvals |  |
| Author C. Neumeyer | Date _____ |
| ATI C. Neumeyer | Date _____ |
| RLM A. Von Halle | Date _____ |
| Responsible Division: NSTX |  |
| Procedure Requirements Labwide: |  |
|  | Work Planning Form #__(ENG-032) |  | Lockout/Tagout (ESH-016) |
|  | Confined Space Permit (5008, Sec. 8, Chap 5) |  | Lift Procedure (ENG-021) |
|  | Master Equip. List Mod (GEN-005) |  | ES&H Review (NEPA, IH, etc.) |
|  | RWP (HP-OP-20) |  | Independent Review |
|  | ATI Walkdown |  | Pre-job Brief |
|  | Post-job Brief * |  |  |
| D-Site Specific: |
|  | D-Site Work Permit (OP-AD-09) |  | Door Permit (OP-G-93) |
|  | Tritium Work Permit (OP-AD-49) |  | USQD (OP-AD-63) |
|  | Pre-job brief (OP-AD-79) |  | T-MOD (OP-AD-03) |
|  | DCA/DCN (OP-AD-104) # _____ |  |  |

REVIEWERS (designated by RLM)

Accountable Technical Individual _____

Test Director _____

Independent Reviewer _____

D-Site Shift Supervisor G. Pearson

NSTX A. Von Halle, M. Williams, M. Ono

TFTR Caretaking _____

Vacuum _____

Computer _____

Tritium _____

Quality Assurance/Quality Control _____

AC Power _____

Maintenance and Operations Division _____

Energy Conversion System/MG System S. Ramakrishnan, E. Baker, R. Marsala

Environmental Restoration & Waste Management Division _____

Water _____

Neutral Beam (Heating Systems Branch of Electrical Engineering) _____

Radiofrequency (Heating Systems Branch of Electrical Engineering) _____

Diagnostics _____

Environmental, Safety, & Health _____

| TRAINING (designated by RLM) No training required Instructor _____ |
| --- |
| Personnel (group, job title or individual name) | Read Only | Instruction | Hands-On |
| _____ |  |  |  |
| _____ |  |  |  |
| Training Rep. ____________________________________ |  |  |  |
| RLM ___________________________________________ |  |  |  |

1.	PURPOSE

  - This procedure provides a means for documenting and implementing changes to the operating envelope and protection system settings for the NSTX magnet and Coaxial Helicity Injection (CHI) systems.

1.2	This procedure is intended to be repeated multiple times as the operating envelope of the machine is adjusted to support the experimental program.

2.	SCOPE

2.1	The scope of this procedure includes:

• definition of allowable operating envelope for coil and CHI power supply sytems

• testing with individual circuit energization

• testing with multiple circuit energization (combined fields)

2.2	The following additional steps are (optionally) invoked:

• exercise of protective features

• confirmation of voltage induced in circuits not under test

• archival of magnetic diagnostic response

• other special tests/measurements as circumstances may dictate

  - This procedure is not intended to produce a plasma in the NSTX device. To prevent plasma formation during test shots, high vacuum conditions will be maintained and gas injection pulse valves will not be operated.

  - Changes to the CHI allowable operating envelope are specified herein but cannot be tested per this procedure since the CHI load consists of the plasma itself.

- REFERENCES

OP-NSTX-16 		Procedure for Setting Rochester Instrument System (RIS) Coil Protection

OP-NSTX-17	Procedure for Setting Analog Coil Protection (ACP) System

OP-PC-735 		ECS Thyristor Rectifer Fault Detector (FD) Settings Procedure for NSTX

D-NSTX-OP-G-141 	Changing Polarities on NSTX Coil Systems

4. 	RESPONSIBILITIES

Head of NSTX Engineering Ops:	Shall appoint Test Director, and approve operating levels called out herein.

Run Copy Head of NSTX Engr. Ops:						  Init.

Chief Operating Engineer (COE): 	Overall responsibility for machine operations, and preparation of machine and ancillary systems in advance of testing.

Run Copy COE:								  Init.

Test Director: 	Overall responsibility for conduct of tests, and documentation of results in the form of a Test Record (completed Run Copy, Test Data Sheets, and any other relevant data or information collected during the tests).

Run Copy Test Director:							  Init.

Protection Engineer:	Responsible for setting coil protection devices including ACP and RIS.

Run Copy Protection Engineer:						  Init.

FCPC Engineer-In-Charge (EIC):	Responsible for configuration and operation of power supply systems, including protection settings in power supply fault detectors.

Run Copy EIC:								  Init.

5. 	PROCEDURE

  - Head of NSTX Engineering Operations shall indicate allowable NSTX operating levels and bus link constraints in Tables 1 through 6.

Table 1 - Current Allowables

|  | Imin (kA) | Imax (kA) | Coil I Rated (kA) | Link Polarity (see note) | PS I Rated (kA) | ∫i2(t)dt (kA2-sec) | ∫i2(t)dt rated (kA2-sec) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| OH |  |  | 24 |  | +/-24 |  | 302.4 |
| PF1A |  |  | 15 |  | +15/-5 |  | 1125.0 |
| PF1B |  |  | 20 |  | 20 |  | 400.0 |
| PF2 |  |  | 20 |  | 20 |  | 2000.0 |
| PF3 |  |  | 20 |  | +20/-5 |  | 2000.0 |
| PF4 |  |  | 20 |  | 20 |  | 2000.0 |
| PF5 |  |  | 20 |  | 20 |  | 2000.0 |
| TF |  |  | 71.2 |  | 71.2 |  | 6711.0 |
| CHI |  |  | 50 |  | 50 |  | 2000.0 |

Note: F = forward only, R = reverse only, F or R = forward or reverse

Table 2 – Minimum Pulse Repetition Period

|  | Minimum Pulse Repetition Period (seconds) | Rated Pulse Repetition Period (seconds) |
| --- | --- | --- |
| TF & PF Coils (except OH), and CHI |  | 300 |

# Table 3 – OH Repetition Rate Constraints

| Pulse Repetition Period (seconds) | Maximum ∫i2(t)dt (kA2-sec) | Maximum ∫i2(t)dt (% of 600 sec value) | Minimum Starting Temperature (degC) |
| --- | --- | --- | --- |
| 600 |  | 100 |  |
| 450 |  |  |  |
| 300 |  |  |  |

Table 4 - Constraints on Independent Control

|  | Independent Control Allowed (yes or no) |
| --- | --- |
| PF1A |  |
| PF2 |  |
| PF3 |  |

Table 5 - Series PSS (Voltage) Allowables

|  | #Series PSS Allowable | #Series PSS Rated Maximum (≈ kV) |
| --- | --- | --- |
| OH |  | 6 |
| PF1AU |  | 2 |
| PF1AL |  | 2 |
| PF1B |  | 2 |
| PF2U |  | 2 |
| PF2L |  | 2 |
| PF3U |  | 2 |
| PF3L |  | 2 |
| PF4 |  | 3 |
| PF5 |  | 3 |
| TF |  | 1 |
| CHI |  | 2 |

Table 6 – Current Combination Constraints

| Constraint | Constraint, Allowable | Constraint, Rated | Max Possible from Table 1 |
| --- | --- | --- | --- |
| IOH*IPF1B |  | ≥ - 480 kA^2-sec |  |
| IPF1A*IPF1B |  | ≥ -50 kA^2-sec |  |
| IOH,IPF1A,ITF |  | ¦IOH+IPF1A¦≤ 24kA if ¦ITF¦ > 35.6kA |  |

Head NSTX Engineering Operations		Init.

5.2  Nominal headroom for protective feature settings over allowables is given in Table 7.

##### Table 7 – Protective Feature Settings Headroom

|  | Overcurrent | ∫i2(t)dt |
| --- | --- | --- |
| PSRTC | 1% | 0% |
| ACP | 2% | Not applicable |
| RIS | 5% | 0% |
| FD | 10% | Not applicable |

5.3 Test Sequence

5.3.1 Preliminaries

a. Generate Test Data Sheets for each shot to be performed under this run copy of this procedure (template for TDS attached in Appendix hereto). Develop appropriate PSRTC files and perform simulations.

Test Director 		Init.

b. Confirm settings of ECS Thyristor Rectifiers Fault Detectors (FD) are consistent with current levels called for herein and/or TDS initial trip levels, in accordance with OP-PC-735. Nominal headroom over the allowables is given in Table 7.

FCPC EIC 		Init.

c. Confirm configuration of power supply system is consistent with polarities and levels indicated in TDS. Execute link change procedure D-NSTX-OP-G-141 if Table 1 differs from existing conditions.

FCPC EIC 		Init.

d. Confirm settings of RIS and ACP are consistent with current levels called for herein and/or initial test levels, in accordance with OP-NSTX-16 and OP-NSTX-17. Nominal headroom for the settings over the allowables is given in Table 7.

Protection Engineer 		Init.

e. Review T-Mod log and confirm that T-Mods in place will not compromise the execution of the tests called for herein.

COE 		Init.

5.3.2 Steps Preceding Each Test Session

Following steps, as applicable, shall be performed each time a new test session is started and documented in the Test Record.

a. Perform scrub and inspection of NTC per OP-NSTX-01 "Preparations of Experimental Areas for Machine Operations".

b. Perform daily startup activities per OP-NSTX-14 "NSTX Operations Guide for Startup and Shutdown".

c. Start up FCPC and Coil Cooling Water systems. Record conductivity of both deionized water systems.

d. Clear and secure all experimental areas per OP-AD-117 "Access Control Procedure". Via HIS, “Enable” all systems, pressurize SLD and place all systems in “Configure”.

e. Using methodology of OP-ECS-245, "FCPC Daily Startup/Shutdown Procedure", perform 500V hipot of all coil systems with power supply system disconnected (SDS open).

f. If/when MG is required, start MG system at 13.8kV, 65Hz.

COE 		Init.

5.3.3 Steps Associated With Each Test Shot

Execute the test shots called out in the TDS and perform the following additional steps as called out therein.

a.  Induced Voltage Confirmation

When called out on the TDS, the PSRTC coil voltage simulation results shall be compared to the digitized coil voltage transducer signals for shape, scale, and polarity.

b.  Diagnostic Calibration Shot

When called out on the TDS, the acquired diagnostic calibration data shall be examined by the Physics Operator and confirmed to be complete prior to declaring the test step complete. If not, the shot shall be repeated.

c.  Protective Feature Tests

When called out on the TDS, PSRTC, RIS, ACP and/or FD tests shall be performed (one circuit at a time only) as follows.

-	Set protective feature to X% (X specified on TDS) of nominal value allowed per this procedure then execute pulse and confirm trip at expected level.

-	Raise setting above allowable specified herein with headroom as listed in the following Table 7, unless otherwise noted on TDS.

d. Additional tests and measurements may be noted on the TDS in the "Other Special Requirements" section. This may include monitoring of special instrumentation (thermocouples, strain gauges, motion transducers, etc.) as called out by the Test Director.

5.3.4 Completion Steps

- Update EPICs page PC98 with latest operating limits.

Test Director		Init.

b. Confirm final settings of ECS Thyristor Rectifiers Fault Detectors (FD) are consistent with current levels called for herein, in accordance with OP-PC-735. Attach settings sheet.

FCPC EIC 		Init.

- Confirm final settings of RIS and ACP are consistent with current levels called for herein, in accordance with OP-NSTX-16 and OP-NSTX-17.  Attach settings sheet.

Protection Engineer 		Init.

- Place run copy in Operations Center.

Test Director		Init.

APPENDIX

• Test Plan Template

• Test Data Sheet Template

Test Data Sheet Sequence #

	Induced Voltage Confirmation

- Diagnostic Calibration Shot

Protective Feature Tests (applicable to single circuit tests only):

	PSRTC Overcurrent			PSRTC ∫i2(t)dt

	RIS Overcurrent			RIS ∫i2(t)dt

	ACP Overcurrent			ACP Overtime

	Fault Detector Overcurrent		Fault Detector Overtime

|  | OH | PF1aU | PF1aL | PF1b | PF2U | PF2L | PF3U | PF3L | PF4 | PF5 | TF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| # Series PSS |  |  |  |  |  |  |  |  |  |  |  |
| # Parallel PSS |  |  |  |  |  |  |  |  |  |  |  |

MG Required:		  Yes		No

| Circuit Allowable Current |  | kA |  |  |
| --- | --- | --- | --- | --- |
| Circuit Allowable I2T |  | kA^2-sec |  |  |
| Protection System | PSRTC | RIS | ACP | Units |
| Overcurrent Initial Setting |  |  |  | % |
| Overcurrent Initial Setting |  |  |  | kA |
| Overcurrent Final Setting |  |  |  | % |
| Overcurrent Final Setting |  |  |  | kA |
| I2T Initial Setting |  |  | n.a. | % |
| I2T Initial Setting |  |  | n.a. | kA^2-sec |
| I2T Final Setting |  |  | n.a. | % |
| I2T Final Setting |  |  | n.a. | kA^2-sec |
| Overtime Initial Setting | n.a. | n.a. |  | sec |
| Overtime Final Setting | n.a. | n.a. |  | sec |

 PSRTC Overcurrent  	Shot # 		  	 PSRTC ∫i2(t)dt 	Shot #

 RIS Overcurrent		Shot # 			 RIS ∫i2(t)dt		Shot #

 ACP Overcurrent		Shot # 			 ACP Overtime	Shot #

 Fault Detector Overcurrent	Shot # 			 Fault Detector OT	Shot #

Test Shot Complete: 				Test Director Init.