EPICS Events and IPCS Messages

# 21OCT98

P. Sichta

Rev 1 13APR99  	P. Sichta  	Added Appendix C & D and section 5 .

Revised Appendix  B and section 4.

Rev 2 28JUL99  P. Sichta		Added EPICS events 52,53.

Added IPCS  message type 301 .

Added specifiers for elements 1 and 2 of  IPCS msgClass.

Added MEL seq number range.

Added event mgr event nstx_tminus1.

Rev 3 20OCT99  	P. Sichta  	Added event 80.

Add "Receiving Messages' section in  Appdx B.

Added msgType 302 and revised msgType 5 format.

Rev 4 26JAN00  	P. Sichta  	Added events 32 - 34.

Rev 5 17JUL00  	P. Sichta		Added events 35 and 88.

Added (32) parameters to IPCS message type 5, specific set #2.

Noted message type 301 no longer used.

Rev 6 25JUL00  	P. Sichta		Added (2) parameters to IPCS message type 5, specific set #2.

Rev 7 26JUL00  	P. Sichta		Added (1) parameters to IPCS message type 5, specific set #2.

Rev 8 29SEP00  	P. Sichta		Added specific set #3.

Rev 9 29JAN01  	P. Sichta		Added LDGIS event #54.

## Table of Contents

### Introduction

### References

### EPICS Events

### IPCS Messages

Appendix A - EPICS Events Listing

Appendix B - IPCS Ground Rules

Appendix C - evtmgr Events Listing

Appendix D - Starting IPCS and the event manager

=================================================================

# 1.0 Introduction

This document specifies the conventions used for record scanning,  EPICS events,  and IPCS messages.

# 2.0 References

- NSTX-WBS6-AD,  Application Development Environment for CI&C.

- EPICS Applications Development Manual,  Marty Kraimer,   EPICS www at ANL/APS.

# 3.0 EPICS Events

EPICS events can be generated (e.g. Event record or Calcout record) and cause other records to process (if those records are set to process on “Event”).  The event numbers range from 0 – 255.  Appendix A will be used to keep track of assigned events.

On the IOC,  function scanpel lists all events and records which use events.

# 4.0 IPCS Messages

IPCS (inter-process communication system) will be used to have EPICS communicate with other processes (such as MDSplus processes) on the same or different computers.  Appendix B will be used to keep track of assigned messages and unique structures.

# 5.0 Event Manager Events

evtmgr (event manager) will be used to broadcast IPCS events to any and all programs which have 'registered' to listen for the event.  Appendix C will be used to keep track of assigned event names

Appendix A :  EPICS Events

| Event Number | Description | Generated by | Comment |
| --- | --- | --- | --- |
| 11 | New Day | ck_gendayEV |  |
| 12 | 1 Hz Timer | ck_gen1hzEV | Active only when NSTX clock inactive |
| 20 | SOC – Start of Cycle | ck_gensocEV |  |
| 21 | SOS – Start of Sequence | ck_gensosEV |  |
| 22 | T(-60) | ck_gentm60EV |  |
| 23 | SOP – Start of Pulse | ck_gensopEV |  |
| 24 | T(0) – Start of Discharge | ck_gensodEV |  |
| 25 | EOP – End of Pulse | ck_geneopEV |  |
| 26 | EOC – End of Cycle | ck_geneocEV |  |
| 27 | ABC – Aborted Cycle | ck_genabcEV | an abort prior to shot # commitment (pre SOS) |
| 28 | ABS – Aborted Sequence | ck_genabsEV | an aborted cycle (SOS - SOP) |
| 29 | KLC – Killed Cycle | ck_genklcEV | an aborted cycle (SOP-EOC) |
| 30 | PSC – PreSequence Check | ck_genpscEV | issued when PreSequence Check is evaluated/tested. |
| 31 | PPC – PrePulse Check | ck_genppcEV | issued when PrePulse Check is evaluated/tested |
| 32 | T(-1) | ck_gentm1EV |  |
| 33 | FBL - Fire Beamline | ck_genfblEV | FBL precedes injection by 16 sec |
| 34 | NBI - Start NB Injection | ck_gennbiEV |  |
| 35 | NNS - NB Sync with NSTX Clock | ck_gennns |  |
| 40 | Begin PC (FCPC) preshot tasks | (2) pc records | Used for FCPC Local shot cycle and for NSTX Clock cycle (at SOS). |
| 42 | Start 908 Acquisition | cm_908acqnow_EV |  |
| 50 | Read PLC31 Analog Group 1. | ?? | Allen Bradley scanning of ... |
| 51 | Read PLC31 Analog Group 2. | ?? | ... Vacuum System PLC |
| 52 | Stop GDC | gs_gdcStop_EV | nominal T-120. also from a CALCOUT |
| 53 | Start GDC | gs_gdcStart_EV | nominal T+30 |
| 54 | Lower Dome Ready for shot | in Db gs_ldgis | around T-8 |
| 80 | IOC1 1-sec scan on IOC2 | ck_scan1Hz_EV | to 'sync' IOC2 with IOC1 1-sec scan |
| 88 | Read Thermocouples from digitizer | tc_?? | used by tc_therm.st |

Appendix B

13APR99

# IPCS Messages Listing

# Formerly [IPCS Ground Rules Rev 2 : 29JAN99  P. Sichta]

## structure ipcsClass (eight shorts)

- majorId = mc_evt  (or decimal 48)

- minorId = -1

- msgType = this will be assigned for each message type.

- status = 1 (odd) for OK.  Set by receiver.

- seqnum = optional for tracking messages.  Set by sender

- available2 = IPCS message format revision

- available1 = optional

- available0 = optional

## IPCS message data

Along with the eight shorts,  an IPCS message can have an arbitrary amount of data,  in an arbitrary format.

- The format will be specified for each msgType.

- ASCII avoids endian and sizeof problems.

## msgType numbering

The most-significant-bit (bit 15) will be used for message acknowledgement (0 from sender, 1 from receiver).  CMD_ACK is defined for this purpose in ~gibney/ipcs/defs.h    .

- Messages which are sourced/sent/initiated by epicsrv1 : 3 – 99 (avoid zero, 1&2 used for testing)

- sourced… by epicsrv2 : 100 - 199

- sourced… by ppcc : 200 - 299

- sourced… by kees : 300 – 399

- sourced… by birch : 400 – 499

- sourced… by mel : 500 – 599

- available : 600 - 32767

## Sending messages

Messages are sent using ipcs_sendmsg.  There are four arguments to this call :

- toWhom is the name of the task to which the message is being sent.

- pointer to the ipcsClass structure

- optional pointer to data (or NULL)

- optional number of bytes in data (or 0)

## Replies to messages

- There are at several ways that a receiver can reply to a (sent) message.  The following should be used.

- ipcs_returnmsg

This will return the original message to the sender.  To inform the sender that the message was received :

- the received ipcsClass structure should be copied to a local structure,

- the ipcsClass.msgType bitwise-OR’ed with CMD_ACK (bit 15),

- ipcsClass.status set = 1,

- send using ipcs_returnmsg.

- After a reply,  the sender should delete the original message using ipcs_deletemsg(msgID).

Note that if the receiver is down and therefore does not reply in a few (10-20?) seconds, the message will be returned unacknowledged.  There is no “queue”.

## Receiving Messages

When receiving a message from another computer node, the following line must be included following the ipcsInit call:

sts= if (sts & 1)  sts = cell_reg();

# Message Definitions

If a field is not listed,  it is not used by the message type,  or it is fixed per the ground rules.

## msgType = 3

| Title | NSTX Clock Event Configuration |
| --- | --- |
| Originating subsystem | EPICS : NSTX Central Clock |
| msgType | 3 |
| status | Receiver to set to 1 if OK |
| seqnum | Sender uses range 1 - 1000. Receiver should return seqnum |
| available2 | Message format specifier : if = 0 : invalid format if = 1 : initial message(data)format |
| available1 | not used |
| Data data pointer *char | Space-delimited ASCII : (all times relative to SOD) SOC_time_value(float) SOS_time_value(float) SOP_time_value(float) TplusC_time_value(float) TplusD_time_value(float) EOD_time_value(float) EOP_time_value(float) EOC_time_value(float) |

## msgType = 4

| Title | Engineering 908 Digitizer Data File Ready |
| --- | --- |
| Originating subsystem | CAMAC 908 Digitizer Data Management |
| msgType | 4 |
| status | Receiver to set to 1 if OK |
| seqnum | Sender uses range 4000 - 5000. Receiver should return seqnum |
| available2 | Message format specifier : if = 0 : invalid format if = 1 : initial message(data)format |
| Data data pointer *char | char* (absolute pathname of file) |

## msgType = 5	 General FORMAT

| Title | Engineering Parameters |
| --- | --- |
| Originating subsystem | EPICS Parameter Acquisition |
| msgType | 5 |
| status | Receiver to set to 1 if OK |
| seqnum | Sender uses range 5000 - 6000. Receiver should return seqnum |
| available2 | Message format specifier : if = 0 : invalid format if = 1 : initial message(data)format if = 2 : July, 2000 format if = 3 : September, 2000 format |
| Data data pointer *char | Space-delimited ASCII : ASCII date/timestamp Number of Parameter Sets Set_1 Quality (0=OK, 1=bad) Set_1 Parameter Count Set_1, Parameter_1 Set_1, Parameter_2 etc ...... Set_1, Parameter_n Set_2 Quality (0=OK, 1=bad) Set_2 Parameter Count Set_2, Parameter_1 Set_2, Parameter_2 etc ...... Set_2, Parameter_n Set_n Quality (0=OK, 1=bad) Set_n Parameter Count Set_n, Parameter_1 Set_n, Parameter_2 etc ...... Set_n, Parameter_n |
| Specific Parameter Sets MESSAGE FORMAT SPECIFIER = 1 (October 1999) | Set 1 for HHFW: Position of Stub#1 at T(0) Position of Sretcher#1 at T(0) ... etc ... Position of Stub#6 at T(0) Position of Sretcher#6 at T(0) Set 2 for CHI: continued on next page ...... |

## msgType = 5 (continued from previous page)

| Specific Parameter Sets MESSAGE FORMAT SPECIFIER = 2 (July 2000) | Set 2 for CHI: PE-106 Prefill Pressure [Torr] PE-106 Sample Timestamp [ASCII] AV119-122 Trigger Time [millisec rel to T(0)] AV123 Trigger Time [millisec rel to T(0)] Lower Dome Gas Type [ASCII] Lower Dome Operating Mode [ASCII] Lower Dome PZV4 Time Breakpoint #1 [sec rel T(0)] ... etc ... Lower Dome PZV4 Time Breakpoint #15 Lower Dome PZV4 Voltage Breakpoint #1 [volts] ... etc ... Lower Dome PZV4 Voltage Breakpoint #15 AV123 air-line pressurization delay (millisec) Delay to move gas thru PZV4 delivery lines (millisec) |
| --- | --- |

| Specific Parameter Sets MESSAGE FORMAT SPECIFIER = 3 (September 2000) | Set 3 for NB: NB1 Calorimeter Position [TRANSIT,OUT,IN,ERROR] NB1 Master Accel Delay [millisec] NB1A Accel Delay[millisec] NB1B Accel Delay[millisec] NB1C Accel Delay[millisec] NB1A Accel Gate Duration[millisec] NB1B Accel Gate Duration[millisec] NB1C Accel Gate Duration[millisec] NB1A Data Analysis Control [ON,OFF] NB1B Data Analysis Control [ON,OFF] NB1C Data Analysis Control[ON,OFF] |
| --- | --- |

## msgType = 6

| Title | Engineering Daily Historical Trending Data File Ready |
| --- | --- |
| Originating subsystem | EPICS Historical Trending Data Management |
| msgType | 6 |
| status | Send immediate reply with status = 1. Send a separate, new message (type 304??) when data written to kees’ RAID. |
| seqnum | Sender uses range 4000 - 5000. Receiver should return seqnum |
| available2 | Message format specifier : if = 0 : invalid format if = 1 : initial message(data)format |
| Data data pointer *char | char* (absolute pathname of file) |

msgType = 301  ***NO LONGER USED ***

| Title | NSTX Vessel Thermocouples |
| --- | --- |
| Originating subsystem | KEES |
| msgType | 301 |
| status | Receiver to set to 1 if OK |
| seqnum | Receiver should return seqnum |
| available2 | Message format specifier : if = 0 : invalid format if = 1 : initial message(data)format |
| available1 | not used |
| Data data pointer *char | Space-delimited ASCII : Module scan rate (int, seconds) Sample Timestamp HH:MM:SS (string) Module_1 CAMAC Logical Name (string) Module_1, Temperature #1(float, degrees Celsius) etc.... Module_1, Temperature #16 Module_2 CAMAC Logical Name (string) Module_2, Temperature #1 etc.... Module_2, Temperature #16 etc... Module_8 CAMAC Logical Name (string) Module_8, Temperature #1 etc.... Module_8, Temperature #16 |

msgType = 302

| Title | HHFW Optimum Tuner Positions |
| --- | --- |
| Originating subsystem | KEES |
| msgType | 302 |
| status | Receiver to set to 1 if OK |
| seqnum | Receiver should return seqnum |
| available2 | Message format specifier : if = 0 : invalid format if = 1 : initial message(data)format |
| available1 | not used |
| Data data pointer *char | Space-delimited ASCII : Stub #1 Setting (cm) Stretcher #1 Setting (cm) Stub #2 Setting Stretcher #2 Setting etc .... Stub #6 Setting Stretcher #6 Setting |

Appendix C

13APR99

Rev. 1  28JUL99  Added Tminus1

Rev. 2  01FEB00  Added FBL & NBI

Event Mgr event names

| Event Name | Description | Source machine |
| --- | --- | --- |
| nstx_soc | NSTX Central Clock event SOC | epicsrv1 |
| nstx_sos | NSTX Central Clock event SOS | epicsrv1 |
| nstx_tminus60 | NSTX Central Clock event T(-60) | epicsrv1 |
| nstx_tminus1 | NSTX Central Clock event T(-1) | epicsrv1 |
| nstx_sop | NSTX Central Clock event SOP | epicsrv1 |
| nstx_sod | NSTX Central Clock event SOD | epicsrv1 |
| nstx_eop | NSTX Central Clock event EOP | epicsrv1 |
| nstx_eoc | NSTX Central Clock event EOC | epicsrv1 |
| nstx_abc | NSTX Central Clock event ABC | epicsrv1 |
| nstx_abs | NSTX Central Clock event ABS | epicsrv1 |
| nstx_klc | NSTX Central Clock event KLC | epicsrv1 |
| nstx_fbl | NSTX Central Clock event FBL | epicsrv1 |
| nstx_nbi | NSTX Central Clock event NBI | epicsrv1 |

Appendix D

13APR99

Starting IPCS & Event Mgr

Note that these task should normally occur during epicsrv1 boot time as part of startup scripts.

Also,  they may be started from medm display CH01.

To START IPCS on epicsrv1 :

13APR99

P. Sichta

=============================================

/opt/ipcs/etc :ipcs.start
Do you want to start IPCS? (y or n, default: y)

ipcs.start: ./getanswer: not found

/opt/ipcs/etc :DLOG by GRANDPA: 08:31:35 04/13/99
Common created, size = 0x40000.
DLOG by GRANDPA: 08:31:35 04/13/99
Common initialized.

/opt/ipcs/etc :ps -al | grep grandpa
8 S 1002 3101 1 0 41 20 50903328 278 5008618e pts/1 0:00 grandpa
/opt/ipcs/etc :

To START event mgr on epicsrv1 :

13APR99

P. Sichta

=============================================

cd  $PPPL_RES/evt : evtmgr &

To verify the evtmgr is working on epicsrv1 :

13APR99

P. Sichta

=============================================

On epicsrv1,  window 1 :

/usr/gibney/PPPL_RES/evt :usrtest

Enter ['']:  request ck

Event 'ck'  sts=1

Enter ['']:  wait ck,

On epicsrv1,  window 2 :

/usr/gibney/PPPL_RES/evt :declare_evt ck 101

ELOG by 03260_unknown: 09:07:09  04/13/99

reached u_exit_handler with 1 sig

/usr/gibney/PPPL_RES/evt :

On epicsrv1,  window 1, OBSERVE :

** Event 'CK' for shot 101

On epicsrv1,  window 1, to exit usrtest :

Enter ['']:  exit

/usr/gibney/PPPL_RES/evt :