# Rev 2 : 29JAN99  P. Sichta

Rev 3 : 24JUN99  P. Sichta

# IPCS Ground Rules

## structure ipcsClass (eight shorts)

- majorId = ignored/not used for NSTX

- minorId = ignored/not used for NSTX

- msgType = this will be assigned for each message type.

- status = 1 (odd) for OK.  Set by receiver.

- seqnum = optional for tracking messages.  Set by sender

- available2 = IPCS message format revision

- available1 = optional

- available0 = optional

## IPCS message data

Along with the eight shorts,  an IPCS message can have an arbitrary amount of data,  in an arbitrary format.

- The format will be specified for each msgType.

- ASCII avoids endian and sizeof problems.

## msgType numbering

The most-significant-bit (bit 15) will be used for message acknowledgement (0 from sender, 1 from receiver).  CMD_ACK is defined for this purpose in ~gibney/ipcs/defs.h    .

- Messages which are sourced/sent/initiated by epicsrv1 : 3 – 99 (avoid zero, 1&2 used for testing)

- sourced… by epicsrv2 : 100 - 199

- sourced… by ppcc : 200 - 299

- sourced… by kees : 300 – 399

- sourced… by birch : 400 – 499

- available : 500 - 32767

## Sending messages

Messages are sent using ipcs_sendmsg.  There are four arguments to this call :

- toWhom is the name of the task to which the message is being sent.

- pointer to the ipcsClass structure

- optional pointer to data (or NULL)

- optional number of bytes in data (or 0)

## Replies to messages

- There are at several ways that a receiver can reply to a (sent) message.  The following should be used.

- ipcs_returnmsg

This will return the original message to the sender.  To inform the sender that the message was received :

- the received ipcsClass structure should be copied to a local structure,

- the ipcsClass.msgType bitwise-OR’ed with CMD_ACK (bit 15),

- ipcsClass.status set = 1,

- send using ipcs_returnmsg.

- After a reply,  the sender should delete the original message using ipcs_deletemsg(msgID).

- Note that if the receiver is down and therefore does not reply in a few (10-20?) seconds, the message will be returned unacknowledged.  There is no “queue”.

# Message Definitions

If a field is not listed,  it is not used by the message type,  or it is fixed per the ground rules.

## msgType = 3

| Title | NSTX Clock Event Configuration |
| --- | --- |
| Originating subsystem | EPICS : NSTX Central Clock |
| msgType | 3 |
| status | Receiver to set to 1 if OK |
| seqnum | Receiver should return seqnum |
| available2 | Message format specifier : if = 0 : invalid format if = 1 : initial message(data)format |
| available1 | not used |
| Data data pointer *char | Space-delimited ascii : (all times relative to SOD) SOC_time_value(float) SOS_time_value(float) SOP_time_value(float) TplusC_time_value(float) TplusD_time_value(float) EOD_time_value(float) EOP_time_value(float) EOC_time_value(float) |

## msgType = 4

| Title | Engineering 908 Digitizer Data File Ready |
| --- | --- |
| Originating subsystem | CAMAC 908 Digitizer Data Management |
| msgType | 4 |
| status | Receiver to set to 1 if OK |
| seqnum | Receiver should return seqnum |
| available2 | Message format specifier : if = 0 : invalid format if = 1 : initial message(data)format |
| Data data pointer *char | char* (absolute pathname of file) |

## msgType = 5

| Title | Engineering Parameter File Ready |
| --- | --- |
| Originating subsystem | EPICS Parameter File Management |
| msgType | 3 |
| status | Receiver to set to 1 if OK |
| seqnum | Receiver should return seqnum |
| available2 | Message format specifier : if = 0 : invalid format if = 1 : initial message(data)format |
| Data data pointer *char | char* (absolute pathname of file) |

## msgType = 6

| Title | Engineering Daily Historical Trending Data File Ready |
| --- | --- |
| Originating subsystem | EPICS Historial Trending Data Management |
| msgType | 6 |
| status | Send immediate reply with status = 1. Send a separate, new message (type 304??) when data written to kees’ RAID. |
| seqnum | Receiver to set to 1 if OK |
| available2 | Receiver should return seqnum |
| Data data pointer *char | char* (absolute pathname of file) |

## msgType = 301

| Title | NSTX Vessel Thermocouples |
| --- | --- |
| Originating subsystem | KEES |
| msgType | 301 |
| status | Receiver to set to 1 if OK |
| seqnum | Receiver should return seqnum |
| available2 | Message format specifier : if = 0 : invalid format if = 1 : initial message(data)format |
| available1 | not used |
| Data data pointer *char | Space-delimited ascii : Module scan rate (int, seconds) Module_1 CAMAC Logical Name (string) Module_1, Temperature #1(float, degrees Celsius) etc.... Module_1, Temperature #16 Module_2 CAMAC Logical Name (string) Module_2, Temperature #1 etc.... Module_2, Temperature #16 etc... Module_8 CAMAC Logical Name (string) Module_8, Temperature #1 etc.... Module_8, Temperature #16 |