## Slide 1
MHD Stability Analysis and Global Mode Identification Preparing for
High Beta Operation in KSTAR*
Y.S. Park1, S.A. Sabbagh1, J.W. Berkery1, Y. Jiang1, J.H. Ahn1,
J.G. Bak2, J.M. Bialek1, H.S. Han2, B.H. Park2, Y.M. Jeon2,
J. Kim2, S.H. Hahn2, J.H. Lee2, W.H. Ko2, J.S. Ko2, Y.K. In2,
S.W. Yoon2, J.G. Kwak2, Y.K. Oh2, Z. Wang3, N.M. Ferraro3,
C.E. Myers3, S.C. Jardin3, A.H. Glasser4, G.S. Yun5
1Department of Applied Physics, Columbia University, New York, NY, USA
2National Fusion Research Institute, Daejeon, Korea
3Princeton Plasma Physics Laboratory, Princeton, NJ, USA
4U. Washington, Seattle, WA, USA
5POSTECH, Pohang, Korea
NSTX-U Physics Meeting
November 30, 2017
PPPL, Princeton, NJ
V1.0
*Work supported by the U.S. Department of Energy under contract DE-FG02-99ER54524 and DE-SC0016614
Supported by
National Fusion
Research Institute
In collaboration with

## Slide 2
Parameters for high bN
  BT in range 0.9-1.3 T
  PNBI = 4.5-5.5 MW
Highest bN = 4.3, bN/li > 6
MHD stability at high bN
  Many equilibria operate above the published ideal n = 1 no-wall stability limit (DCON)
  Plasma is subject to RWM instability, depending on plasma rotation profile
  High bN > bNno-wall operation mostly limited by 2/1 mode
KSTAR H-mode equilibria have reached and exceeded the computed
n = 1 ideal no-wall stability limit
Normalized beta vs. internal inductance from EFIT reconstruction**
containing ~9,000 equilibria produced in the 2016 device campaign
** Y.S. Park, et al., Nucl. Fusion 53 (2013) 083029
*O. Katsuro-Hopkins, et al., Nucl. Fusion 50 (2010) 025019
*
Shot 16295
Shot 16325

## Slide 3
High bN > 3 equilibria limited by MHD - shot 16295
High bN plasmas were significantly extended to longer pulse by utilizing improved plasma control
Sustained high bNavg = 3.3 achieved for 3 s
  Used max. available PNBI = 4.5 MW
  Ip = 430-470 kA, BT = 1.2 T, q95 = 4.0-4.5, Wtot = 270 kJ
2/1 tearing mode onset at high bN phase
  Consequently reduces bN and Wtot by ~35%
Stored energy
KSTAR high bN discharge evolution showing parameters from fully converged EFIT reconstructions
2/1 mode onset
bN > 3
q95 ~ 4

## Slide 4
Onset of strong 2/1 tearing mode terminated high bN
At high bN phase, a benign n = 2 mode (presumably 3/2 mode) exists with strong sawteeth
  No indication of Wtot reduction due to the n = 2 mode having |Bp| ~ 2 G
High bN operation was limited by strong 2/1 tearing mode onset
  Measured mode amplitude > 20 G
  Both Wtot and bN were reduced by ~35% but maintained H-mode
  Similar discharges exhibited different 2/1 tearing mode onset time (expected to be triggered by sawteeth)
Plasma rotation profile significantly reduced by > 20% due to the 2/1 mode onset
Toroidal magnetic probe spectrum and mode amplitude in high bN discharge
Weak n = 2 mode
KSTAR 16295
~

## Slide 5
Comparative equilibria having higher q95 and bp shows very different MHD stability - shot 16325
Plasma operation at elevated BT produced equilibria having higher q95 and bp
Unlike shot 16295, discharge doesn’t experience any major beta-limiting MHD activities
Stored energy
KSTAR 16325 discharge evolution showing parameters from fully converged EFIT reconstructions
bN ~ bp > 2
Toroidal magnetic probe spectrum
q95 > 6
Tearing modes absent
KSTAR 16325

## Slide 6
Kinetic EFIT with MSE constraints used for accurate stability analysis for the first time on KSTAR
Equilibrium reconstruction now uses measured internal profile constraints
  Provides reliable pressure profile and internal magnetic geometry necessary for stability and transport studies
KSTAR is equipped with key internal profile diagnostics
  Charge exchange (Ti, Vf) : 32 CHs
  Thomson scattering (Te, ne) : 27 CHs
  ECE radiometer (Te) : 76 CHs
  Motional Stark Effect : 25 CHs
  Total number of available constraints for fit : 161 magnetics + 160 kinetics & MSE
Reconstructed pressure and safety factor profile from kinetic EFIT using internal profile constraints
SEE Y. Jiang’s talk on 11/29/17
S.A. Sabbagh, Nucl. Fusion 41 (2001) 1601
EFIT pressure profile
(t ~ 2.1 s)
Fp = 3.6
Fp = 3.0
Unconstrained
MSE constrained
(t ~ 2.1 s)
EFIT q-profile

## Slide 7
DCON stability calculation shows high bN equilibria are subject to n = 1 ideal instability
At observed high bN phase, DCON calculates unstable n = 1 mode with no-wall (bN > bN no-wall)
qmin mostly stays below 1 which supports a potential 2/1 mode triggering by sawteeth
DCON computed no-wall dW and EFIT qmin in high bN equilibria of shot 16295
High bN equilibria
DCON dW
KSTAR 16295
bN > 3 phase
High bN equilibria
qmin (w/ MSE)
A.H. Glasser, Phys. Plasmas 23 (2016) 072505
DCON computed dBn of unstable n = 1 mode at t = 2.356 s
Unperturbed
boundary
n = 1
bN = 3.2

## Slide 8
Ideal mode stability computed by M3D-C1 code shows consistent result with DCON
Linear stability of ideal mode computed by using resistive MHD code M3D-C1
  Extended MHD code solving two-fluid resistive MHD equations
The high bN equilibrium is computed to be unstable by M3D-C1 consistent with DCON
Kinetic RWM stability can explain the observed RWM stable operation at bN > bNno-wall
(a) The perturbed poloidal flux of unstable ideal mode from M3D-C1 and (b) corresponding Poincaré plot with exaggerated displacement
1.0
0.5
0
-0.5
-1.0
1.2
1.4
1.6
1.8
2.0
2.2
2.4
(b)
R (m)
Z (m)
M3D-C1
Ideal mode unstable (g > 0) in M3D-C1
KSTAR 16295

## Slide 9
Comparative equilibria with high q95 are stable to n = 1 in DCON
Unlike the high bN case, equilibria at lower bN is mostly stable to n = 1 ideal modes in DCON
The elevated q-profile at higher BT leads to higher qmin above 1
  No indication of sawteeth found in the MHD spectrogram
  Possible lack of non-linear seeding from sawteeth could improve the neoclassical tearing mode stability
High q95 equilibria
DCON
KSTAR 16325
DCON computed no-wall dW and EFIT qmin in high q95 equilibria of shot 16325
High q95 equilibria
qmin (w/ MSE)

## Slide 10
Tearing stability is examined by the resistive DCON code
High q95 equilibria
R-DCON
High bN equilibria
R-DCON
KSTAR 16325
KSTAR 16295
Resistive DCON is used to compute the tearing stability index, D′, at q = 2 surface by using the outer layer solutions
D′ which is mostly positive in the target equilibria predicts unstable tearing mode, and explains the importance of the neoclassical effects in the observed stability
A.H. Glasser, et al., Phys. Plasmas 23 (2016) 112506

## Slide 11
Resistive 2/1 tearing mode stability of high bN equilibria
examined by using M3D-C1
(a) The radial velocity eigenfunction of a 2/1 tearing mode from M3D-C1 and (b) corresponding Poincaré plot with exaggerated displacement
2/1 tearing mode stable
(g < 0) in M3D-C1
(a)
(b)
M3D-C1
1.0
0.5
0
-0.5
-1.0
1.2
1.4
1.6
1.8
2.0
2.2
2.4
R (m)
Z (m)
Linear stability of the observed 2/1 tearing mode computed by M3D-C1
  Used experimental equilibrium and measured Te profile from TS diagnostic for the input resistivity
  Increased resolution around the mode rational surface using the adaptive meshing
The 2/1 tearing mode is marginally stable in M3D-C1
  Unstable experimentally
  Computed negative mode growth rate
KSTAR 16295
S.C. Jardin, et al., J. Comput. Phys. 226 (2007) 2146

## Slide 12
TRANSP analysis examines jBS-profile alignment with tearing rational surface
Interpretive TRANSP analysis using KSTAR experimental equilibria and measured internal profiles to calculate plasma evolutions especially for the non-inductive plasma current
Bootstrap current profile from TRANSP and q-profile from MSE-constrained EFIT will be used for improved tearing stability analysis including the pressure-driven terms
SEE J.H. Ahn’s talk on 11/29/17
KSTAR 16295
High bN
TRANSP jBS
q = 2
(t = 2.3 s)
High q95
TRANSP jBS
q = 2
(t = 8.3 s)
KSTAR 16325

## Slide 13
Kinetic effects modify ideal MHD n = 1 stability (MISK code)
  Collisional dissipation
  Rotational stabilization
Stability modification depends on
  Integrated wf profile: resonances in dWK
  Particle collisionality
Plasma is stable when rotation is in resonance
  l = 0 harmonic : resonance with precession drift frequency
  l = -1 harmonic : resonance with bounce frequency
RWM stability evaluated with ideal and kinetic components allows for passive stabilization of the RWM
B. Hu, et al., PRL 93 (2004) 105002
J.W. Berkery, et al., PRL 104 (2010) 035003
S.A. Sabbagh, et al., Nucl. Fusion 50 (2010) 025020
kinetic
modification
Trapped ion component (typically dominates Re(dWK))
collisionality
precession drift
bounce
E⨉B
J.W. Berkery, et al., MHD Workshop (2015)

## Slide 14
MISK calculations find the equilibrium is stable to RWM as is consistent with experiment (rotation profile is scaled from 0.1 to 2 times in the analysis)
Energetic particles are predicted to give a strong stabilizing effect to RWMs
J.W. Berkery, et al., PRL 104 (2010) 035003
Y.S. Park, et al., Nucl. Fusion 51 (2011) 053001
n = 1 RWM stability diagram with scaled experimental rotation profiles
Kinetic modification of RWM stability is evaluated with including energetic particle effects
w/ Energetic
particles
High q95
MISK dWK
Experiment (w/ EP)
KSTAR 16325 @ 11.975 s
w/o Energetic
particles
Experiment (w/o EP)
Stable
(gtw < 0)
Experiment (w/o EP)
KSTAR 16295 @ 2.315 s
High bN
MISK dWK

## Slide 15
RWM feedback sensors on passive plates
RWM active control system hardware is installed in KSTAR
KSTAR RWM feedback model in VALEN-3D
For plasma operation at bN > bNno-wall, RWM control system is prepared in KSTAR
  The middle in-vessel control coils (IVCCs) minimizes the inductive shielding by the copper passive stabilizing plates during RWM feedback
  Three sets of RWM Bp sensors with max. 8 toroidal locations (Upper – MPZU03 & MPZU04, and Lower – MPZL20) have been installed on the inner surface of the passive plates total 20 independent Bp measurements for RWM identification (fsample = 20 kHz)
Y.S. Park, et al., Phys. Plasmas 21 (2014) 012513
MPs
~8,000 finite elements
RWM sensors
<lower passive plate - top view>
MPZU04 (8 sensors)
(R = 2.10 m,
Z = 0.68 m)
28o
49o
118o
142o
208o
229o
298o
322o
MPZL20 (8 sensors)
(R = 2.18 m,
Z = -0.56 m)
MPZU03 (4 sensors)
(R = 2.18 m,
Z = 0.56 m)
Middle-IVCC
RWM control
coils (4 coils)
f
Primary RWM control coils
(Middle FEC/RWM)
NSTX-type future RWM
sensors (imaginary)

## Slide 16
New RWM sensors will give superior control performance over the previous device sensors
The design advantages of the new RWM sensors result in greater mode control - almost up to the ideal with-wall limit (Cb = 98%, bN = 4.8)
  RWM control performance of the new RWM sensors
(Cb = 37 %)
(Cb = 86 %)
MPZU03-L20 sensor
w/o compensation
MPZU04-L19 sensor
w/o compensation
MPZU03-L20 (8+8) @ R = 2.188 m
MPZU04-L19 (8+8) @ R = 2.099 m
New RWM sensor
performance
SLs
SLs
New RWM sensors
Y.S. Park, et al., Phys. Plasmas 21 (2014) 012513

## Slide 17
Strong coupling between RWM feedback sensors and passive plates could be detrimental to RWM feedback
Transient effects of the induced currents on the passive plates have been examined by VALEN-3D code
KSTAR passive plates are found to give a significant inductive effect on RWM sensor measurement when RWM coils are activated
Computed induced currents on the internal passive conductors when 10 Hz n = 1 rotating field is applied from RWM control coils (m-IVCCs)
15
10
5
0
-5
-10
-15
Magnetic Field (G)
VALEN-3D computed sensor measurement
t = 0.845 s
Time (s)

## Slide 18
DC sensor compensations for RWM identification
Define the DC-compensated dB:
: corrected by base-line subtraction, drift correction
Significant inductive component still remains in dBDC which can be compensated by using either:
  - Voltage loops on passive plates (not presently available in KSTAR)
  - RWM coil current (dIRWM/dt) as vessel current sources
< DC compensated dBDC >
< RWM coil I >
< Raw dB >

## Slide 19
AC sensor compensation can eliminate the remaining dB components after the DC compensations
Similar to NSTX, use low-pass-filtered (LPF) RWM coil currents as the source of the inductive dB
Define the AC compensated dB:
The coefficient matrix p has max. 20 (Nsensor) x 12 (Ncoil) x 3 (Nt) = 720 elements
LPF with 3 different t values has been tested
Tested t set well compensates the inductive effect. For the entire RWM sensors, remaining |dB| < 2 G after DC+AC compensations
< dBAC with t1 >
< dBAC with t1, t2 >
< dBAC with t1, t2 , t3 >
dBDC
dBDC
dBDC
t1 = 92 ms
t2 = 3 ms
t3 = 215 ms
Remaining after t1
Compensated by t2
Compensated by t3

## Slide 20
Algorithms for mode identification (mode-ID)
The magnetic perturbation has an amplitude (ARWM) and phase (fRWM)
At the i-th sensor, the measured mode amplitude is:
Combine signals to form an amplitude and phase of the plasma 3D perturbation
Convert the sensor fields at each time point to amplitude and phase
Outputs passed within PCS to RWM feedback algorithms for control current request
Algorithm is presently being implemented in KSTAR PCS for use in 2018
M : mode-ID matrix (20 x 2) for KSTAR

## Slide 21
Measured amplitude and phase of slowly rotating MHD mode
Since RWMs have yet to be measured on KSTAR, mode identification has been tested for slowly rotating tearing modes (w/o applied feedback)
Used 10 Bp sensor differences (180o opposing sensor pairs) for n = 1 identification
Mode identification well measures the evolution of n = 1 locking tearing mode
KSTAR 15279
Exp. by Y.M. Jeon (NFRI)
2/1 mode
locks
Toroidal magnetic probe spectrum and mode amplitude
Fast Mirnov probe
Measured mode amplitude and phase by mode-ID
Lower Bp
difference #1
Mode starts to be
measured by RWM sensors
(fsample = 200 kHz)

## Slide 22
Conclusions and Next Steps
KSTAR plasmas have exceeded the predicted ideal n = 1 no-wall limit
Ideal and resistive stability of the achieved high bN is analyzed
  Kinetic EFIT with MSE constraints is used for accurate stability analysis
  Achieved high bN equilibria are subject to ideal n = 1 mode instability (DCON, M3D-C1)
  Resistive DCON analysis emphasizes the role of the pressure driven effects in the observed tearing stability
  Kinetic RWM stability can explain the observed stability at high bN (MISK)
Development of algorithm for RWM identification
  Significant dB induced mostly by the passive plate response is well compensated
Next Steps
  Improve stability analysis by employing the pressure driven terms calculated by TRANSP, and by further refinement in the kinetic EFIT reconstructions
  Implement the developed mode-ID routines into the KSTAR PCS
  Attempt experiments in 2018 to improve sustained high bN, and probe MHD stability