## Slide 1
Transient CHI Plasma Start-up
R. Raman
University of Washington / NSTX-U
Acknowledgments
T.R. Jarboe, B.A. Nelson (University of Washington)
D. Mueller, M. Bell, M. Ono, J.A. Menard, S.C. Jardin, F. Ebrahimi (PPPL)
K.C. Hammond (IPP Garching),
K. Kuroda, K. Hanada (Kyushu University)
and the NSTX Research Team
NSTX-U Magnetic Science Meeting
PPPL, February 4, 2019
NSTX
Supported by
College W&M
Colorado Sch Mines
Columbia U
Comp-X
General Atomics
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec
This work is supported by US DOE contract numbers FG03-96ER5436, DE-FG02-99ER54519 and DE-AC02-09CH11466

## Slide 2: Outline
Motivation for solenoid-free plasma startup
Implementation of Transient CHI capability in STs
Results from HIT-II and NSTX
Scaling and modeling results
Implementation on QUEST (Japan) and on URANIA (Univ. of Wisconsin)
Initial results from QUEST
Application to reactors
Summary and conclusions

## Slide 3: Motivation & Plans
Enables lower aspect ratio configurations
  Maybe necessary for a compact ST burning plasma device
  Would also simplify a tokamak, making space in reactor core more useful for other systems (improved fueling, RF launchers, blankets)
Transient Coaxial Helicity Injection plasma startup method first developed on HIT-II at the University of Washington
  NSTX demonstrated Transient CHI feasibility on a large device
  Central Solenoid flux savings
  Transitioning to H-mode when coupled to induction with NBI heating
Now testing reactor relevant electrode configuration on QUEST
  Working on CHI design for URANIA (formerly PEGASUS)
  Examining feasibility for installation on ST-40 (3T device)
  Will conduct Conceptual Design Study for NSTX-U

## Slide 4: Transient CHI: Axisymmetric Reconnection Leads to Formation of Closed Flux Surfaces
Parameters to consider
  - Current multiplication factor
  - Effect of toroidal field
  - Magnitude of generated plasma current
  - New desirable features?
Fast camera: F. Scotti, L. Roquemore, R. Maqueda

## Slide 5: Fast Camera Images of Transient CHI Discharges on NSTX
Fast camera: F. Scotti, L. Roquemore, R. Maqueda

## Slide 6: CHI Initially Developed on HIT-II & Validated and Improved on NSTX
Concept exploration device HIT-II
Built for developing CHI
Many close fitting fast acting PF coils
4kV CHI capacitor bank
Proof-of-Principle NSTX device
Built with conventional tokamak components
Few PF coils
1.7kV CHI capacitor bank
NSTX plasma is ~30 x plasma volume of HIT-II

## Slide 7: Externally Produced Toroidal Field makes CHI much more Efficient in a High Field ST / Tokamak
* T.R. Jarboe, Fusion Tech. 15, 7 (1989)
Injector current* Iinj must meet bubble-burst condition for plasma to expand from injector to main vessel
Toroidal current* generation is proportional to the ratio of toroidal flux ψtor to injector flux ψinj
Capacity to generate plasma current Ip is proportional to ψinj
NO NEED TO FIGHT WITH AN ALREADY FORMED PLASMA

## Slide 8: Very High Current Multiplication (Over 70 in NSTX) Aided by Higher Toroidal Flux
30kA of injector current generates 120kA of plasma current
Best current multiplication factor is 6-7
Current multiplication factor in NSTX is 10 times greater than that in HIT-II
- Over 200kA of current persists after CHI is turned off
R. Raman, B.A. Nelson, D. Mueller, et al., PRL 97, (2006) 17002
Plasma current
Injector
Current
Current Multiplication Factor
(kA)
HIT-II
NSTX
R. Raman, T.R. Jarboe, B.A. Nelson, et al., PRL 90, (2003) 075005-1

## Slide 9: CHI Started Discharge Couples to Induction and Transitions to an H-mode Demonstrating Compatibility with High-performance Plasma Operation
Te & Ne from Thomson
Ti from CHERS
Discharge is under full plasma equilibrium position control
  Loop voltage is preprogrammed
CHERS : R. Bell
Thomson: B. LeBlanc
R. Raman, D. Mueller, B.A. Nelson, al., PRL 104, (2010) 095003

## Slide 10: Using Only 27kJ of Capacitor Bank Energy CHI Started a 300kA Discharge that Coupled to Induction
Ramped up to 1MA after startup, using 0.3Wb change in solenoid flux
Hollow electron temperature profile maintained during current ramp
  - Important beneficial aspect of using CHI startup
B.A. Nelson, T.R. Jarboe, D. Mueller, et al., NF 51, (2011) 063008

## Slide 11: Standard L-mode NSTX Discharge Ramps to 1MA Requiring 50% More Inductive Flux than a CHI Started Discharge
Reference Inductive discharge
  - Uses 396mWb to get to 1MA
CHI started discharge
  Uses 258 mWb to get to 1MA (138 mWb less flux to get to 1MA)
CHI started
Reference NSTX Inductive start-up
Plasma current

## Slide 12: Closed Flux Current Generation in TSC is due to the generation of a positive loop voltage as the injected plasma decays
R. Raman, S.C. Jardin, J. Menard, et al.,
NF 51, 113018 (2011)

## Slide 13: Sweet-Parker Reconnection and Plasmoid Instability also Lead to Reconnection in the Injector Region (NIMROD Simulations)
Sweet-Parker Reconnection
Plasmoid Mediated Reconnection
F. Ebrahimi, et al.,
PoP 20, 090702 (2013)
PoP 21, 056109 (2014)
PRL 114, 205003 (2015)
It would be helpful to experimentally measure these in a ST or off-line setup (with supporting simulations) as it contributes to research related to CHI Start-up, basic plasma sciences, and other applications

## Slide 14: NIMROD Simulations also Show High Fraction of Open Flux Conversion to Closed Flux (~70%, as in HIT-II / NSTX)
F. Ebrahimi, R. Raman, NF-Letter 56 (2016) 044002

## Slide 15: Encouraging Experimental Results From Two STs and Supporting Modeling Results From TSC & NIMROD Motivated Reactor Studies
Toroidally continuous insulator would be located in a region shielded from neutrons
Menard, Brown et al., NF 56 (2016) 106023
Brown, Menard, El Guebaly et al., FS&Technol. 68 (2015) 277
Raman, Brown, El Guebaly et al., FST 68 (2016) 674

## Slide 16
CHI on QUEST is Developing ST-FNSF Relevant Single-Biased Electrode Configuration
R = 0.68m, a = 0.4m, 0.25T

## Slide 17
Transient CHI on QUEST has Shown Reliable Discharge Initiation, and Plasma Growth in Biased Electrode Configuration
K. Kuroda, R. Raman, K. Hanada, et al., Plasma Phys. Control. Fusion 60, (2018) 115001
Current objectives
  Current persistence
  Closed flux current generation
Future objectives
  - Heat CHI plasma with ECH
  - Impurity reduction
  - Increase current magnitude

## Slide 18: Next experiments will bias electrode plate with respect to inner wall, as on NSTX / HIT-II
TSC simulation of previous configuration – electrode biased to outer wall
TSC simulation of next configuration to be tested – electrode biased to inner wall
K. Kuroda (Kyushu University)

## Slide 19
CHI research on URANIA plans to develop a double-biased electrode configuration and maximize current generation
Benefits of double biased electrodes
High Ip up to 300 kA (@ PF coil limits for Ip)
Coupling to ECH
Collaboration with University of Wisconsin
J. Reusch, R. Fonck, M. Bongard
F. Ebrahimi (Theory support)
NOTE: DRAFT Concept under review, revisions, and discussion – This is not the final design (an important objective is to finalize the design soon)
Cathode
Anode
Coax Current Feed
Drawing by J.A. Rogers (U-Wash.)
R ~ 0.45m, a ~ 0.3m, 0.6T

## Slide 20: Super-X Divertor-like Configurations Naturally Suited for CHI & Have Large Injector Flux Capability
Menard, Brown et al., NF 56 (2016) 106023

## Slide 21: Reactor Scenario for Solenoid-free Plasma Start-up and Current Ramp-up to Sustained Operation Levels Has Three Phases
Desirable to to simplify start-up/ramp scenario to two phases
  Reduce reliance on non-inductive current ramp-up phase
  High BT in new emerging experiments should permit CHI start-up at high levels of injector flux
  Super-X divertor configurations may have the needed flux for full current start-up
  NIMROD simulations is studying MHD limits to high current generation, up to levels of full sustained current (no MHD limits obvious thus far)
Start-up &
Ramp-up strategy
SFPS
ECH heating
(Start-up Phase)
ECH assist (Ramp-up phase)

## Slide 22
Simulations with TSC support expectations of higher current, self-heating power, and temperatures with increased injector flux
Tokamak Simulation Code (TSC)
  Time-dependent, free-boundary equilibrium and transport solver
  Solves MHD/Maxwell’s equations coupled to transport and Ohm’s law
Initial study: NSTX configuration with increasing levels of injector flux:
  52 mWb (typical NSTX experiment), 104 mWb, and 208 mWb (NSTX-U capability)
Supports main predicted trends
  Ip increases in proportion with ψinj
  Heating power, Te increase faster

## Slide 23
ST-40 & NSTX-U Have the Potential to
Demonstrate Full Non-Inductive Operations
Parameters | HIT-II | NSTX | QUEST | URANIA (to be finalized) | ST40 | NSTX-U
Major radius [m] | 0.3 | 0.86 | 0.68 | 0.45 | 0.4 – 0.6 | 0.68
Minor radius [m] | 0.2 | 0.66 | 0.4 | ~0.3 | ~0.3 0.35 | 0.65
BT [T] | 0.5 | 0.55 | 0.25-0.5 | 0.15-0.6 | 3 | 1
Injector flux (mWb) | 16 | 50 | 28 | ~60 | TBD | 200
Projected Start-up current (kA) | 100 | 200 | <150 | ~300 | >500 | >500
Nominal Ip (kA) | 250 | 1400 | ~200 | ~300 | 2000 | 2000

## Slide 24: NSTX has Made Considerable Progress Towards Developing Transient CHI as a Viable for Solenoid-Free Plasma Startup Method
Transient CHI first developed on a small ST and then validated on a large ST
Favorable scaling (based on HIT-II / NSTX Experiments and simple scaling relations supported by TSC and NIMROD simulations) gives confidence the method can be applied to larger devices
Successful coupling of CHI started discharges to inductive ramp-up & transition to an H-mode demonstrates compatibility with high-performance plasma operation
CHI start-up has produced the type of plasmas required for non-inductive ramp-up and sustainment (low internal inductance, low density)
Reactor-relevant electrode configuration being developed on QUEST and URANIA
Demonstration of full non-inductive operations including Transient CHI start-up and current ramp-up to sustained operations would provide the confidence necessary to build reactor-scale STs and tokamaks without reliance on the central solenoid

## Slide 25: Back-up Slides

## Slide 26: CHI Started Discharges Require Less Inductive Flux than Discharges in NSTX Data Base
NSTX Data Base Analysis: M. Bell
Most recent CHI-started discharges require less flux than shown here

## Slide 27: Inductively Coupled Current Ramps-up After Input Power Exceeds Radiated Power
HIT-II Results
Identical loop voltage programming for all cases
Coupling current increases as injector flux is increased
Radiated power can be decreased by using W or Mo target plates
  Start-up plasma (inductive or CHI) is cold (few 10s of eV)
    Reduce Low-z line radiation
  Auxiliary heating would ease requirements on current ramp-up system
R. Raman, T.R. Jarboe, R.G. O’Neill, et al., NF 45 (2005) L15-L19
R. Raman, T.R. Jarboe, W.T. Hamp, et al., PoP 14 (2007) 022504

## Slide 28: Plasma Discharge Ramping to 1MA Required 35% Less Inductive Flux when Coaxial Helicity Injection (CHI) is Used
High elongation
Low inductance
Low density
CHI assisted startup in NSTX
CHI generates plasmas with low ne so that ECH could be used to heat these plasmas
27 kJ of stored capacitor bank energy used for CHI plasma start-up
CHI produced plasma is clean
(Discharges have transitioned to H-mode after coupling to induction)