## Slide 1
Sustained High Power Density (SHPD) Facility: Update on Community Initiative in San Diego
presented by
RJ Buttery with thanks to DIII-D colleagues on our SHPD team
for the
PPPL Seminar
April 1st 2019

## Slide 2: We are here to consult with our PPPL & NSXT-U colleagues
Invite participation in this SHPD analysis effort
  Directly join discussions and analysis projects
  Initiate a group on your favorite topic, calculate metrics, draw from equilibria being generated
Invite ideas and good points for SHPD analysis
  What are we missing? What analyses can be done? What metrics can we use?
Identify complementary analysis toward SHPD and wider US roadmap
  Provide richer data set to inform community discussions
Understand points of view, start to find a viable path
Feel free to join our discussion and see what we are up to. All material on our web at: https://diii-d.gat.com/diii-d/SHPD

## Slide 3: What does a Next Step Facility Look Like?
The U.S. program is embarking on a path to a fusion pilot plant
An intermediate facility has been proposed by NAS panel as part of a wider program to close the gap on the pilot
What are its physics missions?
What are its parameters?
We are undertaking an initiative amongst DIII-D program participants (& others interested) to understand how parameters & feature of the facility enable physics missions toward pilot

## Slide 4: U.S. & NAS Context to Private Fusion
DIII-D
NSTX-U
Theory & Sim
New Technology Lines
Sustained High Power Density
ITER
U.S. Pilot Plant & Nuclear Test Facility
International Facilities
Private 4
Private 3
Private 2
Private 1

## Slide 5: What this Initiative is Not
It is not an attempt to determine the mission of the next step U.S. facility
  We see choice of mission as a higher level, community-wide question & discussion
Similarly we do not expect to fix parameters to a particular design point
  We aim to explore a wide parameter space and design choices to inform this
It is not an attempt to develop a DIII-D program position on SHPD
  DOE has merely granted that such community work can be charged to such grants
It is not an attempt to see what can be built in Sorrento Valley
  We neither rule this in or out – its important to simply understand needs from a physics mission & U.S. strategic perspective
It is hoped this effort will lead to a white paper, understanding and capabilities that help assess how physics missions trade off with device parameters and features
Work in this effort might also be used as the basis for other advocacy white papers by participants in this effort or by other colleagues

## Slide 6: Goal of Our Present SHPD Initiative
To develop an understanding of how facility parameters tie to physics missions of an SHPD
  to inform community discussion on what is possible / combinable as a realistic U.S. path

## Slide 7
Physics Needs

## Slide 8: Why an SHPD is Needed
There is a strong and exciting mission for DIII-D and NSTX-U
  Facilities being upgraded to address critical plasma physics, develop new techniques & technologies, find candidate solutions for fusion energy
But there remain critical plasma physics questions that go beyond what the present generation of facilities can address
  To sustain configuration & power handling beyond what ITER can do
  To access reactor like physics regimes & parameters – remove extrapolation gap
  To integrate parts of the solution that trade off against each other
To move to a pilot plant D-T reactor, we need to have robust plasma solutions that we can be confident work reliably
  Expensive and beyond scope for pilot to do all this D-D level work
NAS notes needs for: “increase fusion power density”, “continuous high-pressure compact plasma”, “increased values of normalized size, RB/T0.5”, “larger magnetic field… and… power”, “A follow-on national facility… provide new advanced tokamak studies closer to burning plasma conditions” “high power density research facility”, “high field”, “high bN”, “optimal shaping”
Its vital for us to start on a next step facility ASAP
🙂
🤔
🤓

## Slide 9: Understanding an Integrated Solution Requires Improved Performance
Core and divertor physics are governed by different parameters:
Pedestal
Collisionality,
core
Separatrix
Divertor
Closure & neutrals
Pedestal physics
ndiv
q||
nsep
Pedestal
Edge transport barrier
Core
Radius
Pressure
Notes: Shaping, 𝑆=0.4+2𝛿

## Slide 10: Understanding an Integrated Solution Requires Improved Performance
Core and divertor physics are governed by different parameters:
Pedestal
Collisionality,
core
Separatrix
Divertor
Closure & neutrals
Pedestal physics
ndiv
q||
nsep
Pedestal
Edge transport barrier
Core
Radius
Pressure
Notes: Shaping, 𝑆=0.4+2𝛿

## Slide 11: Understanding an Integrated Solution Requires Improved Performance
Peeling
Low
High
Ballooning
JET pedestal
[Maggi, NF2015]
(Normalized pressure gradient)
Core and divertor physics are governed by different parameters:
Pedestal
Collisionality,
core
Separatrix
Divertor
Closure & neutrals
Pedestal physics
ndiv
q||
nsep
Pedestal
Edge transport barrier
Core
Radius
Pressure
Notes: Shaping, 𝑆=0.4+2𝛿

## Slide 12: Understanding an Integrated Solution Requires Improved Performance
Core and divertor physics are governed by different parameters:
Pedestal
Collisionality,
core
Separatrix
Divertor
Closure & neutrals
Pedestal physics
ndiv
q||
nsep
Core-edge solution depends on progress in each region
  Improved pedestal (nsep:nped) and divertor (ndiv:nsep) solutions play a key role
Super H mode? Shaping, a/r, …
Slots, Snowflake Super-X, SAS…
Notes: Shaping, 𝑆=0.4+2𝛿

## Slide 13: Understanding an Integrated Solution Requires Improved Performance
Core-edge solution depends on progress in each region
  Improved pedestal (nsep:nped) and divertor (ndiv:nsep) solutions play a key role
Core and divertor physics are governed by different parameters:
Pedestal
Collisionality,
core
Separatrix
Divertor
Closure & neutrals
Pedestal physics
ndiv
q||
nsep
Te
ne
Pedestal vs divertor closure
Strong interaction between these regions
  Depends on opacity
  High density an important governing parameter
  Higher field needed for high density & low
Notes: Shaping, 𝑆=0.4+2𝛿

## Slide 14: May Other Examples of Reactor Needs that Motivate Plasma Research Beyond Present Generation of Tokamaks
Understanding pedestal projection (high pedestal opacity low n*)
  Identify density limit
High heat flux divertor solution – with high neutral & g opacity
High bootstrap fraction core to develop predominantly self-driven solutions
  High thermal fraction for relevant EP physics & RWM stabilization physics
  High ion-electron collisionality & low rotation & n* for core transport projection
Advanced RF schemes with high efficiency and survivability
Understanding wall dynamic
Simply reducing the extrapolation gap
ITER provides key complementary data & validations, but steady state reactor solutions poses additional challenges

## Slide 15: Full Physics Simulations Show Key Levering Parameters to Explore
Projects H98~1.3-1.5 leading to solutions at 4m 6-7T
  Converged self-consistent fully non-inductive plasmas
Trade-offs & optimizations:
  Shaping is key: Q~shaping2
  Higher density reduces H&CD needs
  Higher bN raises fusion performance
  Higher BT improves confinement
  Higher efficiencies raise Pnet-electric
  Dissipative divertor vs core radiation
  Transients must be controlled
Important to develop and validate these solutions
Improved physics & technology reduces required scale, fusion power, fluxes and cost
PH/CD (MW)
PH/CD (MW)
PNET
PH/CD
PNET
PH/CD
Fix bN = 3.5
Fix neped/nGW = 0.9
MW
FASTRAN 4m 7T fully non-inductive plasmas stationary TGLF-EPED-CD-EFIT solutions
7T
6T
Fixed IP & density
Notes: ADD SUPER H PART. Shaping is key. NOT ARGUE ONE SPOT…

## Slide 16
Physics Needs
Approach of our Initiative

## Slide 17: SHPD Initiative: Approach and Boundary Conditions
Identify range of potential missions (NAS, Wade FPA, reactor design needs, etc.)
Identify metrics that characterize access to those missions
Develop an equilibrium parameter space and facility options to span the missions
  Simulation and other analysis efforts
  Simulation: Initial 1D about a center point, then some guided
Calculate metrics to understand how physics access changes over this range
  Interpret under various physics themes
  Write neutral white paper to inform community
There may also be position white papers on various topics
  Not centrally coordinated, but subsets of colleagues may cluster to develop
Boundary conditions  not hard ones but, guided by NAS
  Something that can be started soon. Manned access as science tool. Not nuclear?
  Example trade offs to discuss: short/long pulse, hot/cold metal/C wall, …

## Slide 18: FASTRAN Integrated Simulation Suite Provides Tool To Validate Physics Models & Project Performance
Equilibrium/Loop Voltage
EFIT
[Park Comp Phys Com 2017]

## Slide 19: FASTRAN Integrated Simulation Suite Provides Tool To Validate Physics Models & Project Performance
Edge Pedestal
EPED
Equilibrium/Loop Voltage
EFIT
[Park Comp Phys Com 2017]

## Slide 20: FASTRAN Integrated Simulation Suite Provides Tool To Validate Physics Models & Project Performance
Turbulent Transport
TGLF
Edge Pedestal
EPED
Equilibrium/Loop Voltage
EFIT
[Park Comp Phys Com 2017]

## Slide 21: FASTRAN Integrated Simulation Suite Provides Tool To Validate Physics Models & Project Performance
Turbulent Transport
TGLF
Off-axis Current Drive
NUBEAM
Edge Pedestal
EPED
Equilibrium/Loop Voltage
EFIT
[Park Comp Phys Com 2017]

## Slide 22: Initial List of Aspects to Consider
Identify representative mission set & metrics (see next)
Scope out Equilibrium space with integrated physics model solutions
  Serves as basis to calculate range of other parameters
  Shaping: extend codes to calculate & identify benefits
Consider H&CD options
Shaping: extend codes to calculate & identify benefits
Divertor mission, flexibility, metrics
Materials/PMI – mission, choice, needs, metrics
Activation and manned access
Coil options – viability of shape & power needs
More…?
Various subtopic discussions & meetings implied or invited

## Slide 23: Missions To Prepare For a Pilot Plant
Various sources and orthogonal sets (E.g. )
Wade, FPA,18
Key Concepts
Facility close physics gaps on pilot plant – develop robust solutions
Alongside existing technology program & international facilities

## Slide 24: Missions To Prepare For a Pilot Plant
Various sources and orthogonal sets (E.g. )
Some U.S. strengths and distinctive opportunities not addressed elsewhere
Key Concepts
Facility close physics gaps on pilot plant – develop robust solutions
Alongside existing technology program & international facilities

## Slide 25: Missions To Prepare For a Pilot Plant
Various sources and orthogonal sets (E.g. )
Some U.S. strengths and distinctive opportunities not addressed elsewhere
  Some requirements to incorporate into solution / need to be studied
Key Concepts
Facility close physics gaps on pilot plant – develop robust solutions
Alongside existing technology program & international facilities

## Slide 26: Missions To Prepare For a Pilot Plant
Various sources and orthogonal sets (E.g. )
Some U.S. strengths and distinctive opportunities not addressed elsewhere
  Some requirements to incorporate into solution / need to be studied
Break down to specific physics & metrics…
Key Concepts
Facility close physics gaps on pilot plant – develop robust solutions
Alongside existing technology program & international facilities

## Slide 27: Developing a Set of Mission Metrics (in progress)
Mission | Metrics | Method
Core edge | Ped-opacity, n*, nped, fGW, Pped,d,k, ioniz depth. Radiation species: Rpeak, Wall Z | Formulae from simulations
Core transport | Te/Ti, nei, r*, tE, W’ | From simulations
High BS solution | fBS, bN, bNthermal, q95, R/a, tpulse/tR, bNwall, bNnowall | From simulations
Fast ions | fEP, vEP/valfven, tools to accelerate ions | From simulations, plus some flexibility statements
Current drive | Te, B, flexibility, …? | 
Divertor | P/R, PB/R, q¦¦, Ly a, div opacity, radial transport & heat flux width, closure, detachment | TBD
PMI | Material, temperature, retention? Pulse length vs deposition time, heat flux | TBD
Transients | Ip (REs), Bresped, …? Actuators? | TBD
  What missions, metrics & methods should be considered?

## Slide 28: Some Clear Issues of Debate or Trade off Will Need to be Discussed
Long or short pulse?
  Long pulse tests PMI solutions, but will compromise manned access & so flexibility
How high in field?
  Improvements in fusion relevant metrics vs device activation & access
Tritium capability?
Normal or hot walls? Wall material?
HTS or copper?
H&CD, internal/external 3D coils, etc…
  We see these as issues for broader community discussion to converge SHPD mission in wider roadmap
  We hope our analysis can inform the degree of mission possible with various options

## Slide 29: Initial Parameter Range to Explore
Parameter | Range | Rationale
Paux | 1.5PLH  100MW | Good H mode to budget ceiling
fBS | 50 to 100% | Explore self-driven solutions (adjust IP)
BT | 4 – 7 T | High density & opacities with low n*
fpedGW | 60 – 120% | Core-ped-div integration
Elongation | To VS limit | Maximize controllable performance
Triangularity | 0.4 to 0.9 | See where benefits saturate & assess divertor challenge
Aspect ratio | 2.2 – 4 (fix a2R) | Bootstrap, EC access (code limits at 2.2)
(Fix size for now, consider R=1.4, 2m later at fixed R/a) |  | 
High performance & fully NI, high BS
Based on earlier group wide metrics discussion and focusing conversation of Buttery, Petty, Snyder, Solomon

## Slide 30: Initial Parameter Range to Explore
Parameter | Range | Rationale
Paux | 1.5PLH  100MW | Good H mode to budget ceiling
fBS | 50 to 100% | Explore self-driven solutions (adjust IP)
BT | 4 – 7 T | High density & opacities with low n*
fpedGW | 60 – 120% | Core-ped-div integration
Elongation | To VS limit | Maximize controllable performance
Triangularity | 0.4 to 0.9 | See where benefits saturate & assess divertor challenge
Aspect ratio | 2.2 – 4 (fix a2R) | Bootstrap, EC access (code limits at 2.2)
(Fix size for now, consider R=1.4, 2m later at fixed R/a) |  | 
Make pedestal NN set  TGLF scaling tool… FASTRAN
Start in center & expand in 1d
  Then pursue multidimensional exploration with goal to optimize key parameters 
Optimizations
High power, pressure
High bootstrap
High density
Divertor flux / PB/R
Lower field ($)
Lower H&CD power ($)
Size ($)
High performance & fully NI, high BS

## Slide 31: Some Scan Points Exist from 2018 NAS Exercise
Preliminary 4T 1.7m simulations found high bootstrap solutions:
  First tests not ideal: Te>Ti, high n*, needs lots of helicon
Equilibria studies identified high stability and…. ITER like pedestal P
Loarte formula showed opaque pedestal at 4T
NB
  Work needed to explore space and optimize

## Slide 32: Progress So Far – We are at Early Stages
Agreed some preliminary missions to metrify
Set ranges to explore (extendable!)
Scoping tool embarking on multi-dimensional scan
  Single point TGLF + EPED-nn. Start in middle and work out.
FASTRAN work just getting started 
  Simplified assumptions to start: fixed J profile & density peaking (will do self-consistently later)
  Initial scans in B, IP, n, PH  Encouraging trends with density
    But much else to explore & directions to push
H&CD analysis identifies promise options for ECH
  4T O mode efficient off axis CD (25A/kW) with 162GHz unit
  4T top launch 170GHz as efficient at helicon CD! (35A/kW) 
  Higher frequency gyrotrons needed for higher field & on axis (up to 203GHz available, Toshiba)
4 5 6 7 T
170GHz
162 GHz

## Slide 33: All Colleagues Welcome to Join or Tap Into Effort on SHPD
We are just starting equilibria scoping to provide basis for metrics calculation and physics assessments
Consider what is needed in your field – set up your own discussion group
  Discuss with colleagues
  Work out what physics missions, tools
  Map onto parameter & capability range we are exploring
  Feed back requirements into overall effort, so we understand trade-offs.
Join our discussions and contribute to debate with good points
Use simulations being developed as a basis for further
All material on web at: https://diii-d.gat.com/diii-d/SHPD
  Series of meeting on various themes over coming weeks
Or chat to existing participant: Buttery, Ferron, Smith, McClenaghan, Guo, Snyder, Groebner, Park, Garofalo, Leuer, Holcomb, Paz-Soldan, VanZeeland, Wu, Osborne, Grierson, Weisberg, Solomon, Wade, Guttenfelder, Meneghini, Abrams, Leonard , Petty

## Slide 34: We are here to consult with our PPPL & NSXT-U colleagues
Invite participation in this SHPD analysis effort
  Directly join discussions and analysis projects
  Initiate a group on your favorite topic, calculate metrics, draw from equilibria being generated
Invite ideas and good points for SHPD analysis
  What are we missing? What analyses can be done? What metrics can we use?
Identify complementary analysis toward SHPD and wider US roadmap
  Provide richer data set to inform community discussions
Understand points of view, start to find a viable path
Feel free to join our discussion and see what we are up to All material on our web at: https://diii-d.gat.com/diii-d/SHPD

## Slide 36: Preliminary Assessment Suggests Largest Mission Breadth Provided by Modest Size, High Field Facility
A=3,a=0.6,B=4-6T
A=3,a=0.4,B=8-12T
A=2,a=0.6,B=2-4T
Divertor Test Tokamak
Serve as ITER Satellite
Advance Fusion
Performance Metrics
Validate Efficient Current Drive
Approaches
Demonstrate Robust Transient
Control
Mitigate Tritium Retention
Establish Basis for
Low-r* Steady State
Optimize Core-Edge
Integration
Provide Basis for Reactor-Relevant Heat Flux/Erosion Control

## Slide 37: Preliminary Assessment Suggests Largest Mission Breadth Provided by Modest Size, High Field Facility
Serve as ITER Satellite
Advance Fusion
Performance Metrics
Validate Efficient Current Drive
Approaches
Demonstrate Robust Transient
Control
Mitigate Tritium Retention
Establish Basis for
Low-r* Steady State
Optimize Core-Edge
Integration
Provide Basis for Reactor-Relevant Heat Flux/Erosion Control

## Slide 38: U.S. Should Innovate to Enable Low Capital Cost Net Electric Pilot Plant
Key challenges for self-sustaining reactor:
  Breeding – Nuclear materials – Net electricity
Should address these in a compact ‘pilot plant’ test facility
  Combine missions to remove a generation  more compelling
  Low capital cost so affordable to go forward
  Do not need to be at large, low-COE scale to prove approach for that scale
U.S. proposals for ARC, Compact-AT and ST-pilot
  All at scale 100-200MWe, R~3-4m, A~2-3 & benefit from high temperature superconductors
A pilot plant would lever U.S. ITER participation
But requires additional ‘enabling research’
  To raise fusion performance & provide required technologies
Distinctive window of opportunity for U.S.
Power plants | ACT1 | SlimCS | KoreaDEMO | EU DEMO
R m | 6.3 | 5.5 | 6.8 | 7.9
IP MA | 11 | 17 | 17 | 14
Pfus GW | 1.8 | 3 | 2.9 | 2
Pnet GW | 1 | 1 | 0.5 | 0.5
Notes: BE SMARTER

## Slide 39: Research Required in Seven Areas to Enable Low Capital Cost Pilot Plant
ITER participation
  Validated physics models & reactor knowhow
Stable high performance fully noninductive core
Dissipative Divertor
Efficient current drive
Reactor materials
Demountable high temp superconducting magnets
Engineering design & breeding concepts
Tokamak research enables ITER & pilot plant missions
Work on engineering & technologies to advance pilot plant approach
These 7 missions provide opportunities for breakthroughs in understanding & performance that transform fusion prospects
DIII-D provides key opportunity to advance ITER and pilot plant research agendas

## Slide 40: Integrated Facilities Roadmap and Mission Elements
Config
QAX
Big QAX
Nuc
ENG
PMI
Magnum PSI
MPEX
FPNS 14MeV AFNS, Phoenix spallation, GDT 10dpa 50cm3
EAST, C-P: Long pulse wall evolution studies, wear, equilibration, metal and flowing walls,
ITER
Nuclear engineering & licensing
Physics ‘size’ scalings. DMS projection
High power W divertor partial detachment
Opaque pedestal. Radiative optimization
Disruption avoidance
Self-heating & a physics
ITER TBM program
Breeder design
Low dpa tests
...
Simulation Nonlinear evolutions
Engineering design and prototypes
Breeding concepts
Structural elements (joints, etc.) Stress analysis
DIII-D AUG
MASTU
NSTX-U
Theory
Underlying physics
Steady state. Novel CD Transients. Disruption mitigation
Divertor science, closure & magnetic geometry
Sample/tile tokamak tests Metal walls, liquid walls
Sustained High Power Density
Steady state core: CD projection, high bootstrap & thermal fractions, reactor pedestal & transport
High flux divertor, hot walls: recycling particle control, core compatibility
Component tests
I4,8
CFETR
Nuclear materials
Component tests
PISCES
TPE T ret
Hipher
Low dpa tests: structure, blankets embrittle, swel, trap
Liquid concepts
Advanced manufacturing
I4
Pilot Full Design
Compact VNS
GDT ST etc
Compact U.S. Pilot Plant Integrated Nuclear Test Facility
Nuclear Optimization
Breeding technology
Component testing
(Wall/breeder change outs)
Performance
Licensing
Heat extraction
Divertor confirmation
Close Fuel Cycle
Test breeding concepts
Nuclear components High dpa 14MeV evoln
T extraction
HTS
Joints
Coils
SPARC
EU-DEMO
Larger path

## Slide 41: Integrated Facilities Roadmap and Mission Elements
Config
QAX
Big QAX
Nuc
ENG
PMI
Magnum PSI
MPEX
FPNS 14MeV AFNS, Phoenix spallation, GDT 10dpa 50cm3
EAST, C-P: Long pulse wall evolution studies, wear, equilibration, metal and flowing walls,
ITER
Nuclear engineering & licensing
Physics ‘size’ scalings. DMS projection
High power W divertor partial detachment
Opaque pedestal. Radiative optimization
Disruption avoidance
Self-heating & a physics
ITER TBM program
Breeder design
Low dpa tests
...
Simulation Nonlinear evolutions
Engineering design and prototypes
Breeding concepts
Structural elements (joints, etc.) Stress analysis
DIII-D AUG
MASTU
NSTX-U
Theory
Underlying physics
Steady state. Novel CD Transients. Disruption mitigation
Divertor science, closure & magnetic geometry
Sample/tile tokamak tests Metal walls, liquid walls
Sustained High Power Density
Steady state core: CD projection, high bootstrap & thermal fractions, reactor pedestal & transport
High flux divertor, hot walls: recycling particle control, core compatibility
Component tests
I4,8
CFETR
Nuclear materials
Component tests
PISCES
TPE T ret
Hipher
Low dpa tests: structure, blankets embrittle, swel, trap
Liquid concepts
Advanced manufacturing
I4
Pilot Full Design
Compact VNS
GDT ST etc
Compact U.S. Pilot Plant Integrated Nuclear Test Facility
Nuclear Optimization
Breeding technology
Component testing
(Wall/breeder change outs)
Performance
Licensing
Heat extraction
Divertor confirmation
Close Fuel Cycle
Test breeding concepts
Nuclear components High dpa 14MeV evoln
T extraction
HTS
Joints
Coils
SPARC
EU-DEMO
Larger path
20s
30s
40s
50s

## Slide 42: Divertor, Wall & Materials Development: Facilities Role and Time Line
Nuc
ENG
PMI
Magnum PSI
I6
MPEX
20s
30s
40s
50s
FPNS 14MeV AFNS, Phoenix spallation, GDT 10dpa 50cm3
EAST, C-P: Long pulse wall evolution studies, wear, equilibration, metal and flowing walls,
ITER
Nuclear engineering & licensing
High power tests w/ partial detachment  ‘conventional’ divertor physics scaling
W divertor behavior
Opaque pedestal
ITER TBM program
Breeder design
Low dpa tests
...
Simulation Advanced materials evolution
Engineering design and prototypes
Breeding concepts
Structural elements (joints, etc.) Stress analysis
I8
DIII-D AUG
MASTU
NSTX-U
Theory
Divertor science
Closure
Magnetic geometry
Core mitigation
Liquid metal tests
Solid-liquid
Sample/tile tokamak tests
Metal walls
Sustained High Power Density
Steady state fusion core
High heat flux divertor
Relevant recycling
Impurity/particle control with hot metal walls
Component testing (D)
Core-edge compatibility
I4,8
CFETR
Nuclear materials
Component tests
I9
PISCES
TPE T ret
Hipher
I7
Low dpa tests: structure, blankets embrittle, swel, trap
Liquid concepts
Advanced manufacturing
I4
Pilot Full Design
Compact U.S. Pilot Plant Integrated Nuclear Test Facility
Nuclear Optimization
Breeding technology
Component testing
(Wall/breeder change outs)
I9
Performance
Licensing
Heat extraction
Divertor confirmation
Close Fuel Cycle
Test breeding concepts
Nuclear components High dpa 14MeV evoln
T extraction
Compact VNS
GDT ST etc

## Slide 43: U.S. Roadmap to Private Fusion
DIII-D
NSTX-U
Theory
New Technology Lines
Sustained High Power Density
Private 4
Private 3
Private 2
Private 1
HTS
Joints
Coils
SPARC
Steady state
Transients
Stability
Divertor physics & innv’n
Disruption mitigation
Novel CD
Underlying physics
Core-Edge High P Divertor
High bootstrap & thermal fraction
CD projection
Reactor transport
High b control
ITER
Nuclear engineering & licensing
Nuclear diagnostics
Physics ‘size’ scalings
DMS projection
Disruption avoidance
Self-heating & a physics
JT60-SA
High b core SND ITER satellite
CFETR
Nuclear materials
EU-DEMO
Larger path
ENG
Reactor design center
Advanced loading
Efficient power extraction
MAT
Test beds Simulations
Neutron sources…
Long pulse evaluations
CD
DIII-D NSTXU
xxx
SHPD high B T
20s
30s
40s
50s
60s
“Challenge” components
Breeding designs
Compact U.S. Pilot Plant Integrated Test Facility

## Slide 44: U.S. and NAS Context to Pilot Plant
DIII-D
NSTX-U
Theory & Sim
New Technology Lines
Sustained High Power Density
ITER
U.S. Pilot Plant & Nuclear Test Facility
International Facilities

## Slide 45: U.S. Strategy to Lead to Private Fusion
DIII-D
NSTX-U
Theory & Sim
New Technology Lines
Sustained High Power Density
ITER
U.S. Pilot Plant & Nuclear Test Facility
International Facilities
Private 4
Private 3
Private 2
Private 1