## Slide 1: Observation of a toroidal acoustic mode in a current-less toroidal device
Umesh Kumar
Collab:- R. Ganesh, K. Sathyanarayana and Y. C. Saxena
Institute for Plasma Research, Gandhinagar, India

## Slide 2: Introduction
Geodesic Acoustic Modes (GAMs) are pressure oscillations supported by plasma compressibility in a toroidal magnetic geometry where average geodesic curvature provides a restoring force.
It is believed that GAMs interacts weakly with background turbulence and help realize a quasi-stable equilibrium in Tokamaks.
In collision-less plasmas GAMs get damped in Tokamaks due to Landau damping. Collisions also damp GAMs.
GAMs can be driven unstable in Tokamaks by non-linear Reynolds stress (Itoh, 2005) or by suprathermal ions (Nazikian, 2008).
GAMs exhibit for density fluctuation and for potential fluctuation, where are poloidal and toroidal mode number respectively.
; where is ion acoustic speed, is the major radius, is the magnetic rotational transform and [Itoh, 2005].

## Slide 3: Geodesic Acoustic mode (GAM)
++++
-----

## Slide 4: Motivation
In a current-less toroidal device (CTD), is negligible. Plasma is confined only by the application of toroidal magnetic field and/or vertical magnetic field.
In a CTD, effective rotational transform cease to exist, it implies, and and no Geodesic Acoustic mode is possible.
Is it possible to drive an acoustic mode by a regular curvature in plasmas confined by open magnetic field lines?
In the present work, we attempted to experimentally investigate possibility of acoustic mode in a CTD with GAM-like structures in a nearly collision-less regime.

## Slide 5: Currentless toroidal device and Tokamak
Schematic of a Tokamak
Schematic of a CTD
Tokamak has a toroidal current which
provides poloidal magnetic field.
The net magnetic field is helical in nature.
CTD has no toroidal plasma current.
The net magnetic field is resultant due toroidal and vertical magnetic fields.
Image courtesy F. Poli (2007)

## Slide 6: Role of vertical magnetic field
is estimated by equating toroidal magnetic drift to the vertical velocity of the electron. [Nakao et al (1983)], leading to: where is single particle confinement time and a is the minor radius of torus.
Therefore as increases confinement time increases, which can result in higher plasma density.
Schematic showing torus cut open as a cylinder.
Due to , the field lines are slightly shifted in vertical direction.
Electrons follow the resultant field and help in short circuiting the .
+ + +
- - -
a

## Slide 7: Experimental assembly, BETA
EC Resonance
45 cm
15 cm
160 A
Positive direction of vertical field,
Microwave, “O” mode, 1 kW
Vertical field (VF)
coils

## Slide 8
Mode number measurement
R1 and R2 assembly provides toroidal mode number, “n”.
TP and BP assembly provides poloidal mode number “m”.
(b) GAM mode density fluctuation.
Red indicates compression and blue indicates expansion due to GAM phase velocity.

## Slide 9: Experimental profiles
Langmuir probes have been used to measure plasma parameters such as density, electron temperature, plasma potential and floating potential.
Primary ionization is caused by the ECR at -6 cm and unspent energy reflects from wall to produce secondary ionization due to upper hybrid resonance.
Experimental detection of the TAM mode is performed for three different gases viz., Neon, Argon and Krypton.
Let us first discuss the results of Argon plasma in detail.

## Slide 10: Density, electron temperature and UH resonance for Argon plasma
The profile of (a) mean density () and mean electron temperature () and (b) upper hybrid resonance, .
Here gradients in () and () are weak for the region of +1 cm to +6 cm, then scale length changes beyond +7 cm.

## Slide 11: Plasma potential and net poloidal flow
(a) The radial profile of mean plasma potential () and (b) the net poloidal flow measured using the Mach probe.
The EC resonance is shown by a vertical line in (a), which coincides with the peak in the location of electron temperature.

## Slide 12: Nature of modes for Argon plasma
Spectrogram of density fluctuation and radial variation of the observed modes for Argon plasma.
The spontaneously generated driver mode shows interchange like properties (i.e., ), has frequency =1.7 kHz .
The TAM mode excites after, the driver mode achieves its full strength. The frequency of TAM is =3.4 kHz

## Slide 13: Toroidal mode number determination for Argon plasma
Density fluctuation
Potential fluctuation
If toroidal wavelength, ; where is toroidal probe separation and is the measured phase difference.
Coherence, , for all cases (not shown here).
These error-bars are not shown for these measurements.
r

## Slide 14: poloidal mode number determination for Argon plasma
Density fluctuation
Potential fluctuation
The phase for density fluctuation for 3.4 kHz is 0.8 or more beyond ΔZ 10cm.
Coherence > 0.8 and for potential phase varied from 0.2 to 0.7 in the same region.
These error-bars are not shown for these measurements.

## Slide 15: Non-linear interaction of density fluctuation at r=+5 cm
The driver mode at 1.7 kHz interacts with itself.
It implies that the 3.4 kHz peak is due to the self non-linear interaction of the 1.7 kHz.
Presence of low amplitude background fluctuations is visible for frequencies beyond 20 kHz.

## Slide 16: Variation of mode frequencies with ion mass
In order to confirm the acoustic-like nature () of the observed mode, the ion mass has varied.
Both the driver and TAM modes exist for all the ion masses and exhibit acoustic nature.
Ne (20 u)
Ar (40 u)
Kr (82 u)

## Slide 17: Variation of frequency of the observed modes with the ion mass
The error-bars are due to frequency resolution and shot to shot variation in the frequency.
A dashed black line has been added to aid the view.
Thus demonstrating the Acoustic nature of both the modes.

## Slide 18: Summary
Characteristics | Driver Mode | TAM
Generation | Not clear (spontaneously generated) | Generated by non-linear interaction of driver mode with itself
Radial variation | Global, discrete | Global, discrete
Frequency |  | 
Mode characteristics | (for both density as well as potential fluctuation) | (for potential fluctuation) (for density fluctuation)
Acoustic nature |  | 
Nonlinear interaction | Interact with itself and background turbulence | Interact with background turbulence
Nature | Interchange like (), exact nature not known | Analogous to GAM often observed in Tokamak
Characteristics | Driver Mode | TAM
Generation | Not clear (spontaneously generated) | Generated by non-linear interaction of driver mode with itself
Radial variation | Global, discrete | Global, discrete
Frequency |  | 
Mode characteristics |  | 
Acoustic nature |  | 
Nonlinear interaction | Interact with itself and background turbulence | Interact with background turbulence
Nature |  | Analogous to GAM often observed in Tokamak

## Slide 19: Conclusion
A discrete, global TAM mode is observed in a simple toroidal device for the very first time.
The frequency of the observed TAM mode is almost three times that of theoretical GAM frequency for a CTD.
In our finding, we observe that an unstable () finite frequency spontaneously generated acoustic mode, non-linearly couples with itself to drive the TAM mode.
The frequency of both the observed modes, ; is the mass of the ion. Thus confirming the acoustic-like nature of the observed mode. [Umesh Kumar, Physics of Plasmas, 26, 072307 (2019)]

## Slide 20: Unresolved issues
The exact nature and origin of the driver mode is not known.
The reason for high frequency of TAM is not known yet.
The nonlinear interaction shows energy conservation i.e, but not momentum conservation . The reason for this not clear. It indicates that the observed TAM mode is not a normal mode [Zhang (2009), Fu (2011), Qiu (2017)].
The detailed theoretical or numerical explanation of the observed phenomenon is not yet attempted.

## Slide 21: Thank you

## Slide 22: Bonus slides

## Slide 23: Geodesic curvature
For a curve on a surface has normal curvature and geodesic curvature .
In BETA, magnetic field lines are characterized by implies .
For a helical field lines, ; again .
As applied vertical magnetic field varies as a function of (); where could be a function deciding helical nature as well as non-uniformity of the pitch.
; if it implies . For BETA, h(s), could be a nonlinear function in s which determines the geodesic curvature.

## Slide 24: Geodesic curvature

## Slide 25: Cross phase and coherence of driver and TAM modes

## Slide 26: Potential fluctuation spectrogram

## Slide 27: Zoomed in bicoherence plot

## Slide 28: Plasma sources used
Hot cathode source
A 20 cm long and 2 mm thick tungsten filament is mounted at the minor axis at a particular toroidal location.
Toroidal fields at the minor axis are 220 G, 330 G, 440 G and 750 G.
Discharge is struck between wall and hot cathode.
Discharge current is limited to 5 A and discharge voltage obtained is around 45-50 V.
Microwave source
Microwave of frequency GHz in “O” mode is injected from low field side (LFS).
Toroidal field at the minor axis is around 750 G.
So electron cyclotron resonance (ECR) lies around -6 cm inboard from the minor axis.
The upper hybrid (UH) resonance is further facilitates ionization.
Launched Microwave power is estimated to be around 1 kW.

## Slide 29: Experimental parameters
Working pressure has been kept to torr for all the experiments.
Mean free path for electron neutral collision (λen) ~ 1.3 m
λen < L
where L = 2πR, R is the major radius.
R = 0.45 m.
Hence plasma is considered to be weakly collisional with respect to the system.
At 220 G << 1 and < 1,
, << 1, where a = 0.15m (minor radius )
Hence both ion and electrons are magnetized with respect to the system size.
At 750 G, ions are electrons both are collision-less.

## Slide 30: Determination of topology of toroidal magnetic field
S. G. Thatipamula, Umesh Kumar et al, Rev. Sci. Instrm, 86, 033504 (2015)

## Slide 31: Determination of parallel wavenumber
Probe-1 and probe-2 are aligned on the same toroidal field line.
Both probes are rotated in the steps of to find out dip in the floating potential for each VF current.
During regular discharges both probes aligned to the same height as determined earlier.
Probe-1 is kept fixed and probe-2 is rotated to find the maximum coherence between two probes.
; where is the cross phase between probe-1 and probe-2 and is the probe separation.

## Slide 32: Numerical simulation of magnetic field
Contour plots of (a) , (b) , (c) for the ideal case, and (d) , (e) , (f) for the actual co-ordinates of TF coils for BETA for an external VF current of 12 A.
The magnetic field data is obtained using the EFFI simulation for the ideal and the actual case (Thanks to Mrs. Richa Bandopadhyay and Mr. Sharvil Patel)

## Slide 33: Simulated radial profile of vertical magnetic field
Radial profile of vertical magnetic field ; (a) an ideal TF locations and (b) the actual TF locations at different vertical distance Z for the case when VF coils are charged to 12 A current.
It can be observed that for the ideal case shown in (a) has very weak dependency on Z as compared to the actual case (b).

## Slide 34: Topology of toroidal field line
The topology of the toroidal field in Cartesian co-ordinates for actual TF coils locations simulated using EFFI code for VF currents of (a) 0 A or uncharged VF coils, (b) 12 A and (c) 60 A.
It can be observed that for 0 A case, the field lines closes on itself despite the geometrical misalignment in the TF coils.
The simulation does not consider the generation of offset magnetic field due to uncompensated current leads.

## Slide 35: Operating conditions
Base Pressure ~ 5.0 × 10-6 torr
Filament current ~ 142 A.
Discharge current ~ 5 A.
Filling gas :- Argon
Working pressure ~ 1.0 × 10-4 torr
Toroidal Magnetic field coil current~ 1 kA for 220 Gauss at the minor axis.
Vertical magnetic field coil current ~ o A, 12 A (~ 1.0 Gauss), 20 A (~1.5 G), and 60 A (~4.5 G).

## Slide 36: Mean plasma profiles
Radial profiles of (a)density, (b)electron temperature, (c) floating potential and (d) plasma potential are shown here.
•Density for widely opened field line or small higher than other values on inboard side.
•Large dip in floating potential and peak in temperature around minor axis is due to
presence of high energy electrons around minor axis.

## Slide 37: Power spectrum
Auto power spectra for (a) density at -5 cm, (b) density at +5 cm, (c)potential at -5 cm, and (d) potential at
+5 cm for four different values of vertical field coil current.
Though sampling frequency is 200 kHz, but all these plots zoomed in to 35 kHz only.

## Slide 38: Bispectrum
Bispectrum of Isat fluctuation for single shot for VF current of 0A, 12A, 20A, and 60A at -5 cm and +5 cm. for 0A and reduces further for higher currents. These plots are zoomed in up to 40 kHz.

## Slide 39: S(k,) and wavenumber
Contour plots of conditional spectrum S(k,) with embedded line showing vertical wavenumber () estimated four VF currents at -5 cm and +5 cm.

## Slide 40: Net poloidal flow
Radial profile of net poloidal flow measured using Mach probe for four values of the VF coil current.
The net poloidal flow increases slightly for 12A and 20A cases on HFS, but reduces to nearly zero for 60A case on inboard side close to limiter.

## Slide 41: Identification of instabilities
Instability | Necessary Condition | Frequency |  |  | 
Rayleigh-Taylor (RT) | < 1, < 1 |  |  |  | 
Kelvin Helmholtz (KH) | (modifies KH) |  |  |  | 
Drift like |  |  |  |  | 
Simon Hoh (SH) | < 1, 1 |  |  |  | 
Modified Simon Hoh (MSH) | < 1, 1 |  |  |  | 
Instability | Necessary Condition |  |  |  | 
Rayleigh-Taylor (RT) |  |  |  |  | 
Kelvin Helmholtz (KH) |  |  |  |  | 
Drift like |  |  |  |  | 
Simon Hoh (SH) |  |  |  |  | 
Modified Simon Hoh (MSH) |  |  |  |  | 

## Slide 42: Cross phase and coherence
Cross phase normalized to of density and potential fluctuations and Coherence between
density and potential for four values of VF current of 0 A, 12 A, 20 A and 60 A.
Coherence is more than 0.7 for all VF current.
Outboard side is dominated by flute like instabilities.

## Slide 43: Radial profile of ratio of relative potential fluctuations to relative density fluctuations. On HFS for 0 A case the value ranges from 0.5 to 1, but for 12 A and 20 A case it goes from 0.2 to 2.2 which shows presence of shear instabilities.
Ratio of potential fluctuation to density fluctuation

## Slide 44: Summary:- ch-4-I
strongly controls the equilibrium plasma profiles like density, temperature and potential.
for small a broad band exist for higher frequency on the outboard side.
Strong non-linear interaction exist for 0 A, 12 A and 20 A and interaction of dominant modes with background fluctuation is present.
Net poloidal flow tends to zero for small value of
Flute like instabilities are dominant on the outboard side.
Velocity shear is dominant for the all VF values except 60 A, where net poloidal flow is strong.

## Slide 45: Mean density profile
Plasma density with simultaneous variation in in fixed ratios.
Densities are symmetric around minor axis for small case, could be due to effective short-circuiting of the .

## Slide 46: Power spectrum of density fluctuation
Density fluctuation with simultaneous variation in in fixed ratios.
A broad band can be observed for small cases.

## Slide 47: Conclusion:- ch-4 (I & II)
strongly controls the equilibrium plasma parameters. [I & II]
Density increases on inboard side for smaller . [I & II]
Large has few modes followed by turbulent background and small shows broad band for background fluctuations. [I & II]
For small net flow tends to zero on the inboard side. [I]
Outboard side is dominated by R-T kind of instabilities and inboard side shows shear driven fluctuations. [I]
Poloidal flow generates velocity shear which facilitates generation of shear driven instabilities on the inboard side. [I]

## Slide 48: Mean ECR plasma profiles
Mean profile for ECR source with varying .
The vertical line at -6 cm is the EC region.
The EC region coincides with peak in temperature and dip in potential.
The is compared with ionization rate,
It has been observed that

## Slide 49: Resonances
Radial profile of the upper hybrid resonance for different VF current.
The vertical line at -6 cm is due to ECR ionization.
Secondary ionization occurs due to UH resonance.
The location of UH varies with VF current.

## Slide 50: Power spectrum of density fluctuation
Power spectrum of density at r=+5 cm.
For each there exist, one or two dominant mode followed by background fluctuations.
The dominant mode lies in the range of 1.7 kHz to 4 kHz.

## Slide 51: Net poloidal flow
Hot cathode
ECR source
The density for hot cathode plasma is around 5 times more than the ECR plasma.
The toroidal flow measured to be around and hence negligible.
The net flow for hot cathode source is very strong as compared to ECR source.
The horizontal line represents for zero net poloidal flow.

## Slide 52: Particle confinement for 40 A
Hot cathode plasma
ECR plasma
Density fall for hot cathode source for 40 A or large connection length case.
Density shows exponential fall, after the source is turned off.
Density fall for ECR source for 40 A or large connection length case.
Density shows linear followed by exponential fall, after the source is turned off.

## Slide 53: Particle confinement for 160 A
Hot cathode plasma
ECR plasma
Density fall for hot cathode source for 160 A or short connection length case.
Density shows exponential fall, after the source is turned off.
Density fall for ECR source for 160 A or short connection length case.
Density shows linear fall followed by exponential fall, after the source is turned off.

## Slide 54: Comparison of particle confinement time for two sources at at the minor axis
VF Current (A) | Hot cathode source |  |  | Microwave source |  |  | 
 |  | (ms) | (ms) | (ms) |  | (ms) | (ms)
0 | 0.9433 | 0.287 | 19.2 | 0.214 | 0.9337 | 0.021 | 11.3
40 | 0.9052 | 0.422 | 9.1 | 0.192 | 0.9198 | 0.045 | 4.9
160 | 0.8767 | 0.461 | 8.8 | 0.771 | 0.9380 | 0.108 | 3.08
-160 | 0.8327 | 0.589 | 10.1 | 0.291 | 0.9456 | 0.049 | 7.91
VF Current (A) | Hot cathode source |  |  | Microwave source |  |  | 
0 | 0.9433 | 0.287 | 19.2 | 0.214 | 0.9337 | 0.021 | 11.3
40 | 0.9052 | 0.422 | 9.1 | 0.192 | 0.9198 | 0.045 | 4.9
160 | 0.8767 | 0.461 | 8.8 | 0.771 | 0.9380 | 0.108 | 3.08
-160 | 0.8327 | 0.589 | 10.1 | 0.291 | 0.9456 | 0.049 | 7.91