## Slide 1
PPPL Magnetic Fusion Science Meeting
Princeton (NJ), September 9th 2019
Work supported by US DoE under grants DE-FC02-99ER54512,
DE-FC02-04ER54698, DE-SC0014264 and DE-SC0017381 and La Caixa Fellowship
Pablo Rodriguez-Fernandez*
A.E. White1, N.T. Howard1, X. Yuan2, B.A. Grierson2, G.M. Staebler3, J.E. Rice1, L. Zeng4, M.E. Austin5, N.M. Cao1, A.J. Creely1, M.J. Greenwald1, A.E. Hubbard1, J.W. Hughes1, J.H. Irby1, O. Meneghini3, T. Odstrcil1, T. L. Rhodes4, F. Sciortino1, K. Thome3, C. Angioni6, E. Fable6
1MIT-PSFC, 2PPPL, 3GA, 4UCLA, 5UT-Austin, 6MP-IPP
*pablorf@mit.edu
Integrated modeling and predict-first experiments
of perturbative cold pulses in tokamak plasmas
Notes: Presentation time: 25-30min slot

## Slide 2
  Core transport determines plasma density and temperature profiles, critical for fusion power
Turbulent transport is the dominant heat exhaust mechanism in the core of tokamak plasmas.
Nonlinear gyrokinetics as “gold standard” to describe turbulent transport, but too expensive to predict profiles.
Courtesy of N.T. Howard

## Slide 3
  Core transport determines plasma density and temperature profiles, critical for fusion power
Turbulent transport is the dominant heat exhaust mechanism in the core of tokamak plasmas.
Nonlinear gyrokinetics as “gold standard” to describe turbulent transport, but too expensive to predict profiles.
Theory-based reduced models like TGLF are developed based on gyrokinetic simulations.
J.E. Kinsey et al Phys. Plasmas 2008

## Slide 4
  Core transport determines plasma density and temperature profiles, critical for fusion power
Turbulent transport is the dominant heat exhaust mechanism in the core of tokamak plasmas.
Nonlinear gyrokinetics as “gold standard” to describe turbulent transport, but too expensive to predict profiles.
Theory-based reduced models like TGLF are developed based on gyrokinetic simulations.
Worldwide efforts are dedicated to validate predictions of transport and kinetic profiles in current machines.
B.A. Grierson et al Phys. Plasmas 2018
DIII-D
Experiment
Simulation

## Slide 5
  Core transport determines plasma density and temperature profiles, critical for fusion power
Turbulent transport is the dominant heat exhaust mechanism in the core of tokamak plasmas.
Nonlinear gyrokinetics as “gold standard” to describe turbulent transport, but too expensive to predict profiles.
Theory-based reduced models like TGLF are developed based on gyrokinetic simulations.
Worldwide efforts are dedicated to validate predictions of transport and kinetic profiles in current machines.
Reduced models are being used to predict ITER.
B.A. Grierson et al Phys. Plasmas 2018
ITER
DIII-D
Experiment
Simulation
TGLF

## Slide 6
  Core transport determines plasma density and temperature profiles, critical for fusion power
Turbulent transport is the dominant heat exhaust mechanism in the core of tokamak plasmas.
Nonlinear gyrokinetics as “gold standard” to describe turbulent transport, but too expensive to predict profiles.
Theory-based reduced models like TGLF are developed based on gyrokinetic simulations.
Worldwide efforts are dedicated to validate predictions of transport and kinetic profiles in current machines.
Reduced models are being used to predict ITER.
B.A. Grierson et al Phys. Plasmas 2018
ITER
DIII-D
Experiment
Simulation
TGLF
However, some experiments call the fundamental assumptions of these models into question…

## Slide 7
In cold-pulse experiments, edge temperature drops and transient transport is studied as perturbation travels to core.
Expected response from local transport physics (modeled by diffusion):
    Delay in time
    Decreasing in amplitude.
  Transient transport can be tested as an edge
  cold pulse travels to plasma core
CORE
EDGE
CARTOON

## Slide 8
In cold-pulse experiments, edge temperature drops and transient transport is studied as perturbation travels to core.
Expected response from local transport physics (modeled by diffusion):
    Delay in time
    Decreasing in amplitude.
  Transient transport can be tested as an edge
  cold pulse travels to plasma core
CORE
EDGE
Alcator C-Mod

## Slide 9
  Cold-pulse experiment is a classical example of the so-called “nonlocal” transport
At low collisionality, core temperature rapidly rises after edge cold-pulse injection.
Cold-pulse experiments show counter-example to diffusive, local transport.
Past work referred to these phenomena as “non-local” transport events.
K.W. Gentle et al Phys. Rev. Lett. 1995
CORE
EDGE

## Slide 10
  Temperature inversions following edge cold pulses have been observed in many machines around the world
1995
2000
2005
2010
2015

## Slide 11
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
K.W. Gentle et al Phys. Rev. Lett. 1995

## Slide 12
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
M.W. Kissick et al Nucl. Fusion 1996

## Slide 13
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
T.D. de Wit et al Phys. Plasmas. 1998

## Slide 14
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
RTP (Netherlands)
P. Mantica et al Phys. Rev. Lett. 1999

## Slide 15
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
RTP (Netherlands)
F. Ryter et al Nucl. Fusion 2000
ASDEX Upgrade (Germany)

## Slide 16
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
RTP (Netherlands)
JET (UK)
P. Mantica et al Pl Phys. Control Fusion. 2002
ASDEX Upgrade (Germany)

## Slide 17
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
RTP (Netherlands)
JET (UK)
LHD (Japan)
N. Tamura et al Phys. Plasmas 2005
ASDEX Upgrade (Germany)

## Slide 18
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
RTP (Netherlands)
JET (UK)
LHD (Japan)
HL-2A (China)
H.-J. Sun et al Chin. Phys. Lett. 2007
ASDEX Upgrade (Germany)

## Slide 19
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
RTP (Netherlands)
JET (UK)
LHD (Japan)
HL-2A (China)
Alcator C-Mod (US)
J.E. Rice et al Nucl. Fusion 2013
ASDEX Upgrade (Germany)

## Slide 20
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
RTP (Netherlands)
JET (UK)
LHD (Japan)
HL-2A (China)
Alcator C-Mod (US)
KSTAR (Korea)
Y.J. Shi et al Nucl. Fusion 2017
ASDEX Upgrade (Germany)

## Slide 21
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
RTP (Netherlands)
JET (UK)
LHD (Japan)
HL-2A (China)
Alcator C-Mod (US)
KSTAR (Korea)
J-TEXT (China)
Y.J. Shi et al Nucl. Fusion 2018
ASDEX Upgrade (Germany)

## Slide 22
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
RTP (Netherlands)
JET (UK)
LHD (Japan)
HL-2A (China)
Alcator C-Mod (US)
KSTAR (Korea)
J-TEXT (China)
EAST (China)
Y. Liu et al Nucl. Fusion 2019
ASDEX Upgrade (Germany)

## Slide 23
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
RTP (Netherlands)
JET (UK)
LHD (Japan)
HL-2A (China)
Observed in 12 machines.
>40 journal publications have been devoted to this effect.
Featured in plasma physics books and review articles.
Alcator C-Mod (US)
KSTAR (Korea)
J-TEXT (China)
EAST (China)
ASDEX Upgrade (Germany)

## Slide 24
  Temperature inversions following edge cold pulses have been observed in many machines around the world
TEXT (US)
1995
2000
2005
2010
2015
TFTR (US)
Tore Supra (France)
RTP (Netherlands)
JET (UK)
LHD (Japan)
HL-2A (China)
Observed in 12 machines.
>40 journal publications have been devoted to this effect.
Featured in plasma physics books and review articles.
Alcator C-Mod (US)
KSTAR (Korea)
J-TEXT (China)
EAST (China)
ASDEX Upgrade (Germany)
Review article on nonlocal transport [K. Ida et al Nucl. Fusion 2015]:
“[…] the violation of the familiar local expression compels us to explore new approaches to the predictive modelling for burning plasmas.”
ITER transport physics basis paper [E.J. Doyle et al Nucl. Fusion 2007]:
“[the] propagation of the pulses from the plasma edge to the core has been a challenge to be explained by local diffusive transport models.”

## Slide 25
  Transient transport is studied using perturbative cold-pulse injections with Laser Blow-Off
Edge cold-pulses are injected using laser blow-off (LBO) technique.
Laser pulse ablates coating in glass slide, resulting in flux of neutrals to plasma.

## Slide 26
  Transient transport is studied using perturbative cold-pulse injections with Laser Blow-Off
Edge cold-pulses are injected using laser blow-off (LBO) technique.
Laser pulse ablates coating in glass slide, resulting in flux of neutrals to plasma.
As a consequence:
  Radiation sink ➔
  Density “bump” ➔
Line-average density
Total radiation
Core
Edge

## Slide 27
  Strong effect of density and current on temperature inversions is observed experimentally
Temperature inversions get weaker as density increases, and eventually disappear.
Temperature inversions return at high-density with high-current.
Rot. Rev.
Rot. Rev.
Rot. Rev.
Alcator C-Mod
P. Rodriguez-Fernandez et al Nucl. Fusion 2017

## Slide 28
  Integrated modeling of perturbative transport phenomena performed using TRANSP+TGLF
TRANSP power balance code solves for evolution of electron and ion temperatures:

## Slide 29
  Integrated modeling of perturbative transport phenomena performed using TRANSP+TGLF
TRANSP power balance code solves for evolution of electron and ion temperatures:
TGLF SAT1

## Slide 30
  Ion and electron temperatures are evolved until
  reaching steady-state in the simulation
Before perturbing and , steady-state is reached in the simulation.
Boundary conditions for and are chosen at .
Predicted profiles close to experimental values (within 2).
Turbulent and neoclassical transport as predicted.
C-Mod

## Slide 31
  Integrated modeling of perturbative transport phenomena performed using TRANSP+TGLF
TRANSP power balance code solves for evolution of electron and ion temperatures:

## Slide 32
  Integrated modeling of perturbative transport phenomena performed using TRANSP+TGLF
TRANSP power balance code solves for evolution of electron and ion temperatures:
Sources/Sinks
Radiation sink Changes in source term:

## Slide 33
  Integrated modeling of perturbative transport phenomena performed using TRANSP+TGLF
TRANSP power balance code solves for evolution of electron and ion temperatures:
Sources/Sinks
Radiation sink Changes in source term:
Density pulse Changes in density gradients ➔ Effect in transport.
Transport

## Slide 34
  Integrated modeling of perturbative transport phenomena performed using TRANSP+TGLF
TRANSP power balance code solves for evolution of electron and ion temperatures:
Sources/Sinks
Radiation sink Changes in source term:
Density pulse Changes in density gradients ➔ Effect in transport.
Before
pulse
Density Profile
Density gradient
flattens

## Slide 35
  Experimentally-constrained model of LBO injection is introduced in the simulations
Radiative losses and density profiles were not available in high time resolution in Alcator C-Mod.
We made an educated guess: experimentally-constrained Gaussian pulses.
Edge radiation sink constrained by total radiative power (bolometers).
Density perturbation constrained by line-average density (interferometer).

## Slide 36
  Core temperature inversions following edge cold pulses appeared at low collisionality
Core temperature increases at low density following edge drop.
P. Rodriguez-Fernandez et al Phys. Rev. Lett. 2018

## Slide 37
Core temperature increases at low density following edge drop.
Flattening of density gradients
  Core temperature inversions following edge cold pulses appeared at low collisionality
before pulse
during pulse
P. Rodriguez-Fernandez et al Phys. Rev. Lett. 2018

## Slide 38
Core temperature increases at low density following edge drop.
Flattening of density gradients stabilizes TEM turbulence.
before pulse
during pulse
  Core temperature inversions following edge cold pulses appeared at low collisionality
P. Rodriguez-Fernandez et al Phys. Rev. Lett. 2018

## Slide 39
  Simulations with variations of density and plasma current show that trends are captured by the model
Simulation

## Slide 40
  Simulations with variations of density and plasma current show that trends are captured by the model
Simulation
#1: Low density, low current

## Slide 41
  Simulations with variations of density and plasma current show that trends are captured by the model
Simulation
#2: High density, low current

## Slide 42
  Simulations with variations of density and plasma current show that trends are captured by the model
Simulation
#3: High density, high current

## Slide 43
  Simulations with variations of density and plasma current show that trends are captured by the model
Simulation
#3
#2
#1
#3
#2
#1

## Slide 44
  Simulations with variations of density and plasma current show that trends are captured by the model
Density ramp leads to higher collisionality, turbulence becomes more ITG-driven.
Flattening of has weaker effect on electron transport. ITG turbulence destabilized by increase in .
ITG
TEM
ETG
i+-direction
e--direction
TEM
Simulation

## Slide 45
  Temperature inversion had never been observed in DIII-D before. Perfect test case to validate our model
Transition density observed experimentally to follow 1/R dependence.
C. Gao et al Nucl. Fusion 2014
at transition (a.u.)

## Slide 46
  Temperature inversion had never been observed in DIII-D before. Perfect test case to validate our model
Transition density observed experimentally to follow 1/R dependence.
DIII-D?
C. Gao et al Nucl. Fusion 2014
at transition (a.u.)

## Slide 47
  Temperature inversion had never been observed in DIII-D before. Perfect test case to validate our model
Transition density observed experimentally to follow 1/R dependence.
C. Gao et al Nucl. Fusion 2014
DIII-D?
Predictions
at transition (a.u.)

## Slide 48
  Temperature inversion had never been observed in DIII-D before. Perfect test case to validate our model
Transition density observed experimentally to follow 1/R dependence.
C. Gao et al Nucl. Fusion 2014
DIII-D?
Predictions
at transition (a.u.)

## Slide 49
  New predict-first experiments in DIII-D confirm that TGLF predictions capture 1/R dependence
MIT Team has recently installed a new LBO for impurity transport studies, but can also be used to introduce cold pulses in DIII-D!

## Slide 50
  New predict-first experiments in DIII-D confirm that TGLF predictions capture 1/R dependence
MIT Team has recently installed a new LBO for impurity transport studies, but can also be used to introduce cold pulses in DIII-D!
New experiments confirmed validity of predictions.
Experiment

## Slide 51
  New predict-first experiments in DIII-D confirm that TGLF predictions capture 1/R dependence
Predictions
Experiment
MIT Team has recently installed a new LBO for impurity transport studies, but can also be used to introduce cold pulses in DIII-D!
New experiments confirmed validity of predictions.

## Slide 52
  Density pulse consistent with reflectometer data is introduced in simulation
A big caveat in C-Mod was the imposed density pulse (Gaussian, constrained by line-integrated measurements).
Does the density pulse actually move that fast?

## Slide 53
  Density pulse consistent with reflectometer data is introduced in simulation
A big caveat in C-Mod was the imposed density pulse (Gaussian, constrained by line-integrated measurements).
Does the density pulse actually move that fast?
High time resolution density profile reflectometer confirms a density pulse that travels quickly.

## Slide 54
  Simulations with constrained density pulse exhibit temperature inversion effect
Density profile can be constrained in time with experimental data.
Simulation of temperature evolution exhibit inversion.
Sim.
Exp.

## Slide 55
  Simulations with constrained density pulse exhibit temperature inversion effect
Density profile can be constrained in time with experimental data.
Simulation of temperature evolution exhibit inversion.
Temperature inversion triggered by small change in density profile… looks like a “nonlocal” effect!
inversion
region
Very small core density change
Density profile
Sim.
Exp.

## Slide 56
  Fast flattening of the density profile also predicted in
  ASTRA/STRAHL/TGLF simulations
Previously, inverts due to fast density pulse… but is this captured by TGLF?

## Slide 57
  Fast flattening of the density profile also predicted in
  ASTRA/STRAHL/TGLF simulations
Previously, inverts due to fast density pulse… but is this captured by TGLF?
ASTRA/STRAHL/TGLF simulations of ECH-plasma performed with prediction of carbon and main ion densities.

## Slide 58
  Fast flattening of the density profile also predicted in
  ASTRA/STRAHL/TGLF simulations
Previously, inverts due to fast density pulse… but is this captured by TGLF?
ASTRA/STRAHL/TGLF simulations of ECH-plasma performed with prediction of carbon and main ion densities.
Fast flattening of density profile is predicted.

## Slide 59
  Fast flattening of the density profile also predicted in
  ASTRA/STRAHL/TGLF simulations
Previously, inverts due to fast density pulse… but is this captured by TGLF?
ASTRA/STRAHL/TGLF simulations of ECH-plasma performed with prediction of carbon and main ion densities.
Fast flattening of density profile is predicted.
Transiently, Carbon density strongly hollowed (large reversed gradient) → Destabilizes impurity mode → Large inward flux

## Slide 60
  Main message: Nonlocal effects are not needed to capture cold-pulse phenomena in tokamaks plasmas
Summary:
For 20 years, cold-pulse experiments suggested important missing piece of physics in transport models.
Dedicated experiments in Alcator C-Mod were designed to isolate cold-pulse effect from momentum transport.
Simulations of Alcator C-Mod show that local transport models capture full dynamics of cold pulses.
Simulations with measured density pulse in new DIII-D experiments show consistency with Alcator C-Mod results.
Simulations of particle transport in AUG show that local transport models also capture fast inward flux of impurities.
P. Rodriguez-Fernandez et al. Nucl. Fusion 57, 074001 (2017)
K.W. Gentle et al. Phys. Rev. Lett. 74, 3620 (1995)
P. Rodriguez-Fernandez et al. Phys. Rev. Lett. 120, 075001 (2018)
P. Rodriguez-Fernandez et al. Nucl. Fusion 59, 066017 (2019)
P. Rodriguez-Fernandez et al. Phys. Plasmas 26, 062503 (2019)
C. Angioni et al. Nucl. Fusion 59, 106007 (2019)
P. Rodriguez-Fernandez MIT PhD Thesis (May 2019)

## Slide 61
  References