## Slide 1: Filaments as the origin of HHFW losses in NSTX
W. Tierens, R. Bilato, N. Bertelli, S. Shiraiwa, J.R. Myra, L. Colas
Lodestar Research Corporation

## Slide 2: HHFW heating in NSTX
High Harmonic Fast Wave heating
Lodestar Research Corporation
[Perkins et al 2013]

## Slide 3: HHFW edge losses in NSTX
In some conditions, up to about 60% of incident power lost
Lodestar Research Corporation
[Perkins et al 2013]

## Slide 4: HHFW edge losses in NSTX
Up to about 60% of incident power lost Power flow along field lines
Lodestar Research Corporation
[Perkins et al 2013]

## Slide 5: HHFW edge losses in NSTX
Up to about 60% of incident power lost Power flow along field lines Losses increase with increasing density
Lodestar Research Corporation
[Phillips et al 2009]
“A dramatic increase in core heating efficiency was first achieved [...] when the onset for perpendicular wave propagation was moved away from the antenna and nearby vessel structures.
Efficient core heating [...] was then accomplished by reducing the edge density in front of the launcher with lithium conditioning and avoiding operational points prone to instabilities.”

## Slide 6: HHFW edge losses in NSTX
Up to about 60% of incident power lost Power flow along field lines Losses increase with increasing density
Lodestar Research Corporation
[Phillips et al 2009]
“A dramatic increase in core heating efficiency was first achieved [...] when the onset for perpendicular wave propagation was moved away from the antenna and nearby vessel structures.
Efficient core heating [...] was then accomplished by reducing the edge density in front of the launcher with lithium conditioning and avoiding operational points prone to instabilities.”
Note that the conventional point of view is
The Fast Wave must tunnel through an evanescent layer
This evanescent layer is made narrower as the density increases
Thus, higher edge density improves ICRF power coupling
Which is the reasoning behind using gas puffing to improve coupling, as done successfully on AUG [Zhang et al 2017] and planned on ITER [Zhang et al 2022].
But NSTX does the opposite!

## Slide 7: HHFW edge losses in NSTX
Up to about 60% of incident power lost Power flow along field lines Losses increase with increasing density
Lodestar Research Corporation
[Phillips et al 2009]
“A dramatic increase in core heating efficiency was first achieved [...] when the onset for perpendicular wave propagation was moved away from the antenna and nearby vessel structures.
Efficient core heating [...] was then accomplished by reducing the edge density in front of the launcher with lithium conditioning and avoiding operational points prone to instabilities.”
Note that the conventional point of view is
The Fast Wave must tunnel through an evanescent layer
This evanescent layer is made narrower as the density increases
Thus, higher edge density improves ICRF power coupling
Which is the reasoning behind using gas puffing to improve coupling, as done successfully on AUG [Zhang et al 2017] and planned on ITER [Zhang et al 2022].
But NSTX does the opposite!

## Slide 8: HHFW edge losses in NSTX
Up to about 60% of incident power lost Power flow along field lines Losses increase with increasing density
Lodestar Research Corporation
[Phillips et al 2009]
“A dramatic increase in core heating efficiency was first achieved [...] when the onset for perpendicular wave propagation was moved away from the antenna and nearby vessel structures.
Efficient core heating [...] was then accomplished by reducing the edge density in front of the launcher with lithium conditioning and avoiding operational points prone to instabilities.”
Note that the conventional point of view is
The Fast Wave must tunnel through an evanescent layer
This evanescent layer is made narrower as the density increases
Thus, higher edge density improves ICRF power coupling
Which is the reasoning behind using gas puffing to improve coupling, as done successfully on AUG [Zhang et al 2017] and planned on ITER [Zhang et al 2022].
But NSTX does the opposite!

## Slide 9: HHFW edge losses in NSTX
Up to about 60% of incident power lost Power flow along field lines Losses increase with increasing density Losses increase with decreasing B
Lodestar Research Corporation
[Hosea et al 2008]

## Slide 10: HHFW edge losses in NSTX
Up to about 60% of incident power lost Power flow along field lines Losses increase with increasing density Losses increase with decreasing B Losses increase with decreasing
Lodestar Research Corporation
[Hosea et al 2009]

## Slide 11: HHFW edge losses in NSTX
Up to about 60% of incident power lost Power flow along field lines Losses increase with increasing density Losses increase with decreasing B Losses increase with decreasing Double-peaked loss profile
Lodestar Research Corporation
[Perkins et al 2013]

## Slide 12: HHFW edge losses in NSTX
Up to about 60% of incident power lost Power flow along field lines Losses increase with increasing density Losses increase with decreasing B Losses increase with decreasing Double-peaked loss profile Divertor sheath rectification
Lodestar Research Corporation
[Perkins et al 2015]

## Slide 13: Filaments in NSTX
Gas puff imaging reveals many filaments
Density perturbation
Lodestar Research Corporation
[Zweben et al 2016]
Localized radially/poloidally
Stretched along B

## Slide 14: Filaments in NSTX
Gas puff imaging reveals many filaments
Many filaments in SOL at all times
Lodestar Research Corporation
[Zweben et al 2016]

## Slide 15: Filaments in NSTX
Gas puff imaging reveals many filaments
Many filaments in SOL at all times
Filaments are B-aligned
Lodestar Research Corporation
[Zweben et al 2016]

## Slide 16: Surface waves
Given an incident amplitude a, What is the amplitude of the transmitted wave? What is the amplitude of the reflected wave?
Lodestar Research Corporation
Material 1
Material 2
Incident a
Transmitted
Reflected

## Slide 17: Surface waves
Given an incident amplitude a, What is the amplitude of the transmitted wave? What is the amplitude of the reflected wave?
When is this problem underspecified?
Lodestar Research Corporation
Material 1
Material 2
Incident a
Transmitted
Reflected

## Slide 18: Surface waves
Given an incident amplitude a, What is the amplitude of the transmitted wave? What is the amplitude of the reflected wave?
When is this problem underspecified?
Lodestar Research Corporation
Material 1
Material 2

## Slide 19: Surface waves on filaments
Steep density gradient acts as "material interface"
Lodestar Research Corporation
[Zweben et al 2016]

## Slide 20: Surface waves on filaments
Steep density gradient acts as "material interface"
Analytic description possible
Lodestar Research Corporation
[Tierens et al 2020]

## Slide 21: Surface waves on filaments
Steep density gradient acts as "material interface"
Analytic description possible
Simplified dispersion relation
Lodestar Research Corporation
[Myra]

## Slide 22: Surface waves on filaments
Steep density gradient acts as "material interface"
Analytic description possible
Simplified dispersion relation
Lodestar Research Corporation
Density ratio

## Slide 23: Surface waves on filaments
Steep density gradient acts as "material interface"
Analytic description possible
Simplified dispersion relation
Lodestar Research Corporation
Azimuthal mode number

## Slide 24: Surface waves on filaments
Steep density gradient acts as "material interface"
Analytic description possible
Simplified dispersion relation
Lodestar Research Corporation
in HHFW

## Slide 25: Surface waves on filaments
Steep density gradient acts as "material interface"
Analytic description possible
Simplified dispersion relation
Lodestar Research Corporation

## Slide 26: Surface waves on filaments
Steep density gradient acts as "material interface"
Analytic description possible
Simplified dispersion relation
Lodestar Research Corporation
Bessel functions

## Slide 27: Surface waves on filaments
Steep density gradient acts as "material interface"
Analytic description possible
Simplified dispersion relation – favours HHFW
Lodestar Research Corporation
in HHFW

## Slide 28: Surface waves on filaments
Simplified dispersion relation
Lodestar Research Corporation
[Tierens et al 2021]

## Slide 29: Surface waves on filaments
Simplified dispersion relation
Lodestar Research Corporation
[Tierens et al 2021]
Blob-filaments: m=1
Hole-filaments: m=-1

## Slide 30
Filaments exist
Surface waves on filaments exist
Lodestar Research Corporation

## Slide 31
Filaments exist
Surface waves on filaments exist
Lodestar Research Corporation
Carry power along filaments i.e. along B
Favour HHFW conditions

## Slide 32
Filaments exist
Surface waves on filaments exist
How much power can be lost to these waves?
Lodestar Research Corporation

## Slide 33
Filaments exist
Surface waves on filaments exist
How much power can be lost to these waves?
Lodestar Research Corporation
I.e. mode-converted to filament surface waves, to be absorbed either collisionally as they propagate along the filament, or via other loss mechanisms at the filament endpoints.

## Slide 34: Power lost to filament surface waves
For infinite filaments, losses can be quantified by Regularizing the scattering problem
Lodestar Research Corporation

## Slide 35: Power lost to filament surface waves
For infinite filaments, losses can be quantified by Regularizing the scattering problem Taking the collisionless limit
Lodestar Research Corporation

## Slide 36: Power lost to filament surface waves
For infinite filaments, losses can be quantified by Regularizing the scattering problem Taking the collisionless limit, which is finite
Lodestar Research Corporation
This counter-intuitive result stresses the need to regularize the initial scattering problem and to take the collisionless limit only at the end of the calculations, to obtain valid results - L. Colas
[Tierens et al 2021]

## Slide 37: Power lost to filament surface waves
Lodestar Research Corporation
[Tierens et al 2021]

## Slide 38: Power lost to filament surface waves
Density ratio
Lodestar Research Corporation
[Tierens et al 2021]
Incident power spectrum
in HHFW

## Slide 39: Power lost to filament surface waves
Lodestar Research Corporation
[Tierens et al 2021]
Root of surface wave dispersion relation

## Slide 40: Power lost to filament surface waves
Lodestar Research Corporation
[Tierens et al 2021]
Power lost to specific filament
Power lost to average filament

## Slide 41: Power lost to filament surface waves
Lodestar Research Corporation
Power lost to average filament
[Biswas et al 2021] [Garcia et al 2016]

## Slide 42: Power lost to filament surface waves
Lodestar Research Corporation
Power lost to average filament
Or, we could view experimental measurements [NSTX: Zweben et al 2016] as samples drawn from this distribution

## Slide 43: Data from [Zweben et al 2016]: a new perspective
Lodestar Research Corporation
LCFS
antenna
LCFS
antenna
LCFS
antenna

## Slide 44: We promised to explain experimental results…
Lodestar Research Corporation
Double-peaked absorption profile 
[Perkins et al 2013]

## Slide 45: We promised to explain experimental results…
Lodestar Research Corporation
Double-peaked absorption profile  k||-dependence 
[Hosea et al 2009]

## Slide 46: We promised to explain experimental results…
Lodestar Research Corporation
Double-peaked absorption profile  k||-dependence  Density dependence 
P0 scales with density

## Slide 47: We promised to explain experimental results…
Lodestar Research Corporation
Double-peaked absorption profile  k||-dependence  Density dependence 
Magnetic field dependence 
P0 scales with

## Slide 48: We promised to explain experimental results…
Lodestar Research Corporation
Double-peaked absorption profile  k||-dependence  Density dependence 
Magnetic field dependence  Power flow along B 

## Slide 49: We promised to explain experimental results…
Lodestar Research Corporation
Double-peaked absorption profile  k||-dependence  Density dependence 
Magnetic field dependence  Power flow along B  Divertor sheath rectification 

## Slide 50: Other explanations
Lodestar Research Corporation
 | Standing FW | Propagating SW | DC currents | Parametric decay | Filaments
n-dependence |  |  |  |  | 
k¦¦-dependence |  |  |  |  | 
B-dependence |  |  |  |  | 
Parallel power flow |  |  |  |  | 
Edge heating |  |  |  |  (ion specific) | 
IBW harmonics |  |  |  |  | 
Divertor sheath rectification |  |  |  |  | 
Deposition profile |  |  |  |  | 

## Slide 51: Other explanations
Lodestar Research Corporation
[Bertelli et al 2014] proposed that a standing fast wave might be trapped between the antenna and the plasma
 | Standing FW | Propagating SW | DC currents | Parametric decay | Filaments
n-dependence |  |  |  |  | 
k¦¦-dependence |  |  |  |  | 
B-dependence |  |  |  |  | 
Parallel power flow |  |  |  |  | 
Edge heating |  |  |  |  (ion specific) | 
IBW harmonics |  |  |  |  | 
Divertor sheath rectification |  |  |  |  | 
Deposition profile |  |  |  |  | 

## Slide 52: Other explanations
Lodestar Research Corporation
[Smithe et al 2014] proposed that a propagating slow wave, which propagates nearly parallel to B, might be responsible
 | Standing FW | Propagating SW | DC currents | Parametric decay | Filaments
n-dependence |  |  |  |  | 
k¦¦-dependence |  |  |  |  | 
B-dependence |  |  |  |  | 
Parallel power flow |  |  |  |  | 
Edge heating |  |  |  |  (ion specific) | 
IBW harmonics |  |  |  |  | 
Divertor sheath rectification |  |  |  |  | 
Deposition profile |  |  |  |  | 

## Slide 53: Other explanations
Lodestar Research Corporation
[Perkins et al 2015] investigated the role of DC currents, excited by sheath rectification, flowing along B
 | Standing FW | Propagating SW | DC currents | Parametric decay | Filaments
n-dependence |  |  |  |  | 
k¦¦-dependence |  |  |  |  | 
B-dependence |  |  |  |  | 
Parallel power flow |  |  |  |  | 
Edge heating |  |  |  |  (ion specific) | 
IBW harmonics |  |  |  |  | 
Divertor sheath rectification |  |  |  |  | 
Deposition profile |  |  |  |  | 

## Slide 54: Other explanations
Lodestar Research Corporation
 | Standing FW | Propagating SW | DC currents | Parametric decay | Filaments
n-dependence |  |  |  |  | 
k¦¦-dependence |  |  |  |  | 
B-dependence |  |  |  |  | 
Parallel power flow |  |  |  |  | 
Edge heating |  |  |  |  (ion specific) | 
IBW harmonics |  |  |  |  | 
Divertor sheath rectification |  |  |  |  | 
Deposition profile |  |  |  |  | 
[Wilson et al 2005] investigated the role of parametric decay instabilities

## Slide 55: Other explanations
Lodestar Research Corporation
 | Standing FW | Propagating SW | DC currents | Parametric decay | Filaments
n-dependence |  |  |  |  | 
k¦¦-dependence |  |  |  |  | 
B-dependence |  |  |  |  | 
Parallel power flow |  |  |  |  | 
Edge heating |  |  |  |  (ion specific) | 
IBW harmonics |  |  |  |  | 
Divertor sheath rectification |  |  |  |  | 
Deposition profile |  |  |  |  | 
Model for sheath rectification where filament strikes wall

## Slide 56: Other explanations
Lodestar Research Corporation
 | Standing FW | Propagating SW | DC currents | Parametric decay | Filaments
n-dependence |  |  |  |  | 
k¦¦-dependence |  |  |  |  | 
B-dependence |  |  |  |  | 
Parallel power flow |  |  |  |  | 
Edge heating |  |  |  |  (ion specific) | 
IBW harmonics |  |  |  |  | 
Divertor sheath rectification |  |  |  |  | 
Deposition profile |  |  |  |  | 
Speculation that surface waves, rather than FW, may play role in PD

## Slide 57: Other explanations
Lodestar Research Corporation
 | Standing FW | Propagating SW | DC currents | Parametric decay | Filaments
n-dependence |  |  |  |  | 
k¦¦-dependence |  |  |  |  | 
B-dependence |  |  |  |  | 
Parallel power flow |  |  |  |  | 
Edge heating |  |  |  |  (ion specific) | 
IBW harmonics |  |  |  |  | 
Divertor sheath rectification |  |  |  |  | 
Deposition profile |  |  |  |  | 

## Slide 58: Conclusion
Lodestar Research Corporation
 | Standing FW | Propagating SW | DC currents | Parametric decay | Filaments
n-dependence |  |  |  |  | 
k¦¦-dependence |  |  |  |  | 
B-dependence |  |  |  |  | 
Parallel power flow |  |  |  |  | 
Edge heating |  |  |  |  (ion specific) | 
IBW harmonics |  |  |  |  | 
Divertor sheath rectification |  |  |  |  | 
Deposition profile |  |  |  |  | 

## Slide 59: Future work
Lodestar Research Corporation
Interaction between surface waves on filaments and sheaths
Applicability outside of HHFW
Full-wave dispersion relation

## Slide 60: References
Lodestar Research Corporation
[Perkins et al 2013] Perkins, R. J., et al. "Fast-wave power flow along SOL field lines in NSTX and the associated power deposition profile across the SOL in front of the antenna." Nuclear Fusion 53.8 (2013): 083025. [Phillips et al 2009] Phillips, C. K., et al. "Spectral effects on fast wave core heating and current drive." Nuclear Fusion 49.7 (2009): 075015. [Hosea et al 2008] Hosea, J., et al. "High harmonic fast wave heating efficiency enhancement and current drive at longer wavelength on the National Spherical Torus Experiment." Physics of Plasmas 15.5 (2008): 056104. [Hosea et al 2009] Hosea, J. C., et al. "Recent fast wave coupling and heating studies on NSTX, with possible implications for ITER." AIP Conference Proceedings. Vol. 1187. No. 1. American Institute of Physics, 2009. [Perkins et al 2015] Perkins, R. J., et al. "The contribution of radio-frequency rectification to field-aligned losses of high-harmonic fast wave power to the divertor in the National Spherical Torus eXperiment." Physics of Plasmas 22.4 (2015): 042506. [Zweben et al 2016] Zweben, S. J., et al. "Blob structure and motion in the edge and SOL of NSTX." Plasma Physics and Controlled Fusion 58.4 (2016): 044007. [Tierens et al 2020] Tierens, Wouter, et al. "Filament-assisted mode conversion in magnetized plasmas." Physics of Plasmas 27.1 (2020): 010702. [Tierens et al 2021] Tierens, Wouter, et al. "Resonant wave–filament interactions as a loss mechanism for HHFW heating and current drive." Plasma Physics and Controlled Fusion 64.3 (2022): 035001. [Biswas et al 2021] Biswas, Bodhi, et al. "A hybrid full-wave Markov chain approach to calculating radio-frequency wave scattering from scrape-off layer filaments." Journal of Plasma Physics 87.5 (2021). [Garcia et al 2016] Garcia, Odd Erik, et al. "Stochastic modelling of intermittent fluctuations in the scrape-off layer: Correlations, distributions, level crossings, and moment estimation." Physics of Plasmas 23.5 (2016): 052308. [Bertelli et al 2014] Bertelli, Nicola, et al. "Full wave simulations of fast wave heating losses in the scrape-off layer of NSTX and NSTX-U." Nuclear Fusion 54.8 (2014): 083004. [Smithe et al 2014] D. Smithe et al, Plasma in contact with metal: RF antenna near field behaviors in tokamaks, see https://apam.columbia.edu/files/seasdepts/applied-physics-and-applied-math/pdf-files/Smithe_Colloquium_06.pdf [Wilson et al 2005] Wilson, J. R., et al. "Parametric decay during HHFW on NSTX." AIP Conference Proceedings. Vol. 787. No. 1. American Institute of Physics, 2005.