## Slide 1
IEA Spherical Torus Technology Coordination Program (TCP) Annual Report
Rajesh Maingi, Chair of the ST TCP Executive Committee
NSTX-U Magnetic Fusion Science Meeting, 27 March 2023

## Slide 2
ST TCP work conducted under three annexes
Annex I – “Co-operation on ST Science R & D”: Much of the work is carried out under this annex -bi-lateral and multi-lateral research collaboration, joint publications, exchange of equipment and personnel, information exchange at workshops and conferences, organization of the International Spherical Tokamak Workshops, outreach, communication and dissemination to the wider community etc.
Annex II – “Co-operation on the Physics and Technology of Future Spherical Torus Devices”: This work aims to accelerate progress on the physics and technology of future ST devices through co-ordination of activities and exchange of technical information relating to physics and technology challenges which are common to a range of future ST devices.
Annex III – “Co-operation on the Steady State Operation of Fusion Devices”: Here we seek to accelerate progress on the physics and technology of steady state operation of fusion devices through coordinated planning and cooperative research.

## Slide 3
Growing number of STs worldwide, both public and private
China: EXL-50, NCST, SUNIST, SUNIST-2
EU: Proto-Sphera, SMART
Japan: LATE, QUEST, TST-2, TS-6, TS-4U, UTST
S. Korea: VEST, VEST-II
UK: MAST-U, ST-40, STEP
US: LTX-b, NSTX-U, PEGASUS-III

## Slide 4
ST TCP very active in 2022
TCP was renewed in 2022 for 5 years
Outline
International ST Workshop (virtual) held Oct. 31 – Nov. 4, 2022
Highlights from worldwide experiments

## Slide 5: ST Workshop succeeded in re-connecting the worldwide ST community
ST Workshop (virtual) held 10/31-11/3/22
Many members from the IEA ST TCP ExCom served on the ISTW Program Committee – thank you!
Thanks to Prof. Gao for offering Tsinghua Univ. to be the host
Special thanks to Prof. Tan Yi and Jack Berkery for their coordination efforts
ISTW 2024 will be in person, site TBD by ST TCP ExCom – stay tuned
Year | Location
1994 | Oak Ridge, TN
1995 | Princeton, NJ
1996 | Culham, UK
1997 | St. Petersburg, Russia
1998 | Tokyo, Japan
1999 | Seattle, WA
2001 | Sao Jose dos Campos, Brazil
2002 | Princeton, NJ
2003 | Culham, UK
2004 | Kyoto, Japan
2005 | St. Petersburg, Russia
2006 | Chengdu, China
2007 | Fukuoka, Japan
2008 | Frascati, Italy
2009 | Madison, WI
2011 | Toki, Japan
2013 | York, UK
2015 | Princeton, NJ
2017 | Seoul, Korea
2019 | Frascati, Italy
2022 | Virtual (Beijing, China)

## Slide 6: International ST Workshop had excellent worldwide participation
92 people registered
  43 requested an oral presentation
  23 requested a poster
  23 requested no presentation (most of these were from Tsinghua U.)
Eight countries represented
  31 from China
  19 U.S.
  15 U.K.
  11 Japan
  6 Korea
  4 Russia
  3 Spain
  3 Italy
~24 Institutions represented
  Led by:
  25 Tsinghua University
  13 PPPL
  9 UKAEA
  6 Seoul National University
Courtesy of J. Berkery

## Slide 7: Abstract submissions received by ST Workshop
Total number: 66
  43 requested an oral presentation
  23 requested a poster
Courtesy of J. Berkery

## Slide 8
ST TCP very active in 2022
Outline
International ST Workshop (virtual) held Oct. 31 – Nov. 4, 2022
Highlights from worldwide experiments (in reverse alphabetical order)

## Slide 9: US: Next Steps for STs: Elimination of Solenoid to Establish Non-Inductive Startup Pathway for Fusion Energy
PEGASUS-III Mission: Solving solenoid-free startup for STs (and ATs)
  Advanced Local Helicity Injection
  Floating Coaxial Helicity Injection
  Microwave assist, sustainment and startup
  Compatibility with NBI heating and current drive
Research program will provide a predictive understanding of these solenoid-free techniques
  Extrapolatable techniques to MA-class STs (and ATs)
Pegasus-III features:
No solenoid
4x toroidal field
Advanced control
Expanded diagnostics
CHI
EC/EBW
LHI
Divertor Coils
Diem – ISTW 2022
9
Courtesy of S. Diem

## Slide 10: US: All Major Pegasus-III Upgrade Sub-Assemblies Nearing Completion
TF bundle installed in vacuum wall
Contact - indexing area
Six pin blocks and pins installed
on vessel (top shown here)
Pin block with pin attached to
gusset plate reinforced ribs
Diem – ISTW 2022
10
Courtesy of S. Diem

## Slide 11: Three high-level Objectives comprise the mission-oriented NSTX-U research program
  Extend confinement and stability physics basis at low aspect ratio and high beta to lower collisionality
    Enhanced confinement necessary for FPP (of any aspect ratio)
    Does good ST confinement extend to low collisionality?
  Develop non-inductive (NI) operation at high-performance and low-disruptivity
    Steady-state compact ST fusion devices require enhanced confinement, NI operation
    Develop unique high-beta, strong shaping route to NI operation
  Develop and evaluate conventional and innovative power and particle handling techniques
    NSTX-U designed for 8 MW/m2 for 5 s; can access 50-100 MW/m2
NSTX-U rebuild continues, First Plasma 3/2025 (early finish)

## Slide 12
US: NSTX Data Analysis in key objective areas
Core physics: gyrokinetic simulations of electron heat flux match data
  Substantial work on developing an R/a independent pedestal model, both on pressure gradient limits and ideal MHD limits
Evaluating ECCD effectiveness for next step STs based on NSTX-U physics basis
Developing liquid metal PFCs to be tested in NSTX-U, based on designs for FNSF
Guttenfelder IAEA FEC 2023

## Slide 13
US: LTX-beta sustained flat Te profiles with lithium PFCs
Flat Te profiles sustained: edge Te ~ core Te
  Results extended with neutral beam injection to extend core heating beyond ohmic heating
Recycling reduced with Li PFCs: tp* ~ tE
Boyle NF 2023
Maan NME 2022

## Slide 14
UK: MAST-U achieved high performance operating scenarios
Developed 1s long type-I ELMy H-mode scenarios
  Sustained Te,ped up to ~340 eV, 400 eV transiently
  Te,core up to 2 keV, Ti,core up to 3 keV
  Injected NBI power up to 3.6 MW
  ELM mitigation with RMPs observed
Developed initial 1 MA plasma scenario
  Increased toroidal field from 0.65T to 0.72T on axis
Courtesy of H. Meyer

## Slide 15
UK: Preferred non-inductive operating points on STEP give access to ECCD and EBW
F. Casson, F. Koechl, S. Marsden, G. Szepesi, E. Tholerus, T. Wilson
ECCD: Electron cyclotron heating & current drive
EBW: Electron Bernstein wave heating & current drive
K. McClements et al. — 21st International Spherical Torus Workshop (ISTW 2022), 1/11/2022
Courtesy of H. Meyer

## Slide 16
UK: Preferred non-inductive operating points on STEP give access to ECCD and EBW
F. Casson, F. Koechl, S. Marsden, G. Szepesi, E. Tholerus, T. Wilson
ECCD: Electron cyclotron heating & current drive
EBW: Electron Bernstein wave heating & current drive
K. McClements et al. — 21st International Spherical Torus Workshop (ISTW 2022), 1/11/2022
Courtesy of H. Meyer

## Slide 17
S. McNamara, NF 2023
Profiles of (a) electron density, ion and fast particle densities, (b) ion and electron temperature determined using the integrated data analysis approach (#10009, t=58 ms at maximum Ti)
UK: ST-40 achieved Ti in excess of 100 million Kelvins

## Slide 18: UK: Higher and NBI enables access to higher and on ST-40
Scenario optimisation + PNBI increases
Increased power BT acts to suppress sawteeth, which contributes to increase in Te
TRANSP analysis shows that increase in Te and Ti to confinement improvement in both channels
Courtesy of Tokamak Energy

## Slide 19
KO: Interaction between external Blobs and internal MHD modes during IRE
E.C. Jung et al, Nucl. Fusion 62 (2022) 126029
Internal Reconnection Event (IRE)
MHD-correlated blobs before IRE
Phase alignment between MHD and blobs
Courtesy of Y.S. Hwang

## Slide 20
Real experimental results
Virtual ST plasma model
Digital Twins (DT)
VEST (Versatile Experiment Spherical Torus)
Establish Cyber Physical ST System
for the realization of compact ST fusion reactor
KO: Center for ST Fusion Metaware Research (7/2021-12/2025)
VEST will be upgraded by doubling Ohmic power and NBI power as well as diagnostic capabilities
GPU-based 6-D full PIC simulation code
Courtesy of Y.S. Hwang

## Slide 21
JA: progress on QUEST and TST-2
TST-2 (Univ. Tokyo)
Installation of a new off-midplane comb line antenna to excite LHW (100kW/200 MHz) (see the right photograph).
Preliminary results showed better efficiency than an old antenna.
0.20 m
Comparison of plasmas sustained by the outer-midplane(black) and the new off-midplane (red) antennas.
QUEST (Kyushu Univ.)
Transient CHI start-up operation on a single biased electrode configuration.
Single biased electrode incorporated on lower divertor for Transient CHI start-up
Gas nozzles
PF5-1
PF5-2
Ceramic cover
Bt
Center stack
Center stack
Injected plasma is confined in the center.
Courtesy of A. Ejiri

## Slide 22
TS-6, TS-4U, UTST (Univ. Tokyo)
The ST reconnection heating experiments TS-6 and TS-4 studied the ion temperature scaling DwionµBrec2µBp2
for direct access to the burning plasms.
Based on collaboration between TSs and ST-40, high-field merging experiment is being made in TS-40 and documented 106K ion temperature using both of merging and NBI.
Low-beta ST
w/o merging
q0~0
q0~0.8
q0~1.1
q0~1.5(High-beta ST)
Z[m]
0
-0.2
0.2
0.28
0.06
R[m]
TS-6 Merging
Experiment
0
0.3
|B|[kG]
Y
q0~1.5(Low-beta ST)
Y
low-q ST
ST
FRC
The high-power reconnection heating experiments TS-6 successfully formed ultra-high beta STs with absolute minimum-B configuration.
JA: progress on TS-6, TS-4U, UTST
Courtesy of A. Ejiri

## Slide 23
LATE (Kyoto University)
Non-inductive formation of overdense ST plasma by exciting electron Bernstein wave (EBW) via O-X-B mode conversion process.
* Soft X-ray CT system is under development to investigate the plasma ejection phenomena in the overdense ST plasma.
JA: progress on LATE
Courtesy of A. Ejiri

## Slide 24: EU: SMART Will Explore a Wide Shaping Range at Relatively High Ip / Bt
A. Mancini et al, Fus. Eng. Des. 171 112542 (2021)
Parameters | Phase 1 | Phase 2 | Phase 3
Ip [kA] | 100 | 500 | >500
Bt [T] | 0.1 | 0.3 | 1.0
τpulse [sec] | 0.15 | 0.5 | >1
R/a (m) | 0.45 / 0.25 |  | 
Aspect Ratio | 1.4 – 3.0 |  | 
κ | < 3 |  | 
δ | -0.6 – +0.6 |  | 
Pe[kW] | 6 | 6 | 200
PNBI [MW] | - | 1 | 1
M. Garcia-Munoz | 21st International Spherical Torus Workshop (ISTW) | Remote | Nov 1st 2022
  SMART aims at high confinement regimes in Spherical Tokamaks (STs) with flexible shaping, high β, and fusion-relevant Ti, Te, ne, and collisionalities
  Exploiting novel diagnostic and exhaust and plasma control techniques
  Training next generation of fusion physicists and engineers

## Slide 25
PROTO-SPHERA Plasma Torus forms in 5 ms, as the Centerpost Plasma current & toroidal field grow
The Plasma Torus is a slightly oblique rotator
maintained by 3D magnetic reconnections
toroidal Plasma current enters torus in bursts
Preliminary (still with some artifacts) 3D tomographic
reconstruction from 6 cameras around main plasma
5 ms
10 ms
The Plasma Torus grows from a kinked filament, formed inside a pre-existing purely Magnetostatic Field:
→ a toroidal ~ axisymmetric confined plasma could be produced and maintained in steady-state by permanent magnets only
EU: PROTO-SPHERA confined torus sustained for up to 1 sec
Courtesy of H. Meyer and P. Micozzi

## Slide 26: Spherical Tokamaks in China
SUNIST
Tsinghua University, Beijing
Construction started at 2000, first plasma in 2002
R0 / a: 0.3 / 0.23 m
BT0: 0.15 (0.27) T
IP: 50 (120) kA
Black: design, red: achieved
Research topics
Basic properties of spherical tokamak plasmas
EBW heating / Alfven eigenmodes
SUNIST-2
Tsinghua University, Xi’an
Construction started at 2020, first plasma in 2022 (expected)
R0 / a: 0.525 / 0.325 m
BT0: 1 T, IP: 500 kA
Research topics
Confinement of spherical tokamak at 1 Tesla
Reconnection heating
EXL-50
ENN, Langfang, Hebei
Construction started at 2018, first plasma in 2019
R0 / a: 0.58 / 0.39 m
BT0: 0.5 T, IP: 500 (160) kA
EC waves: 1.75 MW 28 / 50 GHz
Research topics
Solenoid-free current drive up to 140 kA by 115 kW 28 GHz EC
p-B11 ST reactor
tanyi@sunist.org
NCST
Nanchang University, Jiangxi
Construction started at 2018, first plasma in 2021
R0 / a: 0.4 / 0.24 m
BT0: 0.36 T, IP: 100-300 (30) kA
Research topics
Solenoid-free startup by merging
Basic properties of spherical tokamak plasmas
Courtesy of T. Yi

## Slide 27
China: SUNIST-2 device construction nearly completed
R = 0.525m, a = 0.325m, k ~ 1.6
Ip ~ 500 kA, Bt from 0.4 – 1.0 T
Substantial shape flexibility
Construction delayed by COVID-19, completion imminent
Courtesy of T. Yi

## Slide 28
China: EXL-50 achieved efficient CD

## Slide 29
Very productive year in the ST TCP!
Looking forward to 2023, with several device upgrades coming online