## Slide 1
Observation of a New Self-generated Current in KSTAR
Yong-Su Na1†, J. Seo1,2, Y. Lee1, G.J. Choi1, M.S. Park1, S.J. Park1, S. Yi3, W.X. Wang4, M.G. Yoo4,5, M.S. Cha1, B.S. Kim1, Y.H. Lee3, B. Kim1, C.Y. Lee3, S.K. Kim4,6, S.M. Yang4, C.S. Byun6, H.S. Kim3, J. Ko3 and T.S. Hahm1
†ysna@snu.ac.kr
NSTX-U / Magnetic Fusion Science Meeting Monday
September 11, PPPL, USA
Yong-Su Na, Jaemin Seo, et al, Nature Comm. 13 6477 (2022)
1Department of Nuclear Engineering, Seoul National University, Seoul, Republic of Korea
2Physics Department, Choong Ang University, Seoul, Republic of Korea
3Korea Institute of Fusion Energy, Daejeon, Republic of Korea
4Princeton Plasma Physics Laboratory, Princeton, New Jersey, USA
5General Atomics, San Diego, California, USA
6Princeton University, Princeton, New Jersey, USA

## Slide 2
Contents
Plasma current in a tokamak
The appearance of a new self-generated current in dedicated experiments on KSTAR
The reproducibility of occurrence of the new current
Evidence that turbulence does not drive the anomalous current
Conclusion

## Slide 3
Tokamak relies on plasma current for confinement
Faraday‘s law
IOH
dt
dIC
Induction
IP = IOH + INI
Plasma current in a tokamak
In a tokamak, is generated by , to mix up the particles poloidally to prevent abrupt ExB losses.
is initially generated by electromagnetic induction of the solenoid.
However, we need to minimize this inductive current for steady state operation in future reactor.

## Slide 4
Non-inductive current drive sources
External current drive: NBI, EC, IC, LH, etc.
Internal current drive (Self-generated): Bootstrap current
Nature Physical Science 229 110 (1971)

## Slide 5
Non-inductive current drive sources
Sumin Yi et al., PoP 23 102514 (2016)
W. Wang et al., NF 59 084002 (2019)
External current drive: NBI, EC, IC, LH, etc.
Internal current drive (Self-generated): Bootstrap current, turbulence-driven current
E. Li et al, PRL 128 085003 (2022)

## Slide 6
The appearance of a self-generated current in KSTAR
To minimize the current drive, (i) Injecting the EC wave in a nearly perpendicular direction (ii) Avoiding the L-H transition by forming an unfavorable null configuration to reduce the bootstrap current
SMBI applied, - To increase the electron density - To decrease the electron temperature
A dedicated experiment (#26381)
→ Increasing the plasma resistivity (η∝Te-1.5)
→ Loop voltage should be increased to keep the plasma current constant! (Ip ~ VL /R)

## Slide 7
The appearance of a self-generated current in KSTAR
A dedicated experiment (#26381)
To minimize the current drive, (i) Injecting the EC wave in a nearly perpendicular direction (ii) Avoiding the L-H transition by forming an unfavorable null configuration to reduce the bootstrap current
SMBI applied, - To increase the electron density - To decrease the electron temperature
→ Increasing the plasma resistivity (η∝Te-1.5)
Why?
→ Loop voltage should be increased to keep the plasma current constant! (Ip ~ VL /R)
→ Loop voltage stays constant or even reduced!

## Slide 8
The appearance of a self-generated current in KSTAR
Interpretive simulation with the integrated tokamak simulator, TRIASSIC(Tokamak Reactor Integrated Automated Suite for Simulation and Computation)* (#26381)
*C. Y. Lee et al. Nucl. Fusion 61 096020 (2021)
Before SMBI - Interpretive simulation agrees with the experiment.
After SMBI - The inductive current reduces due to the increased resistivity by SMBI. - An anomalous current gap (δI) appears between the simulation and the experiment. - This discrepancy is sustained for longer than 2 s until NBI is applied, longer than τr=(μ0a2)/2η~ 0.5 s. - Internal inductance (li) drops.
→ Possibility of an additional steady source of the current! in the off-axis region?
VL from LV23 (inboard)

## Slide 9
The appearance of a self-generated current in KSTAR
There are several uncertainties such as Zeff or neoclassical transport models.
We scanned 1.2≤Zeff≤3.0 with different radial profile shapes and tried other neoclassical models but the discrepancy persists nevertheless.
Interpretive simulation with the integrated tokamak simulator, TRIASSIC(Tokamak Reactor Integrated Automated Suite for Simulation and Computation)* (#26381)

## Slide 10
The reproducibility of occurrence of the new current
This phenomenon is also observed in other discharges, - #29955, #31670: EC with gas puffing (PVD*) instead of SMBI - #31858: Ohmic (no EC) with gas puffing (PVD)
It is apparent that the relation between Te-1.5 (∝η) and VL/Ip in #26381, #29955, #31670, and #31858 diverges from the ohmic relation after the fueling
The trajectory of (η) versus
→ Robust appearance of a new current after the fuelling
*Piezoelectric valve at D-port
reference
EC+PVD
EC+PVD
OH+PVD

## Slide 11
The overviews of PVD discharges, #29955 and #31858
In both shots, PVD instead of SMBI increases the plasma density from t = 3 s to 5 s.
The induced loop voltage remains almost constant even though the electron temperature and the plasma resistivity significantly change.
The internal inductance is also lowered in the same manner as #26381 and maintained after the fueling turned off.
→ The observation of the anomalous current drive is not a special effect caused by SMBI and seems to be related to the level of the density or the collisionality.

## Slide 12
The overviews of PVD discharges, #29955 and #31858
In both shots, PVD instead of SMBI increases the plasma density from t = 3 s to 5 s.
The induced loop voltage remains almost constant even though the electron temperature and the plasma resistivity significantly change.
The internal inductance is also lowered in the same manner as #26381 and maintained after the fueling turned off.
→ The observation of the anomalous current drive is not a special effect caused by SMBI and seems to be related to the level of the density or the collisionality.
Where does this current come from?

## Slide 13
Turbulence driven current?
Kinetic profiles and current density profiles in #26381
Since the anomalous current density is mainly at the off-axis region where the electron temperature gradient is high, there is a possibility that the micro-instabilities such as TEM or ETG mode could drive this additional electric current in this region.

## Slide 14
Evidence that turbulence does not drive the anomalous current (I)
It shows that the electron turbulence is sub-dominant during the whole discharge, and instead, ITG modes are most unstable.
This happens despite Te-profile peaking, probably due to the favorable role of high Te/Ti for the ITG excitation.
Those ITG modes become slightly mitigated after SMBI is applied.
Linear gyro-kinetic analysis by GKW at 𝝆𝑵 = 𝟎.𝟒 in #26381

## Slide 15
Evidence that turbulence does not drive the anomalous current (II)
The level of the additional current driven by the turbulence is notable.
However, considering that the bootstrap current is less than 5 % of the total current, the additional current by the turbulence is not enough to explain the amount of anomalous current observed in the experiment, about 30 % of the total current.
Non-linear gyro-kinetic analysis by GTS at 5 s in #26381

## Slide 16
Evidence that turbulence does not drive the anomalous current (III)
Fluctuation coherence from ECEI in #26381
The fluctuation data measured by ECEI exhibits similar trends with the linear stability analysis.
Before SMBI is applied, fluctuations are observed in the core region and also slightly in the edge region, which are in the ion-diamagnetic direction.
After SMBI, the core fluctuation is mitigated and the edge fluctuation vanishes, whereas the anomaly in the current appears.
→ The anomalous current observed after SMBI is not likely to be driven by the long-wavelength turbulence measured by ECEI.
SMBI

## Slide 17
Evidence that turbulence does not drive the anomalous current (IV)
Comparison of two identical discharges except PEC, #26380 (~1.3 MW) and #26381 (0.6 MW)
#26380
#26381
In #26380, due to the higher EC heating, the electron temperature is higher and the resulting turbulent fluctuations are also stronger.
However, the anomalous current gap exists only in the lower EC heating case, #26381.
There is no new appearance of a fluctuation and the existing fluctuations become even diminished when the anomalous current drive occurs.

## Slide 18
Conclusion
We report a conclusive experimental evidence of a new self-generated current observed in the KSTAR tokamak.
In dedicated experiments with minimized known external and self-generated current drives, we observed an anomalous current gap that is not explained with present theories.
It is a robust phenomenon with high reproducibility observed in a specific electron temperature and density range when density fuelling is applied.
Our studies have not found any supporting evidence for the existing current drive mechanisms so far including those related to micro-instabilities with long-wavelength.
It is required to understand this novel current drive mechanism for its steady-state operation scenario application. - Extend turbulence measurements to a broader kθ-range including shorter wavelengths - Perform further global non-linear gyrokinetic simulations followed by detailed analyses - Evaluate zonal flows which regulate turbulence and nonlocal phenomena - …
Yong-Su Na, Jaemin Seo, et al, Nature Comm. 13 6477 (2022)

## Slide 19
Thank you

## Slide 20
[1019m-3]
#26381(SMBI)
#29955(PVD)
#26354(no fuel)
#31670(PVD)
#31858(PVD)
5.5s
2.15s
2.15s
5.5s
2.15s
5.5s
2.25s
5.0s
* #31858(PVD): Ohmic
#26381(SMBI)
#29955(PVD)
#26354(no fuel)
#31670(PVD)
#31858(PVD)
5.5s
2.15s
2.15s
5.5s
2.15s
5.5s
2.25s
5.0s

## Slide 21
#26381(SMBI)
#29955(PVD) (X)
#26354(no fuel)
#31670(PVD)
#31858(PVD)

## Slide 22
#26354(no fuel)
#26381(SMBI)
#31670(PVD)
#31858(PVD)
①
②
①
②
①
②
③
①
②
③
2.0 – 2.5 s | Red
2.5 - 3.0 s | Orange
3.0 – 3.5 s | Yellow
3.5 – 4.0 s | Green
4.0 – 4.5 s | blue
4.5 – 5.0 s | navy
5.0 – 5.5 s | purple
5.5 – 6.0 s | grey
6.0 – 6.5 s | black
#26354(no fuel)
#26381(SMBI)
#31670(PVD)
#31858(PVD)
무지개 색깔 순서