## Slide 1: The National Spherical Torus Experiment Upgrade – Advancing the Physics of Fusion Energy Dr. Jack Berkery, Princeton Plasma Physics Laboratory March 1, 2024, University of Minnesota

## Slide 2: Outline
Introduction
  Princeton Plasma Physics Lab (PPPL)
  Quick fusion overview
  Tokamaks, spherical tokamaks
The National Spherical Torus Experiment Upgrade (NSTX-U)
  Upgraded magnets, heating, current drive
  Testing the physics of: particle and energy confinement and turbulent transport, long-pulse operation with driven current, potentially damaging instabilities, handling very high heat fluxes
Spherical Tokamaks being considered as Fusion Pilot Plants
  NSTX-U will provide the physics knowledge for confident projection

## Slide 3: The Princeton Plasma Physics Laboratory
One of 17 Dept. of Energy National Labs
Managed by
Magnetic fusion research at Princeton began as a classified government project in 1951 under renowned physicist Lyman Spitzer Jr., using the code name “Project Matterhorn.”
PPPL Today: 700+ employees, $150 Million+ government funding, 300+ annual publications

## Slide 4: Fusion requires very high temperatures, but these can be achieved
D: deuterium
T: tritium
n: neutron
α: helium
E = mc2
“D-T” fusion reaction:
Fusion is easiest here at 200 million °C (!!)
  Requires lowest pressure nT and energy confinement time τE
  Minimum fusion “triple-product” value: 8 atmosphere-seconds
Magnetic fusion has already achieved the necessary high T
TFTR at PPPL (1990’s)
core
boundary
~250 million C

## Slide 5: How close are we, really, to achieving fusion breakeven?
NSTX-U?
NSTX-U is a research device meant to investigate physics – it will never breakeven
New wave of public, and private(!) fusion devices aim to get there soon

## Slide 6: Tokamaks and stellarators are leading magnetic fusion configurations
Tokamak advantages:
  Best confinement, closest to “breakeven”
  Simpler planar coils and power exhaust
Disadvantages:
  Must drive multi MA plasma current
  Prone to rapid loss of plasma = “disruption”
Superconducting tokamak
KSTAR (Korea)
Superconducting stellarator
W7X (Germany)
Stellarator advantages:
  No plasma current drive necessary
  More stable, steady state
Disadvantages:
  More complex coils and exhaust
  Confinement < tokamaks (so far)

## Slide 7: NSTX-U is a spherical tokamak (ST), which has certain advantages
a
R
a
b
Challenges :
  Managing the high heat flux
  Start-up and sustainment of the plasma without as much space in the center column for an induction coil
Toroidal beta βT = p / (BT02/2μ0)
Aspect Ratio A = R /a
A ~ 2.5-4
κ = 1.5-2
βT = 3-10%
A ~ 1.3-2
κ = 2-3
βT = 10-40%
Tokamak
ST
Plasma spends less time in unstable curvature region
Elongation κ = b/a
STs are lower aspect ratio, have natural higher elongation
  Higher elongation and favorable average curvature improves stability, confinement
  Smaller size can mean lower cost

## Slide 8: NSTX-U at PPPL is the highest power spherical tokamak in the world
NSTX-U
National Spherical Torus Experiment-Upgrade

## Slide 9: NSTX-U at PPPL is the highest power spherical tokamak in the world
NSTX-U
National Spherical Torus Experiment-Upgrade

## Slide 10: Add some of the highest achievements of NSTX?

## Slide 11: NSTX energy confinement time increased at higher T (!)
Will the confinement trend continue, or look like conventional aspect ratio?
Favorable confinement results could lead to more compact ST reactors
For low collisionality, need:
  Higher plasma current
  Higher toroidal field
  Higher heating power
  Density control
Normalized electron collisionality ne*  ne / Te2
Higher A scaling
ST Pilot Plant
?
constant q, b, r*
NSTX Upgrade
NSTX

## Slide 12: NSTX-U is currently getting an upgrade which will boost performance
Tangential 2nd Neutral Beam
New Central Magnet
2× toroidal field (0.5  1 T)
2× plasma current (1  2 MA)
5× longer pulse (1  5 s)
2× heating power (5  10 MW)
2× current drive efficiency (tangential NBI)
NSTX-U will access new physics regimes
4× divertor heat flux
Up to 10× higher nTτE (~MJ stored energy)
Higher T  lower particle collisionality
  Unique regime at high β, study new transport and stability physics
Full non-inductive current drive
  Not demonstrated in high β ST
  Essential for future steady-state ST

## Slide 13: To move towards long-pulse operation, STs need to move to non-inductive current drive and stable, steady-state plasmas
Currently NSTX discharges only last about 1 second
What is the source of current?
  Ohmically induced
  Neutral beams and RF heating
  “Bootstrap” current
    Sounds magical, but plasmas create their own current! Density gradients mean more charged particles are moving in one direction than another
NSTX-U projects to 100% non-inductive operation
  Thanks to the new beam
Plasma current in tokamaks is a large source of free energy – can lead to instabilities (next slide)

## Slide 14: Tokamaks are subject to instabilities, which can be disruptive and dangerous
Force balance: when β gets too high, plasmas can develop kink or ballooning instabilities
  These can grow (quickly!), lead to a sudden loss of particle confinement and dump energy, damaging surfaces
But, microscopic motions of particles in the plasma can resonate with the motion of the magnetic field and sap the energy of the mode, stabilizing it
  Particles in plasmas follow complicated motions: bouncing, gyrating, drifting…
Accounting for this effect in NSTX explained plasma stability/instability
Bp
Modelled NSTX distortion (exaggerated)
Measured NSTX growth
Exponential
6ms!
Normalized growth rate
Normalized time to instability
Predictions of experimental instabilities
Experimentally stable

## Slide 15: Ultimately the amount of fusion reactions depends on how high a temperature and density can be sustained, and this is determined by turbulent transport
“Gyrokinetics” follows particle motions and the turbulent eddies they create
Turbulence leads to particle transport and profiles are set up as a balance between fueling and loss
“Pedestal” predictions from large A scalings did not work for NSTX
  Gyrokinetic modeling does!
  STs can have wider pedestals
Another “mode” of instability: edge-localized modes (ELMs)
  High-confinement pedestals collapse periodically, releasing a lot of energy
ELMs in MAST (UK ST)
Pedestal height (normalized)
Pedestal width (norm.)
NSTX
Gyrokinetics
Large A scaling

## Slide 16: Tokamaks use a ‘’divertor” to control where power and particles are exhausted
NSTX-U 2MA
?
Tokamak + ST data: power exhaust width varies as 1/Bp
Issue: if peak heat flux in divertor region exceeds ~ 10 MW/m2 it can lead to material damage
Simulations predict NSTX-U may be different
Wider heat-flux width may offset smaller R, may be better than tokamak
Power / particles contact target plates here
Power exhaust width outside main plasma can be very narrow (few mm)
Turbulence may spread the width
Simulations
Experiment
Magnetic field strength [T]
Layer width [mm]

## Slide 17: Liquid metal walls have proven beneficial for heat handling, plasma performance
Lithium handles high heat fluxes (especially if it is flowing) and captures ions escaping the plasma rather than reflecting cold neutrals back in
NSTX-U explored the benefits of lithium walls by coating the divertor tiles
LTX-β, a smaller ST at PPPL with liquid lithium walls
Liquid lithium divertor design for NSTX-U
  Improved energy confinement time
  Reduction of impurities
  Suppression of ELM instabilities at the plasma edge

## Slide 18: There is already substantial interest in a low-A tokamak as a Fusion Pilot Plant
United Kingdom: Spherical Tokamak for Energy Production (STEP)
Tokamak Energy, Ltd.: high-temperature superconducting devices
PPPL: ST Advanced Reactor (STAR) (design study)
  Understand advantages and disadvantages of ST for a reactor
  Develop high fidelity physics and engineering models
STAR
R = 4 m, A = 2,
BT = 5.2 T, κ = 2.2
Pfus ~ 1 GW,
Pnet ~ 100-500 MWe
Tokamak Energy
ST40
Future Pilot Plant

## Slide 19: Conclusions
The National Spherical Torus Experiment at the Princeton Plasma Physics Lab is investigating the physics of magnetic confinement fusion
  NSTX-U is undergoing an upgrade and is designed to be the highest performance ST in the world
Spherical Tokamaks have certain known advantages, but also open questions
  Non-inductive operation, instabilities, turbulent transport, power handling
The ST concept is under consideration for a Fusion Pilot Plant
  NSTX-U will provide the physics knowledge for confident projection

## Slide 20: PPPL science education department has many opportunities for students
Workshop in Plasma Physics for Undergrads
  Meant for freshman or sophomores
  June 25-28, 2024
  Application closes April 9th
pppl.gov/education
science-education@pppl.gov

## Slide 22: Graduate Study
300+ alumni over a 60+ year program
Program in Plasma Physics, a graduate program in the Dept. of Astrophysical Sciences at Princeton University, based at PPPL.

## Slide 24: Advantages of fusion: safe, sustainable, high energy density, environmentally attractive
Cannot have runaway reaction
  Only small amount of fuel present
  If particles cool, fusion stops
Abundant fuel supply
  D from seawater: HDO, D/H = 1/6400
  T bred from lithium in earth’s crust
High energy density
  1 liter water = 500 liters gasoline
Waste short-lived, low-level
No CO2 production
D: deuterium
T: tritium
n: neutron
a: helium

## Slide 25: At fusion temperatures gas becomes plasma, a “soup” of electrons and positive ions
Water:
0 ᵒC
100 ᵒC
160,000 ᵒC
DT fusion:
200,000,000 ᵒC
At fusion temperatures, particles are so energetic that electrons are stripped from neutral atoms leaving positively charged (+) ions

## Slide 26: Charged particles confined by magnetic fields, but a simple toroidal field gives poor confinement
Charged particles spiral around field lines, move freely along field
Bending field into torus creates non-uniform B~1/R
Electrons and ions drift apart vertically  charge separation
Electric field created  particles expelled outward
R

## Slide 27: Tokamak: toroidal field from magnets and poloidal field from plasma current + create helical field
Position many coils into a donut or “torus” shape
Magnetic field never touches the walls
With plasma current: Helical field = B-field covers toroidal surfaces
Short-circuits electric fields that would otherwise expel plasma
Particles tied to surface and theoretically never touch the walls either
“Tokamak”: Russian acronym for “toroidal chamber with magnetic coils”
× 10-20

## Slide 28: Particle trajectories in a tokamak

## Slide 29: To move towards long-pulse operation, STs need to move to non-inductive current drive and stable, steady-state plasmas

## Slide 30: Magnetic fusion is arguably closest to ultimate goal of electricity generation
Charged particle
Magnetic field
Magnetic
Confinement
Inertial
Confinement
Fuel Pellet
Intense Energy
Beams
Gravitational
Confinement
Fusion
Gravity
Sun
Requires at least ~7% mass of sun
And 10x diameter of Earth
Laser fusion has at best Efusion/Eelectrical ~ 5%
Lots of efficiency losses from wall plug to energy out
ITER, being constructed in France, aims for ~500 MW fusion power for similar level of electrical input

## Slide 31: How would magnetic fusion make electricity?
Spin turbines, generate electricity
Steam or hot helium
Magnets
(-270 - 100ᵒC)
Heat
Blanket
(350 - 1000ᵒC)
helium and deuterium exhaust
Tritium bred from lithium in blanket
External heating
(10’s of MW)
Plasma
(100 million ᵒC)
α self heating
Neutrons

## Slide 32: xxx
xxx

## Slide 33: xxx
xxx

## Slide 34: xxx
xxx

## Slide 35: xxx
xxx